JETPAK

                  DeskJet and LaserJet Printer Utilities

                 For IBM PC and compatibles running MSDOS



                                     by

                               Ross Beresford



                         Version 1.1 (Public Domain)

                              4th August 1991





        MANIFEST
        --------

        The MSDOS release of JETPAK 1.1 (Public Domain) should contain
        the following files:

                MSDOS11.DOC     This document
                JETPAK11.DOC    JETPAK manual
                JETL2D.EXE      LJ to DJ soft font conversion program
                JETD2L.EXE      DJ to LJ soft font conversion program
                JETPRINT.EXE    Summary sheet printing program
                JETPRD.EXE      Printer description file program
                JETDMP.EXE      Soft font dump program
                JETRST.EXE      Soft font restore program


        INTRODUCTION
        ------------

        This file contains usage information specific to the IBM PC
        platform running MS-DOS. General information about the
        utilities can be found in JETPAK11.DOC.




        JETL2D [-h] [-j] [-o] [-t filetype] ljfontfile [ljfontfile...]


        This program converts LaserJet soft font files into the format
        used by DeskJet printers.



        [-h]            This option prints usage information about
                        JETL2D on the screen


        [-j]            The jaggy option: you can disable the bitmap
                        optimisation feature by specifying this.


        [-o]            The old DeskJet option: by default, JETL2D now
                        creates DeskJet 500 format fonts. If you have
                        an original DeskJet or a DeskJet PLUS, you
                        must specify this option, or the output font
                        will be rejected by the printer.


        [-t filetype]   By default, JETL2D names its output files
                        after its input files, but with a .L2D suffix.

                        This option allows you to specify that
                        'filetype' should be used as the suffix.


        ljfontfile      This parameter specifies the name of a
                        LaserJet soft font file to be converted and
                        must be given at least once.

                        A number of LaserJet soft font file parameters
                        may be specified, and each may contain the
                        standard MS-DOS wildcards.



        JETD2L [-h] [-t filetype] djfontfile [djfontfile...]


        This program converts DeskJet soft font files into the format
        used by LaserJet printers.



        [-h]            This option prints usage information about
                        JETD2L on the screen


        [-t filetype]   By default, JETD2L names its output files
                        after its input files, but with a .D2L suffix.

                        This option allows you to specify that
                        'filetype' should be used as the suffix.


        djfontfile      This parameter specifies the name of a DeskJet
                        soft font file to be converted and must be
                        given at least once.

                        A number of DeskJet soft font file parameters
                        may be specified, and each may contain the
                        standard MS-DOS wildcards.




        JETPRINT [-h] fontfile [fontfile...]


        This program prints summary sheets for soft font files to the
        default standard printer device PRN.



        [-h]            This option prints usage information about
                        JETPRINT on the screen


        fontfile        This parameter specifies the name of a soft
                        font file to be printed and must be given at
                        least once.

                        A number of soft font file parameters may be
                        specified, and each may contain the standard
                        MS-DOS wildcards.




        JETPRD [-h] [-t filetype] fontfile [fontfile...]


        This program generates a printer descriptor file which
        contains the information required by word processors to select
        and justify a soft font.



        [-h]            This option prints usage information about
                        JETPRD on the screen


        [-t filetype]   By default, JETPRD names its output files
                        after its input files, but with a .PRD suffix.

                        This option allows you to specify that
                        'filetype' should be used as the suffix.


        fontfile        This parameter specifies the name of a soft
                        font file to be processed and must be given at
                        least once.

                        A number of soft font file parameters may be
                        specified, and each may contain the standard
                        MS-DOS wildcards.




        JETDMP [-h] [-t filetype] fontfile [fontfile...]



        This program creates a symbolic dump file for a soft font.



        [-h]            This option prints usage information about
                        JETDMP on the screen


        [-t filetype]   By default, JETDMP names its output files
                        after its input files, but with a .DMP suffix.

                        This option allows you to specify that
                        'filetype' should be used as the suffix.


        fontfile        This parameter specifies the name of a soft
                        font file to be dumped and must be given at
                        least once.

                        A number of soft font file parameters may be
                        specified, and each may contain the standard
                        MS-DOS wildcards.




        JETRST [-h] dumpfile [dumpfile...]



        This program restores soft font files from symbolic dumps.



        [-h]            This option prints usage information about
                        JETRST on the screen


        dumpfile        This parameter specifies the name of a dump
                        file to be restored and must be given at least
                        once.

                        A number of dump file parameters may be
                        specified, and each may contain the standard
                        MS-DOS wildcards.