***************************** DISK & FILE *******************************

ASMLIB disk & file subroutines (c) Copyright 1991 Douglas Herr
All rights reserved

The MS-DOS file attribute byte tells you whether a file is read-only,
system, a subdirectory, or may provide other information.  File attribute
bits may be combined.  Each bit of the file attribute means:

        0 = normal files
        1 = read-only
        2 = hidden files
        4 = system files
        8 = volume label (only one per disk)
       16 = subdirectories
       32 = archive bit set

   Thus a file with an attribute of 18 is a hidden subdirectory (16 OR 2)

°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

DISKWP:      determines if a floppy disk is write-protected
Source:      diskwp.asm

Call with:   DL = floppy disk number (drive A: = 0)
Returns:     AL = BIOS error code
                0 = no error
                1 = invalid disk number
                3 = disk is write-protected
              128 = drive not ready
Uses:        AX, flags
Example:

include asm.inc

public  mycode
extrn   diskwp:proc

.code
diskwp  proc
        .
        .
        .
        mov     dl,1        ; drive B:
        call    diskwp      ; can I write to this disk?
        or      al,al
        jz      no_problem




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCOPY:       copy a file
FCOPYM:      copy a file using supplied memory buffer
Source:      fcopy.asm

Call with:   DS:[SI] = address of source filename
             ES:[DI] = address of destination filename
             Both filenames must be ASCIIZ strings.  Drive and path need
             not be fully specified; filenames may not include * or ?
             wildcards.
             FCOPY only: Requires 64k DOS memory available
             FCOPYM only: AX = segment address of 64k buffer
Returns:     if CF = 0, no problem
             if CF = 1, AX = DOS error code (AX = -1 if insufficient memory)
Uses:        AX, CF
Example:

.data
        db 'b:'
source  db 'asmlib.lib',0         ; copy the library to b:

extrn   fcopy:proc
.code
; program fragment assumes DS:@data
        .
        .
        push    ds
        pop     es
        assume es:@data
        lea     si,source
        mov     di,si                ; DI also points to source
        sub     di,2                 ; back the pointer to the 'B:'
        call    fcopy
        jc      oops




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FCOUNT:      counts the number of files matching an ASCIIZ filespec string.
             The filespec string may include the '*' and '?' wildcards.
Source:      fcount.asm

Call with:   DS:[DX] pointing to filespec string
             CX = file attributes
             assumes DS:@data
Returns:     AX = number of files matching the filespec string
Uses:        AX, all other registers and flags are saved
Example:

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    dx,filespec      ; address of filespec string
        xor    cx,cx            ; normal files only
        call   fcount


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FEXIST:      determines if a file exists and can be opened with read access
Source:      fexist.asm

Call with:   DS:[DX] pointing to ASCIIZ filename
Returns:     if CF = 0, file exists
             if CF = 1, AX = MS-DOS error code
Uses:        AX, CF; all other flags and registers are saved
Example:

include  asm.inc

extrn    fexist:proc
.data

filename db 'asmlib.doc',0

.code
; program fragment assumes DS:@data
         .
         .
         .
         lea   dx,filename
         call  fexist
         jnc   got_the_file      ; if CF = 0, go on
         jmp   doserror          ; else go to error handling code




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FFLUSH:      flushes the DOS output buffer for specified handle
Source:      fflush.asm

Call with:   BX = file handle
             flushing the buffer guards against data loss in case of system
             failure, such as power loss
Returns:     if CF = 0, no error; function successful
             if CF = 1, AX = DOS error code
Uses:        AX, flags
Example:

include asm.inc

extrn fflush:proc

.code
; program opens file & writes to file
      .
      .
      mov    bx,handle
      call   fflush




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FGETSTR:     read an ASCII string from an open file
Source:      fgetstr.asm

Call with:   BX = file handle
             ES:[DI] pointing to memory buffer
             CX = byte length of buffer
             ASCII strings may be terminated with either 0Dh or 0Dh+0Ah.
             After reading each string, FGetStr positions the file pointer
             to read the next string.  The memory buffer should be at
             least 2 bytes longer than the longest string you expect to
             read.
Returns:     if CF = 0, CX = length of ASCII string
                     if CX = byte length of buffer, string >= size of buffer
             if CF = 1, AX = DOS error code
                     if AX = 0, you've reached the end of the file
Uses:        AX, CX, CF; all other registers and flags are saved
Example:

include   asm.inc

extrn     fgetstr:proc

.data
strbuffer db 102 dup (0)         ; maximum string length is 100

.code
; program opens file with read or read/write access
          .
          .
          .
          mov   bx,file_handle
          mov   cx,102          ; buffer size
          push  ds
          pop   es              ; ES = DS
          lea   di,strbuffer    ; ES:[DI] points to start of buffer
          call  fgetstr
          jc    oops
          mov   bx,di           ; minor parameter juggling
          call  strndup         ; make a copy in near heap so I can re-use
                                ; the buffer
          .
          .
          .




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FILELIST:    creates a list of file names matching a filespec mask
Source:      filelist.asm (fcount.asm, dosalloc.asm)

Call with:   DS:[SI] pointing to filespec mask
             CX = file attribute mask
Returns:     if CF = 0:
               ES = base segment address of list buffer
               AX = number of filenames in list
               CX = list field width
             if CF = 1, AX = MS-DOS error code
             You should use DOS function 49h to release the file list
             buffer when you're done with it.
Uses:        AX, CX, ES, CF
Example:

include asm.inc

public  myproc

.data
filespec db '*.*',0

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    si,filespec
        mov    cx,16            ; normal files and subdirectories
        call   filelist
        jc     cant_do_it       ; oops




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FINDDATE:    given a successful call to FindFirst or FindNext, returns
             the file's date stamp
Source:      findfile.asm

Call with:   DS:[BX] pointing to DTA buffer; assumes DS  @DATA
Returns:     DX = month
             AX = day
             CX = year
Uses:        AX, CX, DX, flags
Example:

.code
; program fragment assumes DS:@data
        .
        .
        .
        lea    bx,filespec
        mov    cx,0              ; normal files only
        call   findfirst         ; find first matching file
        jc     no_more_files
        cmp    ax,-1
        je     no_more_files
        call   finddate




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FINDFIRST:   This subroutine, when used with FindNext, finds files on
             a disk which match an ASCIIZ filespec string.  The filespec
             string may contain the '*' and '?' wildcards.
Source:      findfile.asm (heap.asm)

Call with:   DS:[BX] pointing to ASCIIZ filespec string; assumes DS:@data
             CX = file attribute mask

             FindFirst allocates space for a local DTA buffer from the
             near heap.  See FindNext; also see HINIT.

Returns:     AX = error code
             -1 = insufficient memory in near heap (128 bytes required)
             0 = no error
             CF = 1 if no files match the filespec string
             DS:[BX] -> DTA buffer if the subroutine is successful.  Do not
             alter the 128 bytes in the DTA buffer.
             The name of the file is an ASCIIZ string at 30[BX]
             The file attribute is a byte at 21[BX]
             The low word of the file's size is at 26[BX]
             The high word of the file's size is at 28[BX]
Uses:        AX, BX, flags
Example:

.code
; program fragment assumes DS:@data
     .
     .
     .
     lea    bx,filespec
     mov    cx,0              ; normal files only
     call   findfirst         ; find first matching file
     jc     no_more_files
     cmp    ax,-1
     je     no_memory         ; memory not available

; print the filename on the screen
tprint_next:
     mov    si,bx
     add    si,30             ; point to filename in DTA buffer
     mov    dh,count          ; row value
     mov    dl,0              ; column 0
     mov    ah,12             ; color attribute - RED!
     call   tprint            ; display the file name on the screen
     inc    count             ; next filename on next row
     call   findnext          ; any more matching filenames?
     jnc    tprint_next
no_more_files:


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FINDNEXT:    finds file matching search string; use after FindFirst.
             used only after a successful call to FindFirst.
Source:      findfile.asm (heap.asm)

Call with:   no parameters; assumes DS:@data

             FindNext de-allocates the DTA buffer space after the first
             unsuccessful search for a matching file.

Returns:     DS:[BX] -> DTA buffer
             CF = 1 if no more files match the filespec string.
Uses:        BX, flags
Example:     see FindFirst.


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FINDTIME:    given a successful call to FindFirst or FindNext, returns
             the file's time stamp
Source:      findfile.asm

Call with:   DS:[BX] pointing to DTA buffer; assumes DS:@data
Returns:     DX = hour
             AX = minute
             CX = second
Uses:        AX, CX, DX, flags
Example:     lea    bx,filespec
             mov    cx,0              ; normal files only
             call   findfirst         ; find first matching file
             jc     no_more_files
             cmp    ax,-1
             je     no_more_files
             call   findtime




°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FPUTCR:      writes a CR+LF pair to a file at the current position in
             the file; the file must have been opened with read or
             read/write access
Source:      fputcr.asm

Call with:   BX = file handle
Returns:     if CF = 1, AX = MS-DOS error code
             if CF = 0, no error
Uses:        AX, flags
Example:     mov    bx,handle
             call   fputcr


°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

FSIZE:       determines a file's size
Source:      fsize.asm

Call with:   BX = valid file handle
Returns:     if CF = 0, DX:AX = file size (low word in AX)
             if CF = 1, AX = MS-DOS error code
Uses:        AX, DX, CF
Example:

include asm.inc

extrn   fsize:proc

.data
filenam db 'ASMLIB.DOC',0      ; ASCIIZ filename

.code
        .
        .
        .
        lea     dx,filenam     ; point to filename
        mov     ax,3D00h       ; MS-DOS open file function, read-only
        int     21h
        jc      oops           ; jump to error control
                               ; else no problem - continue
        mov     bx,ax          ; file handle in BX
        call    fsize



°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

QFNAME:      qualifies a filename
Source:      qfname.asm

Call with:   DS:[BX] pointing to a filename; the filename may contain
             drive specification and/or complete or partial path name.
             Drive specification and path name not required.
Returns:     DS:[SI] pointing to the full DRIVESPEC:\PATH\FILENAME
             CX = length of full filename
             Note that DS:[SI] points to QFName's buffer space; the next
             call to QFName will return a new filename at the same address.
Uses:        SI, CX, flags
Example:

include asm.inc

.data
docs   db '*.doc',0         ; search for .DOC files in current directory

.code
; program fragment assumes DS:@data
       .
       .
       .
       lea    bx,docs
       call   qfname