Nicholas Wilt
	 Thermopress Marketing, Inc.
	 24 Harrison Circle
	 Pittsford, NY	14534-4109

	 User's Manual for the Extended Memory Interface Library

	 The Extended Memory Interface Library gives C programmers of
	 MS-DOS applications access to extended memory by interfacing
	 with the HIMEM.SYS extended memory manager.  It will let your
	 programs access extended memory on any machine with HIMEM.SYS
	 installed, including the millions of computers running
	 Windows 3.0.

	 There are several advantages to using the Interface Library.
	 First and foremost, it makes extended memory available to the
	 DOS programmer.  Second, the access is "polite": a DOS
	 application can access extended memory even when running in a
	 DOS shell under Windows.  Finally, the disparate memory
	 management capabilities of the 286 and 386 are transparently
	 supported by HIMEM.SYS, so programmers using the Interface
	 Library need not worry about CPU autodetection or protected
	 mode issues.

	 The freely distributable portion of the library consists of
	 the following files:

	 File		Description
	 userman.doc	This documentation file
	 order.doc	Order form for the source code and technical
			manual
	 hi.h		C header file for the library
	 hi.hpp 	Turbo C++ header file for the library
	 hi.obj 	FAR code object module for the library
	 makefile	Makefile to build testhi.exe
	 testhi.prj	Turbo C++ .PRJ file to build testhi.exe
	 testhi.c	C source file to demonstrate how to use the
			library
	 testhi.exe	Compiled and linked executable for testhi.c

	 The Library consists of a header file and an object module.
	 The object is FAR-callable, so the functions have all been
	 declared "far" in the header file.  The object has been
	 tested for use with Microsoft C and Turbo C and C++.  To use
	 it, you must link against hi.obj.  This may be accomplished
	 by adding "hi.obj" to the Project in the Turbo C++ IDE, or
	 adding "hi.obj" to the linker command line.  TESTHI.PRJ and
	 MAKEFILE illustrate each technique.

	 The hi.hpp header file has been included for C++ users.  It
	 declares the functions with a "C" qualifier so the C++
	 compiler knows not to mangle the function names.  If you are
	 using C++, you should include hi.hpp rather than hi.h.

	 If you use the Extended Memory Interface Library, I request
	 that you register your copy.  In exchange, I will send you
	 the assembler source code and a technical manual (on
	 electronic media) describing how it works.  See the order
	 form for details.






	 Using The Library

	 Extended memory locations are specified as handle/offset
	 pairs.  The handle is a return value from himalloc(); it is a
	 protected mode segment descriptor, and specifies a block of
	 extended memory.  Certain functions which operate on blocks,
	 such as hifree(), hilock(), and hiunlock(), take only the
	 handle.  The offset is used to pinpoint a location in
	 extended memory; it is passed to hi2real() and real2hi().

	 The function interface to the library is described below.
	 The source files (testhi.c and hi.h) provide a lot of
	 guidance as well.

	 int pinghi();
		This function returns nonzero if HIMEM is installed.

	 void hiinit();
		This function must be called once before any other
	     function in the library (except pinghi()).

	 unsigned long hicontig();
		Returns the size of the largest contiguous chunk of
	     memory.

	 unsigned long himemavl();
		Returns the total amount of extended memory available.

	 unsigned himalloc(unsigned long size);
		This function allocates extended memory and returns a
	     handle (actually a protected-mode segment descriptor) to
	     it.  Returns 0 if the memory cannot be allocated.

	 void hifree(unsigned handle);
		This function frees memory allocated by himalloc().

	 hilock(unsigned handle);
	 hiunlock(unsigned handle);
		These functions lock (write-protect) and unlock the
	     memory pointed to by the given handle.

	 hi2real(void far *dest,
		 unsigned src,
		 unsigned long offset,
		 unsigned count);
	 real2hi(unsigned dest,
		 unsigned long offset,
		 void far *src,
		 unsigned count);

		These functions copy to/from extended memory.  real2hi
	 copies from the DOS memory location specified by src to an
	 extended memory location specified by the dest/offset pair.
	 hi2real copies from an extended memory location specified by
	 the src/offset pair to the DOS memory location specified by
	 dest.

	 Return value: 1 if successful, 0 if not successful.

	 IMPORTANT: THE BYTE COUNT MUST BE EVEN.



	 Caveats

	 - If your program crashes on the first call into the library,
	   you probably neglected to call hiinit().  You don't do any
	   harm calling hiinit() even if HIMEM is not present, so
	   unconditionally executing it first is the way to go.
	 - Avoid allocating small objects.  There are two reasons for
	   this:
		- HIMEM allocates memory in increments of 1K.
		- Intel processors have a limited number of segments
		  available (several thousand), so it is wise to
		  allocate large chunks and dice them up using the
		  offsets.
	 - Check return values.  real2hi(), in particular, can catch
	   protected-mode violations such as trying to write beyond a
	   handle's allocated space.
	 - Since DOS knows nothing about extended memory, it can't
	   know to free allocated chunks of extended memory when your
	   application exits.  You are responsible for hifree()'ing
	   all the extended memory you allocate.

	 -------------------------------------------------------------

	 Comments and suggestions are always welcome.  I may be
	 reached at the above address, or at my Internet address
	 (npw@eleazar.dartmouth.edu).