___________________________________________________________________________
                Power Glove Interface for Parallel Port on IBM
___________________________________________________________________________

Nintendo connector layout:   *1      1:Ground           2:Clock
                         7*  *2      3:Latch            4:Data
                         6*  *3      5:N/C (lightgun)   6:N/C (lightgun)
                         5*  *4      7:+5V

Connecting to Parallel Port

                Glove        Printer Port
                1            18 GND
                2            2 DO
                3            3 D1
                4            13 SLCT (input)

___________________________________________________________________________
                             POWER
___________________________________________________________________________
     Connect pin 7 on the glove to any location with +5V on the computer.
     Pin 1 on any gameport is a good place.  You can also use the keyboard
     connector.  On an XT pinout, the +5V connector is pin 5 as follows:
                        Looking at the back of the computer:
                                3    1
                                5    4
                                  2
            Be sure to check the voltage for any other configuration!


___________________________________________________________________________
                             The CABLE
___________________________________________________________________________
You can buy Nintendo extender cable to cut up for the connector... Get the 
longest possible for easy location of the control box...



___________________________________________________________________________
                             The CODE
___________________________________________________________________________
If you don't get steady sampling on the glove, try adjusting the timing on 
your machine by changing the N & D defines...

The Code is currently set for LPT2. (Inport=0x279, Outport=0x278).  For 
LPT1, change Inport to 0x379 and Outport to 0x378...

The code is written for Turbo C/C++/Borland C++.  It uses the BGI library 
for the graphics cursor, so it is easily ported to Microsoft C.

The code is named THEGLOVE.C

___________________________________________________________________________
                              NOTES
___________________________________________________________________________
This is reprinted from Waite Group's "Virtual Reality Playhouse", but they
swiped it from the VR boys on USENET so I don't feel bad about porting it.
Please distriute this freely...






___________________________________________________________________________