Installation instructions and documentation (from sockd help)
 _____________________________________________________________


   The multi-threaded socks server for OS/2 enables to build a
  firewall  gateway on an OS/2 (Warp) system. The objective is
  just to interconnect small TCP/IP PC  Lan  with  the  public
  network (through a "Service Provider").

    Like  in  all  "standard"  sockd server, the protection is
  build in a configuration file (sockd.cfg in the  ETC  direc-
  tory).

    Access  is  controlled with two statements "deny" or "per-
  mit".  Origin address and subnet mask  and  destination  ad-
  dress  and  mask  can  be  checked  for  a  destination port
  number...

  For applications using socks version 4 protocol the support
   is only for TCP application due to the protocol stack.

   The current version has  support  for  three  LAN  adapters
  (LAN0,  LAN1  and  LAN2), and two SLIP or PPP adapters (sl0,
  sl1, ppp0 and ppp1).  One of the "serial"  adapters  can  be
  configured  in  "auto-dial"  to  give access to the Internet
  through a "network" provider.

   The current version supports SOCKS Version 4  and  5.    In
  SOCKS   version  5,  only  NO  AUTHENTICATION  REQUIRED  and
  USERNAME/PASSWORD authentication methods are supported.  The
  GSSAPI support is NOT implemented.

   In V5 only support for IP V4 addresses is provided not V6.
   DNS names are evidendly supported.

    To  be used, a correct support of the TCP/IP names must be
  implemented in
   the way the "client" stations can convert external names in
  IP addresses.
   This restriction can be modified with SOCKS Version 5 where
  DNS names have
   to be resolved only on the SOCKD station.

   To provide the correct "names" support in Socks V4, we  use
  the DNS kit of TCP/IP V2.0
   on  the  same  workstation  as  "sockD".  In  this way this
  "nameD" server can provide
   caching mechanism to the external (and internal) name serv-
  ers.
   We used also the DDNS kit of Warp Server in a similar  con-
  figuration.

   In Socks V5, only a resolv file pointing to a "public" name
  server  and  an "hosts" file to traduce "internal" names are
  required. The usage of a real "caching" name server  is  NOT
  mandatory.  The  customization of the "SockD" server is eas-
  ier.

  The support of UDP associated of V5 is a little bit modified
  to add support for a "remote" ping command when the destina-
  tion  port  is "1".  In this case sockd opens a "raw" socket
  with protocol "icmp" to ping the external host and  communi-
  cates with the standard UDP Associated protocol to the "cli-
  ent" host.

  AUTO-DIAL FACILITY.
  ___________________

  You  need to customize first the access to your network pro-
  vider.

  SockD was only tested with IBM Global Network. When the  ac-
  cess is working with the "dialer.exe", you have to customize
  two  "cmd" files one to get the access and the second one to
  close it.

  This facility is only supported on  one  adapter  sl0,  sl1,
  ppp0 or ppp1.  It was only tested on sl0.

  To  check if the connection is OK, sockd uses the "flags" of
  the   adapter   status.   When   the    sl0    adapter    is
  "<UP,POINTTOPOINT>",     the     flags    are    "811"    or
  "<UP,POINTTOPOINT,RUNNING>" ("851")...

  Sockd reads normally a sockd.cfg and sockd.rte files in  the
  ETC  directory.  These files are the socks configuration. In
  auto-dial mode, sockd tries to build an "automatic"  config.
  It should be OK for the first tests.  If you want to look at
  this  default  config,  you  have just to read the sockd.log
  file (in the sockd directory) after stopping sockd.

  By  sample  I  used  this  sockdial.cmd  whith   a   correct
  userid/password and account to start the connection.

    /************************************************/
    /*                                              */
    /* sockdial.cmd :  to start the slip connection */
    /*                                              */
    /************************************************/
    'start dialer account userid password -d'

  And  this sockclos.cmd to stop the connection after the "de-
  lay" without session is expired.

    /***********************************************/
    /*                                             */
    /* sockclos.cmd :  to stop the slip connection */
    /*                                             */
    /***********************************************/
    'dialer -c'

  These two cmd MUST be put in  a  subdirectory  in  the  PATH
  statement (I used \TCPIP\BIN).

  Evidendly  you  have  to  enable  the  "auto-dial"  function
  through the "dial-up" option of the "config" menu (and setup
  your command names and the "delay" time). Then you  have  to
  stop/start sockd.

  An  other  method consists in starting directly sockd with a
  parameter:

      start sockd -dsl0

      where:  sl0  is the auto-dial adapter

  In  this case you have to keep the default for other parame-
  ters:  "sockdial.cmd", "sockclos.cmd" and 5 minutes  of  de-
  lay.

  The delay time should be shorter than the "delay" set in the
  "dialer" configuration to keep the control of the connection
  in "sockd".


  SOCKD.CFG
  _________

   The configuration files are saved in the ETC directory.

    deny   0.0.0.0 0.0.0.0 9.0.0.0 255.0.0.0 gt 0
    permit 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 ge 1024
    permit 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 eq 21
    permit 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 eq 20
    permit *=PhilG,Test 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 eq 23
    permit 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 eq 70
    permit 9.0.0.0 255.0.0.0 0.0.0.0 0.0.0.0 eq 80

    A  list of userids can be used in addition of IP addresses
  on the "permit" statement.  They  are  case  sensitive.  The
  value  sent  from  the OS/2 Warp station comes from the USER
  variable set in the "config.sys" in SOCKS V4.

   On the time being no checking of  "password"  is  performed
  (through identd).

  In   SOCKS   V5,   the   userid   used   in  userid/password
  authentication is checked with the userid list in the permit
  statement if *= field is set.

   Good practice specifies a first statement to denies all ex-
  ternal accesses to your "private" network (all ports) with:

   "deny 0.0.0.0 0.0.0.0 nnn.nnn.nnn.nnn mmm.mmm.mmm.mmm gt 0"
   where nnn is your network number and mmm the mask.

   then you can permit all stations from your network  to  ac-
  cess all TCP applications through the socks gateway with:

  "permit  nnn.nnn.nnn.nnn  mmm.mmm.mmm.mmm 0.0.0.0 0.0.0.0 gt
  0"

  "proxy" statements can be added if you require to  intercon-
  nect sockd servers. The syntax is like :

  "proxy     IP_addr     port_nb     subnet_nb     subnet_mask
  [site_certificate] "

  Where :
    IP_addr is the IP address of next proxy server
    port_nb is the port number (1080 by default) of this proxy server
    subnet_nb is the destination subnet we can access through this proxy
    subnet_mask the destination subnet mask
    site_certificate  the  file  to use for authentication and encryption
                       (not yet supported)

  SOCKD.PRO
  _________

    SOCKD  uses also a profile file (sockd.pro) in the ETC di-
  rectory to save the number of sessions set, server port  nb,
  the window position, the level of logging used ("Full", "all
  Sessions",  "only  errors and sessions refused (Minimum)" or
  "No logging") and the font used on main window.

   In the second line of this file, we have  the  "auto  dial"
  parameters:
   is  this  facility  enabled (Y or N), the dial command, the
  hangup command,
   and the "short hold mode" delay.

   In addition a "TCP" time-out and a "UDP" time-out (in  sec-
  onds) are
   also set. These permit to "tune" the delay sockd is waiting
  for the next
   transaction before considering the session is lost.
   If these parameters are too short sockd is cutting the ses-
  sion during a
   normal  "wait"  time.  If  they are too long, some "client"
  threads can be
   blocked and are not available for "new" sessions.

   The defaults are respectively 20 minutes  for  TCP  and  50
  seconds for UDP
   applications. TCP is really using a "session". In UDP there
  is no real
   session.  The communication is never really closed. The UDP
  time-out is used
   to standardly close this communication.  SockD  was  tested
  with Real-Audio
   UDP  application  and archie as UDP associate applications.
  The default of
   50 seconds was enough  to  use  both  applications  with  a
  dial-up connection.
   The default of 20 minutes for TCP applications was set big-
  ger than the
   standard  FTP  time-out  (15 minutes). It is NOT enough for
  "permanent"
   telnet sessions.

  A third line contains info on log archiving : yes or no, de-
  lay in hours or days, delay value, maximum number  of  files
  to  archive.  The fifth parm in this line permits to support
  only socks V5 userid/password authentication if a userid  is
  set  on a permit statement. In Socks V4 there is no password
  checking.  Normally sockd is giving the same process  to  V4
  as V5. Enabling this option obliges to use a password in ad-
  dition to the userid.

   This file is created automatically by sockd.exe

  SOCKD.RTE
  _________

    Another  configuration  file  (sockd.rte)  is required for
  SOCKS_BIND in  the  ETC  directory  describing  the  gateway
  adapters  and  IP addresses.   Most of the applications (Web
  Explorer, Rtelnet, ...) use only SOCKS_CONNECT.  That's  the
  reason  why  I  put "sockd.rte" as optional....   But if you
  want to use Rftp you need the SOCKS_BIND  support  and  then
  sockd.rte.

   It is a list of the local adapter addresses and the neworks
  you can reach through these... These definitions are used in
  sequence  for  testing an address.   Thus it seems better to
  put the more restrictive definitions first (describing  pri-
  vate  network  access)  and  the  "public  network"  adapter
  finally (giving access to world).

   By sample :

    9.36.69.41    9.36.69.32 255.255.255.224
    9.132.89.238  0.0.0.0    0.0.0.0

  If you plan to use the auto-dial facility avoid to set rout-
  ing for the dial-up adapter. If  no  route  file  is  found,
  sockd  builds  one  with  your LAN adapters giving access to
  their local subnets and put a last  dynamic  entry  for  the
  switched adapter giving access to world (0.0.0.0).

  You  can want to have other subnets accessible through fixed
  (LAN) adapters.  For that you must define a sockd.rte with a
  line per subnet and setting in first parameter the local  IP
  address  giving  access  to  it. Sockd 'll add dynamically a
  last entry for the switched adapter giving access to 0.0.0.0

   By sample :

    9.36.71.9     9.36.71.0   255.255.255.0
    9.132.89.238  9.0.0.0     255.0.0.0
    9.132.89.238  198.74.69.0 255.255.255.0

  SOCKD.USR
  _________

  This  file  is  in  the  ETC directory   for Socks version 5
  userid/password authentication.  On the time being,  no  en-
  cryption  technic  is  used on this confidential dataset.  A
  userid as a password can theoretically use 256 characters. I
  think in our test implementation it is limited to  255  (due
  to the end of string character).

   By sample :

    userid01 password01
    userid02 password02


  UTILISATION:
  ____________

    Start  sockd  without  any parameter or with some of these
  options:

  ©   "-c" option: The number of concurrent clients is  32  by
      default.    It can be changed at startup with the -c pa-
      rameter or by modifying the sockd.pro profile file  with
      the  menu option.  By sample :"sockd -c64" to support 64
      simultaneous clients. Note there is NO space between  -c
      and  the value. This number should be between 8 and 255.
      Each client uses one thread (in  addition  to  the  base
      sockd thread).

  ©   "-l"  option: to suppress logging (sockd.log file in the
      current directory)

  ©   "-i" option: to start iconized .

  ©   "-d" option: to setup an auto-dial  adapter,  by  sample
      "-dsl0".

  ©   "-p"  option:  by  default sockd uses the port 1080. You
      can change it starting "sockd -p2080" by sample.

   If you want to use more than one option, specify  different
  parameters:  "start sockd -c48 -p2080 -i".

    The  frame  forwarding  MUST be disabled (with the "ipgate
  off" command or through MPTS customization) to  protect  the
  access to your "internal" network.

    The  "socks" support is required to run (and use) applica-
  tions through gateway.  (see SOCKS FORUM) or a  Web  Browser
  with "socks" support (like Web Explorer for
   OS/2).

  SOCKD MENU
  __________

  ©   "Config": create, modify or simply check your configura-
      tion


      ž   "edit":  to  create  or  modify  "line  by line" the
          sockd.cfg in ETC directory

      ž   "proxy": to define proxy  servers  and  the  subnets
          they are giving access.

      ž   "view":  to  review  the configuration in memory and
          eventualy change it
                with the standard  MLE  (Multiple  Line  Entry
          field) keyboard manipulation.
                (select  text with mouse button 1 or Shift key
          and move the cursor,
                then   cut,   copy   and   paste   text   with
          Ctrl+Delete, Shift+Delete and Shift+Insert)

      ž   "profile":  to  change the maximum number of concur-
          rent sessions,
                the server port number or the logging level.

      ž   "route": to configure the sockd.rte file in ETC  di-
          rectory.

      ž   "save  conf":  to  save the sockd.cfg from memory to
          ETC directory

      ž   "userid":    for    Socks     V5     Userid/Password
          authentication method

      ž   "dial-up": to customize auto-dial facility

      ž   "font": to select the font used in the main window.

  ©   "reset": If you want to activate a change, a new profile
      or config

      ž   "server": to stop/restart the server

      ž   "log  file":  to clean the log file when reports are
          too long.

  ©   "Report":


      ž   "accepted":  to  check  all  sessions  through  this
          server

      ž   "denied":  to  check  all  demands  rejected  by the
          server.

      ž   "connect": to read the dial-up  connection  time  in
          auto-dial mode.

  ©   "Help": to read this help file.

  ©   "Exit": to save the "profile" file and exit.



DNS SUPPORT
___________

  HOW TO SETUP A NAME SERVER
  __________________________

    To  solve the V4 "name" problem, I put the DNS kit (at CSD
  UN60004 level) on the PS/VP. This name server should be cus-
  tomized with caching to the external name server(s)  and  to
  internal  domain  name server.   On the "client" station the
  resolv2 file points to the socks gateway address as the name
  server (the DNS running on the sockd station can be the only
  name server on this small subnet).

   Here after the configuration files used during  our  tests,
  where:

  ©    Where test.benelux.ibm.com (9.36.71.0) is the 'private'
      domain

  ©     ztmaixn1.benelux.ibm.com  (9.132.56.2) is the external
      name server for the
        ibm.com domain and ns01.ny.us.ibm.net (165.87.194.244)
      is the external
        DNS server.

  ©     The  socks  gateway  is  using  9.132.89.238  on   the
      "ibm.com" adapter and
       9.36.71.9 on the "secure" side (philg.benelux.ibm.com).

  ©    Tests were performed from testuser.test.benelux.ibm.com
      (9.36.71.10).

  ©   All  "external"  sessions were performed through the sl0
      adapter and a connection to IBM Global Network as  "Ser-
      vice" provider.

  In  fact,  on  a  small  LAN with just a few PCs connected a
  "hosts" file must be enough to succeed with  DNS  conversion
  in Socks V5.

    hosts file in ETC directory

    9.132.89.238      bedb238.benelux.ibm.com
    9.36.71.9         bedb238.philg.benelux.ibm.com
    9.36.71.10        testuser.philg.benelux.ibm.com
    165.87.194.244    ns01.ny.us.ibm.net
    128.123.35.151    hobbes.nmsu.edu
    206.101.97.101    www.lycos.com
    205.216.146.70    www.yahoo.com

  In Socks V4, you can perform the first sockd tests just with
  a similar hosts file. But quickly, you should be blocked and
  due  to  the  protocol you need to start a "named" server on
  your sockd gateway. You need then a "resolv2" file  on  your
  LAN attached PC pointing to your named server.

  In  any case keep also an "hosts" file on your sockd PC, be-
  cause the code uses a "gethostbyaddr()"  macro  to  get  the
  "hostname"  of  the workstation.  Sometimes the named server
  doesn't answer and you have to start sockd before named. You
  need then the "hosts" file to get a name.

  DNS KIT OF TCP/IP V2
  ____________________

  named.bt
  ________

    ;
    ; NAMED.BT file for name server configuration.
    ;
    ; type       domain                      source file or host
    ;
    domain   philg.benelux.ibm.com
    cache    .                          d&colon.\\tcpip\\etc\\namedb\\named.ca
    primary  philg.benelux.ibm.com      d&colon.\\tcpip\\etc\\namedb\\named.dom
    primary  71.36.9.in-addr.arpa       d&colon.\\tcpip\\etc\\namedb\\named.rev
    ;
    ;
    domain   benelux.ibm.com
    primary  ztmaixn1.benelux.ibm.com  9.132.56.2
    primary  9.in-addr.arpa            9.132.56.2
    ;
    domain   ibm.net
    primary  ns01.ny.us.ibm.net        165.87.194.244
    primary  .in-addr.arpa             165.87.194.244
    ;

  named.ca
  ________

    ;
    ; define parent(root) domain nameserver (Note trailing dot)
    ;
    philg.benelux.ibm.com.        99999999  IN  NS  bedb238.benelux.ibm.com.
    71.36.9.in-addr.arpa.         99999999  IN  NS  bedb238.benelux.ibm.com.
    benelux.ibm.com.              99999999  IN  NS  ztmaixn1.benelux.ibm.com.
    ibm.com.                      99999999  IN  NS  ztmaixn1.benelux.ibm.com.
    9.                            99999999  IN  NS  ztmaixn1.benelux.ibm.com.
    9.in-addr.arpa.               99999999  IN  NS  ztmaixn1.benelux.ibm.com.
    in-addr.arpa.                 99999999  IN  NS  ns01.ny.us.net.com.
    ;
    ; address of domain nameservers
    ;
    bedb238.philg.benelux.ibm.com.  99999999  IN  A   9.36.71.9
    bedb238.benelux.ibm.com.        99999999  IN  A   9.132.89.238
    ztmaixn1.benelux.ibm.com.       99999999  IN  A   9.132.56.2
    beda002.benelux.ibm.com.        99999999  IN  A   9.132.88.2
    ns01.ny.us.net.com.             99999999  IN  A   165.87.194.244
    ;

  Where  ns01.ny.us.net.com is the name server of the Internet
  provider...

  named.dom
  _________

    ;
    ;********************************
    ;*  Start of Authority Records  *
    ;********************************
    ;
    @ IN SOA  bedb238.philg.benelux.ibm.com.  bedb238.philg.benelux.ibm.com. (
            93052601 ; Serial number for this data (yymmdd##)
            86400    ; Refresh value for secondary name servers
            300      ; Retry value for secondary name servers
            864000   ; Expire value for secondary name servers
            3600 )   ; Minimum TTL value
    ;
    @      IN  NS   bedb238.philg.benelux.ibm.com.
    ibm.com.   IN  NS   bedb238.philg.benelux.ibm.com.
    ibm.com.   IN  NS   ztmaixn1.benelux.ibm.com.
    com.   IN  NS   bedb238.philg.benelux.ibm.com.
    com.   IN  NS   ns01.ny.us.ibm.net
    edu.   IN  NS   ns01.ny.us.ibm.net
    be.    IN  NS   ns01.ny.us.ibm.net
    ;
    ;********************************
    ;*  Domain Address Information  *
    ;********************************
    ;
    bedb238                    86400  IN  A      9.36.71.9
                                      IN  HINFO  IBM-PS/2 OS/2 3.0
    ;
    testuser                   86400  IN  A      9.36.71.10
                                      IN  HINFO  IBM-PS/2 OS/2 3.0
    ;
    bedb238.benelux.ibm.com.   86400  IN  A      9.132.89.238
    bedb237.benelux.ibm.com.   86400  IN  A      9.132.89.237
    ns01.ny.us.ibm.net         86400  IN  A      165.87.194.244
    ztmaixn1.benelux.ibm.com   86400  IN  A      9.132.56.2
    w3.almaden.ibm.com.        86400  IN  A      129.33.24.62
    w3.pe.au.ibm.com.          86400  IN  A      9.8.32.2
    w3.austin.ibm.com.         86400  IN  A      9.3.246.8
    w3.bocaraton.ibm.com.      86400  IN  A      9.83.4.179
    w3.portsmouth.uk.ibm.com.  86400  IN  A      9.180.145.185
    w3.hursley.ibm.com.        86400  IN  A      9.20.2.34
    w3.issc.ibm.com.           86400  IN  A      9.242.89.217
    isscw3.raleigh.ibm.com.    86400  IN  A      9.67.1.114
    w3nhd.raleigh.ibm.com.     86400  IN  A      9.67.195.102
    netstd.raleigh.ibm.com.    86400  IN  A      9.67.1.114
    w3.raleigh.ibm.com.        86400  IN  A      9.67.4.22
    www.tcp.raleigh.ibm.com.   86400  IN  A      9.67.106.6
    www.lycos.com.             86400  IN  A      206.101.97.101
    www.yahoo.com.             86400  IN  A      205.216.146.70

  The  translation  of  www.lycos.com,  www.yahoo.com, ... Are
  there to have a method to start a dial-up connection without
  the external DNS server.   These name translations  are  re-
  quired for Socks V4 auto-dial process...
  You must setup there the addresses of the WWW servers set in
  the  quicklist  of  the end-users connected on the local LAN
  while Web explorer is not supporting V5.

  named.rev
  _________

    ;
    ;********************************
    ;*  Start of Authority Records  *
    ;********************************
    ;
    71.36.9.in-addr.arpa. IN  SOA   bedb238.philg.benelux.ibm.com. (
            93052601 ; Serial number for this data (yymmdd##)
            86400    ; Refresh value for secondary name servers
            300      ; Retry value for secondary name servers
            864000   ; Expire value for secondary name servers
            3600 )   ; Minimum TTL value

    71.36.9.in-addr.arpa.  IN  NS   bedb238.philg.benelux.ibm.com.
    ;
    9              IN  PTR   bedb238.philg.benelux.ibm.com.
    10             IN  PTR   testuser.philg.benelux.ibm.com.
    237.89.132.9.in-addr.arpa.  IN  PTR   bedb237.benelux.ibm.com.
    238.89.132.9.in-addr.arpa.  IN  PTR   bedb238.benelux.ibm.com.
    101.97.101.206.in-addr.arpa.  IN  PTR  www.lycos.com.
    70.146.216.205.in-addr.arpa.  IN  PTR  www.yahoo.com.

  The  translation  of  bedb238.benelux.ibm.com is required to
  start  sockd  when  the  name  server  is  running,  because
  9.132.89.238 is the IP address of the "lan0" adapter.
  SockD uses a "gethostbyaddr()" macro to get the host-name of
  the  system  where it is running. If the name server can not
  give it, sockd is blocked during start-up...

  DDNS KIT OF WARP SERVER
  _______________________

  In the \MPTN\ETC\NAMEDB  directory  we  used  the  following
  config files.

  named.bt
  ________


   DNS support                                              18


    ;
    ; NAMED.BT file for name server configuration.
    ;
    ; type       domain                  source file or host
    ;
    domain   philg.benelux.ibm.com
    primary  philg.benelux.ibm.com c&colon.\\mptn\\etc\\namedb\\named.dom presecured nokeytosec
    primary  71.36.9.in-addr.arpa  c&colon.\\mptn\\etc\\namedb\\named.rev presecured nokeytosec
    ;
    ;
    cache    .              c&colon.\\mptn\\etc\\namedb\\named.ca  presecured nokeytosec
    ;

  named.dom
  _________

    ;
    ;********************************
    ;*  Start of Authority Records  *
    ;********************************
    ;
    @   IN  SOA        bedb238.philg.benelux.ibm.com. (
            96090101 ; Serial number for this data (yymmdd##)
            86400    ; Refresh value for secondary name servers
            300      ; Retry value for secondary name servers
            864000   ; Expire value for secondary name servers
            3600 )   ; Minimum TTL value
    ;
    @      IN  NS   bedb238.philg.benelux.ibm.com.
    ;
    ;********************************
    ;*  Domain Address Information  *
    ;********************************
    ;
    bedb238                    86400  IN  A      9.36.71.9
                                      IN  HINFO  IBM-PS/2 OS/2 3.0
    ;
    testuser                   86400  IN  A      9.36.71.10
                                      IN  HINFO  IBM-PS/2 OS/2 3.0
    ;
    ns01.ny.us.ibm.net         86400  IN  A      165.87.194.244
    www.lycos.com.             86400  IN  A      206.101.97.101
    www.yahoo.com.             86400  IN  A      205.216.146.70

  named.rev
  _________

    ;
    ;********************************
    ;*  Start of Authority Records  *
    ;********************************
    ;
    71.36.9.in-addr.arpa. IN  SOA  bedb238.philg.benelux.ibm.com. (
            93052601 ; Serial number for this data (yymmdd##)
            86400    ; Refresh value for secondary name servers
            300      ; Retry value for secondary name servers
            864000   ; Expire value for secondary name servers
            3600 )   ; Minimum TTL value

    71.36.9.in-addr.arpa.  IN  NS   bedb238.philg.benelux.ibm.com.
    ;
    9.71.36.9.in-addr.arpa.       IN  PTR   bedb238.philg.benelux.ibm.com.
    10.71.36.9.in-addr.arpa.      IN  PTR   testuser.philg.benelux.ibm.com.
    101.97.101.206.in-addr.arpa.  IN  PTR   www.lycos.com.
    70.146.216.205.in-addr.arpa.  IN  PTR   www.yahoo.com.

  named.ca
  ________

    ;
    ; define parent(root) domain nameserver (Note trailing dot)
    ;
    in-addr.arpa.           99999999  IN  NS  ns01.ny.us.net.com.
    ;
    ; address of domain nameservers
    ;
    ns01.ny.us.net.com.     99999999  IN  A   165.87.194.244
    ;

  RESOLV2 ON SOCKD SERVER
  _______________________

    domain philg.benelux.ibm.com
    nameserver 9.36.71.9

  RESOLV ON SOCKD SERVER
  ______________________

    domain philg.benelux.ibm.com
    nameserver 9.36.71.9

  RESOLV2 ON END-USER WORKSTATION
  _______________________________

    domain philg.benelux.ibm.com
    nameserver 9.36.71.9

  TEST CONFIGURATION
  __________________

                     ----
                ----     ---
            ----            ----
        ----    Internet        --
           ----                    -
               ------ IBM IGN   --
                    ---*-------
                       *
                       *
                    *******                     testuser
                     *   *  Modem              ----------
                      * *   Dial-up            *Thinkpad*
                       *                       ----*-----
          * *          *                           *
        *     *  ------*------    Ethernet         *9.36.71.10
       * T-R   *** PS/VP     *---------------------*---
        *     *  * bebd238   *9.36.71.9
          * *    -------------
             9.132.89.238
     ibm.com                          philg.benelux.ibm.com
     9.0.0.0                             9.36.71.0

  With a correct setup, it is possible to use Internal servers
  (ibm.com)  without  dialing  from "testuser". If an external
  server is used (by sample www.yahoo.com)  the  auto-dial  is
  automaticcally used.

  The choice is done through "sockd.rte" configuration. By de-
  fault  sockd  gives only access to the "local" subnet on the
  LAN adapter (9.132.88.0).


  PROXY  SUPPORT
  ______________

    A  "proxy" socks server is implemented. To use it you need
  to know the IP address of the next sockd for OS/2 server and
  the subnets you can access through this remote sockd.

   From a LAN connected to Internet in "auto-dial" mode it  is
  possible  to access servers located on an other LAN attached
  to Internet through a sockd using a fixed IP address (mainly
  with a leased line).

   You must "permit" the access on both  sockd  servers.  Only
  the  dial-up  sockd has to define the "leased line attached"
  sockd with a "proxy" statement.



  ARCHIVING SOCKD LOG FILES AND REPORTING
  _______________________________________

    Sockd  can  now  archive  its log files. The setup is done
  through the "profile" option of the main window  menu.  Four
  parameters are saved in the third line of the sockd.pro file
  in  the ETC directory.  The first parameter indicates if Yes
  or No the option is selected.  The second parameter  is  "H"
  for hours or "D" for days. The third gives the delay used to
  close  the  sockd.log  file  and rename it to "sockdlog.XXX"
  where XXX is a three digits number. The fourth indicates the
  maximum number of archived files (+ the current sockd.log).

   The default is to keep seven files and to archive every  24
  hours.   With this setup you can build a weekly report using
  the sample REXX reporting program "sockdrep.cmd" (just  type
  "sockdrep"  without  parm  in  the  directory  sockd is run-
  ning)...


  IF PROBLEMS
  ___________


  ©   The  DNS  kit  nameD  server  can block if the system is
      fully  "socksified".    Don't  hesitate  to  rename  the
      "socks.cfg"  file in the ETC directory when you are run-
      ning sockD.

  ©   If your configuration is limited to one LAN adapter  and
      one  dial  adapter,  it  is better to test sockd without
      configuring it...  Use the view menu option to  see  the
      config. After tests, check sockd.log ...

  ©   If  you  have really a problem to setup a name server on
      the gateway station, define a "hosts"  file.  For  that,
      when  you are testing your "sockdial.cmd" after the con-
      nection and authentication are  successfully  completed,
      use :
        host www.yahoo.com
      in  an OS/2 Window. You are able to get the IP addresses
      of your favorite servers.  If you install a  "completed"
      hosts  file  in the ETC directory of the end-user PC you
      can test sockd with WebEx (socks V4) without  setting  a
      name  server.   With a name server and its caching mech-
      anism, you have access to any  server,  with  the  hosts
      file access is limited...

  ©   To  support  socks  V5  DNS,  the  dial-up connection is
      started automatically if the name  can  NOT  be  locally
      traduced...  A  better  solution  is perhaps to define a
      list of the "internal" domain names, and  to  start  the
      connection  only  if  the  request is for another domain
      name.  On the time being, sockd start the  dial-up  con-
      nection  for  V5,  before  checking if the connection is
      "permitted" except  if  the  DNS  name  can  be  locally
      traduced.   With the current implementation:  - in socks
      V4 the first session (to start the  dial-up  connection)
      MUST be
      to  a  "locally" defined DNS name (then sockd check if
      the client has access
      to this address before starting the connection).  - in
      V5 DNS support, the first session  can  be  to  any  DNS
      name, but if this
      name  can  NOT  be  locally translatted, there a delay
      (nearly 1 min. in my tests)
      then the dial-up connection is  started  and  the  DNS
      name translation request
      is sent to the "external" name server.
      The  "permission"  can be checked only after sockd re-
      ceived the destination
      IP address.

  ©   In    this    version    ,    only   the   flags   "811"
      (<UP,POINTTOPOINT>) or "851" (<..,RUNNING>) are  consid-
      ered  as  "good"  status (connection established) on the
      dial-up adapter.   If the "auto-dial"  facility  doesn't
      work for you, please check these flags with:
      "ifconfig ppp0" (by sample)
      Send a note to me and I'll add the required support...

  ©   With  current V4 applications like WebEx, the first ses-
      sion must be done to a DNS name converted locally (named
      or hosts file).  After the dial-up connection is  estab-
      lished,  names  can  be translatted by the Internet pro-
      vider name server, and cached in the local nameD.

  ©   Using WebEx through sockd, some  ".gif"  files  are  not
      correctly received I am investigating why and how to im-
      prove it.

    Any suggestion or question to Philippe Gillain (GILLAIN at
    BRUVMIS1 or Philippe_Gillain@be.ibm.com)...