BGFT (TM)

                                     Version 3.02




                           A BackGround File Transfer System



                                  Rick MacDonald, MSc
                                   Rafael Moya, PhD
                                   Tim Chapman, PhD


                                     Dirac Systems
                                     P. O. Box 476
                                     West Hill, ON
                                     Canada M1E4Y9


                                 Modem (416) 283-7157




                      Copyright (c) 1990-1993 Dirac Systems  \ /
                     -------------------------------------- - o -
                                                             / \







                                   TABLE OF CONTENTS
                                   -----------------


            1.0 Introduction ...........................................5
            1.1 BGFT Concept ...........................................5
            1.2 What's New in Version 3 ................................7
            1.3 Registered User Support ................................8
            1.4 Why Register? ..........................................9

            2.0 Red Tape ...............................................10
            2.1 Disclaimer of Warranty .................................10
            2.2 Copyright Notice .......................................10
            2.3 Upgrade Policy .........................................12
            2.4 Hardware and Software Requirements .....................13
            2.5 Definition of Terms ....................................13

            3.0 Getting Started with BGFT ..............................15
            3.1 Files in the Distribution ..............................15
            3.2 Trying it Out ..........................................19

            4.0 Installation, File Buffers, and Resident Programs ......25
            4.1 The Installation Program ...............................26
            4.1.1 Minimal Installation .................................28
            4.1.2 File Buffer Choice ...................................29
            4.1.3 BGFT Directory .......................................29
            4.1.4 Support Files for Other Communication Products .......30
            4.1.5 Changes to AUTOEXEC.BAT ..............................30
            4.1.6 System Specific Details ..............................30
            4.1.7 Files for Microsoft Windows ..........................31
            4.1.8 Automatic Sequence ...................................31
            4.2 Manually Organizing the Files ..........................32
            4.3 Hard Disk Drive File Buffer Creation ...................34
            4.4 The Resident Programs ..................................35
            4.5 Resident Program Error Messages ........................37
            4.6 Floppy Disk Drive File Buffer Creation .................38
            4.7 BGFT Environment .......................................39
            4.8 Modem Requirements .....................................40
            4.9 Systems Without a Hard Drive ...........................41
            4.10 BGFT and DOS 5 ........................................41
            4.11 BGFT and STACKER ......................................42
            4.12 BGFT and DR DOS .......................................42
            4.13 Multitasking and Communications .......................42
            4.14 BGFT and DESQview .....................................43
            4.15 BGFT and Microsoft Windows ............................44
            4.16 Problem Solving .......................................45
            4.17 Operating Limitations .................................46
            4.18 BGFT Model Summary ....................................47

            5.0 Operation of Main User Interface: BGFT.EXE .............48
            5.1 Starting/Stopping BGFT .................................48
            5.1.1 Starting BGFT ........................................48
            5.1.2 Exiting BGFT .........................................49


                                                                          2






            5.2 The Menu System ........................................50
            5.2.1 File .................................................51
            5.2.2 View .................................................52
            5.2.3 Dial .................................................52
            5.2.4 Transfer .............................................53
            5.2.5 Setup ................................................53
            5.2.6 Utility ..............................................53
            5.2.7 Information ..........................................54
            5.3 Dialog Boxes ...........................................54
            5.3.1 Action Buttons .......................................54
            5.3.2 File Lists ...........................................55
            5.3.3 Drive/Directory Lists ................................56
            5.3.4 Data Input Fields ....................................56
            5.3.5 On/Off Flags .........................................56
            5.3.6 Radio Buttons ........................................57
            5.4 The Help System ........................................57
            5.4.1 Message Line .........................................57
            5.4.2 Alt_Z Help Key .......................................57
            5.5 Configuring BGFT .......................................57
            5.5.1 Terminal Emulation ...................................57
            5.5.2 Modem Parameters .....................................58
            5.5.2.1 Modem Initialization String ........................58
            5.5.2.2 Dialing Command ....................................58
            5.5.2.3 Hang Up Command ....................................59
            5.5.2.4 Time Between Dialing ...............................59
            5.5.2.5 Test for 'BUSY' ....................................59
            5.5.2.6 Direct Connection ..................................59
            5.5.3 Communication Port Settings ..........................60
            5.5.3.1 Communication Port Number ..........................60
            5.5.3.2 Baud Rate ..........................................60
            5.5.3.3 Data Bits ..........................................61
            5.5.3.4 Stop Bits ..........................................61
            5.5.3.5 Parity .............................................61
            5.5.4 Preferences ..........................................61
            5.5.4.1 Confirm Exit .......................................61
            5.5.4.2 Background Sound ON/OFF ............................62
            5.5.4.3 Foreground Sound ON/OFF ............................62
            5.5.4.4 Tab Width ..........................................62
            5.5.4.5 Number of Lines to Scroll Back .....................62
            5.5.4.6 Show When the Scroll Buffer is Full ................62
            5.5.4.7 Save the Scroll Back Buffer on Exit ................63
            5.5.4.8 Default Dialing Directory ..........................63
            5.5.4.9 Mouse Speed ........................................63
            5.5.4.10 Mouse Double Click Time ...........................63
            5.5.4.11 Enable Zmodem Auto-Download .......................63
            5.5.4.12 Auto Save File Directory ..........................63
            5.5.5 ASCII Download Parameters ............................64
            5.5.5.1 Character Pacing ...................................64
            5.5.5.1 Line Pacing ........................................64
            5.5.5.3 Pace Character .....................................65
            5.5.5.4 Expand Blank Lines .................................65
            5.5.5.5 Expand Tabs ........................................65
            5.5.5.6 Add Line Feed to Carriage Return ...................65
            5.5.5.7 Local Echo .........................................65


                                                                          3






            5.5.5.8 End of Line Translation for ASCII Transfers ........65
            5.5.6 Colors ...............................................66
            5.6 Terminal Mode ..........................................67
            5.6.1 Using a Modem ........................................67
            5.6.2 Direct Connection ....................................67
            5.7 Background Dialing .....................................68
            5.7.1 Selecting a Dialing Entry ............................68
            5.7.2 Editing Dialing Entries ..............................69
            5.7.3 Adding Entries .......................................69
            5.7.4 Removing Entries .....................................70
            5.7.5 Dialing an Entry .....................................70
            5.7.6 Kill Background Dialing ..............................71
            5.7.7 Resident's Status Window .............................72
            5.8 Background File Transfer ...............................72
            5.8.1 The File Buffer ......................................73
            5.8.2 Background File Downloading ..........................73
            5.8.3 Manually Moving Downloaded Files .....................74
            5.8.4 Automatically Moving Downloaded Files ................74
            5.8.5 ASCII File Downloading ...............................75
            5.8.6 Preparing Files For Uploading ........................75
            5.8.7 Background File Uploading ............................76
            5.8.8 ASCII Uploads ........................................77
            5.8.9 Acknowledge Communication Errors .....................77
            5.8.10 Ending Transmission .................................78
            5.9 Utility Functions ......................................78
            5.9.1 Turning the Resident Off .............................78
            5.9.2 Initialize the File Buffer ...........................78
            5.9.3 Modem Initialization .................................79
            5.9.4 Status of the BGFT Window ............................80
            5.9.5 Relocate the BGFT Window .............................80
            5.9.6 Clear the Terminal Mode Screen .......................80
            5.10 The Clipboard .........................................80
            5.10.1 Copying Text From the Terminal Mode Screen ..........80
            5.10.2 Copying Text From the Scroll Back Buffer Screen .....81
            5.10.3 The Clipboard Menu ..................................81
            5.11 The Scroll Back Buffer ................................83
            5.12 Screen Capture ........................................84
            5.13 BGFT Status ...........................................84
            5.14 Alt_Key Summary .......................................85
            5.14.1 'Hot' Keys ..........................................85
            5.14.2 'Warm' Keys .........................................86

            6.0 Operation of Auxiliary User Interface: BGFTOPT.EXE .....87
            6.1 External Protocols .....................................87
            6.2 General Considerations .................................88
            6.3 Using BGFT as an External Protocol for Telix ...........91
            6.4 Using BGFT as an External Protocol for PROCOMM PLUS ....95
            6.5 Using BGFT as an External Protocol for Qmodem ..........96
            6.6 Using BGFT as an External Protocol for Telemate ........97
            6.7 Command Mode Options Using BGFTOPT.EXE .................98
            6.8 Conclusion .............................................105

            Index ......................................................106



                                                                          4








            1.0 Introduction
            ----------------

            BGFT is an extraordinary file transfer system for the IBM
            PC/XT/AT family of computers. It allows files to be
            transferred over a serial communications link, in the
            'background', while the PC is being used for other purposes.
            Files can be transferred by downloading, or uploading, using
            either the Zmodem, Ymodem-Batch, Xmodem-CRC or Xmodem-1K file
            transfer protocol. This means, that when you transfer files by
            modem, to or from your favorite Bulletin Board Service (BBS),
            you can be writing a letter with your word processor, updating
            your financial statement with a spreadsheet or doing most of
            the other things that are possible with your computer. A
            convenient background dialer also makes the package ideal for
            accessing busy BBSs.

            What makes BGFT special? BGFT works in the background. It
            overcomes traditional background conflicts with the Disk
            Operating System (DOS). Drive A:, or B: or a 'reserved' file
            on the hard drive C: is used as a special download or upload
            'file buffer' for BGFT. Meanwhile, DOS is freed up to be used
            by other application programs. BGFT requires MS DOS Version
            3.1 or greater to operate.

            The background features of BGFT can also be used with other
            suitable telecommunication packages like PROCOMM PLUS, Qmodem,
            and Telix; script files are provided for them.

            BGFT is also Microsoft Windows 3 compatible. Usually it is not
            possible to run a background DOS program while running a
            Windows program in the foreground on a 286 computer, BGFT can
            do it, even with 8088 computers; this cannot be said for most
            telecommunication packages. A small Windows program is
            provided to show BGFT's file transfer progress while running
            Windows applications. BGFT also works well with multitasking
            systems like DESQview, particularly on computers with limited
            memory; BGFT is compact.

            The registered and unregistered package for BGFT share all the
            same features described above. The only difference is that
            there is no initial screen on the registered executable files,
            BGFT.EXE and BGFTOPT.EXE. Otherwise, all files are identical.

            1.1 BGFT Concept
            ----------------

            BGFT started as a program written by one of the authors who
            could not stand waiting to use his computer while it was
            downloading files. That prototype was in use for over two
            years and did thousands of background file transfers with a
            slow 4.77 MHz IBM PC clone and a 1200 baud modem. That program


                                                                          5






            was developed into BGFT; it was first released commercially in
            January 1990.

            BGFT is intended to provide efficient background file trans-
            fers on 'ordinary' personal computers. It works well on IBM
            PCs, XTs, ATs and compatibles. A 1200 or 2400 baud modem is
            ideal although baud rates up to 57600 are supported. At baud
            rates higher than 9600, background file transfers may not be
            practical, particularly on 'slow' computers. Higher baud rates
            have been included, however, for use by people with high speed
            modems and high power computers or those who want to make use
            of BGFT's background dialer.

            BGFT will serve as a complete communications program. It has
            many of the important features like having a configuration
            file, dialing directory maintenance, menuing system, color,
            context sensitive help, mouse control, connectivity to
            communication ports 1 to 4, terminal emulations and so on.
            BGFT's background dialer will be a superior choice for
            accessing busy BBSs since the user can do something else with
            the computer while waiting for a connection.

            BGFT is a communication environment that actually consists of
            two programs; one operates in the background and one in the
            foreground. The first, a small terminate and stay resident
            (TSR) program acts as a file transfer 'driver' which is capa-
            ble of carrying out background file transfers independently
            once it has been commanded to do so by a foreground program.

            The second program, BGFT.EXE, is the main user interface for
            BGFT. This foreground program acts as a standalone user
            interface to control the resident program's operation. Another
            foreground program, BGFTOPT.EXE, interacts with the resident
            in terms of command line options; it is used for specialized
            applications such as providing external background protocols
            for other telecommunication programs.

            BGFT is a robust background program due to a special way of
            avoiding DOS conflicts that have plagued other background
            utilities. In the technical sense, the background driver for
            BGFT is unusual because it does not use DOS calls; therefore,
            it does not have to wait until a foreground program finishes
            using DOS. This enables BGFT to run concurrently with other
            programs that use DOS.

            The advantages of this approach are easily demonstrated.
            Simply print out a text file using the DOS PRINT command,
            which is a background driver that uses DOS. Then use the DOS
            TYPE command which is a foreground program that uses DOS to
            view a long text file. After a few seconds, the printing will
            stop due to a DOS conflict, and will remain stopped until the
            TYPE command has finished. This kind of operation obviously is
            not suitable for a file transfer program since the file
            transfer would time-out under these conditions.


                                                                          6







            BGFT uses the concept of a file buffer for the temporary
            storage of files. The file buffer may either be on the hard
            drive C: or on a DOS formatted diskette, specially initialized
            by BGFT, in the floppy drive A: or B:. It is written to, and
            read from, by the BGFT resident program. There are two
            resident programs: one is BGFTHDZM.COM for accessing the hard
            drive file buffer and the other is BGFTFDZM.COM for accessing
            the floppy drive based file buffer. We will refer to the
            resident program as BGFTres.COM. One of the programs is used
            during a computer session.

            Downloaded files are stored temporarily in the file buffer and
            moved to DOS files on the hard disk or second floppy drive
            under user control by BGFT.EXE. Files to be uploaded are first
            moved to the file buffer with the foreground program, then
            accessed by BGFTres.COM while uploading. The design of the
            user interface is such that the use of the file buffer is
            nearly transparent to the user.

            When the file buffer is located on the hard disk, a specially
            created 'read-only' file is used as the file buffer. The file
            buffer is created by a program called, BGFTFB.EXE. The
            resident program creates a 'map' of the file used for the file
            buffer and then reads and writes that file directly without
            using DOS. This technique is not totally unique to BGFT, as
            most 'fast' backup programs and all defragmenting programs
            bypass DOS in a similar fashion. BGFT uses several error
            checking algorithms to confirm that the file buffer file has
            not been inadvertently re-located.

            1.2 What's New in Version 3
            ---------------------------

            Version 3 of BGFT is significantly different from the previous
            releases in version 2. Many users have asked for Zmodem. We
            have listened and delivered! Many users have asked for larger
            file buffers. You can now have one several megabytes in size
            on your hard disk. There were many requests for an improved
            user interface. Now there are pull down menus and features
            like a scroll back buffer, clipboard and ASCII capture. Users
            told us that BGFT was not easy to install and get running. Now
            there is an installation program to do much of the set up for
            you.

            All in all, BGFT has matured into a full featured
            communications program in response to our user's requests. We
            hope you enjoy it.








                                                                          7






            1.3 Registered User Support
            ---------------------------

            Registered user support is available via Dirac Systems' BBS;
            the telephone number is modem (416) 283-7157.

            You may also write to us at:

                 Dirac Systems
                 P. O. Box 476
                 West Hill, ON
                 CANADA M1E4Y9

            Dirac Systems will answer your questions, to help you get the
            most out of BGFT; registered users will get preferential
            attention. Also, Dirac Systems will consider making changes to
            suit your needs. Try giving us a call.

            We support BGFT on CompuServe; there are two membership
            numbers that you can contact:

            73670,2424 (Rick MacDonald)
            72570,2633 (Tim Chapman)

            Dirac Systems is also pleased to join Canada Remote Systems
            (CRS) to offer unparalleled BBS support throughout North
            America. Users of our products can send email to the 'BGFT',
            'IBM', 'Shareware Authors' or 'Vendors' conferences on
            NorthAmeriNet (NANET). Address inquiries to Tim Chapman or
            Rick MacDonald on CRS in the Toronto, Ontario area. You can
            also contact Rafael Moya on the Rose Media BBS in Toronto.

            We can also be reached through the Usenet mail network via
            CRS. Our email addresses are:

                 tim.chapman@canrem.com
                 rick.macdonald@canrem.com

            and the Fido address of CRS Main (PCBoard) is

                 1:229/15

            Please note that CRS is likely to change its name in early
            1993.

            Rick MacDonald also has the email address:

                 macdon@ists.ists.ca








                                                                          8






            1.4 Why Register?
            -----------------

            There are a number of reasons why you should register.

            As you can see, there will be extensive user support.

            BGFT is a low cost solution to having the benefits of
            background file transfer in DOS. It is only CAN$34.95. Please
            use the order form, BGFTORDR.FRM, to register.

            Once registered, BGFT is registered for life. There are no
            upgrade costs even if significant functional changes are
            included. See the upgrade policy in Section 2.3.

            The registered version of BGFTres.COM is uniquely serialized
            and replace the unregistered ones. This will get rid of the
            opening screens advertising the registration request on the
            foreground programs.

            We are marketing BGFT through the Shareware method. You get to
            evaluate its full capabilities on a fair trial basis. This is
            beneficial to the customer because he or she can determine
            whether the software product fulfills a need on their own
            hardware.

            We expect you to register the software if you are going to
            continue to use it after the trial. This shows that the
            product has value. It is the moral and financial
            responsibility of the user to then pay for registration.

            We are able to offer a superior product at a low cost due to
            Shareware. Many hours of labor are spent in its production and
            continuing support. A fair return is our measure of product
            value. The authors want to support you and BGFT in the future
            but must have user patronage to do it.




















                                                                          9







            2.0 Red Tape
            ------------

            BGFT is being marketed as Shareware. You are able to try out
            the full capabilities of the programs. After a short trial
            period you will have had the opportunity to evaluate the
            compatibility of the software with your system and whether you
            wish to continue using it. You will then be expected to
            purchase a registered copy.

            2.1 Disclaimer of Warranty
            --------------------------

            This software and documentation are provided 'as is' and
            without warranties as to performance of merchantability or any
            other warranties whether expressed or implied. Because of the
            various hardware and software environments into which these
            programs may be put, no warranty of fitness for a particular
            purpose is offered.

            Good data processing procedure dictates that any program be
            thoroughly tested with non-critical data before relying on it.
            The user must assume the entire risk of using the program. Any
            liability of the seller will be limited exclusively to product
            replacement or refund of purchase price.

            2.2 Copyright Notice
            --------------------

            The BGFT package includes the following executable programs:

            BGFTHDZM.COM:
            Resident program for use with the hard disk file buffer.

            BGFTFDZM.COM:
            Resident program for use with a floppy file buffer.

            BGFTFB.EXE:
            Makes a file buffer up to 65 megabytes on hard drive C:.

            BGFT.EXE:
            Main foreground program to control resident program.

            BGFTOPT.EXE:
            Command line foreground program for resident program.

            BGFTSPY.EXE:
            Windows 3 application to monitor file transfers.

            BGFTFLPY.EXE:
            Puts BGFT initialized floppy back to DOS floppy.




                                                                         10






            BGFTDIR.COM:
            Directory lister for BGFT or DOS floppies and file buffer.

            BGFTXDLG.EXE:
            PROCOMM/Telix/Qmodem phone directories to BGFT format.

            Other support files are:

            BGFTREAD.ME:
            Latest BGFT notes and revision histories.

            BGFTORDR.FRM:
            Order form for registering BGFT package.

            BGFT.DOC:
            BGFT documentation; this file.

            BGFT300.HLP:
            BGFT.EXE help screens.

            BGFT300.SCR:
            Other BGFT.EXE screens.

            BGFT.DLG:
            Sample BGFT dialing directory file.

            BGFTINIT.BAT:
            Initialize resident's communication port and baud rate.

            PROCOMM PLUS Specific:

            BGFTDZPC.ASP: PROCOMM PLUS script for Zmodem download.
            BGFTDYPC.ASP: PROCOMM PLUS script for Ymodem-Batch download.
            BGFTDXPC.ASP: PROCOMM PLUS script for Xmodem CRC/1K download.
            BGFTUZPC.ASP: PROCOMM PLUS script for Zmodem upload.
            BGFTUYPC.ASP: PROCOMM PLUS script for Ymodem-Batch upload.
            BGFTUXPC.ASP: PROCOMM PLUS script for Xmodem-CRC upload.
            BGFTUIPC.ASP: PROCOMM PLUS script for Xmodem-1K upload.

            Qmodem Specific:

            BGFTDZQM.SCR: Qmodem script for Zmodem download.
            BGFTDYQM.SCR: Qmodem script for Ymodem-Batch download.
            BGFTDXQM.SCR: Qmodem script for Xmodem-CRC/1K download.
            BGFTUZQM.SCR: Qmodem script for Zmodem upload.
            BGFTUYQM.SCR: Qmodem script for Ymodem-Batch upload.
            BGFTUXQM.SCR: Qmodem script for Xmodem-CRC upload.
            BGFTUIQM.SCR: Qmodem script for Xmodem-1K upload.

            Telix Specific:

            BGFTADD.BAT: Batch file adds BGFT external protocols to Telix.
            BGFTTELX.DAT: Data file for BGFTADD.BAT; modifies TELIX.CNF.
            BGFTSLC.BAT: Batch file to compile all Telix support scripts.


                                                                         11







            BGFTDZTL.SLT: Telix script for Zmodem download.
            BGFTDYTL.SLT: Telix script for Ymodem-Batch download.
            BGFTDXTL.SLT: Telix script for Xmodem-CRC/1K download.
            BGFTUZTL.SLT: Telix script for Zmodem upload.
            BGFTUYTL.SLT: Telix script for Ymodem-Batch upload.
            BGFTUXTL.SLT: Telix script for Xmodem-CRC upload.
            BGFTUITL.SLT: Telix script for Xmodem-1K upload.

            Microsoft Windows 3:

            BGFTSPY.ICO: Icon for BGFTSPY.EXE.
            BGFT386.PIF: PIF file to set up BGFT DOS session on a 386/486.
            BGFT386.BAT: Batch file to call BGFT DOS session on a 386/486.

            These files are Copyright (c) 1990-1993 by Dirac Systems, with
            all rights reserved. These products are commercial software
            and are licensed to the registered user, and are not to be
            distributed in any way, electronically or otherwise.

            The shareware evaluation package includes all the files listed
            above except that BGFT.EXE and BGFTOPT.EXE have special
            momentary screens which inform the user about registration.
            This may be distributed by the Shareware marketing method. See
            Section 3.1 for some fuller descriptions of the files.

            2.3 Upgrade Policy
            ------------------

            In order to provide our customers with advances in performance
            and convenience there will be new versions of BGFT from time
            to time. Maintenance releases will increase the version number
            in the hundredth's digit of the version number, for example,
            3.10 to 3.11; this is a minor release which will fix small
            problems. Product improvement releases will increase the
            version number in the tenth's digit of the version number, for
            example, 3.11 to 3.20; this is also a minor release. Major
            product changes will require increases in the version number,
            for example, 2.11 to 3.00; this would mean a significant
            functionality change. Changes are not whimsical; they are the
            result of customer input leading to careful development and
            testing. A number of fixes or improvements constitute a change
            so that releases are not too frequent. Releases that are
            referred to as minor will, in fact, provide some more
            substantial abilities or improvements.

            Minor revisions will normally have no cost increase; there may
            be cost changes due to circumstances beyond our control, as in
            changes to taxes, mail rates or inflationary pressures. Since
            prices are subject to change, please refer to the latest
            Shareware release or Dirac Systems to determine the present
            upgrade rates; incorrect upgrade or registration orders cannot
            be processed. The upgrade policy and price is guaranteed for
            1993.


                                                                         12







            Registered users of any BGFT version have registration for
            life. When a Shareware upgrade of the software appears,
            registered users are free to use it regardless of its
            functional change. Provision is made for them to transfer
            their serial number to the new version. Registered users of
            Version 2.x of BGFT should contact Dirac Systems' support BBS
            to find out how to take advantage of their investment under
            this policy.

            A new copy of the latest versions will be sent to registered
            users if they require one. The cost is CAN$10.00 to cover
            postage and handling. Province of Ontario residents must add
            the Provincial Sales Tax (PST) but not the Goods and Services
            Tax (GST).

            2.4 Hardware and Software Requirements
            --------------------------------------

            The requirements are minimal. BGFT will run on IBM PC/XT/AT
            compatible computers using DOS 3.1 or greater. It will run on
            machines with an 8088, 286, 386 or 486 CPU. The resident
            portion, BGFTres.COM, requires about 60K of memory which may
            be loaded high with DOS 5. The main user interface requires up
            to 230K of memory depending on memory allocation; usually it
            is less than 200K. The user interface is not required during
            transfers.

            2.5 Definition of Terms
            -----------------------

            Alt_X: An 'Alt_Key' combination, performed by pressing the
                 Alt key and then the given key 'X' (or 'x') together
                 momentarily.
            ASPECT: Trademark of Datastorm Technologies Inc.
            AT: Advanced Technology computer based on an Intel 80286 or
                 higher central processing unit.
            BBS: Bulletin Board Service.
            BGFT: BackGround File Transfer System, trademark of Dirac
                 Systems.
            BIOS: Basic Input/Output System.
            CompuServe: Registered trademark of CompuServe Incorporated.
            CRC: Cyclic Redundancy Check.
            CRS: Canada Remote Systems.
            DESQview: Trademark of Quarterdeck Office Systems.
            DOS: Disk Operating System.
            DR DOS: Trademark of Digital Research.
            ENTER: The Enter or Return key.
            ESC: The Escape key.
            Fxx: A function key, for example, F10 accepts data from data
                 entry forms.
            IBM: Registered trademark of International Business Machines
                 Corporation.



                                                                         13






            Microsoft Windows: Registered trademark of Microsoft
                 Corporation.
            MS DOS: Registered trademark of Microsoft Corporation.
            PROCOMM: Registered trademark of Datastorm Technologies Inc.
            PROCOMM PLUS: Trademark of Datastorm Technologies Inc.
            PgDn: Page Down key, for requesting a download.
            PgUp: Page Up key, for requesting an upload.
            Qmodem: Trademark of Mustang Software, Inc..
            SALT: Trademark of Exis Inc.
            Smartmodem: Registered trademark of Hayes Microcomputer
                 Products.
            SPACE: The Space bar.
            Stacker: Trademark of Stacker, Inc.
            Telemate: Trademark of White River Software.
            Telix: Trademark of deltaComm Development.
            TSR: Terminate and Stay Resident.








































                                                                         14







            3.0 Getting Started with BGFT
            -----------------------------

            The best way to find out about BGFT is to try it. BGFT's menu
            and help systems make its operation straight forward.

            On installing BGFTres.COM (that is, BGFTHDZM.COM or
            BGFTFDZM.COM), less than 64K of memory is used up for the
            resident part. This is relatively small when it is considered
            that this controls the download and upload functions in back-
            ground. BGFTres.COM was deliberately kept small to leave you
            plenty of memory for foreground applications.

            Even on expensive multitasking systems there is only one CPU
            doing all the work, so it must be shared between all
            processes. BGFTres.COM must use some CPU time to do its work;
            this means that foreground programs may appear to run
            slightly slower than their usual speed. This will depend on
            the speed of the computer and the baud rate used for the file
            transfer.

            3.1 Files in the Distribution
            -----------------------------

            BGFT300A.EXE:
            BGFT300B.EXE:
            The BGFT package is distributed on two 360K 5.25 inch floppy
            diskettes or one 720K 3.5 inch floppy diskette. All the
            necessary files have been archived to save space. The
            distribution files are in the files, BGFT300A.EXE and
            BGFT300B.EXE, and are found on two separate 360K floppies;
            the installation program, INSTALL.EXE will be on the floppy
            with BGFT300A.EXE. The 720K floppy has all the files:
            INSTALL.EXE, BGFT300A.EXE and BGFT300B.EXE. The BGFT files
            are self-unarchiving; we recommend using the installation
            program, INSTALL.EXE, for them (see Section 4.1).

            BGFTORDR.FRM:
            The order form for obtaining and registering BGFT.

            BGFTREAD.ME:
            Release notes and up-to-date information not found in the
            documentation.

            BGFT.DOC:
            This documentation file.

            INSTALL.EXE:
            The program will set up the appropriate directory for BGFT
            and put extracted files to where you want them. The
            installation will give you the opportunity to have your
            system up and ready for running BGFT quickly. See Section 4.



                                                                         15






            For users with a hard disk, it is recommended that these
            files be located in a separate sub-directory such as
            '\BGFT300'; this is done for you by the installation program,
            INSTALL.EXE.

            BGFTres.COM:
            This a generic term for the 'resident' portion of the system.
            You run one of these programs to install the communications
            driver for BGFT. BGFTres.COM is one of: BGFTHDZM.COM or
            BGFTFDZM.COM for the Hard Drive and Floppy Drive file
            buffers, respectively. Each program will perform background
            file transfers using Zmodem, Ymodem-Batch, Xmodem CRC, or
            Xmodem 1K protocols for uploads and downloads.

                 BGFTHDZM.COM:
                 This is the resident program used when using a reserved
                 section of the hard drive C: as a file buffer. You can
                 set up any size of file buffer up to half of the
                 available disk space by using the program, BGFTFB.EXE.
                 It is used when you run the installation program; you
                 are asked how much space you wish to assign to the file
                 buffer. The size of the file buffer may also be changed
                 at any time using the utility, BGFTFB.EXE.

                 BGFTFDZM.COM:
                 This is the resident program used when using a floppy
                 drive for the file buffer. The file buffer size is
                 determined by BGFT depending on the formatted capacity
                 of the floppy. Only the 1.2 megabyte floppy is
                 restricted to 720K. The resident program uses the floppy
                 drive A: or B: as selected; see Section 4.4.

            BGFTFB.EXE:
            Makes the hard drive file buffer on drive C: only. The file
            buffer is used by BGFT exclusively and the rest of the drive
            is available to DOS even during transfers. This program is
            used to delete the file buffer if need be. See Section 4.3.

            BGFT.EXE:
            The main foreground 'interface' portion of the program. It
            provides user control over the background file transfers and
            facilitates moving files to and from the file buffer. See
            Section 5.

            BGFT300.HLP:
            Online help file for BGFT.EXE.

            BGFT300.SCR:
            Screens for BGFT.EXE.

            BGFT.DLG:
            Dialing directory file for BGFT.EXE.




                                                                         16






            BGFTFLPY.EXE:
            You can 'fix' a floppy diskette that has accidentally been
            initialized for use as a BGFT file buffer back to a DOS
            floppy. Data will be lost if used by BGFT for a file
            transfer. This is the only documentation required for this
            utility.

            BGFTDIR.COM:
            Indicates whether a floppy diskette in drive A:, or B:, is a
            'BGFT floppy' or a 'DOS floppy', and prints out its directory
            to the screen. For example, to access drive A: you would
            enter:

                 BGFTDIR A:

            List files in the hard drive file buffer by entering:

                 BGFTDIR C:

            To access the file buffer being used as the active one by
            BGFTres.COM enter:

                 BGFTDIR

            This is the only documentation required for this utility.

            BGFTOPT.EXE:
            Command line processor which does foreground control of the
            resident programs, similar to BGFT.EXE. BGFTOPT can be used
            as an external transfer protocol option for other commu-
            nication programs such as PROCOMM PLUS, Qmodem, and Telix. It
            is explained in detail in Section 6. BGFTOPT.EXE is meant for
            use by the expert user who has specialized applications, such
            as for external communication program protocols. Use BGFT.EXE
            to move files from the file buffer to DOS directories.

            BGFTINIT.BAT:
            Initialize resident's baud rate and communication port. The
            file should be edited to the user's preference. The main
            foreground program, BGFT.EXE, protects the user from most
            inadvertent errors, it is also easier to use. BGFTINIT.BAT is
            not required if BGFT.EXE is used. It is mandatory for use
            with BGFTOPT.EXE; see Section 6.2.

            Below is a list of Telix SALT language scripts which use
            BGFTOPT.EXE as means to use external BGFT transfer protocols
            using the resident background file transfer system. Each
            script has comments to indicate its installation as an
            external protocol and operation (see Section 6.3). The
            example ideas can be used for any script-like language that
            has adequate capability (eg, able to exit without hanging
            up).




                                                                         17






            BGFTDZTL.SLT Telix script for Zmodem download.
            BGFTDYTL.SLT Telix script for Ymodem-Batch download.
            BGFTDXTL.SLT Telix script for Xmodem-CRC/1K download.
            BGFTUZTL.SLT Telix script for Zmodem upload.
            BGFTUYTL.SLT Telix script for Ymodem-Batch upload.
            BGFTUXTL.SLT Telix script for Xmodem-CRC upload.
            BGFTUITL.SLT Telix script for Xmodem-1K upload.

            There are a number of Telix support files; see Section 6.3 on
            their use:

            BGFTADD.BAT Batch file adds BGFT external protocols to Telix.
            BGFTTELX.DAT Data file for BGFTADD.BAT; modifies TELIX.CNF.
            BGFTSLC.BAT Batch file to compile all Telix support scripts.

            There is also a support package for PROCOMM PLUS (see Section
            6.4); it is made up of the following files:

            BGFTDZPC.ASP PROCOMM script for Zmodem download.
            BGFTDYPC.ASP PROCOMM script for Ymodem-Batch download.
            BGFTDXPC.ASP PROCOMM script for Xmodem-CRC/1K download.
            BGFTUZPC.ASP PROCOMM script for Zmodem upload.
            BGFTUYPC.ASP PROCOMM script for Ymodem-Batch upload.
            BGFTUXPC.ASP PROCOMM script for Xmodem-CRC upload.
            BGFTUIPC.ASP PROCOMM script for Xmodem-1K upload.

            There is also a support package for Qmodem (see Section 6.5);
            it is made up of the following files:

            BGFTDZQM.SCR Qmodem script for Zmodem download.
            BGFTDYQM.SCR Qmodem script for Ymodem-Batch download.
            BGFTDXQM.SCR Qmodem script for Xmodem-CRC/1K download.
            BGFTUZQM.SCR Qmodem script for Zmodem upload.
            BGFTUYQM.SCR Qmodem script for Ymodem-Batch upload.
            BGFTUXQM.SCR Qmodem script for Xmodem-CRC upload.
            BGFTUIQM.SCR Qmodem script for Xmodem-1K upload.

            BGFTXDLG.EXE:
            Automatically translates a Version 1.x and 2.x PROCOMM PLUS,
            Version 4.2 Qmodem or Version 3.x Telix telephone list to the
            BGFT format. The PCPLUS.DIR, QMODEM.FON or TELIX.FON file
            must be present in the directory in which the BGFT.DLG file
            will be produced. Just run BGFTXDLG and choose the
            translation you want. It will inform you that any BGFT.DLG
            file in the directory will be overwritten; you can escape the
            process, if required. A number of warnings will be produced
            where items are found that are not appropriate for BGFT
            operation. For example, the maximum baud rate is 57600, so
            that higher ones are set to 57600. You can use your printer
            and issue a 'Ctrl_P' to capture the warning list; you could
            also use file redirection (see your DOS manual for
            information). Fatal errors occur only for gross file problems
            or incompatibilities that preclude further useful processing.
            This is the only documentation required for this utility.


                                                                         18







            BGFTSPY.EXE:
            A Microsoft Windows 3 program to display information regard-
            ing the background file transfer packet count and BGFT
            resident status and the status of the current file transfer.
            Its display may be used in minimized (recommended) or
            maximized mode. An icon, BGFTSPY.ICO, is provided. You can
            acknowledge fatal BGFT errors from the Help menu. Use
            BGFTSPY.EXE only in real or standard mode Windows.

            BGFT386.PIF:
            BGFT386.BAT:
            If you have a 386 or higher type of CPU you can run BGFT as a
            DOS session in Windows enhanced mode. You can use these files
            to manually install BGFT to be called in Microsoft Windows.
            The batch file will have to be edited with an ASCII editor to
            indicated where BGFTres.COM and BGFT.EXE are. The PIF file
            will have to have the path to batch file included.

            3.2 Trying it Out
            -----------------

            In order to introduce you to the operation of BGFT, we
            suggest that you follow the example BGFT session presented
            here. We will illustrate the way you will use BGFT most
            often. The process is simple and has been geared to help you
            "try it out".

            The following assumes that this is the first time that you
            are using BGFT. Let's assume that you first try it out as
            Shareware. You will have downloaded the packages:
            BGFT302A.ZIP and BGFT302B.ZIP if you download from a BBS. For
            this example you will need only the first package,
            BGFT302A.ZIP. After you unzip it you should have the
            resulting files in some working directory; make sure it is
            NOT called, '\BGFT300'. Two of the important files that you
            get from BGFT302A.ZIP are: INSTALL.EXE and BGFT300A.EXE; they
            are used to create a 'minimal' BGFT installation for you to
            try out. The program, INSTALL.EXE, will be used to extract
            the files from the self-unarchiving file, BGFT300A.EXE.

            The following example will show you how to:

                 - do a simplified hard drive C: installation of BGFT,
                 - use BGFT with a modem,
                 - use the Zmodem transfer protocol,
                 - download a file from a BBS in the background,
                 - use the BGFT file buffer and move files to DOS.

            In order to do the installation you must be in the working
            directory where you have INSTALL.EXE and BGFT300A.EXE. You
            run the installation program (if needed, see Section 4 for
            details) by entering:



                                                                         19






                INSTALL

            You will be asked a number of simple questions in order to
            customize your system. You will be prompted along the way.
            Please make sure you do the following:

               - You must have at least 1 megabyte of free space on drive
                C:.

               - Choose to do the minimal installation when asked at the
                beginning of the installation. This will fast track your
                installation of the BGFT file buffer on the hard drive
                C:. You will be able to use the full features of BGFT in
                its own standalone environment.

               - Be prepared to indicate which communication port your
                modem is on.

               - Be prepared to indicate what baud rate your modem
                normally uses.

               - Be prepared to indicate whether your computer is
                connected to a telephone line (normal) or directly to
                another computer.

               - Be prepared to indicate what kind of telephone line you
                have (touch tone or rotary/pulse).

               - When the hard disk file buffer is going to be created you
                are asked how big you want it. Choose the buffer large
                enough for downloading the amount of files you are
                interested in, say 1000K (one million bytes). This is
                done under the constraint of how much room you have left
                on the drive C:.

               - The installation procedure will suggest putting two lines
                in your AUTOEXEC.BAT file to load the BGFT resident
                program that your system needs and an environment
                variable to tell BGFT where its home directory is. Agree
                to add them since BGFT will be available for you each
                time you run your computer.

               - At the end of the installation choose to automatically
                reboot your computer so that the new AUTOEXEC.BAT will be
                executed. This will load the resident part of BGFT for
                you.

            Make sure that your modem is on the desired communication
            port and operating. Be sure to change your active
            drive/directory to C:\BGFT300. You are now ready to use BGFT.

            1) At the DOS prompt, enter

                BGFT


                                                                         20







            This will run the user interface for you. Since this is the
            first time you would have run BGFT, there will be a warning
            indicating that the scroll back buffer file was not found. Do
            not be alarmed; just hit the 'ENTER' key to OK the message.

            2) The standard opening BGFT screen will then appear. Running
            BGFT will automatically activate the resident part. You will
            see the appearance of the resident part's status display
            'BGFT' (ready, with no errors), shown in the upper right
            corner of the screen. It is a four character 'window'.

            3) As prompted, press any key to continue. The opening screen
            disappears.

            For unregistered users, BGFT will then show a screen to
            remind you to register the program for your own use. Read
            this screen and then press any key to continue.

            4) A window message informs you that the modem is being
            initialized. On completion of the modem initialization, you
            will be in 'Terminal Mode'. Terminal Mode connects you to
            your modem. You are able to communicate to the outside world
            via the modem by typing in commands with the keyboard.

            Typing Alt_Z, the help key (see Section 5.14), will show the
            Terminal Mode 'hot' keys. These key combinations allow you to
            access important parts of BGFT's user interface functions
            quickly.

            The Alt_Z key sequence provides context sensitive help
            throughout the program; use it when needed. Alt_O provides a
            convenient overview help to assist you in navigating around
            BGFT's features.

            Typing Alt_M, or clicking the left mouse button on the top
            line of the screen, will display the Main Menu and a little
            bit of exploration will show you the layout of the system.

            Hitting 'ESC' out of the menus will get you back into
            Terminal Mode.

            5) From Terminal Mode you can check your modem's readiness by
            typing 'AT', followed by 'ENTER'. The modem should respond
            'OK'. Some modems will also accept 'at' for the 'attention'
            prompt. When BGFT initialized the modem in step 4) above, it
            sent the command 'ATE1' to cause the modem to echo responses
            in Terminal Mode. If you do not get an 'OK' you should
            consult Section 5.5.2 and your modem documentation. It is
            assumed that your modem's attention commands are nominally
            Hayes compatible; see Section 4.8.

            To dial a number to a BBS, type 'Alt_P' which will display
            the dialing directory. The dialing directory file provided


                                                                         21






            with BGFT has been set up to contain two entries for Dirac
            Systems' BBS: one for local dialing and one for long distance
            dialing. The first entry is 'selected' as shown by the
            highlighted bar.

            Type 'Alt_A', or use the mouse to click the left button on
            the <Add> button, to add a dialing entry between entries 1
            and 2. Fill out the dialog box fields to enter the number,
            name of the BBS you want to dial, and so on. The new entry
            will be entry number 2; the previous entry 2 will be re-
            numbered to entry number 3.

            You can move to different fields by using the tab key. The
            mouse provides direct control. Use the arrow keys to indicate
            choices.

            Once the dialing data entry dialog box has been completed,
            accept your input by pressing 'ENTER' or hit 'ESC' if you
            wish to abandon your input. Assuming you pressed 'ENTER', a
            window pops up to ask if you want to save the changes to
            disk. Type 'Y' to make the change permanent; typing 'N' keeps
            the entry only as long as the dialing directory is on screen.
            If you pressed 'Y' then a dialog box pops up to show that the
            dialing directory will be saved to a file called BGFT.DLG, in
            the current drive/directory. This dialog box allows you to
            save the file with any name you choose on any drive/directory
            on your computer. For now, press 'ENTER' to accept this file
            name and drive/directory.

            At this point BGFT lets you know that this dialing directory
            file already exists and asks if you want to overwrite it. In
            this case press 'Y' to overwrite. Your changes have now been
            saved in the default dialing directory file, BGFT.DLG.

            The new dialing entry will be shown as 'selected' by the
            highlight bar and is ready for dialing. On pressing 'ENTER'
            the dialing entry will be dialed and an information window
            will appear displaying the number dialed. To abort dialing
            press 'ESC'; typing any other key returns you to Terminal
            Mode.

            If you have sound enabled on your modem you should be able to
            hear the modem dial the selected number. The dialing that
            takes place is actually done in the background. This means
            that you can exit BGFT, done by typing Alt_X, and dialing
            will continue. Indeed, you can run any of your normal
            software as dialing continues. For this example, it is
            assumed that the connection is made soon.

            The BGFT status window will indicate the dialing progress.
            When the number is dialed you will see 'DIAL' in the window.
            It will 'WAIT' for a connection until it times out; you will
            see a 'PAUS' as it does this. The number will be retried
            until it gets a connection.


                                                                         22







            When a connection is made, the BGFT resident will 'beep' and
            the status display in the top corner of the screen will
            indicate 'BGFT'. You will be in Terminal Mode.

            Press 'ENTER' a couple of times from BGFT until the BBS re-
            sponds. Some BBSs may respond without any user action. Log on
            normally.

            Give the commands necessary to tell the BBS to start
            downloading a file using Zmodem.

            After a few seconds delay, BGFT's status window will change
            from 'BGFT' to 'DNLD'. A few Zmodem start up characters may
            be seen on the Terminal Mode screen. The menu bar at the top
            of the screen will then appear. You will not be able to
            return to Terminal Mode until the transfer is complete;
            however, a number of BGFT's functions are still available to
            you via the menus. The 'DNLD' will be replaced by '1', '2',
            '3', and so on to indicate 1 Kilobyte blocks being
            transferred to your system. Pressing the Alt_N 'hot' key
            displays an information window which provides the status of
            the file currently being transferred.

            Exit BGFT at any time by typing Alt_X. You can use your
            computer for whatever compatible purposes you want while the
            background file transfer is occurring. On exiting BGFT, a pop
            up window asks whether you really want to exit. Press 'Y' to
            exit. You can configure BGFT (see Section 5.5.4.1) using the
            Setup menu to exit without confirmation; this is much
            quicker. Unregistered users will see another screen; press
            any key to continue.

            While in DOS you will see the BGFT status window receiving 1
            Kilobyte packets.

            6) When the downloading is completed, the BGFT resident will
            beep a few times to let you know it has finished downloading
            the file. The BGFT status window will show 'OK'.

            To retrieve the downloaded file you must run BGFT again. To
            do this, return to the DOS prompt and enter 'BGFT'. As
            before, you must get through the opening screens
            (unregistered version only). The scroll back buffer file,
            BGFT300.SBB, will have been created so you will not get any
            warning. A dialog window appears and BGFT beeps once to tell
            you that there is a downloaded file in the file buffer. Press
            'Y' to indicate that you wish to 'move' the file from the
            file buffer so you can use it.

            Another dialog box appears and shows the downloaded file in a
            list. You choose files to move by hitting the space bar. The
            'd' (download) symbol to the right of the file name will
            toggle to '*' to indicate that it is tagged for moving. You


                                                                         23






            can also tag all the files by typing Alt_T; this is useful if
            you download many files.

            A default download target DOS directory is shown at the top.
            You can change it by tabbing to the 'Directories' list and
            using arrow keys to choose a new one by entering the
            highlighted choice; the path for moving will then change. You
            may use a mouse to achieve the same thing. Type Alt_M or
            click on <Move> with your mouse to start the file move. A
            status window then shows the progress of the files as they
            are moved from the file buffer to the DOS directory.

            On completion of the file move you will then be in Terminal
            Mode. Type Alt_L to list the files in the file buffer; there
            should be none since they were moved to the DOS directory.
            Type Alt_X to leave BGFT. The downloaded file can be found in
            the download drive/directory you accepted. It is now
            available for your use.

            The download example is now complete.

            You can see that BGFT is easy to use and that it is
            effective. Section 5 goes into detail about using BGFT.EXE
            and its advanced features. You may want to configure BGFT
            more to your preferences. You will be an expert in its use
            very quickly; remember, it is full of context sensitive help.






























                                                                         24






            4.0 Installation, File Buffers, and Resident Programs
            -----------------------------------------------------

            This Section will describe how to install and run the BGFT
            resident programs on your computer system.

            Installation of BGFT is normally a one time event. It can be
            done manually or semi-automatically with the provided program,
            INSTALL.EXE. We recommend using INSTALL.EXE to set up your
            system. It will guide you through a set up depending on what
            you determine your needs to be. You can either run the
            installation again at some other date to change things or
            change them yourself.

            The BGFT package has a lot of potential. Some users may not
            want all of it so the INSTALL.EXE program will minimize the
            files that you need. Moreover, there is a minimal installation
            that can be done; this will give you the standalone BGFT
            environment using the hard drive C: file buffer.

            In the full installation, one of the major choices you have in
            setting up your system is the choice of file buffer that you
            will use. We recommend the hard drive file buffer since it is
            faster and more convenient than the floppy based buffer. If
            you use the hard drive file buffer you will use the resident
            program, BGFTHDZM.COM for background file transfers. If you
            use the floppy drive you will use the resident program,
            BGFTFDZM.COM. We will refer to either by a generic name,
            BGFTres.COM. The installation program will take care of all
            these details and will load the resident you wanted through
            your AUTOEXEC.BAT file.

            The file buffer is used as a means to avoid conflicts with DOS
            during BGFT background transfers. The hard drive file buffer
            is a special initialized file reserved for BGFT on Drive C:. A
            whole floppy drive A: or B: can also be used as a file buffer;
            it is just a DOS formatted diskette which is manually
            initialized by BGFT.

            Running the BGFT communication environment is started by
            loading the resident part, BGFTres.COM, and then running the
            interface part, BGFT.EXE. BGFTres.COM exists as a TSR to do
            the dialing and file transfers in background and to be
            accessed and commanded by BGFT.EXE. The user interface, for
            example, allows you to move downloaded files from the file
            buffer to DOS directories for use. The operation of BGFT.EXE
            is explained in Section 5.

            If you reinstall BGFT or are upgrading from a former version,
            you should delete all the old files except the dialing
            directory, BGFT.DLG. Save the dialing directory either for
            information or for use with the new files, if it is
            compatible. In upgrading from version 3 files you may want to
            protect the configuration file, BGFT300.CNF.


                                                                         25






            4.1 The Installation Program
            ----------------------------

            When you receive BGFT as a registered package there should be
            the following files on the distribution floppy or floppies:

            BGFT300A.EXE:
            BGFT300B.EXE:
            These are the archived packages of BGFT programs and files;
            they are not "executable" in the normal sense, they contain
            files that are extracted during the installation process.
            There are two files so that they can be distributed more
            easily. When you register BGFT and order the files sent on a
            720K floppy, you will receive one floppy with the two
            registered distribution files and the installation program,
            INSTALL.EXE. If you order the files on 360K floppies then you
            will receive two floppies; one will have INSTALL.EXE and
            BGFT300A.EXE on it and the other will have BGFT300B.EXE on it.
            The installation program will look for both distribution files
            and deal with them; if it cannot find the second
            (BGFT300B.EXE) then it assumes it is on a second floppy and
            will ask you to insert it in your 5.25 inch floppy drive.

            BGFT300A.EXE contains all the files required for a minimal
            installation of BGFT on a hard drive. If you are new to BGFT
            or just want to evaluate the Shareware version, this might be
            all you need to get going. If you want the use the floppy
            based file buffer, Microsoft Windows 3.1 files, or files to
            run BGFT with other communications products then you can run
            the full installation again with BGFT300B.EXE included.

            The following files are in BGFT300A.EXE:

                 BGFTREAD.ME
                 BGFT.EXE
                 BGFT.DLG
                 BGFT.DOC
                 BGFT300.HLP
                 BGFT300.SCR
                 BGFTFB.EXE
                 BGFTHDZM.COM
                 BGFTORDR.FRM

            BGFT300B.EXE contains all the other files. If you want the
            full installation you must have both the A and B files.

            INSTALL.EXE:
            This is the installation program. It will appear with
            BGFT300A.EXE on a two 360K floppy distribution; BGFT300B.EXE
            will be on the other floppy. A 720K floppy distribution will
            have INSTALL.EXE, BGFT300A.EXE, and BGFT300B.EXE on the one
            floppy.




                                                                         26






            BGFTREAD.ME:
            This is a file, or a number of similar files, with information
            you should read for uptodate information not in the
            documentation.

            If you download BGFT as a Shareware evaluation package it
            should be the two files: BGFT302A.ZIP and BGFT302B.ZIP. Be
            sure that you start off in a directory that is not called,
            '\BGFT300' since the construction of such a directory is part
            of the installation itself. Keep all files in the same
            directory. BGFT302A.ZIP allows a minimal hard drive
            installation of BGFT. You should use the appropriate
            unarchiving program to extract the above files. For PKZIP from
            PKWARE you would enter

                PKUNZIP BGFT302A.ZIP

            This will produce the two files: INSTALL.EXE and BGFT300A.EXE
            and, perhaps, a text file to read. Do the same to BGFT302B.ZIP
            to produce the file, BGFT300B.EXE.

            You are able to use BGFT in a variety of ways. It can be used
            as a standalone telecommunications program or it can be used
            as an add-on with other popular packages. It can use a hard
            drive or floppy drive file buffer. There are numerous
            combinations of settings that you have for your modem and so
            on. The installation program, INSTALL.EXE, helps you make
            these choices that define your system. This is of particular
            use if this is the first time that you have encountered BGFT.

            If you have the Shareware files, go to the directory where you
            unzipped the files and enter:

                INSTALL

            and follow the prompts.

            If you have the registered distribution 720K floppy, put it in
            Drive A:, for example (assuming the drive supports the media).
            The installation program is easy to run; just go to drive A:
            by entering

                A:

            and then enter:

                INSTALL

            and follow the prompts.

            If you have the two floppy registered distribution be sure to
            put in the floppy with INSTALL.EXE on it first. When the
            second floppy is required you will be informed.



                                                                         27






            You can have an installation strategy at the beginning. If you
            are new to BGFT we recommend that you start off using our user
            friendly program, BGFT.EXE, as your interface program. It is
            convenient and easy to use. If you want to use the
            capabilities of BGFT with other programs you will have to use
            the less friendly program, BGFTOPT.EXE; it is described in
            Section 6.

            When you run the installation you always have the ability of
            quitting the program. You can always start again. The question
            for quitting requires a yes or no answer (y/n); a 'No'
            requires the 'n' or 'N' to be pressed, otherwise, any other
            answer, including 'y' or 'Y', will be taken as a 'Yes'.

            The INSTALL program is straight forward. The following is
            provided to describe what is available.

            You can run INSTALL with command line switches; normally you
            don't use them. There is a debugging mode that can be used by
            entering:

                INSTALL /D

            This will do all the things done normally but will tell you
            some information about your system and what it is constructing
            internally for path statements and so on. You can use this if
            you want to see what the program is assuming in case things
            did not turn out the way you expected.

            You can enter,

                INSTALL /B

            to see a little background on the BGFT story.

            Normally, you would just enter

                INSTALL

            to start the installation.

            If you want to do a manual installation see Section 4.2.

            4.1.1 Minimal Installation
            --------------------------

            BGFT is commonly used as a communications program that does
            background file transfers. As a standalone program you can use
            it for most of your needs. The hard drive C: file buffer gives
            the best performance since the hard drive is so much faster.
            The installation program will allow you to 'fast track' in
            this direction if you want.




                                                                         28






            When BGFT300A.EXE is found, the installation will ask whether
            you want to use it for the minimal installation. You can chose
            to do so or do the full installation instead. The minimal path
            will not ask about file buffer choices (Section 4.1.2), files
            for other communication products (Section 4.1.3), or Microsoft
            Windows files (Section 4.1.6) since they will not be
            installed.

            4.1.2 File Buffer Choice
            ------------------------

            The first choice you have is to use a hard drive file buffer
            or a floppy drive file buffer.

            If you choose the floppy drive file buffer you will be asked
            which floppy drive (A: or B:) that you want to use. The whole
            floppy is used as a BGFT file buffer and is unavailable for
            other uses.

            If you choose the hard drive file buffer you will cannot have
            the BGFTres.COM already loaded. You will have to leave the
            installation and reboot your system so that BGFTres.COM is not
            loaded.

            The hard drive file buffer directory must go on Drive C:. This
            is a limitation. You must have adequate space on any drive for
            the installation; otherwise, you are informed about the
            deficiency and will have to leave the installation. If you
            have to leave, go to the drive to make room as suggested.

            Users of STACKER are supported. The unstacked companion drive
            to C: will be used for the file buffer location.

            If BGFTres.COM loads automatically in your AUTOEXEC.BAT, you
            will have to edit it to avoid loading the resident.

            When you get back to this point where you left off, you will
            be allowed to continue. The reason you must not have the
            resident programs loaded is for making sure that there will
            not be a conflict over the hard drive file buffer when it is
            being created.

            Only a portion of drive C: is used as a BGFT file buffer. The
            rest of the drive is always accessible by DOS.

            4.1.3 BGFT Directory
            --------------------

            You are required to have your BGFT directory called
            '\BGFT300'. If a hard drive file buffer is chosen then it must
            be on drive C:. If a floppy drive file buffer is chosen then
            it cannot be where the file buffer will be. Otherwise, the
            directory can be on any legal drive that has enough space for
            the installation.


                                                                         29






            4.1.4 Support Files for Other Communication Products
            ----------------------------------------------------

            After you have completed the choice of file buffer, you will
            be asked if you want to install files to support other
            telecommunication programs. There are specific files for
            PROCOMM PLUS, Qmodem, and Telix. You will have the files
            copied to the corresponding directory where you keep other
            files for them. Any other installations you require, such as
            script compilation, will have to done manually. You can, in
            fact, move a basic (generic) set of these support files to any
            directory.

            When you input the directory name for the destination of the
            support files, you can edit your entry. Press 'F1' for help on
            the editing functions. The edit entry will appear yellow on
            color screens.

            4.1.5 Changes to AUTOEXEC.BAT
            -----------------------------

            The installation program will have determined where your BGFT
            directory should be and what command is appropriate to load
            the resident part of BGFT. This information is recommended to
            go into your AUTOEXEC.BAT so that it is available to you each
            time you turn on your computer. The AUTOEXEC.BAT file is
            always run first and the objective is to load the correct
            resident you specified and the environment variable used by
            BGFT to tell it where its home directory is.

            You will be presented with the additions expected to go into
            the AUTOEXEC.BAT file. You can keep them, reject them, or
            quit.

            Your AUTOEXEC.BAT is checked for occurrences of the string
            "BGFT". This will indicate that there may have been previous
            installations of BGFT. You will have the choice of keeping,
            making the entry a remark (makes the line inoperative in the
            batch file) or deleting the lines of the new AUTOEXEC.BAT.

            The installation will not put the BGFT directory in your PATH
            statement.

            4.1.6 System Specific Details
            -----------------------------

            The user interface program, BGFT.EXE, has a configuration file
            that it uses to correspond to your system and preferences. The
            INSTALL program sets up a basic configuration file,
            BGFT300.CNF, for BGFT.EXE. One of the most important things
            that BGFT.EXE does when it is first run is to initialize
            BGFTres.COM as to the communication port to be used and what
            its default baud rate is. The baud rate may be changed during
            a computer session but the communication port cannot. The


                                                                         30






            INSTALL program will ask for the communication port you want
            to use and its baud rate.

            There are two ways to use a communication port. It can be
            connected directly to another computer or, more normally, to a
            modem. You will be asked which to use.

            There are two types of telephone dialing methods that are
            used: the older pulse kind and the modern tone dialing kind.
            You will be asked which one you want.

            4.1.7 Files for Microsoft Windows
            ---------------------------------

            Some users will have Windows 3. BGFT will run under Windows
            and there is a Windows program that will monitor the progress
            of background file transfers. There is also an icon available
            for it. There is also support files for 386/486 users You will
            be asked if you want it in your BGFT directory. You will have
            to install it in Windows yourself. See also Section 4.15.

            4.1.8 Automatic Sequence
            ------------------------

            You have given the required information to allow the automatic
            installation.

                 One of the first things you are asked to choose a minimal
                 or full installation. The course of the installation will
                 vary depending on what you choose.

                 A BGFT directory, \BGFT300, is created on the drive that
                 you specified. There is no problem if it was created
                 before. Typically you would have deleted all the files
                 from it.

                 All the files in the distribution files, BGFT300A.EXE and
                 BGFT300B.EXE, are expanded to the target BGFT directory.
                 If the same files exist already from a previous
                 installation, the unarchiving program will prompt you as
                 to whether you want them overwritten with the new files.
                 Normally you would overwrite the files; you may want to
                 backup your dialing directory, BGFT.DLG, if it has been
                 modified for your use.

                 The support files for other communication products are
                 copied to the respective directory, if chosen. The BGFT
                 initialization batch file, BGFTINIT.BAT, is updated with
                 the relevant input.

                 The support files for Microsoft Windows 3 use are
                 retained in the BGFT target directory, if chosen.

                 Unnecessary files are deleted.


                                                                         31







                 The hard drive C: file buffer, BGFTHDFB.DAT, is created
                 interactively with another program, BGFTFB.EXE, if it was
                 specified. Just enter a size of file buffer that you
                 want. Sometimes there may be times when retries are
                 needed to successfully create a file buffer; you will be
                 notified. Floppy file buffers have to be manually
                 created; see Section 4.6.

                 The old AUTOEXEC.BAT file is backed up to AUTOEXEC.BAK in
                 the boot up root directory (taken to be the C: drive).

                 The new AUTOEXEC.BAT file replaces the old one.

                 The configuration file, BGFT300.CNF, is created for the
                 BGFT user interface program, BGFT.EXE. If an old
                 configuration file is found then old settings are
                 retained that are not asked about during the normal
                 installation. This allows you to retain old color choices
                 and so on.

                 You will be able to reboot your computer at the end of
                 the installation to run the new AUTOEXEC.BAT file or go
                 to DOS.

            That is the end to this installation procedure.

            The BGFT.EXE configuration file can be more fully set up to
            your needs. See Section 5.

            When you reboot your computer the correct BGFT resident will
            be loaded and ready for use with the interface, BGFT.EXE. If
            you desire a more custom setup or addition features you can
            read the rest of this Section. If you chose the floppy drive
            as the file buffer you will have to initialize a floppy
            diskette as described in Section 4.6. Otherwise, you are ready
            to use BGFT.

            4.2 Manually Organizing the Files
            ---------------------------------

            If you did not use the installation procedure above, you must
            keep all the files associated with BGFT in one directory,
            '\BGFT300' to do the manual installation. Specifically, use
            the DOS Make Directory command to make a directory from the
            root directory, for example:

                MD BGFT300

            If you use the hard disk file buffer then the directory must
            be on Drive C:. Suppose you set up BGFT on Drive C:.





                                                                         32






            BGFT is distributed via BBSs for Shareware evaluation in an
            archived format as files, BGFT302A.ZIP and BGFT302B.ZIP. Copy
            the archived files into the directory '\BGFT300' by entering:

                COPY BGFT302A.ZIP C:\BGFT300\*.*

            and

                COPY BGFT302B.ZIP C:\BGFT300\*.*

            Then use the change directory command to enter the new
            directory:

                CD \BGFT300

            To unarchive the files you will require PKWARE's PKUNZIP,
            Version 1.10 or greater. Enter the following:

                PKUNZIP BGFT302A.ZIP

            and

                PKUNZIP BGFT302B.ZIP

            and the files INSTALL.EXE, BGFTREAD.ME, BGFT300A.EXE and
            BGFT300B.EXE will be produced.

            To further extract the files you can run the self unarchiving
            files by entering:

                BGFT300A

            and

                BGFT300B

            When you register BGFT you will receive a one or two floppy
            distribution as you request; copy all the distribution files
            on the floppies we send you into the new directory. Supposing
            that the distribution diskette is in drive A: and that you
            made a '\BGFT300' directory is on hard drive C: as described
            above, you would enter:

                COPY A:*.* C:\BGFT300

            for each of the floppies.

            The files, BGFT300A.EXE and bgft300B.EXE, will automatically
            unarchive the necessary files themselves. Simply enter:

                BGFT300A

            and



                                                                         33






                BGFT300B

            You should be careful about overwriting your dialing directory
            if you had one before.

            You will be able to use the files as you see fit.

            4.3 Hard Disk Drive File Buffer Creation
            ----------------------------------------

            Normally the hard disk file buffer is made as part of the
            installation but it may be made manually at any time. The
            program, BGFTFB.EXE, is used.

            BGFTres.COM must not be loaded when using BGFTFB.EXE so there
            is a guarantee of no access conflict between the two programs.

            The only hard drive BGFTFB.EXE can create a file buffer on is
            Drive C:. It must be made in the directory, \BGFT300. It
            cannot be run on a floppy drive or other hard drive partitions
            (D:, E:, and so on).

            To run the program enter,

                BGFTFB

            and follow the prompts. If you just hit RETURN when asked to
            create a hard drive file buffer, it will delete any previous
            one that you made. Otherwise, enter a number corresponding to
            the size, in Kilobytes, that you want the file buffer to be.
            The only restriction is that the file buffer cannot be larger
            than 32767 Kilobytes on your C: drive.

            From time to time you may find that the program cannot make a
            file buffer the first time. The program will retry five times.
            If a file buffer cannot be made and verified, it may be due to
            disk defragmentation or other reasons.

            The file that is produced, BGFTHDFB.DAT, is a 'read-only' file
            to make it difficult to modify or move unintentionally; it
            should be reserved for BGFT's sole use. You will not be able
            to delete it with DOS unless the read-only status is changed;
            use BGFTFB.EXE if need be. Users must not use any utility or
            means to modify or relocate this file while transfers take
            place. The file is automatically initialized by BGFTFB.EXE for
            BGFT's use. You may 'initialize' it (see Section 5.9.2) with
            BGFT.EXE which would be equivalent to 'erasing' all files from
            the file buffer.

            The file buffer is used to contain download and upload files
            for use by the resident program, BGFTHDZM.COM. The downloaded
            files may be moved to regular DOS files by BGFT.EXE; see
            Section 5. The upload files may be uploaded as commanded by
            using BGFT.EXE.


                                                                         34







            From time to time you will notice that there is a file
            reorganization that takes place with the file buffer. This is
            a house keeping chore needed to organize the file buffer
            effectively. The BGFT window at the top right will show
            progress in the reorganization as a percentage.

            It is advisable for you to back up your drive before using
            this file buffer utility and downloads with BGFT. Please read
            the disclaimer in Section 2.1.

            It is advisable to defragment your disk too. If you defragment
            your disk you should delete the file buffer before doing so
            and then create it again afterwards. The file buffer has its
            own special mapping that may not make sense after
            defragmentation.

            4.4 The Resident Programs
            -------------------------

            If you installed BGFT with the INSTALL program then the
            desired resident program will be loaded into memory and ready
            for use on rebooting your computer. Otherwise, you will have
            to load it manually. BGFTres.COM is normally loaded after
            turning on your computer and before any application programs
            are run.

            If you are going to use the hard drive file buffer you use the
            resident program, BGFTHDZM.COM.

            If you are going to use the floppy drive file buffer you use
            the resident program, BGFTFDZM.COM.

            The resident program, BGFTres.COM, accepts some command line
            options. However, for normal operation, it is only necessary
            to invoke the program with the command:

                BGFTHDZM

            when using the hard disk as the file buffer (previously
            prepared by BGFTFB.EXE; see Section 4.3). The hard drive file
            buffer must be on Drive C:.

            To use floppy drive A: as the file buffer, enter

                BGFTFDZM

            Or, enter

                BGFTFDZM /B

            to use floppy drive B: for the file buffer.




                                                                         35






            The floppy drive resident program will determine the size of
            the file buffer that BGFT can support. See Sections 4.4 and
            4.6. They are:

                DOS Floppy          BGFT File
                Disk Size:          Buffer Size:

                 360K                360K
                 720K                720K
                1200K                720K
                1440K               1440K

            The command line options recognized by BGFTres.COM are:

             /1 - Use COM port 1 (only if BGFT300.CNF does not exist).

             /2 - Use COM port 2 (only if BGFT300.CNF does not exist).

             /3 - Use COM port 3 (only if BGFT300.CNF does not exist).

             /4 - Use COM port 4 (only if BGFT300.CNF does not exist).

             /B - Use floppy drive B: as the file buffer. Only used for
                 BGFTFDZM.COM. Using floppy drive A: as the file buffer
                 needs no command since it is the default.

             /C - Chain interrupts. Use if COM port 1 has a mouse and if
                 COM port 3 has a modem, similarly for the COM 2,4 pair.
                 Otherwise, do not use (eg, COM port 1 and COM port 4 are
                 all right.)

             /E - 'Spawn' the resident program, that is, do not run it as
                 a TSR. Run it this way from a DOS shell if you want to
                 delete it from memory after use. Enter 'EXIT' at the DOS
                 prompt to exit the shell and release the program.

             /I - Initialize the file buffer to BGFT format on startup.
                 This is not normally recommended. The hard drive file
                 buffer is automatically initialized on creation; the
                 floppy file buffer is usually manually initialized. An
                 initialization will erase existing files in the file
                 buffer. Initialization can be done from the interface
                 programs, BGFT.EXE or BGFTOPT.EXE.

             /L - Loopback mode used to echo characters on the given port.
                 This is not normally used; it is used as a system debug
                 tool only.

             /S - Use a String compare in background dialer. If a modem
                 cannot handle the carrier detect line properly for BGFT
                 operation, this command forces the BGFT resident to look
                 at modem string responses rather than relying on the
                 carrier detect line state. The problem may arise for new
                 types of modems when the modem initialization string


                                                                         36






                 forces the carrier detect to be always true. BGFT will
                 not do a modem initialization since it sees a connection
                 already made and will ignore the request.

             /? - This will list the valid list of arguments for the
                 command line options. This will only work if a resident
                 is not already loaded.

            4.5 Resident Program Error Messages
            -----------------------------------

            The resident part displays error messages in its 'BGFT'
            status window when it is turned on. The status window is a
            small four character 'window' normally located at the upper
            right corner of the screen. Its normal display is 'BGFT'
            which means it is dormant and error free. The error messages
            are displayed in the form: '**n' or '!!n' where n is a
            number. The '**' messages are 'soft' errors which do not
            cause file transfer to stop; the '!!' errors are 'hard'
            errors which will cause the file transfer to terminate.

            All hard errors must be acknowledged. You should use the
            Transfer menu in BGFT.EXE to acknowledge hard errors (see
            Section 5.8.9) or enter terminal mode where the
            acknowledgement is done automatically. They may also be
            acknowledged with BGFTOPT.EXE or BGFTSPY.EXE if you are in
            Windows.

            The following is a list of the 'soft' error messages:

             **0 In download or upload this is a timeout while
                 synchronizing to the host. It is normal to receive one
                 of these at the beginning of a transfer.

             **1 In download (only), this is a timeout while receiving a
                 block. The usual cause of this is that something has
                 happened to lose a character; for example, running a
                 program during background transfers that disables
                 interrupts for an excessive period of time, which is
                 common of some CGA programs.

             **2 This is a block check error during transfer. The block
                 will be present according to the Xmodem-CRC, Xmodem-1K,
                 or Ymodem-Batch protocols.

             **3 This is a CRC error, meaning the block had bad data in
                 it. This may be experienced if the telephone line is
                 noisy or a foreground program temporarily disabled
                 computer interrupts.

             **4 This is a duplicate block error, meaning the host sent
                 the same block twice for some reason. This is highly
                 unusual.



                                                                         37






             **5 This is an error specific to Zmodem. It could be the
                 result of line noise or a protocol error from the host.

            The following is a list of the 'hard' error messages:

             !!0 This is a fatal timeout that would occur if the host was
                 not responding.

             !!1 This error means that the host canceled the transfer.

             !!2 This error indicates a file buffer error. This could be
                 due to an I/O disk error or, on uploading, due to no
                 upload files in the file buffer.

             !!3 This occurs when the user requests to halt the transfer.

             ERR This occurs when an unknown error condition is detected.

            4.6 Floppy Disk Drive File Buffer Creation
            ------------------------------------------

            The floppy disk file buffer must be made manually. The
            floppies are formatted with DOS as usual and initialized for
            use by BGFT. The user interface program, BGFT.EXE, is normally
            used to initialize the diskette; see Section 5.9.2. The
            program BGFTOPT.EXE may also be used with the '/I' command
            line switch; see Section 6.7. The recommended procedure using
            BGFT.EXE will be described here.

            As explained above, each kind of floppy drive is capable of
            having a certain size of file buffer. The whole drive is taken
            over by BGFTFDZM.COM when it is used as a BGFT file buffer and
            it will not accessible from DOS. It is possible to 'turn off'
            the resident program so that the floppy can be accessed by DOS
            for another DOS floppy; see Section 5.9.1.

                 Place a new floppy in the floppy drive when BGFTres.COM
                 is turned off or not loaded. Format it with the usual DOS
                 FORMAT command for the normal size of the drive. Do not
                 use custom format utilities. It is important that the
                 floppy diskettes must not have any bad sectors on them;
                 use the CHKDSK program that came with your version of DOS
                 to make sure. It is recommended that you throw away
                 diskettes that have bad sectors as a good practice
                 anyway; there is something wrong with the floppy.

                 Please be careful about using old diskettes with data on
                 them. Using them as BGFT diskettes will destroy the data.
                 However one of the supplied BGFT programs, BGFTFLPY.EXE,
                 will deinitialize a BGFT floppy; but is must be done
                 before it is used for BGFT file transfers.

                 Floppy drive file buffers must be initialized manually.
                 In order to initialize the floppy, BGFTres.COM must be


                                                                         38






                 loaded. Put the DOS formatted floppy in the drive to be
                 used as the file buffer. Use BGFT.EXE to initialize the
                 floppy from the Utility menu.

                 You may also use BGFTOPT.EXE to initialize the floppy.
                 BGFTres.COM must be loaded and initialized with the
                 communication port and baud rate; use an edited version
                 of BGFTINIT.BAT with your communication port and default
                 baud rate (see Section 6.2). You then enter:

                    BGFTOPT /I

            The file buffer is used to contain download and upload files
            for BGFTFDZM.COM. See Section 5.8. There can be a combination
            of 31 files in the file buffer.

            The use of the floppy file buffer will be slower than the hard
            drive file buffer for essentially the same reasons as in DOS
            use. The size is restricted somewhat. However, many users like
            to be able to use this piece of rarely used equipment for a
            useful purpose. It is also a source of disk space that some
            users may not have on their hard drive. A floppy with 1.44
            Megabytes of room can make for a handy download area.


            4.7 BGFT Environment
            --------------------

            If you wish to run BGFT interface program, BGFT.EXE, from any
            directory, you should include the BGFT directory in a PATH
            statement in your AUTOEXEC.BAT file. For example, if you have
            installed BGFT in the directory '\BGFT300' on drive C:, then
            the following PATH statement would suffice:

                PATH = C:\BGFT300

            You should append the BGFT directory name to an already
            existing PATH statement. The installation program will not
            change your PATH statement.

            BGFT uses a number of support files. In particular:

                BGFT300.HLP - used for context sensitive help,
                BGFT300.CNF - used to store the user configuration,
                BGFT.DLG - used to store the dialing directory,
                BGFT300.SCR - used for program screens.

            Although BGFT will function without the file, BGFT300.HLP, it
            will inform you that the help file is not available. You are
            strongly recommended not to modify the help file in any way
            because this will almost certainly upset the correct
            functioning of the help system.




                                                                         39






            BGFT will work happily without the files, BGFT300.CNF and
            BGFT.DLG; it will create these files the first time you save
            the user configuration and the first time you save the dialing
            directory, respectively. Again, if you modify these files, by
            some means other than by using BGFT, the functioning of BGFT
            may become unpredictable. Updated versions of BGFT may change
            the format of the files so that it is recommended that old
            ones should be deleted.

            BGFT is designed to look for these four support files in one
            of two possible locations. First, BGFT looks in the current
            directory; if it cannot find the files there, it will look in
            a user directory specified by the environment variable 'BGFT'.
            The environment variable can be set, in your AUTOEXEC.BAT
            file, as given in the following example:

                 SET BGFT=C:\BGFT300

            In this example, the environment variable 'BGFT' is set to the
            directory '\BGFT300' on drive C:; that is, to the directory
            containing all the BGFT system files. This is recommended. If
            the environment variable method is used then BGFT will place
            the files BGFT300.CNF and BGFT.DLG in the directory specified
            by the environment variable the first time it creates them. If
            you wish to set up independent versions of these files in
            other directories, but still set the environment variable,
            then you should copy a version of these files, from the
            directory specified by the environment variable, into the
            desired directory, and then use BGFT to modify these files to
            suit your needs.

            For example, if you require to use more telephone numbers than
            BGFT allows (200), simply set up another DOS directory and
            place in it a copy of the file BGFT.DLG. With this new DOS
            directory as the current directory, run BGFT, and use it to
            modify the copy of BGFT.DLG to suit your needs.

            4.8 Modem Requirements
            ----------------------

            Your modem must be 'nominally' Hayes compatible. This means
            that it must respond to the normal 'ATxx' command set; for
            example, 'ATDT 555-6789' will dial the number 555-6789, with
            touch-tone dialing. The initialization string and the dialing
            command can be changed via the 'Modem...' option in the
            'Setup' menu. If your modem can detect a BUSY connection, then
            the dialer can also be configured to redial immediately. See
            Section 5.5.2.

            It is important to note that your modem must be set up such
            that the carrier detect line is active when a connection is
            made. BGFT assumes that the carrier detect line will indicate
            the status of the connection, ie. connected or disconnected.
            If this is not the case then there are several consequences.


                                                                         40






            First, BGFT must be set up to be in 'direct connect' mode (see
            Section 5.5.2). Second, the background dialer will be
            inoperable but file transfer will still be possible. In most
            cases, a Hayes compatible modem can be easily set up to
            manipulate the carrier detect line, so this should not be a
            problem; refer to your modem setup documentation for further
            information. BGFT can be set up to use modem strings instead
            of the carrier detect line; see Section 4.4.

            4.9 Systems Without a Hard Drive
            --------------------------------

            Even though BGFTres.COM makes exclusive use of drive A: or B:
            floppy, it is possible to use the system with a computer
            having only two floppy drives. Of course, the range of
            operation will be limited, but it is possible.

            In order to run your application from drive B:, it is
            necessary to set the COMSPEC environment variable to point to
            COMMAND.COM on drive B:. Use a command like:

                 SET COMSPEC=B:\COMMAND.COM

            which may be placed in your AUTOEXEC.BAT file. Of course,
            COMMAND.COM must be present on drive B: in order for DOS to
            operate correctly.

            4.10 BGFT and DOS 5
            -------------------

            The BGFT resident portion is quite small and is one of its
            biggest benefits. You can use the DOS 5 LOADHIGH utility to
            put BGFTres.COM into upper memory. This will leave the whole
            640K transient area unaffected by BGFT's presence. You will
            then be able to run large foreground programs while
            BGFTres.COM is coincidentally being used in upper memory. See
            your DOS 5 manual for details.

            For example, you may add a line like the following to your
            AUTOEXEC.BAT:

                 LOADHIGH C:\BGFT300\BGFTHDZM

            to load the hard drive file buffer resident into upper memory.

            Your CONFIG.SYS should have the proper memory management and
            so on for your system. An example for a 386 system might look
            like:

                 DEVICE=C:\WINDOWS\HIMEM.SYS
                 DEVICE=C:\WINDOWS\EMM386.EXE NOEMS
                 DEVICE=C:\DOS\SETVER.EXE
                 FILES=30
                 BUFFERS=30


                                                                         41






                 DEVICE=C:\DOS\EGA.SYS
                 SHELL=C:\DOS\COMMAND.COM C:\DOS\ /p
                 DOS=HIGH,UMB
                 STACKS=9,256

            4.11 BGFT and STACKER
            ---------------------

            BGFT version 3.01 and above is compatible with STACKER.

            In order to avoid DOS conflicts, BGFT uses its own mapping for
            managing files in the BGFT file buffer. The location of the
            hard drive file buffer is normally restricted to the directory
            \BGFT300 on drive C:. STACKER uses file compaction techniques
            to increase disk storage but this alters the mapping that BGFT
            requires if drive C: is stacked.

            If a user stacks the C: hard drive with STACKER then a pseudo
            drive C: is created that is 'really' not C:. If there was only
            one drive partition (C:) before installing STACKER then there
            will be an associated unstacked 'drive' created. It will be
            called the D: drive here since STACKER chooses the next drive
            letter after all the existing partitions. The BGFT hard drive
            file buffer maker, BGFTFB.EXE, will detect STACKER and create
            its file buffer on the uncompressed portion of the C: drive
            which is drive D: in this case.

            STACKER normally reserves a megabyte of uncompressed space and
            puts a few files there that are needed to boot the computer.
            Usually this leaves about 900K bytes free that can be used for
            a hard drive file buffer. If a larger file buffer is required
            then run the STACKER utility, SDFRAG, to create more
            uncompressed space; see the STACKER manual for detail.

            4.12 BGFT and DR DOS
            --------------------

            BGFT version 3.01 and above is compatible with DR DOS
            formatted drives. However BGFT version 3.02 is not compatible
            with the compaction utility, SUPERSTOR, in DR DOS.

            4.13 Multitasking and Communications
            ------------------------------------

            Multitasking with DOS is one of those ideas that is much
            simpler in theory than in practice. DOS just was not designed
            to do more than one job at a time. Even the common exceptions
            to this, such as the DOS print spooler or 'pop up' type
            programs, are specific to the application at hand and the
            techniques used to achieve the multitasking are not generally
            applicable.

            The 'lifeline' of a multitasking system is interrupts. Even
            more importantly, a communications program relies on


                                                                         42






            interrupts to process characters when they are received. If
            the characters are not 'taken away', then they will be lost.
            If an application program can easily disable interrupts then
            multitasking, and therefore communications, is going to be
            unreliable at best. Unfortunately with DOS on a PC, this is
            the case.

            Another major problem with DOS, as far as multitasking is
            concerned, is that DOS is non-reentrant. This means that DOS
            cannot be easily shared by applications running at the same
            time. This is because its data areas are not protected from
            simultaneous access.

            Most TSRs, eg. pop ups, work around the reentrant problems by
            trying to determine when DOS is busy; however, many DOS
            internal routines, such as the 'TYPE' command for example,
            keep DOS busy for as long as they execute. This again is a
            problem for multitaskers.

            OK, that is the bad news. The good news is that it is
            possible to circumvent DOS, or, in some cases, to ignore it.

            BGFT uses the latter approach. It does not use DOS in any
            part of the file transfer operation; therefore, it cannot be
            affected by DOS being busy.

            Disabling interrupts is another story. With a PC running DOS
            there is just no way to prevent disabling interrupts from
            happening if a running piece of software does it. This is
            true even with sophisticated multitaskers like Microsoft
            Windows 3 and DESQview 386.

            BGFT performs as well as running a 'standard' communications
            program under one of those multitaskers but does not require
            an Intel 80386 CPU and does not use anywhere near as much
            memory.

            The consequence of the interrupt disabling problem for file
            transfer is that retries will occur during downloading. If
            this is considered to be a serious problem in your
            application, then there are some possible hardware solutions
            such as the NS16550AS chip for your communications port;
            contact Dirac Systems for assistance in this area.

            BGFT will automatically detect the presence of the NS16550AS
            chip and take advantage of its capabilities.

            4.14 BGFT and DESQview
            ----------------------

            BGFT works exceptionally well with DESQview, particularly on
            computers that have expanded memory or with DESQview 386
            which emulates EEMS by using extended memory. This is because
            of the following two reasons:


                                                                         43







            1) On the Intel 80386 CPU, the 'LOADHI' program can run
            BGFTres.COM outside the 640K DOS address range. This means
            that the resident part of BGFT does not use up any
            conventional memory.

            When installing QEMM.SYS it is necessary to specify the 'ram'
            option. This is configuration dependent; see your DESQview
            user's manual or give us a call as we may be able to help.

            2) BGFT does not need to be made non-swappable. Thus DESQview
            can swap BGFT.EXE to disk or to expanded memory without af-
            fecting the communications.

            If you use DESQview then give BGFT a try. That is the advan-
            tage of Shareware.

            4.15 BGFT and Microsoft Windows
            -------------------------------

            BGFT is Microsoft Windows 3 compatible. Many DOS based
            telecommunications programs cannot even run under Windows.
            Others will have problems when trying to run Windows
            applications and DOS programs; this is especially true for
            286 or 8088 based machines.

            BGFT allows the user to engage in DOS as well as Windows 3
            activities while doing background transfers. Even Windows
            based telecommunication programs will generally not let you
            do that if not running in 386 protected mode.

            You must install the BGFT resident, BGFTres.COM, before
            running Windows. You must also initialize the resident with
            the communications port and baud rate by using a variant of
            the supplied batch file, BGFTINIT.BAT. Alternatively, you can
            run BGFT.EXE briefly to automatically do the initialization.
            You may then run Windows and use BGFT as you would normally.

            Your Windows documentation will show you how to install
            BGFT.EXE as a non-Windows application. The basic procedure is
            as follows. In the Program Manager of Windows choose the DOS
            applications group that you may have. Choose 'File' from the
            Program Manager and then choose 'New' to install BGFT as an
            item of the group. Where is asks for a 'Description' put in
            'BGFT'. Click with your mouse onto the 'Command line' prompt
            and enter the path name. where BGFT can be found; for
            example,

                 C:\BGFT300\BGFT.EXE

            You can activate BGFT by clicking twice on the icon you
            choose from the Program Manager.




                                                                         44






            A Windows 3 program, BGFTSPY.EXE, is included with BGFT to
            allow you to monitor background file transfers while you use
            other Windows programs. It can also acknowledge hard
            transmission errors. Install BGFTSPY.EXE as above and call it
            BGFTSPY; the supplied icon, BGFTSPY.ICO, will also be loaded.
            This program is most useful in minimized mode as it will
            show, in a compact form, the file packet number during file
            transfers and other status messages from the BGFT resident
            program. In maximized mode it will show more information. It
            is loaded in iconic form which is minimized mode; click twice
            on the icon for maximized mode.

            You should only run BGFTSPY.EXE if the BGFT resident program
            has been installed and initialized for communication port and
            baud rate. You will be warned it you did neither. BGFTSPY.EXE
            should only be run in Windows real or standard mode; under
            protected mode, there is likely to be a conflict with
            accesses to the resident program.

            To use BGFT.EXE with older versions of Microsoft Windows it
            is again necessary to load BGFTres.COM prior to running
            Windows; this is true for both Windows/286 and Windows/386.
            BGFT may then be executed as a 'standard' application under
            Windows. Windows will complain about a conflict with the
            communications port; select BGFT.EXE in the dialogue box and
            OK.

            For Windows/386 it is important that the parameter
            'windowmemsize' in the WIN.INI file is left at the default of
            640.

            The primary advantage to using BGFT.EXE under Windows,
            instead of a standard DOS communications package, is that
            BGFT.EXE can be 'swapped' out of memory whereas the standard
            DOS communications package would have to remain 'locked' in
            memory, using up valuable address space. This may be of
            importance in some applications such as Windows 2.X with
            expanded memory.

            If you use both DOS and Windows on an AT compatible computer
            then BGFT may be your best bet.

            4.16 Problem Solving
            --------------------

            Some programs, usually games, are not compatible with BGFT.
            In most cases, the conflict will be evident as retries during
            download. The retries are caused by the application disabling
            interrupts and, therefore, causing characters to be lost. The
            best thing to do is to experiment; in some cases, reducing
            the baud rate may help.





                                                                         45






            If BGFT fails to run properly on your system its probable
            cause can either be due to software or hardware conflicts.
            The most common cause is incompatible TSRs.

            The resident portion of BGFT is a TSR. Sometimes there may be
            other TSRs or software that hog resources or interfere with
            BGFT. In order to trouble shoot these problems you should
            delete all TSRs other than BGFT's. If BGFT runs all right
            then one of your other TSRs may be the problem. Try to
            isolate the problem and arrive at a solution or work around
            for your system.

            The order of installation of TSRs can also be important. Try
            reordering them. We recommend that you install BGFT as your
            first TSR in your AUTOEXEC.BAT file.

            BGFT, by its very nature, is carefully written so as to abide
            by the correct rules of building TSRs. BGFT is very robust
            software.

            If BGFT still fails to operate it may be your hardware. If the
            floppy file buffer version fails, then try the hard drive
            version.

            4.17 Operating Limitations
            --------------------------

            Users should be aware of the following limitations:

            1) The maximum recommended baud rate is normally 9600. Higher
            baud rates will tie up your CPU too much for effective
            foreground use by other programs. If you have a '486 then you
            may find that higher baud rates can be supported.

            2) Floppy diskette file buffers must not have any bad
            sectors.

            3) The floppy drive used for the file buffer is unavailable
            for DOS while under the control of BGFTFDZM.COM.

            4) The file buffer can have a total maximum of 31 files. The
            files can be downloads or uploads.

            5) When running graphics applications with a monochrome
            graphics card, BGFTres.COM does not automatically disable its
            status display as it does with color systems. This is easily
            overcome by the user manually disabling the display from the
            Utility menu before running the application. Even if this is
            not done, there will usually only be a remnant of the BGFTres
            display window appearing during monochrome graphics
            applications.

            6) The hard drive file buffer must be on Drive C: in
            directory '\BGFT300'. Its maximum size is 32767 Kilobytes.


                                                                         46






            4.18 BGFT Model Summary
            -----------------------

            This Section explained how to install a file buffer and a
            resident program needed for background file transfers. If you
            used the INSTALL.EXE program most of the details are taken
            care of for you. Having done a download with the example in
            Section 3.2 you should be convinced that BGFT is easy to use
            in spite of all the detailed features.

            Your mental model of BGFT should be:

            - A resident program, BGFTres.COM, does background file
            transfers to and from a file buffer.

            - The file buffer can exist on part of the hard disk C: or on
            a whole floppy drive diskette. The file buffer is used to
            avoid conflicts with DOS. Files are moved from the file
            buffer to DOS directories for your use.

            - The user interface program, BGFT.EXE or BGFTOPT.EXE, allows
            the user to communicate with the BBS connected to the modem
            or command the resident program to perform some function.
            When the use of the interface is completed only the resident
            part is left in memory to do transfers.

            This is somewhat like the modern vision of a client-server
            technology. The back end or the server is the resident doing
            most of the heavy work in the background. The front end is
            BGFT.EXE being used by you as the client to get files from
            the server via the file buffer.

























                                                                         47







            5.0 Operation of Main User Interface: BGFT.EXE
            ----------------------------------------------

            Section 3.2 described how to operate BGFT in a basic step by
            step way. Experienced users will demand more, so this Section
            gives the details that will be needed. The operation of BGFT
            is presented from a 'functional' point of view. This means
            that the menus are not described in order of appearance,
            except where deemed necessary.

            After a little bit of experimentation with the menu system,
            BGFT will be found to be easy to use. 'Hot' keys are provided
            if you wish to bypass the menu system; see Section 5.14 for
            the Alt_Key summary.

            5.1 Starting/Stopping BGFT
            --------------------------

            5.1.1 Starting BGFT
            -------------------

            The main user interface, BGFT.EXE, is normally invoked with
            no arguments specified on the command line, that is, by
            entering

                BGFT

            In this case BGFT runs in its normal interactive mode.
            However, it will accept the following command line 'switches'
            which cause it to carry out specific operations:

                 BGFT /H   The command line help switch, /H, or any
                           unsupported switch, will activate a help
                           screen.

                 BGFT /K   BGFT terminates (Kills) background dialing and
                           then exits.

                 BGFT /M   This forces BGFT to read the file buffer, and
                           if downloaded files are detected, to initiate
                           the sequence that moves the downloaded files
                           from the file buffer to a given download file
                           directory, and then proceed to terminal mode.
                           This is useful if you switched your computer
                           off after downloading files into the file
                           buffer but did not move them from the file
                           buffer to hard disk first. Some manual
                           operations will be required.

                 BGFT /N   When BGFT is first run, it will initialize the
                           modem with the modem command string taken from
                           the configuration file, BGFT300.CNF. There may
                           be times when you are already connected to a


                                                                         48






                           remote computer, by some other means, and want
                           to use BGFT for the first time but do not want
                           to send the modem string. To avoid sending the
                           string, use the command line switch, /N.

                 BGFT /R   BGFT suspends the resident part and then
                           exits. This is useful, in the case that a
                           floppy drive has been used as the file buffer
                           to gain quick access to the floppy drive when
                           the resident part is active. If you have
                           elected to use a floppy drive for the file
                           buffer, you cannot use this floppy drive for
                           non-BGFT purposes while the resident part is
                           active.

            5.1.2 Exiting BGFT
            ------------------

            You may exit BGFT by selecting the 'Exit' option from the
            'File' menu or by means of the 'hot' key Alt_X.

            If you set 'Confirm Exit' to on, as per Section 5.5.4.1, then
            a window pops up to ask you if you are sure; typing 'Y' will
            exit from BGFT, typing 'N', or any other key, will return you
            to where you were before you requested exit.

            If you chose to set 'Confirm Exit' to off, as per Section
            5.5.4.1, then BGFT will cleanly and swiftly exit to DOS.
            Exiting BGFT will not affect the resident part, particularly
            if the resident part is transferring files; it will leave the
            line open. Also, you can re-enter BGFT at any time; however,
            if you enter BGFT while background transfer is in progress,
            then you will be prevented from entering terminal mode until
            the transfer is completed.

            BGFT also provides an Alt_J key to enable you to run a DOS
            shell. This means that when you have initiated a file
            transfer you could run a shell so that you can run a DOS
            application while the file transfer continues in the
            background. However, this is not the recommended way because
            BGFT.EXE uses a substantial amount of memory. The recommended
            way is to exit BGFT is with Alt_X. This enables you to
            maximize the amount of memory available for your DOS
            applications. BGFT was carefully designed to allow quick in
            and out access. It remembers your configuration so that you
            would re-enter into the same state that you were in when you
            left.

            When you are running the unregistered package, you will
            always see a screen that provides you with registration
            information. Press any key to clear this screen and so
            complete the exit operation.




                                                                         49






            Sometimes, when you exit applications such as BGFT.EXE, you
            may experience a disturbance of the file transfer that is in
            progress. You may see a '**3' in the BGFT status window. This
            indicates that the application program may have suspended all
            interrupts. This is only a soft error and the transmission
            should recover. The problem is a limitation of Personal
            Computers and not BGFT.

            5.2 The Menu System
            -------------------

            If your system has a mouse, see Section 5.5.4.9 and 5.5.4.10
            for configuring it, BGFT will automatically detect it and
            enable it to be used to select items in the pull down menus.
            In the following description, appropriate mouse movement may
            be used instead of using the key board. In particular,
            pressing the left mouse button corresponds to 'ENTER' and
            simultaneous pressing of the left and right buttons
            corresponds to 'ESC'.

            The main menu system for BGFT is activated from terminal mode
            by typing 'Alt_M', or clicking the left mouse button on the
            top line of the screen. The menu is of the pull down type.
            Pull down menu items can be activated by either typing the
            first letter of the option/sub-menu name, or by using the
            left and right arrow keys to select it, followed by pressing
            'ENTER', or by dragging or clicking the left button of the
            mouse. Similarly, items on the pull down menus can be
            activated by pressing the key corresponding to the
            highlighted letter, or by using the arrow keys followed by
            'ENTER', or by using the mouse.

            For example, to view the current status of BGFT, press Alt_V
            to pull down the 'View' menu. Then use the down arrow key to
            highlight the 'BGFT Status' option; pressing 'ENTER' will
            activate the status display. An alternative to using the
            arrow key would be have been to press the highlighted letter
            of the menu option, in this case 'b'.

            If you have a mouse installed, the above could have been
            achieved by pressing the left button of the mouse with the
            mouse cursor on the top line of the screen. Keeping the left
            button pressed, drag the mouse cursor to the 'View' option,
            the view menu will pull down. Then drag the mouse so as to
            highlight the 'BGFT Status' option and release the mouse
            button. The status window will appear.

            If you are using a color monitor, pull down menu items that
            are currently in-active are displayed in grey without a
            highlighted letter. If using a monochrome monitor, in-active
            menu items can be identified as ones that do not have a
            highlighted letter. If you attempt to use an in-active menu
            item then you will simply return to your previous state
            without further action.


                                                                         50







            Pull down menu items that show '...' after the description,
            lead to dialog boxes where further user interaction is
            required, for example, the 'Prepare Files For Upload...',
            option from the 'Files' menu.

            Some menu options have a '>' character at the right hand
            side. This indicated that there is a side pull down menu that
            will appear if this option is selected, for example, the
            'Colors' option from the 'Setup' menu.

            Some menu items simply toggle features 'On/Off'. If BGFT is
            in the 'toggled' state then the menu option will show a check
            mark on the left hand side.

            Pressing 'ESC' from any point in the main menu system will
            return you to terminal mode. Typically, the 'ESC' key exits a
            BGFT menu or window without any action being taken and
            returns you to your previous state.

            The main menu entries are briefly described as follows:

            5.2.1 File
            ----------

            Selection of this item using Alt_F, or the mouse, pulls down
            a menu list with the following operations:

            Save Downloaded Files: Moves download files from the file
                 buffer to a DOS file.

            Prepare Files For Upload: Copies DOS files into the file
                 buffer ready for uploading.

            Echo Screen To A File (ON): Sends all the text that appears
                 on the terminal mode screen to a DOS file for later
                 retrieval.

            Terminal Mode: Returns operation to terminal mode.

            DOS Shell: This will run a DOS shell. This allows you to
                 suspend execution of BGFT.EXE and run other applications
                 from the DOS prompt.

                 When in the DOS shell, the DOS prompt will show the
                 message: "Type 'EXIT' to return to BGFT".

                 When in the shell, BGFT is still in memory. WARNING: if
                 the DOS PRINT command is used to print a file but the
                 PRINT driver was not loaded into memory before BGFT was
                 run then the driver will 'lock' BGFT into memory. When
                 BGFT is exited, about 180K of space will unavailable to
                 do foreground tasks. TSRs like PRINT, which are to be
                 run in the shell, should be loaded before running BGFT.


                                                                         51







            Exit: This exits BGFT. Typing 'Alt_X' at any location in BGFT
                 has the same effect.

            5.2.2 View
            ----------

            Selection of this item using Alt_V, or the mouse, pulls down
            a menu list with the following operations:

            File Buffer: Alt_L. Lists the files in the file buffer.

            BGFT Status: Alt_N. Shows the current status of BGFT, in
                 particular, it shows the status of the files being
                 transferred.

            Scroll Back Buffer: Alt_B. Allows viewing of text that has
                 scrolled off the terminal mode screen.

            Clipboard: The prime purpose of the clip board is to be able
                 to capture text from the terminal mode screen, edit it,
                 and then send the modified text back to the remote
                 computer. A simple example would be to capture to the
                 clipboard a list file names from the remote computer and
                 then to use the clipboard to pick out a subset of the
                 files you wish to download. The clipboard allows you to
                 send this modified list back to the remote computer.
                 This would normally be in response to the remote
                 computers request for a list of file names. This can
                 save a lot of typing and avoids mis-spelling the file
                 names.

            5.2.3 Dial
            ----------

            Selection of this item using Alt_D, or the mouse, pulls down
            a menu list with the following operations:

            Default Dialing Directory: Provides access to the default
                 dialing directory. The dialing directory allows you to
                 organize your telephone numbers and dial them quickly.
                 The name of the default dialing directory is specified
                 as described in Section 5.5.4.

            Other Directories: Provides access to any BGFT format dialing
                 directory on your computer.

            Kill Dialing: Terminates background dialing.

            Hang-up The Phone: Hangs up the line and breaks the
                 communication.





                                                                         52






            5.2.4 Transfer
            --------------

            Selection of this item using Alt_T, or the mouse, pulls down
            a menu list with the following operations:

            Download Files: Allows selection of protocols for downloading
                 files.

            Upload Files: Allows selection of protocols for uploading
                 files.

            Kill Transfer: Enables file transfer to be aborted (Killed).

            Acknowledge Errors: Allows resetting of the resident part in
                 the event of a file transfer hard error.

            5.2.5 Setup
            -----------

            Selection of this item using Alt_S, or the mouse, pulls down a
            menu list with the following operations:

            Terminal Emulation: Allows selection of a given terminal
                 emulation type. Terminal emulations are normally set in
                 the dialing directory.

            Modem: Change modem parameters.

            Communications Port: Change communication port settings.

            Preferences: Define user preferences.

            ASCII Communications: Set ASCII communications parameters,
                 such as end of line translation.

            Color: Alter the colors (if you have a color system) of the
                 various types of menus and windows used by BGFT.

            5.2.6 Utility
            -------------

            Selection of this item using Alt_U, or the mouse, pulls down
            a menu list with the following operations:

            Turn Resident OFF: De-activates the resident part.

            Initialize File Buffer: Prepares the file buffer ready for
                 use.

            Modem Initialization: Sends the initialization string to the
                 modem.

            Status BGFT Window: Toggles the 'BGFT' window on/off.


                                                                         53







            Relocate BGFT Window: Allows relocating the 'BGFT' to
                 anywhere along the top line of the screen.

            Clear Screen Terminal Mode: Clears the terminal mode screen.

            5.2.7 Information
            -----------------

            Selection of this item using Alt_I, or the mouse, pulls down
            a menu list with the following operations:

            Overview: Provides a brief overview of the operation of BGFT.

            Errors: Describes the possible error codes.

            About: Provides copyright information for BGFT.

            5.3 Dialog Boxes
            ----------------

            All the dialog boxes use the concept of an 'active area'. The
            active area defines the current area of focus. For example,
            the 'Save As' dialog box has six areas; namely, the file
            name, file list, drive/directory list, open button, cancel
            button and the help button. You can move from one area to
            another using the tab or shift_tab keys. The active area is
            always identifiable because it is the area with the cursor
            displayed. You can also move to a different area by clicking
            the left button of the mouse with the mouse cursor in the
            desired area, for example, anywhere in a file list or within
            the borders of a given set of radio buttons. You can also
            change areas using the Alt keys together with the indicated
            highlighted letter. However, as for the mouse method, some of
            these areas lead to immediate action, for example, clicking
            on the <Help> button.

            In addition to the active area concept, BGFT dialog boxes may
            have one or more of the following features:

            5.3.1 Action Buttons
            --------------------

            BGFT's dialog boxes have action buttons, for example, <Move>.
            In most cases the result of the action is adequately
            described by the description given between the <>. The
            actions can be initiated in one of the following three ways:

            1) By pressing an Alt key corresponding to the highlighted
            letter, for example, for the above example this would be
            Alt_M.





                                                                         54






            2) Use the tab (shift tab) to move forward (backward) from
            one button to another. When the cursor is located at the
            desired button, press the <ENTER> key to activate the button.

            3) Click the left button of the mouse on, or between, the <>
            characters.

            On BGFT's dialog boxes, three of the buttons always have the
            same meaning; these are:

            a) <Ok> : the Ok button accepts the information selected on
            the dialog box and then closes the box. Choices made remain
            in memory and, in many cases, can be saved to the
            configuration file.

            b) <Cancel> : The Cancel button exits the dialog box without
            any changes to the parameters listed in the box.

            c) <Help> : The Help button provides context sensitive help
            and provides descriptions of the parameters listed in the
            box.

            5.3.2 File Lists
            ----------------

            A file list is simply a list of file names showing the size
            of the file, and, in some cases the type of file, that is,
            whether the file is for uploading or was downloaded. The file
            lists each have a vertical scroll bar to enable moving
            through the file list by using a mouse.

            If you are using the keyboard, you can move through the list
            using the vertical arrow keys, PgUp and PgDn, Home and End
            keys.

            If you have a mouse you can move through the file list by
            dragging the file cursor bar using the left mouse button.
            Also, clicking the left mouse button on the up/down arrows of
            the scroll bar will move up/down through the file list one
            file at a time. Furthermore, clicking the left mouse button
            on the vertical scroll bar will page the file list up/down
            depending which side of the scroll bar tag you click. Also,
            you can drag the scroll bar tag up and down if you wish to
            move quickly through the list.

            In the dialing directory there is a horizontal scroll bar and
            this works in a similar way to the vertical scroll bar.

            Files in the file list can be 'tagged' using the 'SPACE' bar,
            or by double clicking the left mouse button on the desired
            file name. A tagged file can be identified by the '*'
            character. Some dialog boxes have a <Tag All> button that
            toggles the tag status of all the files in the list.



                                                                         55






            5.3.3 Drive/Directory Lists
            ---------------------------

            You can move around a drive/directory list in much the same
            way as you would a file list.

            To change to the previous directory simply locate the
            highlighted cursor bar on the '..' symbol and then press
            'ENTER'. If using a mouse double click the left mouse button
            on the '..' symbol.

            To change to another directory locate the highlighted cursor
            bar on the desired directory name and then press 'ENTER'. If
            using a mouse double click the left mouse button on the
            desired directory name.

            To change to another drive, locate the highlighted cursor bar
            on the desired drive letter and then press 'ENTER'. If using
            a mouse double click the left mouse button on the desired
            drive letter.

            5.3.4 Data Input Fields
            -----------------------

            Data input fields are of two distinct types, character input
            or numeric input. For both types you can edit the characters
            or numbers types using the left and right arrow keys,

                 Home           goes to the beginning of the field.
                 End            goes to the end of the field.
                 BACKSPACE      deletes the previous character.
                 DEL            deletes the character under the cursor.
                 INS            toggles insert mode.
                 Alt_B          blanks the input field.

            If invalid characters are typed BGFT beeps as a warning.

            Where accurate input is required, BGFT checks to make sure
            that valid input has been typed. A message window appears to
            inform of invalid input. For example, if BGFT is expecting
            the name of a drive/directory BGFT will check to see that
            drive/directory exists; if not, a warning message appears.
            You must type a valid entry before you can move to the next
            field.

            5.3.5 On/Off Flags
            ------------------

            On/Off flags are distinguishable by the [ ] characters. If
            the flag is 'true' then you will see [X]; otherwise you will
            see [ ]. To set a flag first of all, move the active position
            to the desired flag. Then use the 'SPACE' bar to toggle the
            flag. If using a mouse simply click the left button of the
            mouse on the [ ].


                                                                         56






            5.3.6 Radio Buttons
            -------------------

            Radio buttons are distinguishable by the ( ) characters.
            Radio buttons are used where a parameter has a number of
            distinct values, such as the baud rate. If using the keyboard
            move the active point to the desired radio button sequence.
            Then use the left/right arrow keys to move to the desired
            value. If using a mouse simply click the left button of the
            mouse on the desired ( ).

            5.4 The Help System
            -------------------

            BGFT provides the following two types of context sensitive
            help:

            5.4.1 Message Line
            ------------------

            A message line at the bottom of the screen is provided for
            practically all functions of BGFT to indicate current status
            of the given function or to give brief guidance on the
            available options. For example, a reminder that pressing
            'ESC' will return you to terminal mode.

            5.4.2 Alt_Z Help Key
            --------------------

            A help key for more detailed help information. BGFT uses
            Alt_Z as the help key. The help key is active practically
            anytime keyboard input is required. Pressing the help key in
            terminal mode gives a list of 'hot' keys used to speed up
            certain BGFT operations from terminal mode.

            5.5 Configuring BGFT
            --------------------

            BGFT allows you to change its appearance to suit your needs
            and preferences. In particular, the 'Setup' pull down menu is
            provided to allow you to customize BGFT. The 'Setup' menu can
            be accessed via the main menu or directly from terminal mode
            using Alt_S; the pull down menu has the following options:

            5.5.1 Terminal Emulation
            ------------------------

            This option pops up a side menu which is a list of the
            terminal emulations that can be selected to suit the computer
            system that you are connected to. The available emulations
            are: NONE, ANSI, VT100, and VT52. BGFT has a limited set of
            basic terminal emulations because these are normally
            sufficient for background file transfer purposes.



                                                                         57






            The VT100 keypad is mapped to the PC function keys as
            follows:

            PF1 > F1    PF2 > F2    PF3 > Shift_F1    PF4 > Shift_F2

             7  > F3     8  > F4     9  > Shift_F3     -  > Shift_F4

             4  > F5     5  > F6     6  > Shift_F5     ,  > Shift_F6

             1  > F7     2  > F8     3  > Shift_F7    Enter>Shift_F8

             0  > F9     0  > F10    .  > Shift_F9    Enter>Shift_F10

            'Shift_F10' indicates that the Shift key and then the F10 key
            should be held down together momentarily.

            5.5.2 Modem Parameters
            ----------------------

            On selecting the modem parameter option, 'Modem', a dialog
            box pops up allowing you to select various modem setup
            commands.

            The following are the parameters that can be modified:

            5.5.2.1 Modem Initialization String

            This entry should be used to set the initialization string to
            be sent to your modem on starting BGFT. BGFT was designed to
            work with Hayes compatible modems, so you should check your
            modem documentation to decide appropriate setup commands.
            BGFT does not automatically send the modem attention string
            'AT', so you should include that at the start of the command.

            If you start BGFT without a configuration file, then it uses

                ATE1 S7=255 S0=0 V1

            as the default string. The S7 modem register is used by the
            modem to wait the indicated number of seconds for a
            connection. However, BGFT configures its own wait time (see
            5.5.2.4 and 5.5.2.5 below) which will override it. Change
            this with care to suit your needs and your modem.

            5.5.2.2 Dialing Command

            The following commands instruct the modem to auto-dial:

                ATDT instructs the modem to use Tone dialing,
                ATDP instructs the modem to use rotary-Pulse dialing.

            BGFT defaults to tone dialing if you are not using a config-
            uration file. You must use one of these commands if auto-
            dialing is to work.


                                                                         58






            5.5.2.3 Hang Up Command

            BGFT uses two methods to hang up the line. The quickest, and
            so probably the most desirable, is by inhibiting 'DTR'.
            However, you will have to check your modem documentation to
            make sure that this feature is supported by your particular
            modem model. On earlier, and consequently slower modems, this
            would be done by means of the appropriate 'dip' switch
            settings. On later modems, for example, the Hayes Smartmodem
            2400, this can be done with software through a suitable modem
            command.

            The second method, which is somewhat slower than the DTR
            method, is to send the modem hang-up string, for example:

                ATH0

            See your modem documentation for further information on this
            command. BGFT handles the appropriate time delays so that you
            should not include any time delay instructions. BGFT uses the
            DTR method first and, if unsuccessful, then sends the modem
            hang-up string.

            5.5.2.4 Time Between Dialing

            This command sets the number of seconds BGFT will wait for a
            carrier before it gives up, assuming that the line was not
            busy. The 'Time Between Dialing' allows you to set the
            interval between dialing cycles from 1 to 999 seconds. If you
            run BGFT without a configuration file it defaults to 55
            seconds. International connect times can take over a minute;
            local calls typically take 30 seconds or less.

            5.5.2.5 Test for 'BUSY'

            BGFT is able to use modem information, if available, as to
            whether the line is busy when dialed. If the line is busy,
            BGFT will drop the line without waiting for the connection
            and background re-dialing will recommence. The default is 'Y'
            to enable this feature.

            5.5.2.6 Direct Connection

            If you are using a null modem connection to communicate with
            another computer, rather than a modem, then you should enter
            'Y'. In that case, the above modem commands are ignored. If
            you are using a modem then you should select 'N'.

            If you run BGFT without a configuration file then it will
            default to 'N'; it assumes that you are using a modem.






                                                                         59






            5.5.3 Communication Port Settings
            ---------------------------------

            Selecting the communication port option, 'Comm port', pops up
            a dialog box that allows you to make the following communica-
            tion port selections:

            5.5.3.1 Communication Port Number

            BGFT is designed to work with one of the communication ports
            1 (default), 2, 3, or 4; you must have the appropriate
            hardware installed. You cannot set up background
            communications on more than one port at a time.

            It is recommended that your modem be connected to
            communication port 2 and, if you have a mouse, that it be
            connected to port 1. Port 2 has a higher priority when
            dealing with hardware interrupts; having your modem there
            will aid in communications.

            There are general hardware limitations on the PC for users
            who wish to use a combination of odd or even serial
            communication port pairs. This is due to the physical
            construction and the way hardware interrupts were designed to
            be handled on the PC. For example, some users may want to
            have COM 1 for the mouse and COM 3 for the modem since some
            internal modems use COM 3. This is not recommended (the mouse
            on COM 1 and modem on COM 4 is all right). Under BGFT, there
            is a 'work around' solution provided. The mouse driver should
            be loaded in before BGFTres is activated and the resident
            part should be loaded with the '/C' command line option. For
            example,

                BGFTres /C

            This will inform the resident part about the existence of the
            mouse on the other paired port and allow for a proper
            'chaining' of interrupts between the modem and the mouse.
            This option should not be used if they are on an odd and even
            COM port as recommended.

            If you attempt to run BGFT without a configuration file then
            it will check to see whether or not a communication port has
            been specified earlier via the BGFTres command line. If not,
            it will prompt you to specify an appropriate communication
            port number.

            5.5.3.2 Baud Rate

            BGFT allows you to specify the following baud rates:

            300, 1200 (default), 2400, 4800, 9600, 19200, 38400 and 57600




                                                                         60






            If you run BGFT without a configuration file it prompts you
            to specify a value.

            When using the automatic dialer, the baud rate must be
            specified. This is done by setting the baud rate in the
            dialing directory; this will override any value set
            previously.

            5.5.3.3 Data Bits

            Serial communications make use of various data formats,
            usually of the following two forms:

            8 data bits, 1 stop bit, and No parity (8 1 N) or,
            7 data bits, 1 stop bit, and Even parity (7 1 E).

            Most BBSs use (8 1 N) but some mainframe computer networks
            may use (7 1 E). With BGFT you may chose several formats;
            valid entries for data bits are: 7 or 8 (default).

            5.5.3.4 Stop Bits

            Valid entries for stop bits are: 1 (default) or 2.

            5.5.3.5 Parity

            Valid entries for parity are: N for No (default), E for Even,
            O for Odd, M for Mark, or S for Space.

            5.5.4 Preferences
            -----------------

            The user Preferences menu option pops up a dialog box to
            allow selection of user preferences to suit your needs. The
            following are the available options:

            5.5.4.1 Confirm Exit

            As BGFT is a background utility, it is highly desirable to be
            able to get into and out of it as quickly as possible. For
            example, you might want to initiate the upload of a
            collection of unrelated files using Zmodem and then quit out
            to DOS to run your favorite spread sheet package. To this
            end, BGFT has a 'hot' key Alt_X, that allows you to exit BGFT
            from any location. When using the program for the first time
            it can be a little disconcerting to discover just how easy it
            is to exit BGFT. Consequently, this user option allows you to
            request a confirmation prompt before exiting.

            After frequent use of BGFT you will almost certainly want to
            turn confirmation off. If you run BGFT without a
            configuration file it defaults to 'Y', for confirmation.




                                                                         61






            5.5.4.2 Background Sound ON/OFF

            This option allows you turn off all sound effects related to
            the operation of the BGFT resident part, for example, the
            sound that you hear when BGFT has established a connection or
            has completed a file transfer. This can be useful if you are
            running BGFT late at night and you do not wish to disturb
            others. This option does not affect BGFT's foreground sound;
            the foreground sound can be controlled as described in
            5.5.4.3 below.

            Turning sound off for BGFT will not turn sound off for any
            other application program that you might be running while
            BGFT is performing its background activities. If you run BGFT
            without a configuration file then it defaults to background
            sound 'on'.

            5.5.4.3 Foreground Sound ON/OFF

            This option allows you turn off all sound effects related to
            the foreground operation of BGFT, for example, the sound that
            you hear when you type an invalid entry in a dialog box. This
            can be useful if you are running BGFT late at night and you
            do not wish to disturb others or if you simply do not like
            BGFT beeping at you.

            If you run BGFT without a configuration file then it defaults
            to foreground sound 'on'.

            5.5.4.4 Tab Width

            When using terminal emulation you may need to set the tab
            width as required. If you run BGFT without a configuration
            file, the default tab width is 8.

            5.5.4.5 Number of Lines to Scroll Back

            This option allows specification of the number of lines used
            for the scroll back buffer. The smaller this number the less
            memory BGFT will use. Valid entries range from 25 to 999; the
            default is 200.

            5.5.4.6 Show When the Scroll Buffer is Full

            The scroll back buffer is a circular buffer so that when the
            buffer is full it starts to overwrite the characters that
            were put into the buffer first. When this happens, the
            overwritten contents are lost. If the "Show Scroll Buffer
            Full" flag is set to on, then BGFT prompts each time the
            buffer gets full and so provides you with the option of
            saving the contents of the buffer to a file before any of the
            contents get overwritten. The default is not to prompt when
            the buffer is full.



                                                                         62






            5.5.4.7 Save the Scroll Back Buffer on Exit

            This option instructs BGFT to save the contents of the scroll
            back buffer to a file, BGFT300.SBB, on exit and to
            automatically restore the contents of the buffer the next
            time BGFT is run; this is the default.

            If the flag is set to off, the scroll back buffer contents
            are not saved and the buffer is 'emptied' each time BGFT is
            run.

            5.5.4.8 Default Dialing Directory

            When the 'Default Directory' option is selected from the
            'Dial' menu, BGFT looks for a dialing directory with the name
            specified by the 'Default Dialing Directory' field. This
            field must be a valid file name and that file must have been
            previously created using the BGFT dialing directory system.
            The default is 'BGFT.DLG'.

            5.5.4.9 Mouse Speed
            This field allows setting of the desired mouse speed; valid
            values lie in the range 1 to 100. The default value is 50; a
            value of 100 corresponds to the maximum speed setting.

            5.5.4.10 Mouse Double Click Time

            This field allows setting the maximum time between mouse
            button clicks for mouse double click operations. The default
            values is 5 and the units of measure are tenths of a second.

            5.5.4.11 Enable Zmodem Auto-Download

            When downloading with Zmodem this feature allows downloading
            to start automatically. This means that as soon as the remote
            computer has been instructed to download using Zmodem, then
            the download will start without any further user interaction;
            this is the default setting. If this feature is not set then,
            after having instructed the remote computer to download using
            Zmodem, it is necessary to select Zmodem download from the
            BGFT 'Transfer' menu.

            5.5.4.12 Auto Save File Directory

            When BGFT downloads a file it first of all downloads the file
            into the file buffer. The files that are transferred into the
            file buffer are in a format that cannot be accessed by DOS
            and so have to be converted to a DOS readable file and moved
            to another drive/directory before they can be used.

            When the file transfer is complete, and you return to BGFT
            from whatever you were doing while transfer took place, BGFT
            will semi-automatically transfer the files that had been
            downloaded into the file buffer to the drive/directory


                                                                         63






            specified by 'Auto Save File Directory' You are given the
            option to change the drive/directory if required.

            If you do not wish to have this process done semi-
            automatically then simply enter 'MANUAL' instead of a path
            specification. You may manually move files from the file
            buffer to another drive/directory using the 'File' menu.

            If you run BGFT without a configuration file it will default
            to the current drive/directory because it has no way of
            knowing which directory you want the files to be moved to.

            Each time you run BGFT it checks with the resident part to
            see if any files have been downloaded, that is, assuming that
            you had specified a 'Auto File Save Directory' name. It does
            this, rather than reading the file buffer directly, to save
            time and to enable you to get into the program quickly in the
            case that no files have been downloaded; for example, after
            an upload. However, if you switch your machine off, or re-
            boot it after a download, then BGFT will not initiate an
            auto-move of files until after your next download. In that
            case, you may wish to use the manual method from the 'File'
            menu to move your downloaded files or use the '/M' command
            line option.

            5.5.5 ASCII Download Parameters
            -------------------------------

            The following parameters are provided to enable adjustment of
            your setup so as to effectively perform ASCII file transfers
            to, or from, a wide variety of remote computer systems.

            5.5.5.1 Character Pacing

            Some remote computer systems have limit on the speed at which
            they can receive characters. This is typical for older
            computer systems that expect characters to be sent no faster
            than the speed of a fast typist. For such a case, a small
            time delay can be inserted between each character. These time
            delays are measured in 1/20 th second intervals; the default
            is zero. This feature applies to ASCII upload only.5.5.5.2
            line pacing.

            5.5.5.1 Line Pacing
            Some remote computers require a brief time delay (line
            pacing), after the transmission of each line of text. If some
            of the characters are getting lost in the transmission, try
            increasing the line pacing value. The default value is 5.
            This feature applies to ASCII upload only.







                                                                         64






            5.5.5.3 Pace Character

            The pace character is a distinct character that is used to
            denote the end of a line of text. The default is a 'blank'.

            5.5.5.4 Expand Blank Lines

            If this flag is set, then blank lines will show as blank
            lines; otherwise downloaded text will appear without any
            separating blank lines. The default is to expand blank lines.

            5.5.5.5 Expand Tabs

            This field determines how tabs are to be treated; if set,
            tabs will be expanded to the value of tabs set as described
            in Section 5.5.4.4. If this option is not set then a
            transmitted tab has no effect. The default is to expand tabs.

            5.5.5.6 Add Line Feed to Carriage Return

            Some remote computers do not send line feeds after a carriage
            return. Evidence of this would be the text overwriting itself
            on the same line on the screen. If this option is set then a
            line feed is added to each carriage return sent by the remote
            computer; the default is not to add the line feed.

            This feature is not strictly related to ASCII upload/download
            but is generally available.

            5.5.5.7 Local Echo

            When communicating with some remote computers characters
            typed on the keyboard do not show up on the screen. When this
            option is set, it enables key strokes to be 'echoed' to the
            screen; the default is no echo.

            This feature is not strictly related to ASCII upload/download
            but is generally available.

            5.5.5.8 End of Line Translation for ASCII Transfers

            The following two situations are catered for:

            Translation for Carriage Return

            The available options are:

            - None.
            - Strip (remove carriage returns).
            - Add Line Feeds.






                                                                         65






            Translation for Line Feed

            The available options are:

            - None.
            - Strip (remove line feeds).
            - Add Carriage Returns.

            The defaults have been set to give correct translation when
            communicating with PC Board BBS's.

            5.5.6 Colors
            ------------

            If you have a monochrome system then the screen appearance
            can be changed only to toggle a white or black background.
            WARNING: If you configure BGFT to be monochrome but then
            install a color system, you will have to delete the
            configuration file, BGFT300.CNF, and re-configure to get
            colors.

            The following Section is only applicable if you have a CGA,
            EGA or VGA color system. If you have a monochrome monitor,
            with a color type video card, then the options in this
            Section will have limited affect on the display.

            The 'color' option allows you to change the colors of the
            various BGFT screens. The method of changing color is first
            to select the screen feature that you wish to modify using
            the side pull down menu. At this point a window pops up
            showing the current colors for the given screen feature.
            Simply follow the instructions listed in the pop up window to
            change the colors. For example, if you wish to change the
            colors of the terminal mode screen then:

            1) Select the terminal mode option, 'Terminal Mode', from the
            side pull down menu.

            2) Type 'f' or 'F' to step through the available foreground
            colors.

            3) Type 'b' or 'B' to step through the available background
            colors.

            (If you use a mouse simply click on the lines with the 'f' or
            'b' to step through the available colors.)

            WYSIWYG stands for 'What You See Is What You Get' so that the
            color changes that you make by following 1) to 3) above are
            those that you will actually see when you return to the
            terminal mode screen. Once you are happy with your color
            scheme, press 'ENTER' to accept the colors and return to
            terminal mode. If, on the other hand, you decide that you



                                                                         66






            would rather keep the old color scheme, simply press 'ESC'
            instead of 'ENTER'.

            5.6 Terminal Mode
            -----------------

            When you first run BGFT after turning on your computer you
            arrive in terminal mode after you have negotiated the opening
            screens. At this stage you will be either connected to your
            modem or you will be in direct contact with another computer
            via a null modem cable (a direct connection). These two cases
            are described separately below:

            5.6.1 Using a Modem
            -------------------

            If you are using a modem, assuming you have set your modem
            configuration switches appropriately and/or have set the
            modem initialization string to suit (including the 'ATE1'
            command), then characters typed at the keyboard will be
            echoed on the screen. For example, typing 'AT' followed by
            pressing 'ENTER' will produce the familiar 'OK' response from
            the modem. In fact, you can type any valid modem command
            string and the modem will respond accordingly. For example,
            you can manually type the appropriate commands to dial a
            given telephone number; normally you would not do that
            because it is so much more convenient to use the dialing
            directory and so get the benefits of background dialing.

            Occasional users are not recommended to send manual commands
            to the modem via terminal mode because BGFT makes certain
            assumptions about how the modem is set up. If you somehow the
            modem gets into a weird state, inadvertently via manual
            terminal mode commands, then the response of BGFT may become
            unpredictable. Just in case, BGFT allows re-initialization of
            the modem; this is done via the 'Modem Initialize' option
            from the 'Utility' menu. To do this, BGFT first sends the
            'ATZ' command which, for earlier modems, such as the Hayes
            Smartmodem 300, resets the modem to its power up condition,
            initializes its registers, reads the configuration switch
            settings and does the power up test. For later modems, such
            as the Hayes Smartmodem 2400, the 'ATZ' command resets the
            user configuration.

            5.6.2 Direct Connection
            -----------------------

            Any characters typed in terminal mode are transmitted directly
            to the other computer and what is seen on the screen depends
            upon how the other computer is set up.






                                                                         67






            5.7 Background Dialing
            ----------------------

            An important feature of BGFT is that it can do dialing in the
            background. That means once dialing is initiated and BGFT is
            exited, dialing will continue even though the computer may be
            used for other activities. When dialing is complete and a
            connection is made, an audible beeping sound will be heard,
            that is, assuming that the default option of 'BackGround
            sound' is set to on. If you wish to terminate dialing before
            a connection has been made, then this can be done by using
            the Alt_K 'hot' key if you are running BGFT, or by typing
            'BGFT /K' from the DOS prompt assuming that you left BGFT
            earlier.

            To assist with the process of dialing, BGFT has a dialing
            directory. The dialing directory can be accessed from termi-
            nal mode via the main menu (Alt_D) or directly via the Alt_P
            'hot' key. You can select a dialing entry as described in 1)
            below. Pressing 'ENTER', or double clicking the left mouse
            button, will dial the number of the selected entry (if
            connected to a modem).

            The following operations are possible from the dialing
            directory dialog box:

            5.7.1 Selecting a Dialing Entry
            -------------------------------

            - Use the up and down arrow keys to move from one entry to
            another.

            - Use the 'PgUp' and 'PgDn' keys, on the key pad, to move one
            page up or down one page at a time.

            - Use the 'Home' key, on the key pad, to move to the first
            entry in the directory.

            - Use the 'End' key, on the key pad, to move to the last
            entry in the directory.

            - Drag the highlight cursor using the left mouse button.

            - Use the mouse on the vertical scroll bar.

            - By typing the first digit of the dialing entry number (not
            to be confused with the actual telephone number), a window
            pops up showing the digit typed. By completing the number and
            pressing 'ENTER', the entry with the given number is
            selected. On entering a number out of range, a message to
            this effect will be displayed.

            - Use of the <Find> button will display a pop up window that
            allows specification of a character string to be search for


                                                                         68






            (in the forward direction); the search is case sensitive. The
            dialing entry which contains the first occurrence of the
            given string will be selected; wild cards are not supported.

            Use the right arrow key to display additional information
            contained in the dialing directory. The password for the
            computer to be logged on to can be seen in this way. Use the
            left arrow key to return to the original display.

            If you are employing a mouse, the horizontal scroll bar can
            be used instead of the left/right arrow keys.

            Pressing 'ESC' gets you back to terminal mode.

            5.7.2 Editing Dialing Entries
            -----------------------------

            The selected (highlighted) dialing entry can be edited by
            using the <Edit> button. A dialog box, identical to that used
            when creating new entries, allows editing of all the fields
            of the highlighted dialing entry. On using the <OK> button,
            you will be prompted to determine if you wish to make your
            changes permanent by writing the modified dialing directory
            to disk.

            5.7.3 Adding Entries
            --------------------

            A dialing entry can be added by using the <Add> button. The
            new dialing entry is inserted immediately after the selected
            (highlighted) dialing directory entry. On initiating the
            'Add' option, a dialog box pops up requesting the following
            information:

            Name: Use the 'name' field to make it easy to identify the
                 telephone number. Keywords may be used to facilitate the
                 search feature.

            Number: The telephone number may include the characters: '(',
                 ')' and '-' to assist with readability. The characters,
                 'W' and 'R', are also allowed by some modem
                 manufacturers and are permissible.

            Password: This is optional since it is not used except for
                 your own information. It should be the password that you
                 will have to use when you log on to the remote computer
                 system.

            Baud: BGFT allows 300, 1200, 2400, 4800, 9600, 19200, 38400
                 and 57600 baud rates.

            Terminal: This allows you to store, in the dialing directory,
                 the type of terminal emulation you require. This means
                 that when you dial a particular number, BGFT will


                                                                         69






                 automatically set the terminal emulation to the one
                 specified by this field. The valid choices are: NONE,
                 ANSI, VT100, and VT52.

            Data bits: Choose '7' or '8' (default).

            Stop bits: Choose '1' (default) or '2'.

            Parity: Choose 'N' for None (default), 'E' for Even, 'O' for
                 Odd, 'M' for Mark, or 'S' for Space.

            On using the <OK> button, you will be prompted to see if you
            wish to make your changes permanent by writing the modified
            dialing directory to disk.

            5.7.4 Removing Entries
            ----------------------

            The dialing entry under the highlighted cursor bar can be
            deleted by using the <Delete> button. On using the <OK>
            button, you will be prompted to see if you wish to make your
            changes permanent by writing the modified dialing directory
            to disk. If you do not save your changes to disk they will
            remain in memory only until you leave the dialing.

            5.7.5 Dialing an Entry
            ----------------------

            Select the desired dialing directory entry as described in 1)
            above. To dial the highlighted entry press 'ENTER', or double
            click the highlighted entry using the left mouse button, or
            use the <Dial> button.

            On initiating dialing an information window pops up to allow
            you to confirm that you have dialed the desired number.
            Assuming that the modem is appropriately set up, then you
            will hear it start to dial. At this time one of the following
            may be done:

            - Wait until the resident part beeps to inform that a
            connection has been made. You may also hear the familiar
            sound that the modem makes, if the modem speaker is enabled,
            also telling you that a connection has been made. The
            information window automatically clears and terminal mode is
            entered. You would normally press 'ENTER' until the remote
            computer issues the log-on identification prompt. Some
            systems respond without any user action.

            - Press any key (except 'ESC') to clear the information
            window; this takes you to the terminal mode screen. Terminal
            mode will be disabled but it will automatically be enabled
            once the connection has been made.




                                                                         70






            The advantage of going straight to terminal mode, as de-
            scribed above, is that you can now make use of some of BGFT's
            features (via the Alt_Keys or menus) while dialing continues
            in background. For example, you could select the 'Files' menu
            and prepare some files for uploading and so not waste time
            waiting for the connection to be made.

            - Type 'Alt_X' and leave BGFT and then run some other
            application program while dialing continues in background.
            This background ability is what makes BGFT significant. It is
            very convenient to have a background dialing capability if
            you are trying to connect to a busy BBS.

            Most application programs these days allow you to temporarily
            return to DOS without quitting the application. This is
            called "Shelling to DOS". When you hear the resident part
            beep, to tell you that the connection has been made, you can,
            if your system has sufficient spare memory, temporarily leave
            your application and then re-run BGFT from the DOS prompt.
            For example, you can run a DOS shell from your application
            program and then use BGFT to log-on to a remote computer and
            initiate file transfers, then leave BGFT and 'EXIT' back to
            your applications program, carrying on from where you left
            off. BGFTres will take care of your file transfers in
            background.

            - Type 'Alt_J' and suspend BGFT.EXE to run other applications
            from the DOS prompt. You can EXIT back to BGFT when the
            connection is made.; this is not the preferred mode. It is
            better to leave BGFT using Alt_X because in this way you will
            free up the maximum amount of memory for other applications.

            - Pressing 'ESC' will cause dialing to be terminated. This is
            useful if you have inadvertently dialed the wrong number.

            5.7.6 Kill Background Dialing
            -----------------------------

            Termination of background dialing can be done in three ways:

            1) Background dialing may be terminated at any time while
            running BGFT by using the Alt_K 'hot' key.

            2) It may also be terminated by selecting the 'Kill Dialing'
            option from the 'Dial' pull down menu.

            3) If you have exited BGFT and you wish to terminated back-
            ground dialing, simply run BGFT with the '/K' command line
            option:

                BGFT /K

            This will instruct the resident part to terminate dialing and
            will


                                                                         71






            automatically exit BGFT.

            5.7.7 Resident's Status Window
            ------------------------------

            The resident part displays specific dialing information in
            the upper right hand corner (default location of the BGFT
            window), while it performs the task of background dialing.
            The following is a explanation of the displayed codes:

            WAIT: dialing is in progress,

            PAUS: dialing has timed out, the resident part will wait
                 'time between calls' seconds and then redial,

            DIAL: dialing is being re-initiated,

            STOP: dialing was terminated using one of the following,
                 'ESC' from the dialing information window, the Alt_K
                 'hot' key, or the /K command line option.

            5.8 Background File Transfer
            ----------------------------

            BGFT supports uploads and downloads for:

            Zmodem: This is the most popular batch file transfer protocol
                 and, due to its high reliability, is the protocol of
                 choice for BGFT.

            Ymodem-Batch: This is also known as DSZ-Ymodem. This protocol
                 allows for multiple file transfers and its
                 implementation in BGFT is excellent.

            Xmodem-CRC: This is the classic CRC version of the Xmodem
                 protocol which sends 128 byte packets. No checksum is
                 done by BGFT as it is much less reliable than CRC
                 checking, so it was not included. Xmodem-CRC is
                 sometimes known as just Xmodem. BGFT will report packets
                 sent in terms of 1K sizes.

            Xmodem-1K: This is the one Kilobyte (1024 byte) packet
                 version of Xmodem-CRC. Xmodem-1K is sometimes referred
                 to as Ymodem.

            Since the resident part of BGFT uses a file buffer, it is
            occasionally necessary to do some file buffer 'housekeeping'.
            This means that before uploading, the DOS files to be
            uploaded must be moved into the file buffer and, after
            downloading, the files must be moved from the file buffer to
            DOS files.





                                                                         72






            5.8.1 The File Buffer
            ---------------------

            BGFT uses the concept of a file buffer to avoid having to
            access DOS during file transfer When downloading, the data
            received is copied into the file buffer. After downloading is
            completed, the files in the file buffer may be copied into
            regular DOS files, on your drive/directory of choice, through
            the use of the 'Save Downloaded Files' option from the 'File'
            pull down menu. For uploading, the files must first be copied
            into the file buffer, with the 'Prepare Files For Upload'
            command, before the upload is initiated.

            The file buffer may either be on the C: hard drive
            (preferred), or on either floppy drive A: or B:. When using a
            floppy drive as the file buffer, that drive becomes
            unavailable for use by other programs. The floppy drive can
            be made temporarily available for other programs as described
            in Section 5.9.1.

            5.8.2 Background File Downloading
            ---------------------------------

            There are four background file transfer protocols available
            for downloading: Zmodem, Ymodem-Batch, Xmodem-CRC and Xmodem-
            1K.

            Section 3.2 described the basic operations to enable your
            computer to accept downloads with BGFT. When the host
            computer is ready to download files to your computer, choose
            the corresponding protocol set up on the host by pressing the
            'PgDn' key and then select the same protocol from the pull
            down menu list. When using Zmodem with the auto-download
            feature enabled it is not necessary to select the protocol
            using 'PgDn'.

            If you are using a floppy drive as the file buffer, be sure
            that your floppy drive door is shut and the drive contains a
            BGFT initialized diskette when you want to do file transfers.

            The Zmodem and Ymodem-Batch protocols are similar; they are
            both multiple (batch) file transfer protocols. Zmodem can be
            viewed as being more sophisticated than Ymodem-Batch. For
            example, Zmodem has a powerful feature that allows a file
            transfer to be resumed after some interruption. For example,
            imagine you are transferring a large file, say 1 megabyte,
            and a power interruption occurs aborting the transfer just
            before the transfer is complete.

            For Ymodem-Batch, you would have to go back to the beginning
            and transfer the file all over again. For Zmodem you simply
            re-connect and start the transfer again. However, this time
            the file transfer will start from where you left off, that
            is, it is smart enough to know that you have transferred most


                                                                         73






            of the file already. This makes Zmodem very suitable for
            transferring large files over noisy telephone lines. Zmodem's
            automatic download start feature is not part of the Ymodem-
            Batch protocol.

            Partial Zmodem files are identified by a 'a' in the listing
            of the file buffer directory.

            When using Zmodem or Ymodem-Batch, it is important to keep in
            mind the size of the file buffer. If BGFT receives a file
            that will overflow the file buffer, it halts the transfer and
            shows an error on the status display.

            If attempting to download with Zmodem (auto-download
            disabled) or Ymodem-Batch a file that already exists in the
            file buffer, the file will be saved with a modified name. The
            modified name is formed by using punctuation to replace the
            first character of the file name. Thus the name used is
            recognizable and the original file is not overwritten. The
            sequence of characters used to replace the first character of
            the file name is: '$', '#', '&', '@', '!', '{', '}', '~'.
            Only eight levels of renaming are available; however, this
            should be more than enough in most cases.

            If Xmodem-CRC or Xmodem-1K is selected, then BGFT will prompt
            for the file name to be used; if BGFT's 'guess' at the file
            name is all right, which it is if the file name was the last
            'word' typed, just hit 'ENTER' to accept it. If the file name
            was not the last 'word' typed, simply use the up arrow key to
            show the previous 'words'. Continue until you find the
            required file name. You may also edit the displayed 'word' if
            desired; use Alt_Z to show the editing details.

            5.8.3 Manually Moving Downloaded Files
            --------------------------------------

            To move downloaded files manually from the file buffer to a
            DOS file, select the 'File' option from the main menu. On
            selecting the 'Save Downloaded Files' file option from the
            pull down menu, a dialog box appears that allows you to
            easily select the drive and directory that you wish to move
            the downloaded files to.

            5.8.4 Automatically Moving Downloaded Files
            -------------------------------------------

            The easiest way to move files from the file buffer is simply
            to type Alt_Q from Terminal Mode. This is equivalent to
            tagging all the downloaded files in the file buffer and
            moving them to the default download directory.






                                                                         74






            5.8.5 ASCII File Downloading
            ----------------------------

            The ASCII protocol is provided for the convenience of
            transferring small text files. For example, you can prepare a
            text message off-line and save it in a DOS file. Then, use
            ASCII upload to insert that text directly into a message when
            you are using a message editor on a BBS.

            The ASCII protocol is a foreground protocol, that is, it is
            only active when you are running BGFT.EXE. Furthermore, the
            ASCII protocol does not have any form of error checking. So
            if the telephone line is noisy, spurious characters may show
            up in the transmitted text. If you need accurate transfer of
            information, you should use one of the other protocols, as
            they all have error checking capabilities.

            5.8.6 Preparing Files For Uploading
            -----------------------------------

            There are four background file transfer protocols available
            for uploading: Zmodem, Ymodem-Batch, Xmodem-CRC and Xmodem-
            1K.

            Uploads from your computer are initiated by pressing the
            'PgUp' key, or via the 'Transfer' menu, and protocols are
            chosen in a similar fashion to downloading. The receiving
            computer should have been prepared to receive the files with
            the same protocol which is used to send files.

            To prepare files for uploading, first go to the 'File' pull
            down menu using the Alt_F from terminal mode; select the
            'Prepare Files For Upload' option. At this point a dialog box
            appears. This dialog box enables you to select a given
            drive/directory and then to copy selected files to the file
            buffer.

            Having selected the chosen drive/directory, go to the file
            list and, using the arrow keys or the mouse, highlight a file
            that you wish to upload. Then press 'SPACE', or double click
            with the left mouse button, to tag the file (note the '*'
            tag). Repeat this for all the files you wish to upload and
            then use the <Copy> button to instruct BGFT to copy the
            tagged files into the file buffer. Up to 31 files may be
            tagged. BGFT will display the status of the files as it
            copies them to the file buffer.

            The moved files may have different file sizes than the
            originals; this is merely a result of transferring files in
            512 byte packets and will have no impact on the files
            themselves.

            To check that you have copied all the files that you
            intended, select the 'File Buffer' option from the 'View'


                                                                         75






            menu. The files contained in the file buffer will then be
            displayed. Files tagged ready for upload are marked with a
            'u'. If, for some reason, the file buffer contains files that
            were previously downloaded, then they will be tagged with a
            'd' or an 'a'.

            Zmodem and Ymodem-Batch protocols will upload all the files
            marked 'u' in the file buffer. This is a handy feature for
            uploads in using the file buffer; Zmodem transfers will start
            automatically if configured for it. If you decide that you do
            not need to upload all the files that you placed in the file
            buffer, after all, then the unwanted files may be delete
            files as described below:

            1) Select the 'File Buffer' option from the 'View' menu to
            view the files in the file buffer.

            2) Move the cursor bar to highlight the file you wish to
            delete.

            3) Press 'SPACE', or double click the left mouse button, to
            tag the file.

            4) Repeat 3) to tag all files you wish to delete.

            5) Use the <Delete> button to initiate the deletion. BGFT
            responds by asking you if you are sure that you wish to
            delete the tagged files, type 'Y', or use the mouse. After a
            brief pause, the files are deleted and an examination of the
            file buffer list confirms that the unwanted files have been
            removed.

            6) Press 'ESC' to return to terminal mode. If you deleted
            files then an information window will appear to inform you
            that the file buffer is being reorganized. This
            reorganization is done so that the file buffer is optimized
            for file transfer. This may take some time if the file buffer
            contains many large files.

            5.8.7 Background File Uploading
            -------------------------------

            There are four file transfer protocols available for
            background uploading: Zmodem, Ymodem-Batch, Xmodem-CRC,
            Xmodem-1K. Before negotiating an upload with the host, you
            must copy the files to be uploaded into the file buffer; see
            Section 5.8.7. If Zmodem or Ymodem-Batch is used, then all
            files marked for upload will be uploaded. If one of the
            Xmodem upload protocols is used, then the files must be
            specified individually; you will be prompted for the file
            names at the appropriate time.





                                                                         76






            5.8.8 ASCII Uploads
            -------------------

            ASCII upload is only for text files. Non-text files should be
            uploaded with one of the other protocols provided with BGFT.

            ASCII uploads are done in the foreground, that is, BGFT.EXE
            must be running. To initiate ASCII upload, press 'PgUp' and
            then select ASCII from the protocol pull down menu list. A
            dialog box pops up to enable you to easily select a file from
            any drive/directory on your computer. Select the desired file
            and initiate the upload by using the <Open> button. BGFT will
            beep when the transfer has been completed. If ASCII upload is
            initiated when using an editor on a remote computer, then the
            uploaded text will display on the screen.

            ASCII upload is useful because it enables preparation of
            messages off-line and then to upload it directly into a
            remote computers message editor. This way you avoid using on-
            line time to compose messages.

            ASCII uploads can be terminated by pressing 'ESC'.

            5.8.9 Acknowledge Communication Errors
            --------------------------------------

            Occasionally, transmission errors will occur that will
            terminate a file transfer or prevent a file transfer from
            being successfully initiated. These errors could, for
            example, be due to a poor quality telephone line connection
            or due to running a poorly behaved applications program while
            you are running background file transfers.

            Errors are identified by the error codes displayed in the
            resident part's status window (BGFT window); these codes are
            listed in Section 4.5. Explanation of errors is also
            available on-line by means of the 'Information' pull down
            menu. The errors appear in the form '!!n' where 'n' is a
            single digit. To acknowledge an error, select the
            'Acknowledge Errors' option from the 'Transfer' pull down
            menu. The resident part's status display will clear and show
            the familiar 'BGFT'. If you re-enter terminal mode after an
            error condition has occurred, then BGFT will automatically
            acknowledge errors.

            In the event of a Zmodem or Ymodem-Batch upload abort, you
            will get a time-out condition which may last for an extended
            period (approximately one minute); you will not be able to
            acknowledge this error during this period, since it is not
            yet a hard error. If you are in a rush, then you will have to
            'Kill' (see Section 5.7.6) the transfer to get the 'hard'
            error condition. The 'Kill Transfer' transfer option, from
            the 'Transfer' pull down menu, automatically acknowledges the
            'hard' error condition that generates it.


                                                                         77







            You will not be able to access the file buffer until any
            errors have been acknowledged.

            5.8.10 Ending Transmission
            --------------------------

            If you are transferring files and you wish to 'Kill' the
            transfer, then select the 'Kill Transfer' option from the
            'Transfer' pull down menu.

            5.9 Utility Functions
            ---------------------

            Utility functions can be accessed via the 'Utility' menu
            using Alt_U, or the mouse. The following functions are
            available:

            5.9.1 Turning the Resident Off
            ------------------------------

            The most common use of this option occurs when a floppy drive
            is being used as the file buffer: in this case, when the
            resident part is active it takes full control of the chosen
            floppy drive, even if you have exited BGFT and are not
            transferring files. This means that if you try to use the
            drive for any other purpose, such as using the DOS format
            command, it will be unavailable and DOS will report an error.
            To enable you to use the drive, you can turn the resident
            part off using the 'Turn Resident OFF' option. Normal
            functioning of BGFT cannot be achieved unless the resident
            part is re-enabled. Re-enabling the resident part can be done
            by selecting the 'Turn Resident OFF ' option again, or simply
            by re-running BGFT. BGFT automatically enables the resident
            part when ever you run it.

            It may be necessary to disable the resident part when you are
            not running BGFT. For example, suppose that you were using
            BGFT for file transfers earlier in the day and now you have a
            need to use the floppy drive for some other purpose. Rather
            than run BGFT, and go to the 'Utility' menu to turn the
            resident off, you can toggle the resident part from the
            command line using the '/R' option. Use:

                BGFT /R

            The resident part may also be activated/suspended using Alt_A
            from terminal mode.

            5.9.2 Initialize the File Buffer
            --------------------------------

            BGFT uses a file buffer when either uploading or downloading
            files. Furthermore, BGFT uses a non-standard format for the


                                                                         78






            files in the file buffer, so that it is necessary to use BGFT
            to initialize the file buffer before use. This needs to be
            done only once.

            In the case you are using a hard drive file buffer, the
            buffer will have been initialized when it was created by
            BGFTFB.EXE, that is, during the install procedure. However,
            you can re-initialize it again any time you like; sometimes
            you may find this a convenient way to clean out ALL files in
            the buffer (when you are sure you do not need them).

            In the case that you are using a floppy diskette for the file
            buffer, BGFT has a number of features designed to reduce the
            likelihood of accidentally initializing a regular DOS
            formatted diskette. If by chance you do manage to initialize
            a DOS formatted diskette containing files that you wish to
            keep, all is not lost. The utility, BGFTFLPY.EXE, allows you
            to recover an inadvertently initialized diskette.

            WARNING: only error free diskettes can be used with BGFT.

            To initialize a diskette, simply place a error free DOS
            formatted diskette into the selected floppy disk drive, then
            select the 'Initialize File Buffer' option. If the diskette
            has not previously been initialized you will be prompted to
            confirm that you wish to continue. If the diskette has
            previously been initialized then initialization will occur
            without further prompting providing that it does not contain
            any files.

            If BGFT is, for some reason, unable to initialize the disk-
            ette, then an information window will appear instructing you
            on how to proceed. This happens if the floppy drive is left
            open, for example.

            5.9.3 Modem Initialization
            --------------------------

            By selecting the 'Modem Initialization' option, the modem
            initialization string is sent to the modem. This option is
            only available if you are not using the direct connection
            option and the line is not connected.

            This option is useful for re-setting the modem in the case
            that you have changed the modem settings (possibly by running
            some other communications software which may have some other
            modem setup requirements). The same modem commands are used
            when you run BGFT for the first time after turning your
            computer on.







                                                                         79






            5.9.4 Status of the BGFT Window
            -------------------------------

            Occasionally you may find that the resident part's status
            window, which normally displays the 'BGFT' code, is not
            desired and that you would like to turn it off. A good
            example is if you are using a screen capture program; in that
            case you would capture the 'BGFT' as well. To toggle the
            resident status display on/off, select the 'Status' option.
            This will not affect transfer operations.

            You can also toggle the status display from terminal mode
            using Alt_W.

            5.9.5 Relocate the BGFT Window
            ------------------------------

            Selecting 'Relocate BGFT' from the 'Setup' pull down menu
            allows relocation of the status BGFT window along the top
            line of the screen. This can be used so that both the BGFT
            window and some other concurrently running software will not
            conflict with the top right hand corner, the default BGFT
            position. The BGFT display can be turned off with Alt_W from
            the terminal mode; see also Section 5.9.4.

            Use the left and right arrow keys, or mouse, to drag the BGFT
            display along the top of the screen. Press 'ENTER' when you
            have reached the location you want, or 'ESC' to keep the old
            position.

            5.9.6 Clear the Terminal Mode Screen
            ------------------------------------

            This option clears the terminal mode screen.

            5.10 The Clipboard
            ------------------

            The purpose of the clipboard is to provide a mechanism by
            which text can be copied from either the terminal mode or the
            scroll back buffer screen; then to edit this text using the
            clipboard editor, and then re-directed it back to the remote
            computer. This is useful for replying to messages or for
            selecting specific text to be used to reply to prompts from
            the remote computer system without having to do a lot of
            typing.

            5.10.1 Copying Text From the Terminal Mode Screen
            -------------------------------------------------

            First of all you must 'select' the text from the terminal
            mode screen that you wish to copy to the clipboard.




                                                                         80






            If using the keyboard use 'Shift_F5' to switch into 'select'
            mode. Now use the arrow keys to move the cursor to the
            beginning of the block to be marked. Then use Shift_Arrow_key
            to start highlighting the desired text. If text is
            highlighted then you can use Shift_Arrow_key to extend the
            selection, any other key will clear the highlighted text.

            If using a mouse then use Shift + dragging of the left mouse
            button to make the selection.

            To copy the selected text to the clipboard editor simply use
            'Ctrl_Ins'. To check that the selected text was copied to the
            clipboard, select the 'Clipboard' option from the 'View'
            menu.

            5.10.2 Copying Text From the Scroll Back Buffer Screen
            ------------------------------------------------------

            First of all you must 'select' the text from the scroll back
            buffer screen that you wish to copy to the clipboard.

            If using the keyboard use 'Shift_F5' to switch into 'select'
            mode. Now use the arrow keys to move the cursor to the
            beginning of the block to be marked. Then use Shift_Arrow_key
            to start highlighting the desired text. If text is
            highlighted then you can use Shift_Arrow_key to extend the
            selection, any other key will clear the highlighted text.

            If using a mouse then use simply drag the left mouse button
            to make the selection.

            To copy the selected text to the clipboard editor use
            'Ctrl_Ins'. To check that the selected text was copied to the
            clipboard, select the 'clipboard' option from the 'View'
            menu.

            5.10.3 The Clipboard Menu
            -------------------------

            The clipboard is accessed by means of the 'Clipboard' option
            from the 'View' pull down menu. On selecting the 'Clipboard'
            option, the clipboard screen appears with the clipboard pull
            down menu at the top. The menu options include:

            File: Selection of this item using Alt_F, or the mouse, pulls
                 down a menu list with the following operations:

            Open A File: Imports a given file into the clipboard editor.

            Save To A File: Saves the contents of the clipboard editor to
                 a DOS file.

            Send Clipboard To A Port: Send the test from the clipboard
                 editor to the port for transmission to the remote


                                                                         81






                 computer. If text is selected then BGFT prompts to see
                 if only the selected text should be sent; otherwise the
                 entire contents of the clipboard are sent.

            Return To Terminal Mode: Returns to terminal mode but retains
                 the clipboard in memory.

            Edit: Selection of this item using Alt_E, or the mouse, pulls
                 down a menu list with the following operations:

            Cut: Cuts the selected text to a paste buffer, that is, the
                 selected text is removed from the screen but remains in
                 memory.

            Paste: Paste the text in the paste buffer to the current
                 cursor location.

            Copy: Copies the selected text to the paste buffer but does
                 not remove the selected text from the screen.

            Clear: Clears the entire contents of the clipboard editor.

            Search: Selection of this item using Alt_S, or the mouse,
                 pulls down a menu list with the following operations:

            Search: Searches the clipboard editor for a given string of
                 text.

            Replaces: Replaces a given string of text with another
                 string.

            Search Again: Allows searching again for another occurrence
                 of a text string that was previously specified with the
                 'Search' menu.

            Help: Selection of this item using Alt_H, or the mouse, pulls
                 down a menu list with the following operations:

            Cursor Movement Commands: Shows how to move around the
                 clipboard editor, that is,

            PgUp                     Page up
            PgDn                     Page down
            Arrow up                 Up one line
            Arrow down               Down one line
            Home                     Beginning of the line
            End                      End of line
            Arrow right              Right one character
            Arrow left               Left one character
            Ctrl_Home                Beginning of clipboard
            Ctrl_End                 End of clipboard
            Ctrl_R                   Page up
            Ctrl_C                   Page down
            Ctrl_E                   Up one line


                                                                         82






            Ctrl_X                   Down one line
            Ctrl_Q R                 Beginning of clipboard
            Ctrl_Q C                 End of clipboard
            Ctrl_Q S                 Beginning of the line
            Ctrl_Q D                 End of line
            Ctrl_I                   Tab foreword
            Ctrl_Q I                 Tab backward
            Ctrl_F                   Foreword one word
            Ctrl_A                   Backward one word
            Ctrl_D                   Right one character
            Ctrl_S                   Left one character
            Ctrl_Right arrow         Foreword one word
            Ctrl_Left arrow          Backward one word

            Block Commands: Shows how to select text, move, copy, delete
                 blocks of text, that is,

            Shift arrow keys         Mark block
            Ctrl_Q Y                 Delete to end of line
            Ctrl_Q B                 Delete to start of line
            Ctrl_Ins                 Copy block
            Shift_Del Shift_Ins      Move block
            Del                      Delete block
            Shift_Del                Cut block to paste buffer

            Drag mouse to highlight block. Cut and an paste operations
                 can also be done using the Edit menu.

            Other Commands: Provides help on other features of the
                 clipboard, that is,

            F2        Save clipboard contents to a file
            F3        Loads contents of a file into the clipboard
            F4        Search for text
            F5        Send contents of the clipboard to the COMM port
            Alt_Z     Help
            ESC       Returns to terminal mode
            Backspace Deletes the character before the cursor position
            Ctrl_H    Deletes the character before the cursor position
            Del       Deletes the character at the cursor position
            Ctrl_G    Deletes the character at the cursor position
            Ctrl_T    Deletes the word the cursor is on
            Ctrl_Y    Deletes the line the cursor is on
            Ctrl_L    Search again
            Ins       Toggle insert mode
            Ctrl_V    Toggle insert mode

            5.11 The Scroll Back Buffer
            ---------------------------

            The purpose of the scroll back buffer is to save the contents
            of the terminal screen in such a way that it is easy to
            'scroll' back to 'look' at the previous contents of the
            terminal mode screen. The scroll back buffer can be viewed by


                                                                         83






            selecting the 'Scroll Back Buffer' option from the 'View'
            pull down menu or via Alt_B from terminal mode. The scroll
            back buffer is displayed in reverse colors so that it is easy
            to distinguish it from the active terminal mode screen.

            Once in the scroll back buffer display, it is possible to
            view the previous contents of the terminal mode screen using
            'PgUp'. Keys such as 'PgDn', 'Home', 'End', up/down arrow
            keys provide the expected responses to move backwards and
            forwards through the buffer.

            The size of the scroll buffer is under user control, as
            described in Section 5.5.4.5. Also, Alt_F enables saving the
            contents of the buffer to a file. This can be useful if a
            message you have just viewed from a BBS has scrolled off the
            screen but you desire to save it for later retrieval.

            As users of BGFT often "run" BGFT many times in a session,
            the user is able to configure BGFT so that it will
            automatically save the scroll back buffer on exiting. This is
            done in such away that when you re-run BGFT it restores the
            scroll buffer as you left it. For example, if the last time
            you were logged on to a BBS and you had been viewing a list
            of files, then the next time you run BGFT, say a couple of
            days later, you can display the scroll buffer and still see
            the list of files. This feature of being able to "see" some
            of your previous session, in the scroll buffer, provides you
            with considerable continuity from one session to another.

            You can also copy selected text from the scroll buffer window
            to the clipboard; this is described in Section 5.10.

            5.12 Screen Capture
            -------------------

            The purpose of screen capture is to continuously "Echo" the
            text that appears on the terminal mode screen to a file. In
            this way, a record of an entire session can be saved.

            Screen capture is initiated by means of the 'Echo To A File'
            option from the 'File' pull down menu, or Alt_G. On
            activation this option, a 'Save File' dialog box pops up to
            allow you to specify the name of the file to put the screen
            contents to, and the drive/directory in which to store the
            file. Screen capture stays active until the option is re-
            selected or you exit BGFT.

            5.13 BGFT Status
            ----------------

            The BGFT status display can be displayed from the 'View' pull
            down menu, using 'BGFT Status', or via Alt_N from anywhere in
            BGFT. On selecting the 'BGFT Status' information option, BGFT



                                                                         84






            will display a window that shows the status of a number of
            key parameters.

            In particular, it will show BGFT in one of the following
            states:

            DORMANT: denotes that the resident part is 'idling' and ready
                 to accept commands from BGFT.

            RECEIVE: denotes that the resident part is downloading into
                 the file buffer.

            TRANSMIT: denotes that the resident is uploading from the
                 file buffer.

            SYNCHRONIZING: is an intermediate state associated with
                 RECEIVE and TRANSMIT.

            ERROR: denotes that the resident part is in an error state
                 associated with a 'hard' error condition. On ac-
                 knowledging this error state the resident part will
                 return to the DORMANT state.

            WAIT: denotes that the resident part is waiting for a re-try
                 condition to clear.

            Also displayed is the progress of the current file being
            transferred.

            5.14 Alt_Key Summary
            --------------------

            An 'Alt_Key' combination, Alt_X, is performed by pressing the
            'Alt' key and then the given key 'X' (or 'x') together
            momentarily.

            BGFT.EXE provides both menus and Alt_Key combination to
            navigate through the user interface program. The Alt_Key
            combinations are used to provide a fast alternative to the
            menu system and can be viewed as 'accelerator' keys. There
            are two kinds of these 'accelerator' keys:

            5.14.1 'Hot' Keys
            -----------------

            In particular, BGFT provides the following 'hot' keys, which
            have the same function wherever they are applied:

                 Alt_J to Jump to a DOS shell.
                 Alt_K to Kill background dialing.
                 Alt_N to give Information on BGFTres status.
                 Alt_X to eXit BGFT to DOS without hanging up the line.




                                                                         85






            5.14.2 'Warm' Keys
            ------------------

            Warm keys are keys that are active only within a given
            context. For example, Alt_Z gives context sensitive help.
            BGFT provides online help to give the following 'warm' key
            information on-line.

            Terminal Mode:

                 Alt_A to suspend/Activate the resident part.
                 Alt_B to show the scroll Back buffer.
                 Alt_C to Clear the screen.
                 Alt_D for Dialing menu options.
                 Alt_E for clipboard Editor.
                 Alt_F for File menu options.
                 Alt_G to echo (Grab) the screen to a disk file.
                 Alt_H to Hang up the telephone line.
                 Alt_I for the Information menu options.
                 Alt_L to List the file buffer directory.
                 Alt_M to show the main Menus.
                 Alt_O for an Overview of BGFT operation.
                 Alt_P for Phone directory.
                 Alt_Q to Quickly auto-move file buffer files to default
                       download DOS directory.
                 Alt_S to Setup menu options.
                 Alt_T for Transfer menu options.
                 Alt_U for Utility menu options.
                 Alt_V for View menu options.
                 Alt_W to toggle the BGFT status Window.
                 Alt_Z to give context sensitive help.

                 PgUp to upload files.
                 PgDn to download files.

                 Shift_F5 highlight terminal screen for clipboard. (Do
                       not have the Num Lock key on).



















                                                                         86







            6.0 Operation of Auxiliary User Interface: BGFTOPT.EXE
            ------------------------------------------------------

            Section 5 described the operation of the main BGFT user
            interface, BGFT.EXE. It is user friendly and full of useful
            features. There are times when a smaller user interface is
            needed; the program, BGFTOPT.EXE, is used in this case. The
            primary use of this would be for installing the capabilities
            of BGFT as an add-on to other telecommunication products.
            BGFT is 'open' in this regard; it allows you to choose your
            preferred interface. BGFT can migrate with you when you
            change from one program to another.

            This Section will describe how to use BGFTOPT.EXE as an add-
            on to other programs such as PROCOMM PLUS, Qmodem, Telemate,
            or Telix. The operational details of the BGFT interface
            utility, BGFTOPT.EXE, are explained at the end of this
            Section.

            6.1 External Protocols
            ----------------------

            Most of the popular telecommunications programs such as
            PROCOMM PLUS, Qmodem, or Telix do not have the background
            capabilities of BGFT. However, BGFT can be easily used with
            them as an external protocol to provide it. The standalone
            user interface, BGFT.EXE, is not used to do this; the
            program, BGFTOPT.EXE, allows the installation of BGFT as an
            external protocol.

            BGFT's supported download or upload protocols are Zmodem,
            Ymodem-Batch, Xmodem-CRC, and Xmodem-1K. Each can be used as
            an external protocol and run in the background to do the file
            transfers.

            The basic idea to using BGFT as an external protocol with
            other telecommunication programs is to use the script
            capabilities of those programs. One of the main requirements
            to do this is that the script be capable of exiting the host
            telecommunications program without hanging up the telephone.
            The communication link must be left open so that BGFT can use
            it.

            Some programs will use BGFT better in a script file than as
            an installed external protocol; it is a matter of what works
            best with the chosen telecommunications package.

            Example scripts are provided with the BGFT package for
            PROCOMM PLUS, Qmodem, and Telix. These are offered as models
            on which to build either new scripts for other programs or as
            a basis for newer program releases of the ones provided.
            These programs sometimes change in ways that require editing
            of the scripts; Dirac Systems will not necessarily update the


                                                                         87






            scripts just because there are newer revisions of other
            products. Users are encouraged to construct or update scripts
            and make them available for others on your local BBS or Dirac
            Systems' Support BBS.

            The examples show how BGFTOPT.EXE can be used and how file
            names are passed for various programs and transmission
            protocols. For example, Xmodem requires a manual input for
            file names while Ymodem-Batch and Zmodem pass them as part of
            the protocol.

            You will find BGFTOPT.EXE to be a versatile program and you
            will be able to think of many other specialized uses for it.
            For example, background dialers can easily be set up.

            Remember that BGFTOPT.EXE was made so that it can work with
            other programs without taking up a lot of room. So be careful
            in its use since it does not contain all the user friendly
            safety nets of BGFT.EXE. It will be useful when you have
            repetitive tasks that are well known.

            6.2 General Considerations
            --------------------------

            The use of BGFT with other programs is easy. The basic steps
            are:

            Preliminary:

            - the file buffer should have been initialized (done on
             creation with hard drive version of BGFTres.COM, manually on
             floppy drive version).
            - the scripts edited to refer to your modem's port and normal
             baud rate.
            - if BGFT was not installed with INSTALL.EXE then the
             BGFTINIT.BAT file must be edited to put in your
             communications port and default baud rate.

            On turning on your computer:

            - choose the BGFTres.COM for the file buffer that you want.
            - have BGFTres.COM loaded before running any programs.
            - run BGFTINIT.BAT once to initialize BGFTres.COM.

            Setting up the transfer:

            - use your telecommunications program and set up the file
             transfer.
            - run the BGFT script to do the file transfer in background.
            - use your computer for other things while BGFT does the
             transfer.





                                                                         88






            After the transfer:

            - use the 'BGFTOPT /f*.*' command (or BGFT.EXE) to move the
             BGFT transferred files to the DOS directory from the file
             buffer.
            - use the telecommunications program to continue with the
             host.

            When running BGFT as an add-on to other telecommunication
            programs there are a few general rules to follow.

            The Installation procedure, Section 4.1, copies the required
            files to various directories for using BGFTOPT.EXE with other
            telecommunication programs. For example, if you are using
            PROCOMM PLUS, then all the ASP script files should be in its
            \PCPLUS directory. BGFTOPT.EXE should also be available for
            use by being in the telecommunication program's directory or
            in a directory of your computer's PATH environment variable.

            BGFT allows you to use your computer's hard C: drive, floppy
            A: drive or floppy B: drive as a file buffer. This should
            have been set up already. The correct BGFT resident program,
            BGFTres.COM, is required for the particular file buffer. Use
            the resident program, BGFTHDZM.COM, when using a hard drive
            file buffer and BGFTFDZM.COM when using a floppy drive file
            buffer.

            Be sure that BGFTres.COM is loaded before any other program
            is run. Typically BGFTres.COM is loaded when you boot your
            computer so that it is in memory, ready for use at any time.
            See Section 4.4 on how to load the resident part of BGFT and
            how it should be put into your AUTOEXEC.BAT file; the
            INSTALL.EXE program should have done this for you.

            If you ran the installation program, it would have updated
            the provided batch file, BGFTINIT.BAT, with the communication
            port and baud rate normally used as chosen by you. If you did
            not use the BGFT installation program then the  file,
            BGFTINIT.BAT, must be edited, prior to use, with an ASCII
            editor to specify your modem's normal communication port
            number and baud rate. The file has the following arbitrary
            defaults: the communication port is 1 and the baud rate is
            1200. The batch file is then used only once during a computer
            session to initialize BGFT. This makes sure that BGFT is set
            up properly. It MUST be done in spite of the fact that most
            scripts will perform similar functions. Run the batch file by
            entering,

                BGFTINIT.BAT

            BGFTINIT.BAT uses the command:

                BGFTOPT /r1 /b1200



                                                                         89






            which tells BGFTres.COM to use communications port 1 at a
            baud rate of 1200. BGFTOPT.EXE uses a number of such command
            line switches (BGFT OPTions); see the details in Section 6.7.

            The USER DEFINED data for communication port used and baud
            rate must be edited in the script files with an ASCII editor.
            This will make the script agree with the baud rate you have
            told the host computer to download at. The baud rate may be
            different than what you used in BGFTINIT.BAT. However, the
            communication port must be the same as initialized with
            BGFTINIT.BAT.

            The scripts correspond to two types of transfer: download and
            upload. For each, there is a corresponding transmission
            protocol: Xmodem-CRC, Xmodem-1K, Ymodem-Batch, and Zmodem.
            BGFTOPT.EXE uses more command line switches to communicate
            the choice of protocol to the resident program. Each script
            shows how it is set up in the corresponding script language.

            Downloaded files are put into the file buffer by the resident
            program during the transfer.

            If you are uploading files then you must manually move files
            from the DOS directory to the file buffer. You may use
            BGFT.EXE or BGFTOPT.EXE. The resident knows where the file
            buffer is so you need not specify it. For example, to copy
            the file, TEST.TXT, in the present DOS directory to the file
            buffer for uploading you would enter

                BGFTOPT /mTEST.TXT

            All the preliminaries and edits should have been
            accomplished. You can now run your other telecommunication
            program for the first time. Use it as you normally would. Set
            up your download or upload with the host.

            Each script is run in a particular manner depending on the
            telecommunication program. There are descriptions below for
            PROCOMM PLUS, Qmodem and Telix.

            WHEN TRANSFERRING FILES WITH BGFT, DO NOT RUN THE
            TELECOMMUNICATIONS PROGRAM OR YOU WILL GET THE TRANSMISSION
            ON THE SCREEN INSTEAD OF THE FILE BUFFER. THIS CAN RUIN A
            TRANSMISSION BY CAUSING A TIME OUT. Most programs are not
            aware of BGFT; the BGFT user interface program, BGFT.EXE, is,
            of course.

            After the transfers are over you can use the
            telecommunication program again in terminal mode to
            communicate with the host. You may use BGFT.EXE instead, if
            you wish. There is also a basic terminal emulator in
            BGFTOPT.EXE itself.




                                                                         90






            If you downloaded files, use BGFT.EXE to move your files to
            the desired DOS directory where you want to use them. See
            Section 5.8.3.

            You may use BGFTDIR.COM to get a file listing of the BGFT
            file buffer. Each file has a designator:

            - 'd' means the file was downloaded with BGFT.
            - 'u' means the file is in the file buffer ready for upload
            with BGFT.
            - 'a' means the file was interrupted in a Zmodem transfer.
            Upon recovery it will be marked as complete (either 'd' or
            'u').

            6.3 Using BGFT as an External Protocol for Telix
            ------------------------------------------------

            Be sure that the BGFT resident and file buffer are set up
            correctly as described in Section 6.2. You must have run
            BGFTINIT.BAT.

            Background file transfer using BGFT with Telix is
            accomplished by means of the provided Telix SALT scripts.
            These scripts provide for the selection of a BGFT file
            transfer protocol and initiation of BGFTOPT.EXE to start the
            background file transfer. Having done this, the scripts will
            then make Telix automatically exit to DOS without hanging up
            the telephone line.

            There are two ways to install BGFT protocols in the Telix
            external protocol list. One is manual, which is described
            next, and a more automatic way which is described later on.

            The following outlines how to manually install a Telix SALT
            script for using BGFT as an external protocol in Telix. The
            particular example is for Zmodem download.

            Please refer to the Telix SALT script in the file,
            BGFTDZTL.SLT.

            Change the port assignment and baud rate in the script to
            your set up where a USER DEFINED quantity is indicated. Use
            an ASCII editor.

            Compile the BGFT Zmodem download script file, BGFTDZTL.SLT,
            by using the Telix script compiler, CS.EXE; enter,

                CS BGFTDZTL

            This will produce the compiled script file, BGFTDZTL.SLC, for
            use in the Telix program.

            From terminal mode in Telix enter 'Alt_O' for 'Configure
            Telix'.


                                                                         91







            - Choose 'Terminal Options'.

            - Choose 'N' for Zmodem auto-downloads.

            - In response to "Allow Zmodem auto-downloads?" choose "No"
            by moving the right/left arrow keys and then 'ENTER'. This
            will stop Telix from autodownloading the file before BGFT
            does.

            - Choose 'Protocol Options'.

            - 'Change which setting?': Choose one of the four external
            protocol options provided for in Telix: 'A', 'B', 'C', or
            'D'.

            - 'Key': When in the download operation, pressing this key
            will choose the protocol. The key should not be used
            elsewhere; for example, 'Z' is already used for the Telix
            internal 'Z'modem. Choose 'D', for example. The 'D' will be
            highlighted during the Telix download operation in the
            protocol name list: the 'D' in 'BGFTZMDM' (see the next
            paragraph).

            - 'Protocol name': This is what will show up in the list of
            protocols when you choose the download operation. Call it,
            'BGFTZMDM'.

            - 'Upload file name': For this example, leave it blank.
            Normally it will be the corresponding upload script for the
            chosen BGFT Zmodem protocol (see the script, BGFTUZTL.SLT).

            - 'Download file name': Enter, 'BGFTDZTL' which is the BGFT
            download Zmodem protocol. This will be the compiled script
            made above.

            - 'BAT or Script': Choose 'Script' since BGFTDZTL.SLT
            operates as a script.

            - 'DL name': For Zmodem (or Ymodem-Batch), the protocol
            itself will pass the name of the file to the script so choose
            'N'. (If you install Xmodem you will choose 'Y' for Yes since
            you want Telix to pass the name of the file to the script.)

            - ESC out of the screen and save the set up to disk by
            hitting 'W'. This get you back into Telix terminal mode.

            In Telix, tell the host to send the files desired by Zmodem
            download as you normally would. Then hit 'PgDn' in Telix to
            set up to receive the files. Choose the BGFTZMDM protocol
            using arrows plus an 'ENTER' or by the Key ('D') defined
            above.




                                                                         92






            The script will begin to give some messages, start the
            background transfer, and then exit the Telix program. You
            will be at the DOS prompt. You should see the BGFT window
            indicate normal transmission counts.

            Now you can do your work in foreground as the file is
            downloaded in background.

            After completion of the file transfer, you can use BGFT.EXE
            to move your files to some DOS directory. The files are ready
            to use.

            The installation of BGFT external protocols is only done
            once. They will be available to you each time you run Telix.

            This completes the manual installation. The more automatic
            procedure is described next.

            A number of utilities are included to automatically perform
            some of the functions needed to process the scripts or change
            the Telix configuration file, TELIX.CNF. The following files
            will be of use here:

            BGFTSLC.BAT    Batch file to compile scripts.
            BGFTTELX.DAT   Data file to append to TELIX.CNF.
            BGFTADD.BAT    Batch file to update TELIX.CNF; uses
                           BGFTTELX.DAT.

            The Telix SALT (script) compiler, CS.EXE, must exist in your
            Telix directory. In your Telix directory, enter

                BGFTSLC.BAT

            to compile all the SALT scripts for the BGFT external
            protocols for Telix.

            To automatically add the protocols to Telix, you can enter

                BGFTADD.BAT

            This appends the protocol information to TELIX.CNF so that
            the BGFT protocol will show up in the protocol list. It will
            also turn off the Telix auto-download feature so that it will
            not interfere with BGFT's Zmodem. Writing the Telix
            configuration file to disk (Alt_O command in Telix and
            'W'rite set up to disk) will reorganize TELIX.CNF properly.

            You will install the external protocols as 'A', 'B', 'C', and
            'D' under the names:

            BGFTXMDM
            - install BGFTDXTL as Xmodem-CRC download.
            - install BGFTUXTL as Xmodem-CRC upload.



                                                                         93






            BGFTIMDM
            - install BGFTDXTL as Xmodem-1K download.
            - install BGFTUITL as Xmodem-1K upload.

            BGFTYMDM
            - install BGFTDYTL as Ymodem-Batch download.
            - install BGFTUYTL as Ymodem-Batch upload.

            BGFTZMDM
            - install BGFTDZTL as Zmodem download.
            - install BGFTUZTL as Zmodem upload.

            If this is not desirable, for example, if you already use
            other external protocols as 'A', 'B', 'C', or 'D', then you
            must do the installation manually. If you do this automatic
            method then any former protocols are preempted. When you do
            Alt_O and choose 'Protocols' in Telix you should see the
            following BGFT external protocols installed:

                Key  Protocol   Upload  Download  BAT or   DL
                       Name    Filename Filename  Script  Name

            A..  B  BGFTXMDM   bgftuxtl  bgftdxtl  Script  Y
            B..  I  BGFTIMDM   bgftuitl  bgftdxtl  Script  Y
            C..  F  BGFTYMDM   bgftuytl  bgftdytl  Script  N
            D..  D  BGFTZMDM   bgftuztl  bgftdztl  Script  N

            When the file transfer has been completed, you may enter
            Telix again without disturbing the connection by entering:

                TELIX O

            (the 'O' tells Telix not to send the modem initialization
            string).

            Some modems respond to a 'break' character by switching to
            modem command mode. This will prevent BGFT from carrying out
            background file transfers. Telix appears to generate a
            'break' when it exits; therefore, the modem should be set to
            ignore 'break' (this is usually possible, consult your modem
            manual).

            Uploads are done with files that are in the BGFT file buffer
            and not with those in the Telix default upload directory.
            Nevertheless, Telix will search its upload directory and will
            report that it found "No Matching File(s)" if the named file
            is not found. This is a recognized deficiency with Telix.
            Telix has to be tricked; the same files for BGFT upload in
            the file buffer must be in the Telix upload directory, to
            keep both BGFT and Telix happy.

            See Section 6.7 for the complete description of the operation
            of BGFTOPT.EXE so that you can customize your own scripts.



                                                                         94






            The following SALT scripts for Telix version 3.x have been
            included in the BGFT package for your use:

            BGFTDXTL.SLT Telix script for Xmodem-CRC/1K download.
            BGFTDYTL.SLT Telix script for Ymodem-Batch download.
            BGFTDZTL.SLT Telix script for Zmodem download.

            BGFTUXTL.SLT Telix script for Xmodem-CRC upload.
            BGFTUITL.SLT Telix script for Xmodem-1K upload.
            BGFTUYTL.SLT Telix script for Ymodem-Batch upload.
            BGFTUZTL.SLT Telix script for Zmodem upload.

            6.4 Using BGFT as an External Protocol for PROCOMM PLUS
            -------------------------------------------------------

            Be sure that the BGFT resident and file buffer are set up
            correctly as described in Section 6.2. You must have run
            BGFTINIT.BAT.

            PROCOMM PLUS also has a good script language to allow BGFT's
            capabilities to be used.

            The following description outlines how to use BGFT's Zmodem
            download with a PROCOMM PLUS version 2 Aspect language
            script. Using a script to do the file transfer with
            BGFTOPT.EXE seems to be more convenient than using BGFT as an
            external protocol in PROCOMM PLUS.

            Please refer to the Aspect language script in the file,
            BGFTDZPC.ASP.

            The PROCOMM PLUS script, BGFTDZPC.ASP, should be in the
            \PCPLUS directory. The USER DEFINED data for communication
            port used and baud rate must be edited in the file with an
            ASCII editor. The script must be compiled if PROCOMM PLUS
            version 2 is used; an ASX file is produced.

            Get the remote system ready to download the chosen files to
            you with Zmodem.

            From your terminal mode in PROCOMM PLUS hit 'Alt_F5' to begin
            to set up the ASX file for running the file transfer. Hit
            RETURN to get a list of compiled ASX files. Choose
            BGFTDZPC.ASX with the up or down arrows keys and then enter
            your choice to do a Zmodem download. BGFTDZPC.ASX will
            initiate the download using the baud rate and communication
            port defined in the script file. The BYE command in the
            script will exit PROCOMM PLUS without hanging up; you will
            then be at the DOS prompt. The files(s) will be transferred
            in the background by the BGFT resident program; you can use
            your computer for other purposes while this takes place.





                                                                         95






            After the transfers are over you can use PROCOMM PLUS again
            in terminal mode to communicate with the host. You may use
            BGFT.EXE instead, if you wish.

            See Section 6.7 for the complete description of the operation
            of BGFTOPT.EXE so that you can customize your own scripts.The
            following Aspect scripts for PROCOMM PLUS version 2 have been
            included in the BGFT package for your use:

            BGFTDXPC.ASP PROCOMM PLUS script for Xmodem-CRC/1K download.
            BGFTDYPC.ASP PROCOMM PLUS script for Ymodem-Batch download.
            BGFTDZPC.ASP PROCOMM PLUS script for Zmodem download.


            BGFTUXPC.ASP PROCOMM PLUS script for Xmodem-CRC upload.
            BGFTUIPC.ASP PROCOMM PLUS script for Xmodem-1K upload.
            BGFTUYPC.ASP PROCOMM PLUS script for Ymodem-Batch upload.
            BGFTUZPC.ASP PROCOMM PLUS script for Zmodem upload.

            6.5 Using BGFT as an External Protocol for Qmodem
            -------------------------------------------------

            Be sure that the BGFT resident and file buffer are set up
            correctly as described in Section 6.2. You must have run
            BGFTINIT.BAT.

            The following description outlines how to use BGFT's Zmodem
            download with a Qmodem SCR language script. Using a script to
            do the file transfer with BGFTOPT.EXE seems to be more
            convenient than using BGFT as an external protocol in Qmodem.

            Qmodem is a very simple program to interface to BGFT's
            capabilities. Qmodem has similar usage as PROCOMM PLUS.

            The version of Qmodem considered for script operation is
            4.52. There are newer versions of Qmodem; you can adapt the
            scripts as necessary.

            The following outlines how to install a Zmodem download file
            transfer script for using BGFT in Qmodem.

            Please refer to the script in the file, BGFTDZQM.SCR.

            Change the port assignment and baud rate in the scripts to
            your set up where a USER DEFINED quantity is indicated. Use
            an ASCII editor.

            Get the remote system ready to download the chosen files with
            Zmodem.

            From terminal mode in QMODEM hit 'Alt_F' to begin to set up
            the SCR file for running. Type in 'BGFTDZQM' for the script
            name to be run. Enter nothing for parameters to the script.
            BGFTDZQM.SCR will initiate the download using the baud rate


                                                                         96






            and communication port defined in the script file. The
            'SYSTEM X' command will exit QMODEM without hanging up; you
            will be at the DOS prompt. The files(s) will be transferred
            to the BGFT file buffer in the background so you can use your
            computer for other purposes while this takes place.

            After the transfers are over you can use Qmodem again in
            terminal mode to communicate with the host. You may use
            BGFT.EXE, if you wish.

            See Section 6.7 for the complete description of the operation
            of BGFTOPT.EXE so that you can customize your own scripts.
            The following SCR scripts for Qmodem version 4.x have been
            included in the BGFT package for your use:

            BGFTDXQM.SCR Qmodem script for Xmodem-CRC/1K download.
            BGFTDYQM.SCR Qmodem script for Ymodem-Batch download.
            BGFTDZQM.SCR Qmodem script for Zmodem download.

            BGFTUXQM.SCR Qmodem script for Xmodem-CRC upload.
            BGFTUIQM.SCR Qmodem script for Xmodem-1K upload.
            BGFTUYQM.SCR Qmodem script for Ymodem-Batch upload.
            BGFTUZQM.SCR Qmodem script for Zmodem upload.

            6.6 Using BGFT as an External Protocol for Telemate
            ---------------------------------------------------

            Be sure that the BGFT resident and file buffer are set up
            correctly as described in Section 6.2. You must have run
            BGFTINIT.BAT.

            Although it is easy to write a Telemate Version 4 script to
            set up BGFT for background transfers, it will not work
            properly. BGFT will get the correct instructions but it
            appears that Telemate will regain control of the communication
            port from BGFT on exit of the script.

            Here is a work around solution which may also be used in other
            similar circumstances. Let's assume you want to do a Zmodem
            download and that your modem is on communication port 1 and
            will do the transfer at 2400 baud. Be sure to turn off the
            internal Telemate Zmodem auto-download feature so that BGFT
            can do its own. Set up the download with the BBS and then exit
            Telemate with Alt_X. You will be at the DOS prompt. You can
            enter the BGFT commands directly as:

                 BGFTOPT /5 /A /R1 /B2400 /~5 /S

            Since BGFTOPT.EXE is not in quiet mode, it will give the
            following replies:

                Turning resident part on.
                Acknowledging error.
                Reconnecting communication port 1.


                                                                         97






                New baud rate: 2400.
                Zmodem download protocol.
                Starting file transfer.

            You could put the BGFTOPT command in a batch file and run it
            each time you needed it. For the other BGFT supported
            protocols you could create other batch files.

            After the transfers are over you can use Telemate again in
            terminal mode to communicate with the host. Since you are
            already online you should enter:

                TM /O

            so that the modem initialization string is not sent to the
            host.

            See Section 6.7 for the complete description of the operation
            of BGFTOPT.EXE so that you can customize your own batch files.

            6.7 Command Mode Options Using BGFTOPT.EXE
            ------------------------------------------

            BGFTOPT.EXE can be used in place of BGFT.EXE where a simple
            user interface is needed. For example, BGFTOPT.EXE would be
            used for installing BGFT external file transfer protocols in
            another communications package. BGFTOPT.EXE is used to send
            certain pertinent messages to the resident about the file
            transfer such as the chosen communication port, baud rate,
            and file name.

            The supplied files with file extension ASP, SCR and SLT give
            examples on how BGFTOPT is used to support background file
            transfers for external protocols in PROCOMM PLUS, Qmodem, and
            Telix.

            BGFTOPT.EXE is able to send and receive a number of messages
            from the resident part of BGFT. This is accomplished by using
            the command line switches that are provided. For example,
            suppose you are in the DOS shell and the 'BGFT' window
            indicated an error condition such as '!!1' due to the host
            canceling the transfer. This 'hard' error condition can be
            acknowledged by entering:

                BGFTOPT /A

            The '/A' is referred to as a switch (or BGFT OPTion) and is a
            DOS command line argument (input) to BGFTOPT.EXE. The case of
            the switch is not significant, so that '/a' would produce the
            same result. The space is not required between BGFTOPT and
            the switch '/' symbol. However, there should not be a space
            between the '/' and the 'a'; for example, '/ a', would be
            incorrect.



                                                                         98






            Some of the switches can be chained, such as:

                BGFTOPT /a1

            which would acknowledge any error and then hang up the phone.
            The chain is parsed from left to right. A chain starts with
            the '/' symbol.

            If quiet mode, '/q', is not switched on, then most switches
            will give a little message. For example, the '/a' switch will
            announce "Acknowledging error" plus an internal BGFTOPT
            reporting number which can be used to test for an error exit
            (in general, BGFTOPT will return with a '0' if no error
            occurs). The switch chain, '/qa', will not produce a message,
            for example.

            The chains can be broken with no effect such as in the case:

                BGFTOPT /a /a

            This is the same as if there was one switch chain, '/aa'. If
            the chain is broken then there must be at least one space
            separating each chain.

            Continuous chains can be used for the following set of
            symbols:

            ? a h i k q s t 1 4 5 6 9

            This is shown in the usage prototype which appears when the
            help screen is produced by using the '/?' switch. The first
            part of it looks like:

            BGFTOPT[/?ahikqst14569 ]

            The square brackets indicate the any one of the symbols can
            be chained together in any logical fashion; they may be
            repeated.

            Sometimes broken chains must be used so that the command line
            parser can determine the correct instructions for BGFTOPT.
            Notice that the prototype above ends with a space just before
            the ']'; this indicates that the other command line switches
            should be switches that are separated by at least one space.
            The prototype for these switches could be shown as:

            [ /~<#>][ /b<#>][ /d<filename>][ /f<[path]files>]
            [ /m<[path]files>][ /r<#>][ /u<filename>]
            [ /7<parity>][ /8<parity>][ /0<P|T><#>]

            For example, one could manage the switches like:

                BGFTOPT /5a /r2 /b1200 /~1 /dtest.txt /s



                                                                         99






            which would activate the resident part of BGFT, acknowledge
            any errors, reconnect the second serial communication port,
            set the port's baud rate to 1200 baud, choose the Xmodem
            download protocol, tell BGFT to expect a file called
            'TEST.TXT', and send a signal to the remote host to start
            sending the file.

            The following notes describe all the available switches.

            6.7.1 /~<Protocol>

            1 for XMODEM-CRC or XMODEM-1K download or XMODEM-CRC upload
            2 for Ymodem-Batch download
            3 for Ymodem-Batch upload
            4 for XMODEM-1K upload
            5 for ZMODEM download
            6 for ZMODEM upload

            One of the six values (1, 2, 3, 4, 5, or 6) is to be entered
            for <Protocol> depending on the desired transmission
            protocol. The number should be right next to the '~'. The
            resident part of BGFT will automatically distinguish whether
            a downloaded packet for Xmodem is of the 128 byte (CRC) or
            1024 (1K) byte size. Also, for Xmodem, selecting upload or
            download is done when entering the file name. When using
            Ymodem or Zmodem for uploading or downloading, there is no
            need to give a command line entry for the file names since
            the protocol provides them.

            Summary:

            Xmodem-CRC download needs the switch, '/~1'.
            Xmodem-1K download needs the switch, '/~1'.
            Ymodem-Batch download needs the switch, '/~2'.
            Zmodem download needs the switch, '/~5'.

            Xmodem-CRC upload needs the switch, '/~1'.
            Ymodem-Batch upload needs the switch, '/~3'.
            Xmodem-1K upload needs the switch, '/~4'.
            Zmodem upload needs the switch, '/~6'.

            6.7.2 /b<Baud> 300,1200,2400,4800,9600,19200,38400,57600

            One of the eight indicated values is to be used for <Baud
            rate>. The number should be right next to the 'b'. The
            communication port must have its baud rate set appropriately.

            This must be set, along with the communication port, once
            when BGFTres.COM is loaded.

            6.7.3 /? Display this help screen

            This displays a help screen which shows the Copyright
            information, the prototypes for BGFTOPT, and a short reminder


                                                                        100






            of what each switch does. The text of the reminder is stated
            in a similar fashion as to what is seen in this list of
            switches. The screen is displayed when an unknown or illegal
            command is entered.

            The help screen is also displayed when only 'BGFTOPT' is
            entered, that is, without any switches. BGFTOPT will return
            '0' if both the port and the baud rate are set, and '1'
            otherwise.

            6.7.4 /a Acknowledge error

            Hard (!!n type) transmission errors must be acknowledged.

            6.7.5 /d<filename> Download file entry

            The name of the file being downloaded should be inserted
            right next to the 'd'. The Xmodem download protocols require
            that a file name be supplied; Ymodem-Batch and Zmodem do not.

            6.7.6 /h Halt background file transfer

            A file transfer, either upload or download, which is in
            progress may be terminated with this switch. This will
            produce a hard error condition '!!3' which must be
            acknowledged. The remote system, that was communicating, will
            time out due to not hearing from the locally halted system.

            6.7.7 /i Initialize active file buffer

            The file buffer is initialized for use by BGFT. The correct
            file buffer will be accessed since it is known by the
            resident program, which should be loaded and active. Any DOS
            floppies used as the file buffer must have been formatted by
            DOS and checked by CHKDSK for error free condition. The hard
            disk file buffer is initialized automatically upon
            installation of it.

            Using this function on BGFT initialized file buffers will
            delete BGFT directory information. This effectively 'erases'
            the buffer.

            6.7.8 /k Kill background dialer

            Background dialing is terminated with this switch.

            6.7.9 /f<[path]files> Files to DOS from buffer

            Move BGFT downloaded files from the file buffer to DOS
            directories with this command. The resident part of BGFT must
            be loaded and active to move the files. The file name,
            <files>, of the file in the BGFT file buffer, including
            optional DOS destination path, [path], if needed, should be
            right next to the 'f'.


                                                                        101







            Wild card operation is allowed. For example, to move all
            downloaded files in the active file buffer to the present DOS
            directory use:

                BGFTOPT /f*.*

            Drive and directory information can be used to direct the
            files elsewhere. For example, to move all BGFT downloaded
            files in the file buffer with file extension 'ZIP' to drive
            D: in directory 'HOLD' use:

                BGFTOPT /fD:\HOLD\*.ZIP

            Recall that if BGFTDIR.COM is used to list the active file
            buffer the BGFT downloaded files will have the 'd' designator
            to the right. Partial Zmodem downloads/uploads will have the
            'a' designator. This command will move partial Zmodem
            download files to DOS; they will likely be unusable.

            Once files are moved from the file buffer their file slots
            are freed up by BGFT. Therefore, it is not possible to do the
            same operation twice; use the DOS COPY command if you want
            multiple copies of the downloaded files in other directories.

            As with many BGFTOPT.EXE commands, BGFT.EXE can be used in a
            more user friendly manner, including error reporting, to move
            the files. You can use its file tagging file ability and so
            on if you wish. BGFTOPT.EXE will not do or report any
            incorrect operations for this command. For example, if you
            directed the files to a non existent DOS directory the
            operation would not delete the files in the file buffer.

            6.7.10 /m<[path]files> Move file to buffer

            Move DOS files to the file buffer for uploading with this
            command. There is  a maximum of 31 file slots available in
            the file buffer. The resident part of BGFT must be loaded and
            active to move the files; it knows where the active file
            buffer is. The DOS file name, <files>, including optional DOS
            path, [path], should be right next to the 'm'. For example,
            to move the file TEST.TXT from the present directory, the
            active directory on another drive F:, or the path D:\BGFT300
            to the file buffer use, respectively:

                BGFTOPT /mTEST.TXT

                BGFTOPT /mF:TEST.TXT

                BGFTOPT /mD:\BGFT300\TEST.TXT

            Wild card operation is allowed. For example, to move all
            files in the present DOS directory to the file buffer use:



                                                                        102






                BGFTOPT /m*.*

            This move command is non destructive to DOS files, that is,
            they will actually be copied to the file buffer.

            If BGFTDIR.COM is used to list the active file buffer the
            files for upload will have the 'u' designator to the right.

            As with many BGFTOPT.EXE commands, BGFT.EXE can be used in a
            more user friendly manner, including error reporting, to move
            the files. You can use its file tagging file ability and so
            on if you wish. BGFTOPT.EXE will not do or report any
            incorrect operations for this command.

            6.7.11 /q Quiet message mode

            Subsequent command line switches to the right of the first
            'q' will have their switch messages to the standard output
            disabled. Another 'q' will not turn the messages back on.
            Subsequent BGFTOPT command line entries will not be quiet.

            If '/q' is used as the only command line argument there will
            be no help listing.

            6.7.12 /r<Reconnect COMM port> 1,2,3,4

            This switch indicates that one of the four indicated values
            is to be substituted for <Reconnect COMM port>. The number
            should be right next to the 'r'. The number corresponds to
            the number of the communication port which is to be
            reconnected. The communications port must be set. It should
            not be changed during a computer session without turning your
            computer off and then on.

            This must be set, along with the baud rate, once when
            BGFTres.COM is loaded.

            6.7.13 /s Start background file transfer

            Uploads and downloads must be initiated with this switch
            after setting up the transmission.

            6.7.14 /t Terminal emulator

            A basic terminal emulator is invoked which enables sending
            keyboard instructions to the remote host. This can be used
            for logging in to a BBS, for example. The terminal is exited
            by typing 'Ctrl_E' or 'Alt_X'.

            6.7.15 /u<filename> Upload file entry

            Xmodem-CRC and Xmodem-1K require that a file name be provided
            when uploading a file from the file buffer. It should be
            placed right next to the 'u'.


                                                                        103







            Ymodem-Batch and Zmodem do not require a file name; all files
            marked as upload are sent.

            6.7.16 /1 Hang up phone

            This will hang up the telephone line.

            6.7.17 /4 Wait for end of transfer

            This switch will not allow a normal exit of BGFTOPT after
            being parsed. BGFTOPT will wait until the transmission is
            over before continuing.

            6.7.18 /5 Turn resident program on

            The resident part is turned on with this switch; the file
            buffer is taken over and is made inaccessible from DOS. The
            switch is 'one way'; turning the resident off requires the
            '/6' switch.

            6.7.19 /6 Turn resident program off

            The resident part of BGFT will be turned off. This would
            allow access to the floppy drive file buffer. This should
            only be done when the resident is not otherwise busy with any
            file buffer. The switch is 'one way'; turning the resident on
            requires the '/5' switch.

            6.7.20 /7<parity> 7 bit & parity N,E,O,S,M

            One of the five indicated choices is to be substituted for
            <Parity>. The letter should be right next to the '7'. The
            letter corresponds to the required parity: N for None, E for
            Even, O for Odd, S for Space, or M for Mark. Only one stop
            bit is supported. The resident part of BGFT will
            automatically revert to the correct settings for file
            transfer (normally 8 data bits, no parity, and one stop bit).

            6.7.21 /8<parity> 8 bit & parity N,E,O,S,M

            One of the five indicated choices is to be substituted for
            <Parity>. The letter should be right next to the '8'. The
            letter corresponds to the required parity: N for None, E for
            Even, O for Odd, S for Space, or M for Mark. Only one stop
            bit is supported. The resident part of BGFT will
            automatically revert to the correct settings for file
            transfer (normally 8 data bits, no parity, and one stop bit).

            6.7.22 /9 Start background dialer

            The resident's internal dialing string is set up with the
            '/0' switch and the actual dialing is commenced with this
            command.


                                                                        104







            6.7.23 /0<P|T><#> Pulse or Tone & number

            This command needs two inputs. The first is for the type of
            dialing that your phone line supports. The <Pulse|Tone> means
            that you have a choice of Pulse or Tone dialing; use 'P' or
            'T' respectively.

            The desired phone number must be entered for <#>. The number
            should be entered in a form suitable to the modem. Generally,
            this is a combination of numbers and certain specific
            punctuation characters (for example, the ',' is a pause and
            '-' is a separator). (If you plan to use this in a batch file
            you will have to use '.' instead of ',' since the batch file
            processor considers ',' to be a separator. BGFTOPT will
            convert and understand it.)

            For example, to start tone dial to Dirac Systems' local BBS,
            you would enter:

                BGFTOPT /0T283-7157 /9

            6.8 Conclusion
            --------------

            This Section explained the use of an auxiliary user interface
            for using the capabilities of BGFT in a wider context.
            BGFTOPT.EXE is 'auxiliary' since it is a functional subset of
            the main user interface, BGFT.EXE.

            Finally, congratulations to you for having gotten this far in
            the manual. For all the ease of use that has been built into
            BGFT there may be times when you ought to read parts of the
            documentation. Rick, Rafael, and Tim at Dirac Systems hope
            that it has been useful to you.

            Last, but not least, we wish to thank all our beta testers and
            customers for your input. We look forward to hearing from you
            and for your continuing support. For new users, we trust you
            will find BGFT to be one of the most useful software purchases
            you ever make.















                                                                        105








            Index
            -----

            A                                 BGFTDZQM.SCR, 11,97
            acknowledge error, 77             BGFTDZTL.SLT, 12,95
            Alt_Key, 85                       BGFTFB.EXE, 7,10,16,34,79
            ASCII, 64,75,77                   BGFTFDZM.COM, 7,10,16,35,38
            ASPECT, 13                        BGFTFLPY.EXE, 10,17,79
            AUTOEXEC.BAT, 20,25,30            BGFTHDFB.DAT, 32,34
            B                                 BGFTHDZM.COM, 7,10,16,35
            background                        BGFTINIT.BAT, 11,17,31,88,91
              dialing, 68                     BGFTOPT.EXE, 10,17,87,98
              file downloading, 73            BGFTORDR.FRM, 9,11,15
              file transfer, 72               BGFTREAD.ME, 11,15,27
              file uploading, 76              BGFTres.COM, 16
              sound, 62                       BGFTSLC.BAT, 11,93
              status, 80                      BGFTSPY.EXE, 10,19,45
            baud rate, 60,100                 BGFTSPY.ICO, 12,45
            BGFT, 13,48                       BGFTTELX.DAT, 11,93
              configuring, 57                 BGFTUIPC.ASP, 11,96
              dial menu, 52                   BGFTUIQM.SCR, 11,97
              exiting, 49                     BGFTUITL.SLT, 12,95
              file menu, 51                   BGFTUXPC.ASP, 11,96
              help, 48,55,57,82,86            BGFTUXQM.SCR, 11,97
              information menu, 54            BGFTUXTL.SLT, 12,95
              registration, 9                 BGFTUYPC.ASP, 11,96
              setup menu, 53                  BGFTUYQM.SCR, 11,97
              starting, 48                    BGFTUYTL.SLT, 12,95
              status window, 37               BGFTUZPC.ASP, 11,96
              transfer menu, 53               BGFTUZQM.SCR, 11,97
              trying it out, 19               BGFTUZTL.SLT, 12,95
              utility menu, 53                BGFTXDLG.EXE, 11,18
              view menu, 52                   C
            BGFT.DLG, 11,16                   Canada Remote Systems, 8,13
            BGFT.DOC, 11,15                   client-server, 47
            BGFT.EXE, 7,10,16,48,89           clipboard, 80
            BGFT300.CNF, 30,48                  editing, 81
            BGFT300.HLP, 11,16                  scroll back buffer, 81
            BGFT300.SCR, 11,16                  terminal, 80
            BGFT300A.EXE, 15,26               color, 66
            BGFT300B.EXE, 15,26               COMMAND.COM, 41
            BGFT386.BAT, 12,19                communication port, 60,103
            BGFT386.PIF, 12,19                CompuServe, 13
            BGFTADD.BAT, 11,93                COMSPEC, 41
            BGFTDIR.COM, 11,17                CONFIG.SYS, 41
            BGFTDXPC.ASP, 11,96               D
            BGFTDXQM.SCR, 11,97               DESQview, 13,43
            BGFTDXTL.SLT, 12,95               dialing directory, 63,68
            BGFTDYPC.ASP, 11,96               Dirac Systems, 8
            BGFTDYQM.SCR, 11,97               DORMANT, 85
            BGFTDYTL.SLT, 12,95               DOS 5, 41
            BGFTDZPC.ASP, 11,96               DR DOS, 42


                                                                        106






            E                                 Q
            ERROR, 85                         Qmodem, 11,14,30,96
            error messages, 37                R
            external protocol, 87             RECEIVE, 85
            F                                 Rose Media, 8
            file buffer, 5,73                 S
              floppy drive, 38                SALT, 14
              hard drive, 34                  screen capture, 84
              initialization, 34,38,78        scroll back buffer, 62,81
            G                                 SET, 40
            graphics, 46                      Shareware, 9,10,26
            GST, 13                           Smartmodem, 14
            I                                 STACKER, 29,42
            IBM, 13                           SYNCHRONIZING, 85
            initialization                    T
              floppy buffer, 38               tab width, 62
              hard drive buffer, 34           Telemate, 14,97
              resident, 17                    Telix, 11,14,30,91
            INSTALL.EXE, 15                   terminal emulation
            installation                        ANSI, 57
              automatic, 31                     NONE, 57
              INSTALL.EXE, 26                   VT100, 57
              manual, 32                        VT52, 57
              minimal, 20,29                  terminal mode, 67
              package, 26                     Tone, 105
            interrupts, 42                    TRANSMIT, 85
              chain, 36                       TSR, 6,46
            L                                 U
            limitations, 46                   upgrade, 9,13
            LOADHIGH, 41                      Usenet, 8
            M                                 W
            menu system, 50                   WAIT, 85
            Microsoft Windows, 14,44          warranty, 10
            modem, 21,40,58,67,79             X
              busy, 59                        Xmodem-1K, 73,76,87,100
              carrier detect, 36              Xmodem-CRC, 73,76,87,100
            mouse, 50,63                        1K packets, 72
            MS DOS, 5,14                      Y
            multitasking, 42                  Ymodem-Batch, 73,76,87,100
            N                                 Z
            NorthAmeriNet, 8                  Zmodem, 19,63,73,76,87,100
            NS16550AS, 43
            P
            parity, 61,104
            PATH, 39
            PgDn, 14
            PgUp, 14
            PKUNZIP, 27,33
            PKWARE, 27,33
            PKZIP, 27
            PROCOMM PLUS, 11,14,30,95
            protocol, 100
            PST, 13
            Pulse, 105


                                                                        107