TABLE OF CONTENTS

sana2.device/AbortIO
sana2.device/CloseDevice
sana2.device/CMD_CLEAR
sana2.device/CMD_FLUSH
sana2.device/CMD_INVALID
sana2.device/CMD_READ
sana2.device/CMD_RESET
sana2.device/CMD_START
sana2.device/CMD_STOP
sana2.device/CMD_UPDATE
sana2.device/CMD_WRITE
sana2.device/OpenDevice
sana2.device/S2_ADDMULTICASTADDRESS
sana2.device/S2_BROADCAST
sana2.device/S2_CONFIGINTERFACE
sana2.device/S2_DELMULTICASTADDRESS
sana2.device/S2_DEVICEQUERY
sana2.device/S2_GETGLOBALSTATS
sana2.device/S2_GETSPECIALSTATS
sana2.device/S2_GETSTATIONADDRESS
sana2.device/S2_GETTYPESTATS
sana2.device/S2_MULTICAST
sana2.device/S2_OFFLINE
sana2.device/S2_ONEVENT
sana2.device/S2_ONLINE
sana2.device/S2_READORPHAN
sana2.device/S2_TRACKTYPE
sana2.device/S2_UNTRACKTYPE

sana2.device/AbortIO                                     sana2.device/AbortIO

   NAME
	AbortIO -- Remove an existing device request.

   SYNOPSIS
	error = AbortIO(Sana2Req)
	D0              A1

	LONG AbortIO(struct IOSana2Req *);

   FUNCTION
	This is an exec.library call.

	This function aborts an ioRequest. If the request is active, it may or
	may not be aborted. If the request is queued it is removed. The
	request will be returned in the same way as if it had normally
	completed.  You must WaitIO() after AbortIO() for the request to
	return.

   INPUTS
	Sana2Req	- Sana2Req to be aborted.

   RESULTS
	error		- Zero if the request was aborted, non-zero otherwise.
			  io_Error in Sana2Req will be set to IOERR_ABORTED
			  if it was aborted.

   NOTES

   SEE ALSO
	exec.library/AbortIO(), exec.library/WaitIO()

   BUGS


sana2.device/CloseDevice                             sana2.device/CloseDevice

   NAME
	CloseDevice -- Close the device.

   SYNOPSIS
	CloseDevice(Sana2Req)
		    A1

	void CloseDevice(struct IOSana2Req *);

   FUNCTION
	This function is called by exec.library CloseDevice().

	This function performs whatever cleanup is required at device closes.

	Note that all IORequests MUST be complete before closing. If any are
	pending, your program must AbortIO() then WaitIO() each outstanding
	IORequest to complete them.

   INPUTS
	Sana2Req	- Pointer to IOSana2Req initialized by OpenDevice().

   NOTES

   SEE ALSO
	exec.library/CloseDevice(), exec.library/OpenDevice()

   BUGS


sana2.device/CMD_CLEAR                                 sana2.device/CMD_CLEAR

   NAME
	Clear -- Clear internal network interface read buffers.

   FUNCTION
	There are no device internal buffers, so CMD_CLEAR does not apply to
	this class of device.

   IO REQUEST
	ios2_Command	- CMD_CLEAR.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO

   BUGS


sana2.device/CMD_FLUSH                                 sana2.device/CMD_FLUSH

   NAME
	Flush -- Clear all queued I/O requests for the SANA-II device.

   FUNCTION
	This command aborts all I/O requests in both the read and write
	request queues of the device.  All pending I/O requests are
	returned with an error message (IOERR_ABORTED).  CMD_FLUSH does not
	affect active requests.

   IO REQUEST
	ios2_Command	- CMD_FLUSH.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.

   NOTES

   SEE ALSO

   BUGS


sana2.device/CMD_INVALID                             sana2.device/CMD_INVALID

   NAME
	Invalid -- Return with error IOERR_NOCMD.

   FUNCTION
	This command causes device driver to reply with an error IOERR_NOCMD
	as defined in <exec/errors.h> indicating the command is not supported.

   IO REQUEST
	ios2_Command	- CMD_INVALID.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO

   BUGS
	Not known to be useful.


sana2.device/CMD_READ                                   sana2.device/CMD_READ

   NAME
	Read -- Get a packet from the network.

   FUNCTION
	Get the next packet available of the requested packet type. The data
	copied (via a call to the requestor-provided CopyToBuffer function)
	into ios2_Data is normally the Data Link Layer packet data only. If
	bit SANA2IOB_RAW is set in ios2_Flags, then the entire physical frame
	will be returned.

	Unlike most Exec devices, SANA-II device drivers do not have internal
	buffers.  If you wish to read data from a SANA-II device you should
	have multiple CMD_READ requests pending at any given time.  The
	functions provided by you the requestor will be used for any incoming
	packets of the type you've requested.  If no read requests are
	outstanding for a type which comes in and no read_orphan requests are
	outstanding, the packet will be lost.

   IO REQUEST
	ios2_Command	- CMD_READ
	ios2_Flags	- Supported flags are:
	                    SANA2IOB_RAW
	                    SANA2IOB_QUICK
	ios2_PacketType	- Packet type desired.
	ios2_Data	- Abstract data structure to hold packet data.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.
	ios2_Flags	- The following flags may be returned:
	                    SANA2IOB_RAW
	                    SANA2IOB_BCAST
	                    SANA2IOB_MCAST
	ios2_SrcAddr	- Source interface address of packet.
	ios2_DstAddr	- Destination interface address of packet.
	ios2_DataLength	- Length of packet data.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   NOTES
	The driver may not directly examine or modify anything pointed to by
	ios2_Data.  It *must* use the requester-provided functions to access
	this data.

   SEE ALSO
	S2_READORPHAN, CMD_WRITE, any_protocol/CopyToBuffer

   BUGS


sana2.device/CMD_RESET                                 sana2.device/CMD_RESET

   NAME
	Reset -- Reset the network interface to initialized state.

   FUNCTION
	Currently, SANA-II devices can only be configured once (with
	CMD_CONFIGINTERFACE) and cannot be re-configured, hence,
	CMD_RESET does not apply to this class of device.

   IO REQUEST
	ios2_Command	- CMD_RESET.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO

   BUGS


sana2.device/CMD_START                                 sana2.device/CMD_START

   NAME
	Start -- Restart device operation.

   FUNCTION
	There is no way for the driver to keep queuing requests without
	servicing them, so CMD_STOP does not apply to this class of device.
	S2_OFFLINE and S2_ONLINE do perform a similar function to CMD_STOP
	and CMD_START

   IO REQUEST
	ios2_Command	- CMD_START.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO
	S2_ONLINE, S2_OFFLINE

   BUGS


sana2.device/CMD_STOP                                   sana2.device/CMD_STOP

   NAME
	Stop -- Pause device operation.

   FUNCTION
	There is no way for the driver to keep queuing requests without
	servicing them, so CMD_STOP does not apply to this class of device.
	S2_OFFLINE and S2_ONLINE do perform a similar function to CMD_STOP
	and CMD_START

   IO REQUEST
	ios2_Command	- CMD_STOP.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO
	S2_ONLINE, S2_OFFLINE

   BUGS


sana2.device/CMD_UPDATE                               sana2.device/CMD_UPDATE

   NAME
	Update -- Force packets out to device.

   FUNCTION
	Since there are no device internal buffers, CMD_UPDATE does not
	apply to this class of device.

   IO REQUEST
	ios2_Command	- CMD_UPDATE.

   RESULTS
	ios2_Error	- IOERR_NOCMD.

   NOTES

   SEE ALSO

   BUGS


sana2.device/CMD_WRITE                                 sana2.device/CMD_WRITE

   NAME
	Write -- Send packet to the network.

   FUNCTION
	This command causes the packet to be sent to the specified network
	interface. Normally, appropriate packet header and trailer information
	will be added to the packet data when it is sent.  If bit SANA2IOB_RAW
	is set in io_Flags, then the ios2_Data is assumed to contain an entire
	physical frame and will be sent (copied to the wire via
	CopyFromBuffer() unmodified.

	Note that the device should not check to see if the destination
	address is on the local hardware.  Network protocols should realize
	that the packet has a local destination long before it gets to a
	SANA-II driver.

   IO REQUEST
	ios2_Command	- CMD_WRITE.
	ios2_Flags	- Supported flags are:
	                    SANA2IOB_RAW
	                    SANA2IOB_QUICK
	ios2_PacketType	- Packet type to send.
	ios2_DstAddr	- Destination interface address for this packet.
	ios2_DataLength	- Length of the Data to be sent.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	The driver may not directly examine or modify anything pointed to by
	ios2_Data.  It *must* use the requester-provided functions to access
	this data.

   SEE ALSO
	CMD_READ, S2_BROADCAST, S2_MULTICAST, any_protocol/CopyFromBuffer

   BUGS


sana2.device/OpenDevice                               sana2.device/OpenDevice

   NAME
	Open -- Request an opening of the network device.

   SYNOPSIS
	error = OpenDevice(unit, IOSana2Req, flags)
	D0		   D0    A1          D1

	BYTE OpenDevice(ULONG, struct IOSana2Req *, ULONG);

   FUNCTION
	This function is called by exec.library OpenDevice().

	This function performs whatever initialization is required per
	device open and initializes the Sana2Req for use by the
	device.

   INPUTS
	unit		- Device unit to open.
	Sana2Req	- Pointer to IOSana2Req structure to be initialized by
			  the sana2.device.
	flags		- Supported flags are:
				SANA2OPB_MINE
				SANA2OPB_PROM
	ios2_BufferManagement	- A pointer to a tag list containing
				  pointers to buffer management functions.

   RESULTS
	error		- same as io_Error
	io_Error	- Zero if successful; non-zero otherwise.
	io_Device	- A pointer to whatever device will handle the calls
			  for this unit.  This pointer may be different
			  depending on what unit is requested.
	ios2_BufferManagement	- A pointer to device internal information
				  used to call buffer management functions.

   NOTES

   SEE ALSO
	exec.library/OpenDevice(), exec.library/CloseDevice()

   BUGS


sana2.device/S2_ADDMULTICASTADDRESS       sana2.device/S2_ADDMULTICASTADDRESS

   NAME
	AddMulticastAddress -- Enable an interface multicast address.

   FUNCTION
	This command causes the device driver to enable multicast packet
	reception for the requested address.

   IO REQUEST
	ios2_Command	- S2_ADDMULTICASTADDRESS.
	ios2_SrcAddr	- Multicast address to enable.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	Multicast addresses are added globally -- anyone using the device
	may receive packets as a result of any multicast address which has
	been added for the device.

	Since multicast addresses are not "bound" to a particular packet type,
	each enabled multicast address has an "enabled" count associated with
	it so that if two protocols add the same multicast address and later
	one removes it, it is still enabled until the second removes it.

   SEE ALSO
	S2_MULTICAST, S2_DELMULTICASTADDRESS

   BUGS


sana2.device/S2_BROADCAST                           sana2.device/S2_BROADCAST

   NAME
	Broadcast -- Broadcast a packet on network.

   FUNCTION
	This command works the same as CMD_WRITE except that it also performs
	whatever special processing of the packet is required to do a
	broadcast send. The actual broadcast mechanism is neccessarily
	network/interface/device specific.

   IO REQUEST
	ios2_Command	- S2_BROADCAST.
	ios2_Flags	- Supported flags are:
				SANA2IOB_RAW
				SANA2IOB_QUICK
	ios2_PacketType	- Packet type to send.
	ios2_DataLength	- Length of the Data to be sent.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   RESULTS
	ios2_DstAddr	- The contents of this field are to be
			  considered trash upon return of the IOReq.
	ios2_Error	- Zero if successful; non-zero otherwise.
	                  This command can fail for many reasons and
	                  is not supported by all networks and/or
	                  network interfaces.
	ios2_WireError	- More specific error number.

   NOTES
	The DstAddr field may be trashed by the driver because this function
	may be implemented by filling DstAddr with a broadcast address and
	internally calling CMD_WRITE.

   SEE ALSO
	CMD_WRITE, S2_MULTICAST

   BUGS


sana2.device/S2_CONFIGINTERFACE               sana2.device/S2_CONFIGINTERFACE

   NAME
	ConfigInterface -- Configure the network interface.

   FUNCTION
	This command causes the device driver to initialize the interface
	hardware and to set the network interface address to the address in
	ios2_SrcAddr. This command can only be executed once and, if
	successful, will leave the driver and network interface fully
	operational and the network interface in ios2_SrcAddr.

	To set the interface address to the factory address, the network
	management software must use GetStationAddress first and then call
	ConfigInterface with the result. If there is no factory address then
	the network software must pick an address to use.

	Until this command is executed the device will not listen for any
	packets on the hardware.

   IO REQUEST
	ios2_Command	- S2_CONFIGINTERFACE.
	ios2_Flags      - Supported flags are:
				SANA2IOB_QUICK
	ios2_SrcAddr	- Address for this interface.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.
	ios2_SrcAddr	- Address of this interface as configured.

   NOTES
	Some networks have the interfaces choose a currently unused interface
	address each time the interface is initialized. The caller must check
	ios2_SrcAddr for the actual interface address after configuring the
	interface.

   SEE ALSO
	S2_GETSTATIONADDRESS

   BUGS


sana2.device/S2_DELMULTICASTADDRESS       sana2.device/S2_DELMULTICASTADDRESS

   NAME
	DelMultiCastAddress -- Disable an interface multicast address.

   FUNCTION
	This command causes device driver to disable multicast packet
	reception for the requested address.

	It is an error to disable a multicast address that is not enabled.

   IO REQUEST
	ios2_Command	- S2_DELMULTICASTADDRESS
	ios2_SrcAddr	- Multicast address to disable.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	Multicast addresses are added globally -- anyone using the device
	may receive packets as a result of any multicast address which has
	been added for the device.

	Since multicast addresses are not "bound" to a particular packet type,
	each enabled multicast address has an "enabled" count associated with
	it so that if two protocols add the same multicast address and later
	one removes it, it is still enabled until the second removes it.

   SEE ALSO
	S2_ADDMULTICASTADDRESS

   BUGS


sana2.device/S2_DEVICEQUERY                       sana2.device/S2_DEVICEQUERY

   NAME
	DeviceQuery -- Return parameters for this network interface.

   FUNCTION
	This command causes the device driver to report information about the
	device. Up to SizeAvailable bytes of the information is copied
	into a buffer pointed to by ios2_StatData. The format of the data is
	as follows:

	    struct Sana2DeviceQuery
	    {
	    /*
	    ** Standard information
	    */
	        ULONG SizeAvailable;    /* bytes available */
	        ULONG SizeSupplied;     /* bytes supplied */
	        LONG  DevQueryFormat;   /* this is type 0 */
	        LONG  DeviceLevel;      /* this document is level 0 */

	    /*
	    ** Common information
	    */
	        UWORD AddrFieldSize;    /* address size in bits */
	        ULONG MTU;              /* maximum packet data size */
	        LONG  BPS;              /* line rate (bits/sec) */
	        LONG  HardwareType;     /* what the wire is */

	    /*
	    ** Format specific information
	    */
	    };

	The SizeAvailable specifies the number of bytes that the caller
	is prepared to accomodate, including the standard information fields.

	SizeSupplied is the number of bytes actually supplied,
	including the standard information fields, which will not exceed
	SizeAvailable.

	<devices/sana2.h> includes constants for these values.  If your
	hardware does not have a number assigned to it, you must contact
	CATS to get a hardware number.

   IO REQUEST
	ios2_Command	- S2_DEVICEQUERY.
	ios2_StatData	- Pointer to Sana2DeviceQuery structure to fill in.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES

   SEE ALSO

   BUGS


sana2.device/S2_GETGLOBALSTATS                 sana2.device/S2_GETGLOBALSTATS

   NAME
	GetGlobalStats -- Get interface accumulated statistics.

   FUNCTION
	This command causes the device driver to retrieve various global
	runtime statistics for this network interface. The format of the
	data returned is as follows:

	    struct Sana2DeviceStats
	    {
	        ULONG PacketsReceived;
	        ULONG PacketsSent;
	        ULONG BadData;
	        ULONG Overruns;
	        ULONG UnknownTypesReceived;
	        ULONG Reconfigurations;
	        timeval LastStart;
	    };

   IO REQUEST
	ios2_Command	- S2_GETGLOBALSTATS.
	ios2_StatData	- Pointer to Sana2DeviceStats structure to fill.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES

   SEE ALSO
	S2_GETSPECIALSTATS

   BUGS


sana2.device/S2_GETSPECIALSTATS               sana2.device/S2_GETSPECIALSTATS

   NAME
	GetSpecialStats -- Get network type specific statistics.

   FUNCTION
	This function returns statistics which are specific to the type of
	network medium this driver controls. For example, this command could
	return statistics common to all Ethernets which are not common to all
	network mediums in general.

	The supplied Sana2SpecialStatData structure is given below:

	    struct Sana2SpecialStatData
	    {
	        ULONG RecordCountMax;
	        ULONG RecordCountSupplied;
	        struct Sana2StatRecord[RecordCountMax];
	    };

	The format of the data returned is:

	    struct Sana2StatRecord
	    {
	        ULONG Type;     /* commodore registered */
	        LONG Count;     /* the stat itself */
	        char *String;   /* null terminated */
	    };

	The RecordCountMax field specifies the number of records that the
	caller is prepared to accomodate.

	RecordCountSupplied is the number of record actually supplied which
	will not exceed RecordCountMax.

   IO REQUEST
	ios2_Command	- S2_GETSPECIALSTATS.
	ios2_StatData	- Pointer to a Sana2SpecialStatData structure to fill.
			  RecordCountMax must be initialized.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	Commodore will maintain registered statistic Types.

   SEE ALSO
	S2_GETGLOBALSTATS, <devices/sana2specialstats.h>

   BUGS


sana2.device/S2_GETSTATIONADDRESS           sana2.device/S2_GETSTATIONADDRESS

   NAME
	GetStationAddress -- Get default and interface address.

   FUNCTION
	This command causes the device driver to copy the current interface
	address into ios2_SrcAddr, and to copy the factory default station
	address (if any) into ios2_DstAddr.

   IO REQUEST
	ios2_Command	- S2_GETSTATIONADDRESS.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.
	ios2_SrcAddr	- Current interface address.
	ios2_DstAddr	- Default interface address (if any).

   NOTES

   SEE ALSO
	S2_CONFIGINTERFACE

   BUGS


sana2.device/S2_GETTYPESTATS                     sana2.device/S2_GETTYPESTATS

   NAME
	GetTypeStats -- Get accumulated type specific statistics.

   FUNCTION
	This command causes the device driver to retrieve various packet type
	specific runtime statistics for this network interface. The format of
	the data returned is as follows:

	    struct Sana2PacketTypeStats
	    {
	        LONG PacketsSent;            /* transmitted count            */
	        LONG PacketsReceived;        /* received count               */
	        LONG BytesSent;              /* bytes transmitted count      */
	        LONG BytesReceived;          /* bytes received count         */
	        LONG PacketsDropped;         /* packets dropped count        */
	    };

   IO REQUEST
	ios2_Command	- S2_GETTYPESTATS.
	ios2_PacketType	- Packet type of interest.
	ios2_StatData	- Pointer to TypeStats structure to fill in.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	Statistics for a particular packet type are only available while that
	packet type is being ``tracked''.

   SEE ALSO
	S2_TRACKTYPE, S2_UNTRACKTYPE

   BUGS


sana2.device/S2_MULTICAST                           sana2.device/S2_MULTICAST

   NAME
	Multicast -- Multicast a packet on network.

   FUNCTION
	This command works the same as CMD_WRITE except that it also performs
	whatever special processing of the packet is required to do a
	multicast send. The actual multicast mechanism is neccessarily
	network/interface/device specific.

   IO REQUEST
	ios2_Command	- S2_MULTICAST.
	ios2_Flags	- Supported flags are:
				SANA2IOB_RAW
				SANA2IOB_QUICK
	ios2_PacketType	- Packet type to send.
	ios2_DstAddr	- Destination interface address for this packet.
	ios2_DataLength	- Length of the Data to be sent.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	                  This command can fail for many reasons and
	                  is not supported by all networks and/or
	                  network interfaces.
	ios2_WireError	- More specific error number.

   NOTES
	The address supplied in ios2_DstAddr will be sanity checked (if
	possible) by the driver. If the supplied address fails this sanity
	check, the multicast request will fail immediately with ios2_Error
	set to S2WERR_BAD_MULTICAST.

	Another Amiga will not receive a multicast packet unless it has had
	the particular multicast address being used S2_ADDMULTICASTADRESS'd.

   SEE ALSO
	CMD_WRITE, S2_BROADCAST, S2_ADDMULTICASTADDRESS

   BUGS


sana2.device/S2_OFFLINE                               sana2.device/S2_OFFLINE

   NAME
	Offline -- Remove interface from service.

   FUNCTION
	This command removes a network interface from service.

   IO REQUEST
	ios2_Command	- S2_OFFLINE.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	Aborts all pending reads and writes with ios2_Error set to
	S2ERR_OUTOFSERVICE.

	While the interface is offline, all read, writes and any other
	command that touches interface hardware will be rejected with
	ios2_Error set to S2ERR_OUTOFSERVICE.

	This command is intended to permit a network interface to be
	tested on an otherwise live system.

   SEE ALSO
	S2_ONLINE

   BUGS


sana2.device/S2_ONEVENT                               sana2.device/S2_ONEVENT

   NAME
	OnEvent -- Return when specified event occures.

   FUNCTION
	This command returns when a particular event condition has occured
	on the network or this network interface.

   IO REQUEST
	ios2_Command	- S2_ONEVENT.
	ios2_Flags	- Supported flags are:
				SANA2IOB_QUICK
	ios2_WireError	- Mask of event(s) to wait for
			  (from <devices/sana2.h>).

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- Mask of events that occured.

   NOTES
	If this device driver does not understand the specified event
	condition(s) then the command returns immediately with
	ios2_Req.io_Error set to S2_ERR_NOT_SUPPORTED and ios2_WireError
	S2WERR_BAD_EVENT.  A successful return will have ios2_Error set to
	zero ios2_WireError set to the event number.

	All pending requests for a particular event will be returned when
	that event occurs.

	All event types that cover a particular condition are returned when
	that condition occures. For instance, if an error is returned by
	a buffer management function during receive processing, events of
	types S2EVENT_ERROR, S2EVENT_RX and S2EVENT_BUFF would be returned if
	pending.

	Types ONLINE and OFFLINE return immediately if the device is
	already in the state to be waited for.

   SEE ALSO

   BUGS


sana2.device/S2_ONLINE                                 sana2.device/S2_ONLINE

   NAME
	Online -- Put a network interface back in service.

   FUNCTION
	This command places an offline network interface back into service.

   IO REQUEST
	ios2_Command	- S2_ONLINE.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES
	This command is responsible for putting the network interface
	hardware back into a known state (as close as possible to the
	state before S2_OFFLINE) and resets the unit global and special
	statistics.

   SEE ALSO
	S2_OFFLINE

   BUGS


sana2.device/S2_READORPHAN                         sana2.device/S2_READORPHAN

   NAME
	ReadOrphan -- Get a packet for which there is no reader.

   FUNCTION
	Get the next packet available that does not satisfy any	then-pending
	CMD_READ requests. The data returned in the ios2_Data structure is
	normally the Data Link Layer packet type field and the packet data. If
	bit SANA2IOB_RAW is set in ios2_Flags, then the entire Data Link Layer
	packet, including both header and trailer information, will be
	returned.

   IO REQUEST
	ios2_Command	- CMD_READORPHAN.
	ios2_Flags	- Supported flags are:
				SANA2IOB_RAW
				SANA2IOB_QUICK
	ios2_DataLength	- Length of the Data to be sent.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.
	ios2_Flags	- The following flags may be returned:
				SANA2IOB_RAW
				SANA2IOB_BCAST
				SANA2IOB_MCAST
	ios2_SrcAddr	- Source interface address of packet.
	ios2_DstAddr	- Destination interface address of packet.
	ios2_DataLength	- Length of the Data to be sent.
	ios2_Data	- Abstract data structure which packet data is
			  contained in.

   NOTES
	This is intended for debugging and management tools.  Protocols should
	not use this.

	As with 802.3 packets on an ethernet, to determine which protocol
	family the returned packet belongs to you may have to specify
	SANA2IOB_RAW to get the entire data link layer wrapper (which is where
	the protocol type may be kept). Notice this necessarily means that
	this cannot be done in a network interface independent fashion.  The
	driver will, however, fill in the PacketType field to the best of its
	ability.

   SEE ALSO
	CMD_READ, CMD_WRITE

   BUGS


sana2.device/S2_TRACKTYPE                           sana2.device/S2_TRACKTYPE

   NAME
	TrackType -- Accumulate statistics about a packet type.

   FUNCTION
	This command causes the device driver to accumulate statistics about
	a particular packet type. Packet type statistics, for the particular
	packet type, are zeroed by this command.

   IO REQUEST
	ios2_Command	- S2_TRACKTYPE.
	ios2_PacketType	- Packet type of interest.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES

   SEE ALSO
	S2_UNTRACKTYPE, S2_GETTYPESTATS

   BUGS


sana2.device/S2_UNTRACKTYPE                       sana2.device/S2_UNTRACKTYPE

   NAME
	UntrackType -- End statistics about a packet type.

   FUNCTION
	This command causes the device driver to stop accumulating
	statistics about a particular packet type.

   IO REQUEST
	ios2_Command	- S2_UNTRACKTYPE.
	ios2_PacketType	- Packet type of interest.

   RESULTS
	ios2_Error	- Zero if successful; non-zero otherwise.
	ios2_WireError	- More specific error number.

   NOTES

   SEE ALSO
	S2_TRACKTYPE, S2_GETTYPESTATS

   BUGS