sSSSSs      FFFFFFFFFF    sSSSSs
                       sSSSSSSs     FFFFFFFFF    sSSSSSSs
                      sSs     sS    FF          sSs     sS
                      SS            FF          SS
                      sSs           FF          sSs
                       sSSSSSSs     FFFFFFF      sSSSSSSs
                             sSs    FF                 sSs
                              SS    FF                  SS
                      Ss      Ss    FF          Ss      Ss
                       sSSSSSSs     FF           sSSSSSSs
                        sSSSSs      FF            sSSSSs


                       S e c u r e   F i l e S y s t e m


                     Copyright Peter C.Gutmann  1993, 1994


      "The right to privacy... is the most comprehensive of rights and the
       right most valued by civilized man"
                          - Justice Louis Brandeis, US Supreme Court, 1928


Ever since Julius Caesar used the cipher which now bears his name to try to
hide his military dispatches from prying eyes, people have been working on
various means to keep their confidential information private.  Over the years,
the art of cryptography (that is, of scrambling information so only those in
possession of the correct password can unscramble it) has progressed from
simple pencil-and-paper systems to more sophisticated schemes involving complex
electromechanical devices and eventually computers.  The means of breaking
these schemes has progressed on a similar level.  Today, with the
ever-increasing amount of information stored on computers, good cryptography is
needed more than ever before.

There are two main areas in which privacy protection of data is required:

  - Protection of bulk data stored on disk or tape.
  - Protection of messages sent to others.

SFS is intended to solve the problem of protecting bulk data stored on disk.
The protection of electronic messages is best solved by software packages such
as PGP (available on sites the world over) or various versions of PEM
(currently available mainly in the US, although non-US versions are beginning
to appear).

SFS has the following features:

  - The current implementation runs as a standard DOS device driver, and
    therefore works with plain old DOS as well as other software such as
    Windows, QEMM, Share, disk cacheing software, Stacker, and so on.

  - Up to five encrypted volumes can be accessed at any one time, chosen from
    a selection of as many volumes as there is storage for.

  - Volumes can be quickly unmounted with a user-defined hotkey, or
    automatically unmounted after a certain amount of time.  They can also be
    converted back to unencrypted volumes or have their contents destroyed if
    required.

  - The encryption algorithms used have been selected to be free from any
    patent restrictions, and the software itself is not covered by US export
    restrictions as it was developed entirely outside the US (although once a
    copy is sent into the US it can't be re-exported).

  - SFS complies with a number of national and international data encryption
    standards, among them ANSI X3.106, Federal Information Processing Standard
    (FIPS) 180, Australian Standard 2805.5.2, ISO 10116:1991 and ISO
    10126-2:1991, and is on nodding terms with a several other relevant
    standards.

  - The documentation includes fairly in-depth analyses of various security
    aspects of the software, as well as complete design and programming details
    necessary to both create SFS-compatible software and to verify the
    algorithms used in SFS.

  - The encryption system provides reasonable performance.  One tester has
    reported a throughput of 250 K/s for the basic version of SFS, and 260 K/s
    for the 486+ version on his 486 system, when copying a file with the DOS
    copy command from one location on an SFS volume to another.  Throughput on
    a vanilla 386 system was reported at around 160 K/s.

Although the use of DOS is described throughout this document, SFS is not
limited to any particular operating environment, and can be used to contain
virtually any type of filesystem.  In the future an SFS driver for OS/2 HPFS
filesystems may be developed, and there have been discussions on creating a
Linux SFS driver for Unix machines.  A 68000 version of SFS is also reported to
be under development.


Overview
--------

This document is organised to give step-by-step instructions on setting up the
SFS driver, creating an encrypted volume, and using the encrypted volume to
store information securely.  The first three sections cover each of these
steps, with a special quick-start section preceding them giving a rapid
introduction to getting an encrypted disk volume up and running.  The next
sections provide extra details on topics such as password management,
incompatibility problems, other encryption software, and the politics of
cryptography and privacy.  The final sections provide an in-depth security
analysis, technical information on the SFS driver and data formats for those
wishing to write SFS-compatible software or wanting to check the security of
the software for themselves.

The document is divided into sections as follows:

  Terminology
        An explanation of some of the technical terms use in this
        document.  Experienced users can skip this section.
  Quick Start
        A quick overview of the use of SFS which summarizes the
        next three sections for people in a hurry
  Loading the SFS Driver
        How to set up the SFS driver needed to handle encrypted
        volumes.
  Creating an SFS Volume
        How to prepare an SFS encrypted volume for use.
  Mounting an SFS Volume
        How to mount a previously prepared SFS encrypted volume
        so the operating system can use it.
  Advanced SFS Driver Options
        Various advanced options such as how to mount SFS volumes
        at startup so that they are automatically available when the
        system is booted, and customzing the SFS driver user
        interface.
  Changing the Characteristics of an SFS Volume
        How to change various characteristics of an SFS volume such
        as the password, volume name, and serial number, and how to
        delete SFS volumes.
  Sharing SFS Volumes Between Multiple Users
        How to securely share a single encrypted SFS volume between
        multiple users.
  Creating Compressed SFS Volumes
        How to create a compressed drive inside a normal SFS volume
  WinSFS - Using SFS with Windows
        An overview of the Windows version of SFS.
  Command Summary
        A summary of the commands available with the various SFS
        programs.
  Incompatibilities
        Comments on unusual hardware and software combinations which
        may create problems for SFS.
  Authentication of SFS Software
        How to verify that the SFS distribution you have is indeed the
        real thing.
  Applications
        Various applications and uses for SFS.
  The Care and Feeding of Passwords
        Details on how to chose and handle a password to protect
        an SFS volume.
  Other Software
        An overview of other available security software and the
        weakness and problems present in it.
  Data Security
        Various issues in data security which should be taken into
        consideration when using SFS and similar encryption software.
  Politics
        A discussion on the politics of cryptography, the right to
        privacy, and some of the reasons why SFS was written.
  Security Analysis
        An analysis of the level of security offered by SFS and
        some possible attacks on it.
  An Introduction to Encryption Systems
        A brief introduction to encryption systems with an emphasis
        on the methods used in SFS.
  Design Details
        Various in-depth design details not covered in the security
        analysis.
  SFS Disk Volume Layout
        Details on the disk layout used by SFS.
  Interfacing with SFS
        How to control the SFS driver through software.
  Interfacing with mountsfs
        How to control the mountsfs program from external software such
        as graphical front-ends.
  Selected Source Code
        A walkthrough of selected portions of the source code to allow
        verification and help implementors.
  Future Work
        Various enhancements which may be incorporated into future
        versions of SFS.
  Recommended Reading
        A short list of recommended reading material for those wishing
        to know more about the design of SFS and encryption in general.
  Using SFS
        Conditions and terms for use of SFS.
  Credits
  Warranty


Terminology
-----------

Throughout this document a number of specialised terms are used to describe the
operation of the SFS encryption software.  This section provides a brief
explanation of the terms used.  Experienced users can skip this material and go
directly to the "Loading the SFS Driver" section below.

  Disk volume:

    An individual logical disk drive, volume, partition, or filesystem.  A
    single physical hard disk can (and usually does) contain more than one
    volume on it.  Under DOS, each of these volumes is assigned its own drive
    letter and appears as a separate drive, even though they all reside on the
    same physical hard disk.  Thus a system might have a single 128MB hard disk
    which contains four 32MB volumes accessed by the drive letters C:, D:, E:,
    and F:.

    This system is rather confusing and dates back fifteen to twenty years. SFS
    refers to these volumes by name rather than an arbitrary letter, so that
    the volumes might be called "Encrypted data", "Personal correspondence", or
    "Accounts receivable, March 1993".  Unfortunately once SFS has set up the
    volume for DOS to access, it's back to the old F: to identify your data.

  Password, key:

    The password or encryption key is used to protect the data on an encrypted
    volume.  Despite its name, a password can (and should) be more than just a
    single word.  The SFS software will accept up to 100 characters of
    password, so that perhaps the term "passphrase" would be more appropriate.

    For maximum security, each volume should be protected by its own unique
    password.  The SFS software takes the password for a volume, adds extra
    keying information to it, and converts the result into an encryption key
    which is used to encrypt and decrypt data on a given volume.  Great care
    should be taken in the choice of passwords and in keeping them secret. More
    details on this are given in the section "The Care and Feeding of
    Passwords" below.

  Device driver:

    A device driver is a special piece of software which is used by the
    operating system to access hardware which it wasn't designed to.  Unless
    the device driver is loaded, the operating system generally won't recognise
    that a piece of hardware even exists.  Even the computer's monitor,
    keyboard, and disk drives are accessed through device drivers, although
    their presence is hidden by the operating system.

    An example of a visible device driver is the one used to handle a mouse.
    Networked disk drives may be accessed through a device driver.  RAM disks
    are implemented as device drivers.  CDROM drives are handled via a device
    driver.  Finally, encrypted SFS volumes are accessed through a device
    driver.

  Mount point:

    The locations provided by the SFS driver for mounting encrypted volumes -
    in other words the number of encrypted volumes which can be accessed by the
    driver at any one time.  By default the driver provides one mount point,
    which means one encrypted volume can be accessed through it at any given
    time.  The exact number of mount points can be specified when the SFS
    driver is loaded.


Quick Start
-----------

This section contains a condensed version of the next three sections and allows
a quick start for SFS.  Although it is recommended that the full text be read,
it should be possible to install and use a minimal SFS setup using only the
quick-start information.

Initially, the SFS driver must be loaded by adding an entry for it to the
CONFIG.SYS file.  For example if the SFS.SYS driver was located in the DOS
directory on drive C: the following line should be added to the CONFIG.SYS
file:

  DEVICE=C:\DOS\SFS.SYS

Alternatively, the DEVICEHIGH option can be used to load the driver into high
memory under those versions of DOS which support it.  The system should now be
rebooted to make sure the driver is installed.

The use of the SFS driver is covered in more detail in the sections "Loading
the SFS Driver" and "Advanced SFS Driver Options" below.

Once the driver is loaded, the encrypted volume can be created with the "mksfs"
program.  This is run with the letter of the drive to encrypt, and the name of
the encrypted volume preceded by the "vol=" option.  For example to encrypt the
E: drive to create a volume with the name "Encrypted disk", the command would
be:

  mksfs "vol=Encrypted volume" e:

Note that that "vol=..." option is quoted, as the volume name contains a space.
Volume names without a space don't need to be quoted.

mksfs will confirm that the given drive is indeed the one to be encrypted, and
then ask for an encryption password of between 10 and 100 characters.  After
asking for the password a second time to confirm it, it will encrypt the drive.
This will take a few minutes, and the program will display a progress bar as
the encryption takes place.

There are a great many options and special safety checks built into mksfs to
ensure no data is accidentally destroyed, and it is recommended that the
section "Creating an SFS Volume" is at least glanced through to provide an
overview of the functioning of mksfs before it is run.

Once the encrypted volume has been created, it can be mounted with the
"mountsfs" utility.  Mounting a volume makes it available to DOS as a normal
disk volume, with all encryption being done transparently by the SFS driver.
Like mksfs, mountsfs must be told the encrypted volume's name in order to
access it.  The full name doesn't need to be used, mountsfs will accept any
part of the name in upper or lower case.  Using the name from the previous
example, the command to mount the volume would be:

  mountsfs vol=encrypt

mountsfs will match the partial name "encrypt" with the full volume name
"Encrypted volume", ask for the encryption password for the volume, and mount
it.  The volume will now be accessible as a normal DOS drive.

More details on the use of mountsfs are contained in the section "Mounting an
SFS Volume" below.  Other methods for mounting volumes are given in the section
"Advanced SFS Driver Options" below.


Loading the SFS Driver
----------------------

The SFS device driver SFS.SYS or SFS486.SYS can be loaded in the usual manner
by specifying it in the CONFIG.SYS file:

  DEVICE=[drive][path]SFS.SYS [/SILENT] [/UNITS=n] [/DRDOS] [/NOXMS]
                              [/PROMPT=xxxx] [/READONLY] [/READWRITE]
                              [/AUTOMOUNT=nnnn] [/HOTKEY=xxxx] [/TIMEOUT=nn]

It can also be loaded high under those versions of DOS which support this with:

  DEVICEHIGH=[drive][path]SFS.SYS [/SILENT] [/UNITS=n] [/DRDOS] [/NOXMS]
                                  [/PROMPT=xxxx] [/READONLY] [/READWRITE]
                                  [/AUTOMOUNT=nnnn] [/HOTKEY=xxxx] [/TIMEOUT=nn]

The SFS486.SYS driver is loaded the same way.  This driver contains code for
'486 and higher processors, and is about 400 bytes smaller and 5 percent
faster.

The arguments to SFS are not case-sensitive, and can be given in upper or lower
case.  For example if your copy of the SFS.SYS driver was located in the DOS
directory on drive C: you would add the following line to your CONFIG.SYS file:

  DEVICE=C:\DOS\SFS.SYS

The driver will only work on systems with an 80386 or higher processor.  This
is because the en/decryption code (over 10,000 lines of assembly language) has
to have a 32-bit processor to run on.  Virtually all recent PC's fulfil these
requirements, and a 16-bit version would both be much slower and require about
three times as much code space to run in[1].

If an attempt is made to load SFS.SYS on a machine which doesn't have a 32-bit
CPU, the message:

  Error: Processor must be 386 or higher

will be displayed and SFS will de-install itself.

The drive currently recognises ten options, /AUTOMOUNT, /DRDOS, /HOTKEY,
/NOXMS, /PROMPT, /READONLY, /READWRITE, /SILENT, /TIMEOUT, and /UNITS:

  The /AUTOMOUNT option is used to mount SFS volumes automatically at startup,
  and is explained in more detail in the section "Advanced SFS Driver Options"
  below.

  The /DRDOS option is needed when running the SFS driver under Novell/DR-DOS
  instead of MS-DOS or an MS-DOS derivative.  This tells the driver to use
  Novell/Digital Researches way of accessing disk volumes larger than 32MB,
  which is slightly different from the method other versions of DOS use.

  The /HOTKEY option is used to specify the quick-unmount hotkey which can be
  used to instantly unmount all currently mounted SFS volumes, and is explained
  in more detail in the sections "Mounting an SFS Volume" and "Advanced SFS
  Driver Options" below.

  The /NOXMS option is used to disable SFS buffering data in extended memory.
  By default SFS will allocate a 64K write buffer to speed up disk writes.  If
  no extended memory is available or if the /NOXMS option is used, SFS will
  print:

    Warning: No XMS buffers available, slow writes will be used

  The driver will then switch to using slow disk writes which are about half as
  fast as normal reads and writes.  These are necessary to fix buffering
  problems in MSDOS 6.x and some disk utilities.  If an extended memory buffer
  is used, the slow writes aren't necessary.

  The /PROMPT option is used in conjunction with the /AUTOMOUNT option to
  display a user-defined prompt when asking for the password for the SFS volume
  to be automounted, and is explained in more detail in the section "Advanced
  SFS Driver Options" below.

  The /READONLY and /READWRITE options are used in conjunction with the
  /AUTOMOUNT option to disable write access to the volumes being mounted.
  The /READONLY option disables write access to all following automounted
  volumes; the /READWRITE option enables write access to all following
  automounted volumes.  The default setting is to allow read and write access
  to all volumes.  More details on read-only access to SFS volumes is given in
  the section "Mounting an SFS Volume" below.

  The /SILENT option can be used to suppress the printing of the start-up
  message.

  The /TIMEOUT option is used to specify the time in minutes after which SFS
  volumes are automatically unmounted if they haven't been accessed during that
  time, and is explained in more detail in the sections "Mounting an SFS
  Volume" and "Advanced SFS Driver Options" below.

  The /UNITS=n option specifies the number of mount points (or number of disk
  volumes) the driver will provide, where `n' is the number of units and can
  range from 1 to 5.  Each drive mount point requires 384 bytes of extra memory
  storage.  By default, the driver allocates storage for one mount point.

As an example, to suppress the printing of the start-up message and to specify
that the driver should handle up to three encrypted volumes, the previously
given example for loading the driver would be changed to:

  DEVICE=C:\DOS\SFS.SYS /SILENT /UNITS=3

The number of mount points can range from 1 to 5.  If a number outside this
range is specified, the message:

  Error: Invalid number of units specified

will be displayed and SFS will de-install itself.  Finally, if an invalid
option is given (such as a misspelled or badly-formatted parameter) SFS will
again de-install itself after displaying:

  Error: Unknown parameter specified

All the remaining driver options are covered in the section "Advanced SFS
Driver Options" below.

If the driver installs successfully and unless the /SILENT option is used it
will, after displaying a general message showing that it has been installed,
indicate which which drive will be used as the encrypted one.  For example if
the encrypted drive is made available as E:, the message would be:

  Encrypted volume will be mounted as drive E:

This indicates that once an encrypted volume is mounted, DOS will access it as
drive E:  If more than one mount point is specified, the range of drives which
will be made available is shown, so that if the option /UNITS=3 were used the
message would be:

  Encrypted volumes will be mounted as drives E: - G:

When installed SFS consumes around 6.5K of memory, most of which is encryption
code.

Footnote [1]: There have been calls for 286 versions of SFS from countries in
              which 386+ machines are still difficult to obtain.  There may
              eventually be a 16-bit version, although at the current rate by
              the time it's written everyone will be using Pentiums anyway.


Creating an SFS Volume
----------------------

Before SFS can use an encrypted volume, it must be converted from a normal DOS
volume to an encrypted SFS one.  The program which performs this task is mksfs,
(Make Secure Filesystem) and is very loosely patterned after the Unix mkfs
utility.  mksfs takes a standard DOS volume (which may be either freshly
formatted or may already contain files) and turns in into an encrypted SFS
volume.  The encryption process is non-destructive, so in general no data will
be lost.  The only case in which a data loss could occur is if there is a power
cut while the volume is being encrypted (this means that power to the system is
removed as the disk is being written to, which would cause problems under
virtually any software).  If the data being encrypted is extremely valuable or
there is a risk of a power cut occurring, the volume should be backed up
completely before being encrypted.  This should only be necessary in
exceptional circumstances, however.

If used on a fixed disk, mksfs will encrypt an entire disk partition rather
than individual files.  This is necessary because an SFS partition may contain
a DOS filesystem, or an OS/2 one, or a HPFS one, or an NTFS one, or any one of
a dozen other possible filesystems.  However, many people have only a single
large partition on their hard drive which is used entirely for DOS, which would
require a complete backup of the partition before the FDISK utility can be used
to create two smaller partitions, followed by a restore of the backup to one of
the new partitions.  This problem can be avoided by using one of several
programs which will split an existing partition into two smaller partitions.
One of them is FIPS, currently at version 0.9 and available as
garbo.uwasa.fi:/pc/diskutil/fips09.zip and from all garbo mirror sites.  This
allows a partition to be nondestructively split into two smaller partitions,
one of which can be used as an SFS volume.

If the hardware or software setup you are using is somewhat unusual (for
example you have drives which are compressed with DoubleSpace or Stacker, or
you have unusual drive hardware which needs special software like SpeedStor to
manage it), you should read the section "Incompatibilities" below.  In
addition, mksfs may, during normal operation, trigger a number of virus
detectors which monitor access to certain critical disk and memory areas which
software would not normally access.  Finally, mksfs will check whether it is
being run under Quarterdeck's DesqView or Microsoft Windows, as it should in
general not be run while DesqView, Windows, or some other multitasking software
is running.  Since mksfs takes an entire disk volume and encrypts it sector by
sector, any other software which tries to simultaneously access the volume
while mksfs is running will come to grief.  If mksfs detects that it is being
run under either DesqView or Windows, it will display a warning message with an
option to quit and re-run it from DOS only.  Only if there is no chance that
any other program will access the disk volume being encrypted is it safe to run
mksfs under multitasking software.

The mksfs program is run in the following manner:

  mksfs [-c] [-o] [-t] [serial=<serial number>] [multiuser]
        [vol=<volume name>] <drive>

Since all arguments are named, they can be given in any order.  The order shown
here is merely an example.

The -c and -t options are present to allow integrity checks on the SFS
encryption code and the operation of mksfs itself, and are covered in more
detail in the sections "Incompatibilities" and "Security Analysis"
respectively.

The drive specifies the DOS drive letter for which the SFS volume will be
created.  For example to create an SFS volume on the disk currently in the A:
drive the command would be:

  mksfs a:

It is recommended that each SFS volume be given a unique name for
identification purposes.  Although it is possible to create an unnamed (or
anonymous) volume, this practice is strongly discouraged for fixed disks which
may contain multiple SFS volumes.  If the volumes are anonymous then the user
has no easy way of informing SFS which one it should be accessing apart from
using the automount option with the SFS driver, which is explained in more
detail in the section "Advanced SFS Driver Options" below.  mksfs will check
for the creation of anonyous volumes on fixed disks and print a warning if this
occurs.

The volume name can be specified with the `vol=' option.  For example if the
volume name "Secure disk volume" was to be created on drive D: then the create
command would be:

  mksfs "vol=Secure disk volume" d:

Note that the volume name, which in this case contains spaces, has been quoted.
This is necessary since DOS will break apart the name into separate words if it
contains spaces.  If the name is a single word, no quoting is necessary.

The volume serial number can be specified with the `serial=' option.  If no
serial number is provided, mksfs will generate one itself.  In normal usage
there is no need for the user to specify a volume serial number, but the option
has been provided just in case.  If a serial number is specified, it should be
a unique value since SFS may use it to distinguish between different volumes.
If mksfs is left to chose the serial number it will automagically use a unique
value.  The serial number is independant of the volume automount identifier,
which is explained in the section "Advanced SFS Driver Options" below.

A special option for removable disks only is the `-o' option.  This is
necessary because some (mostly extinct) variants of DOS treat removable disks
in a peculiar manner.  If mksfs cannot determine the disk format due to the
disk having been created with a strange DOS version, it will exit with the
error message[1]:

  Error: Disk information reports unusual disk format, won't process disk.
         Use `-o' option to override this check.

If mksfs is re-run, this time with the `-o' option, it will perform a check on
secondary format information stored on the disk.  If the information checks
out, it will report (assuming the disk being checked is a 1.2 MB 5 1/4" disk):

  Warning: Disk information reports unusual disk format, performing check on
           secondary information...

           Disk appears to be in 1.2 MB DSHD format

If mksfs still can't be sure of the disk format, it will exit with an error
message.

If multiple-user access to the volume is required, the `multiuser' option
should be set to enable this.  This option records extra information which may
later be edited with the adminsfs program to allow other users access to the
volume.  More details on multiuser SFS volumes are given in the section
"Sharing SFS Volumes Between Multiple Users" below.

If the `multiuser' option is used, mksfs will warn:

  Warning: You have specified that access to the volume for multiple users
           be enabled.  Are you sure you want to do this [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

The program will now check to see whether the chosen volume name and serial
number conflict with the name and serial number of an existing volume.  If both
the volume name and serial number conflict, this will make future manipulation
of the volume difficult as there is no real way to uniquely identify it, and
mksfs will exit with the error message:

  Error: An SFS volume with the given name and serial number already exists.
         Either a new name or serial number should be chosen, or no serial
         number at all specified, in which case mksfs will chose a unique
         serial number for the new volume.

An alternative possibility, if the conflicting volume is on removable media, is
to temporarily remove the disk from the drive until mksfs has been run.
However this still creates the problem of accessing the volume in the future.
A much easier solution is to either chose unique volume names or to let mksfs
chose the volume serial number - it will always chose a number which doesn't
conflict with an existing volume serial number.

If only the volume name clashes, mksfs will warn:

  Warning: An SFS volume with the given name already exists.  Are you sure
           you want to create a new volume with the same name [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

If an anonymous volume is to be created on a fixed disk, mksfs will warn:

    Warning: You have not specified a name for the volume to be created.
             This may make future manipulation of the volume difficult.  Are
             you sure you want to create an anonymous volume [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

If it's really necessary, these checks can be overridden by using chsfs to
change the volume's characteristics after it has been created.  Unlike mksfs,
chsfs is not particular about what the volume name and serial number are set
to, as it assumes that the user knows what they are doing when they use chsfs.

Once the preliminary processing has been done, mksfs will, in the case of a
fixed disk, scan it for the volume which is to be converted into an SFS one.
Along the way it will perform various checks on the volume to make sure the
volume is accessible, is a standard DOS volume, is not marked as being bootable
(booting off an encrypted volume is somewhat difficult), is not the one
currently in use, and can be converted.  Note that the bootability check may
not be completely foolproof, as some disk managers perform strange tricks with
bootable volumes to handle multiple operating systems on the same disk.

mksfs performs an additional check if the volume specified for encryption is
the C: drive, which is usually the primary DOS drive and which should under
normal circumstances never be encrypted.  If an attempt to encrypt the C: drive
is made, mksfs will prompt:

  Warning: You have chosen to encrypt the C: drive which is usually the
           primary DOS drive.  Are you sure you want to do this [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

If the various checks succeed, it will display an informational message giving
details on the volume to be created.  An example of the information displayed
for a fixed drive might be:

  Volume `Encrypted disk' will be created on fixed drive D:
  This drive has a capacity of 75.2 MB and is labelled `Accounting'
  Are you sure you want to encrypt this volume [y/n]

If the volume is the one to be converted, a response of 'Y' will proceed with
the creation of the SFS volume, and a response of 'N' will abort the operation.

It is vitally important that the information printed by mksfs is checked before
a `yes' response is given.  Due to the vast array of unusual disk systems,
networked drives, compressed disks, device drivers, and other strangeness, it
could be that mksfs and DOS disagree on which volume is to be encrypted.  In
addition it is very easy to specify the wrong drive accidentally when running
mksfs.  Although this situation will hopefully never occur, it is nevertheless
a good idea to stop for a second and make absolutely certain that the volume
being encrypted is the one which should be encrypted.  Treat mksfs the same way
you would treat the DOS `format' command.

For a floppy drive the information is slightly different:

  Volume `Secure backup' will be created on 1.44MB disk in drive B:

No yes/no prompt is given for removable disks since they contain far less
information than fixed disk volumes, and will typically be freshly-formatted,
blank diskettes.  This allows the quick bulk encryption of quantities of
diskettes without having to answer the same question for each disk.  If
necessary the encryption operation can be aborted at the password-entry stage.

mksfs will now check the volume to be encrypted for bad sectors.  Most newer
fixed disks will automatically map out bad sectors (if there are any) and use
sectors from spare space on the disk instead (all this is invisible to the
system software and is done internally by the drive itself).  However older
drives may still explicitly report bad sectors.  The presence of bad sectors on
a disk may also indicate a virus infection, or may be used by certain kinds of
(hopefully extinct) copy-protection schemes.  If mksfs finds any of these, it
will print an advisory message:

  Warning: This disk contains bad sectors which won't be encrypted by SFS.

If the disk being encrypted is a floppy disk, mksfs will print a message
recommending that another disk be used instead.  If the data is valuable enough
to need encryption, then it should really be stored on an error-free medium
rather than its loss risked with defective floppy disks:

  Warning: This disk contains bad sectors.  Use of damaged disks is not
           recommended as recovery of encrypted data could be difficult if
           further bad sectors develop.  Are you sure you want to encrypt
           this disk [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.  SFS will encrypt the disk, but will skip any sectors marked as
being defective.  A similar message will be printed if any bad sectors are
found during the encryption process.  Note that if further bad sectors develop
on the floppy disk, recovery of the data stored in the bad sectors will be
difficult.  It is strongly recommended that only error-free floppy disks be
used with SFS[2].

Once the disk checks have been completed, mksfs will ask for a password to use
when encrypting the volume.  This password can range in length from 10 to 100
characters, and should be made up of a complete phrase or sentence rather than
just a single word (mksfs will complain if it thinks the password is of an
insecure form and request that another one be used).  More details on choosing
a password are given in the section "The Care and Feeding of Password" below.

When asking for the password, mksfs will prompt:

  Please enter password (10...100 characters), [ESC] to quit:

At this point a password in the given length range can be entered.  For
security reasons the password is not echoed to the screen.  Any typing errors
when entering the password can be corrected with the backspace key.  The Esc
key can be used to quit.  The software will check for a password longer than
the maximum of 100 characters or an attempt to backspace past the start of the
password, and beep a warning when either of these conditions occur.

Once the password has been entered, mksfs will again prompt:

  Please reenter password to confirm, [ESC] to quit:

This confirmation is necessary to eliminate any problems with hitting an
incorrect key when entering the password the first time.  Note that every
single letter, space, and punctuation mark in the password is critical.  Making
a single mistake (getting a letter mixed up, typing a letter in upper case
instead of lower case, or missing a punctuation mark) will completely change
the encryption key.  For this reason, mksfs performs a double-check on the
password to ensure it really is the correct one.

Once the password has been entered, there is a brief delay while mksfs performs
the complex processing needed to turn it into a key suitable for the encryption
system.  When this has been completed, mksfs will begin converting the disk.
As it processes the volume, it prints a progress bar going from 0% complete to
100% complete.  The conversion process will take a few minutes on most disks,
and is somewhat slower than a standard disk formatting procedure which only
writes a very small amount of data to the start of the disk, whereas mksfs has
to read, encrypt, and write the entire disk volume.

As the conversion progresses, the progress bar will gradually fill up until it
shows that the conversion is complete.  Once this has finished, mksfs will exit
with the message:

  Encrypted volume created.  You can now mount it with the `mountsfs' command.

If the volume is created on a fixed disk, additional information about mounting
it using the SFS driver's automount option will be given (this is explained in
more detail in the section "Advanced SFS Driver Options" below).

If the volume is created on a removable disk, mksfs will ask:

  Do you wish to encrypt another disk [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.  If the 'Y' response is chosen, mksfs will prompt:

  Please insert a new disk in the drive and press a key when ready

and then repeat the disk encryption cycle.

The encrypted volume is now ready to be used.  If it was created on a fixed
disk, DOS will still think the volume it was created on is a DOS one rather
than an encrypted SFS one.  It is strongly recommended that you reboot your
machine at this point to clear any memories of the old volume from the system,
as any attempt by DOS to access the encrypted volume as a normal DOS volume
will cause it to become very confused.

Footnote [1]: Certain boot sector viruses also change the information needed by
              mksfs, so mksfs printing this message may be an indication of a
              viral infection.

Footnote [2]: Although SFS has been written so that if any data does become
              corrupted, only the corrupted sector and no others will be lost,
              if data which is important to the operating system (such as a
              directory or a file allocation table) is lost, the damage may
              (just as it would for a normal non-encrypted disk) be more
              significant.  In this case any standard disk-recovery program can
              be used to make repairs, just as with a normal DOS disk.


Mounting an SFS Volume
----------------------

When the operating system first starts, it finds all disk volumes it can
recognise and automatically makes them available as different logical drive
letters.  However it can't do anything with encrypted SFS volumes, and so they
are effectively invisible to it.  In order to make them visible, they must be
mounted using the mountsfs program.  Operating systems such as Unix mount
filesystems in this manner (in fact the general feel of mountsfs is vaguely
like the Unix filesystem mount utility).

When the operating system mounts a disk volume, it uses the rather primitive
mechanism of assigning a letter of the alphabet to it and referring to the
drive by that letter.  SFS, on the other hand, refers to the volume by the name
given when the volume is created with mksfs rather than some arbitrary letter
(although volumes in removable drives can optionally be referred to by the
driver letter).  Therefore if the encrypted volume was named "Secure disk
volume", mountsfs would mount "Secure disk volume" rather than, say, "E:".  A
fixed disk can contain multiple encrypted volumes, mountsfs will chose the
appropriate one based on the volume name.  When searching for volumes to mount,
all fixed disks are checked before any removable disks are checked, so that a
volume with a given name on a fixed disk would override a volume of the same
name on a floppy disk.

Once the volume is mounted, DOS will still refer to it by a drive letter as
usual (there's only so much the SFS software can do), so that "Secure disk
volume" will, after being mounted with SFS, appear as another DOS drive, for
example E:.

With removable disks it may sometimes be desirable to refer to the volume by
the drive it is in rather than the volume name.  In this case the drive can be
specified by the usual letters A: or B:, and the actual volume name will be
ignored.  As before, once the disk is mounted with SFS, the volume will appear
as another DOS drive, for example E:.  If the disk is accessed as E:, the SFS
driver will encrypt and decrypt data being written and read.  If the disk is
accessed as A: or B:, DOS will either display garbage or report a general
failure error as it doesn't understand the encrypted disk. The A: or B: drive
letters can still be used to read normal DOS disks, however.  In order to
prevent accidental overwriting of disks, the SFS driver will automatically
unmount a volume if it detects that a disk change has occurred since the last
time it accessed the drive.

The mountsfs program is run in the following manner:

  mountsfs [+r] [+rw] [status] [unmount] [info] [information]
           [hotkey=<Ctrl>-<Alt>-<LeftShift>-<RightShift>-<letter>]
           [timeout=<timeout>] [user=<user name>] [userfile=<user file>]
           [vol=<volume name>] [<drive>]

Since all arguments are named, they can be given in any order.  The order shown
here is merely an example.

When mountsfs starts, it first performs a number of checks on the internal
status of the SFS driver.  If it can't find the driver, it will exit with the
error message:

    Error: Cannot find SFS driver

This is due to the driver not being loaded, either because it is not being
specified in the CONFIG.SYS file, or because there was some error when it was
loaded and it de-installed itself.  More information on this is given in the
section "Loading the SFS Driver" above.

If the driver reports a general internal consistency check failure or a
consistency check failure for a particular drive unit (in this case drive F:),
mountsfs will exit with the error message:

    Error: SFS driver internal consistency check failed

or:

    Error: SFS driver consistency check failed for unit F:

A driver check failure is generally due to some other program or system
software corrupting the driver's internal state.  Possible solutions to this
problem can be found in the section "Incompatibilities" below.

In general the volume name would be specified with the `vol=' option.  For
example if the volume name was "Secure disk volume" then the mount command
would be:

  mountsfs vol=secure

The volume name can be in upper or lower case, and the full name need not be
given.  mountsfs will match whatever part of the name is given to any SFS
volume names found until it finds a match.  The SFS volumes are checked in the
same order as they are displayed with the `info' or `information' command.

Alternatively, if the SFS volume to be accessed is on a removable disk, the
drive letter can be specified instead of the volume name.  For example if the
disk drive was A: then the command to mount whatever volume it contained would
be:

  mountsfs a:

mountsfs will not mount volumes using the automount ID, as this is reserved for
use with volumes mounted when the SFS driver is loaded.  More information on
this is given in the section "Advanced SFS Driver Options" below.

In order to find all available SFS volumes, the `info' option can be used.
This will by default search the system for available SFS volumes and print a
list of the volume name, creation date, size, and whether the volume is
currently mounted. For example on a system with two SFS volumes the output from
`mountsfs info' might be:

    Date     Size   Type Mount status  Volume Name
  -------- -------- ---- ------------- ----------------------------------------
  01/11/93  Floppy  DOS    Unmounted   Data backup
  06/09/93  10.0 MB DOS  Mounted as E: Personal financial records
  12/04/93  42.5 MB DOS    Unmounted   Encrypted data disk

This shows three SFS volumes, an unmounted volume in a floppy drive containing
backup data, a smaller one on a fixed disk containing personal financial
records which is currently mounted as drive E:, and a larger one containing
general encrypted data which is currently unmounted.  Note that removable media
is treated in a special manner and the exact disk size is indeterminate as the
media may change at any time.  The volume creation date is formatted according
to the country setting on the machine being used, so that the datestamp is
day/month/year in Europe and related countries, month/day/year in the US and
related countries, and year/month/day in Japan.  Both volumes shown here are
DOS volumes, but future versions of SFS will support other volume types such as
OS/2 HPFS, Windows NTFS, and Linux Unix ones.

If more information is desired, the longer "information" form of the command
can be used.  This will display extra information such as the volume serial
number, the automount parameter (see the section "Advanced SFS Driver Options"
below for more information), the volume filesystem type, whether multiuser
volume access is possible, and the volume name character set, as well as the
other information displayed by the usual `mountsfs info' command.  If, in the
previous example, we had used `mountsfs information' instead of `mountsfs info'
the output might have been:

  Volume name  : Data backup
  Volume date  : 01/11/93, 10:13:01  Volume serial number  : 1234
  Volume size  : Removable media     Volume filesystem type: DOS
  Mount status : Unmounted           No automount possible
  Multiuser access : Disabled        Volume name char.set  : ISO 646/ASCII

  Volume name  : Personal financial records
  Volume date  : 06/09/93, 11:22:19  Volume serial number  : 177545
  Volume size  : 10.0 MB             Volume filesystem type: DOS
  Mount status : Mounted as E:       Automount ID          : 03A12F7B
  Multiuser access : Disabled        Volume name char.set  : ISO 646/ASCII

  Volume name  : Encrypted data disk
  Volume date  : 12/04/93, 22:17:00  Volume serial number  : 69231461
  Volume size  : 42.5 MB             Volume filesystem type: DOS
  Mount status : Unmounted           Automount ID          : 42DD2536
  Multiuser access : Enabled         Volume name char.set  : ISO 646/ASCII

By default these two command will display information on all available volumes.
If information on an individual volume is required, then the volumes' name or
drive letter can be given in addition to the `info' or `information' option.
To change the previous use of the `info' command to apply only to the volume
named "Data backup", the command might be:

  mountsfs info vol=backup

and the output would be as follows:

    Date     Size   Type Mount status  Volume Name
  -------- -------- ---- ------------- ----------------------------------------
  01/11/93  Floppy  DOS    Unmounted   Data backup

The `status' option can be used to check whether any volumes are currently
mounted.  As with the `info' and `informaton' options, by default information
on all mounted SFS volumes is displayed.  If information on an individual
volume is required, then the volumes' name or drive letter can be given in
addition to the `status' option.  Thus the command:

  mountsfs status

will return a list of the status of the volumes on all mount points, as well as
an indication of the current setting of the quick-unmount hotkey and
auto-unmount time settings (the latter are explained in more detail below),
whereas the command:

  mountsfs status f:

will return the above status information only on the volume currently mounted
as F:.  An example of the output of the `status' command when run on the setup
shown in the `info' command examples with a total of two mount points available
might be:

  SFS volume `Personal financial records' is mounted as drive E:
  Drive F: has no volume mounted

  The quick-unmount hotkey is set to `LeftShift-RightShift'.
  The auto-unmount timer is deactivated.

The `+r' and `+rw' options specify read and write access to the encrypted
volume.  `+r' allows read-only access and `+rw' allows read and write access.
The default is to allow read/write access.  Note that although mounting an SFS
volume read-only will stop all standard software from writing to it, it may not
stop some malicious programs such as viruses which have been specially written
to attack the SFS driver itself, or which are created specifically to destroy
disk data by bypassing the operating system and accessing the disk hardware
or firmware directly.  The read-only option is provided mainly to stop any
accidental overwriting of valuable data on encrypted volumes.

Read-only access can also be specified when an SFS volume is auto-mounted.
More details on this and on auto-mounting volumes are given in the section
"Advanced SFS Driver Options" below.

The read/write status of a volume can be changed once it has been mounted by
running mountsfs with only the '+r' or '+rw' option.  This will change the
read/write status of the currently mounted volume as appropriate.  For example
to allow read/write access to the currently mounted SFS volume the command
would be:

  mountsfs +rw

If the volume allows multiuser access, only the volume administrator can
directly mount it in the manner described above.  Normal volume users must
specify their user name with the `user=<username>' command in addition to the
usual mount parameters in order to mount the volume[1].  The user name is the
name under which access is granted by the system administrator.  Like the
volume name, any portion of the user name can be given and mountsfs will match
whatever part of the name is given to any user names until it finds a match.
Users can also specify the name of the file to search for user access
information using the `userfile=<user file>' command.

For example if the volume in the previous example allowed multiuser access and
one of the users granted access to the volume was "Henry Akely", he could mount
it with the command:

  mountsfs vol=secure user=henry

If an attempt to mount a volume with no multiuser access capabilities is made,
mountsfs will exit with the error message:

  Error: This volume has multi-user access disabled

If access information for the given user cannot be found in the user access
file or files, the program will exit with an error message:

  Error: Cannot find access information for user `henry'

An individual users access rights to the volume, as set by the volume
administrator, may override certain options specified in mountsfs.  More
details on this, and on the operation of shared SFS volumes as a whole, are
given in the section "Sharing SFS Volumes Between Multiple Users" below.

If mountsfs is asked to mount a volume, it will first check to see whether
there is room to mount it.  If all available mount points are already occupied,
the program will print:

  Error: All available drives are allocated - unmount an existing volume first

and exit.  In this case either an existing volume must be unmounted to free up
a mount point and allow the new volume to be mounted, or the number of mount
points must be increased with the /UNITS command when the SFS driver is loaded.
More details on this are given in the section "Loading the SFS Driver" above.

If mountsfs is asked to mount a volume, it will search all available disks for
the named volume (if the volume is accessed by name), or check the removable
disk for the volume (if the volume is accessed by disk drive letter).  If the
volume is already mounted, mountsfs will print:

  Error: Encrypted volume is already mounted

and exit.  Otherwise, it will print a summary of the volume giving the
read/write status, the drive type, and the volume name and date if one exists:

  Volume will be mounted read-only as fixed drive E:.
  Encrypted volume is `Personal correspondence', created 12/08/93

Then it will prompt for the encryption password:

  Please enter password (10...100 characters), [ESC] to quit:

At this point a password in the given length range can be entered.  For
security reasons the password is not echoed to the screen.  Any typing errors
when entering the password can be corrected with the backspace key.  The Esc
key can be used to quit.  The software will check for a password longer than
the maximum of 100 characters or an attempt to backspace past the start of the
password, and beep a warning when either of these conditions occur.  Once the
password has been entered, mountsfs will process it and reprogram the SFS
device driver to reflect the change in status.

If the disk being mounted is a removable one, mountsfs will check that the
drive being used supports disk change checking.  This is necessary to ensure
that the wrong disk isn't accidentally accessed by the driver.  If the disk is
changed without first being unmounted, the SFS driver will automatically
unmount it the next time an attempt is made to access it[2].  However if the
drive doesn't support the disk change check (generally only rather old drives
have this problem), this automatic unmount won't be possible, and mountsfs will
warn:

  Warning: The floppy drive this volume is mounted on does not support disk
           change checking.  This means that great care must be taken to ensure
           the existing volume is unmounted (using either the `mountsfs' utility
           or the quick-unmount hotkey) when a new disk is inserted.

If the drive does not support the disk change check, it is essential that the
volume be unmounted when the disk is changed.  The easiest way to unmount a
volume is through the quick-unmount hotkey, which is explained in more detail
below.

The `unmount' option is used to unmounts SFS volumes.  This is used to remove
any access to volumes after any work which requires them has been completed, or
to free up a mount point so a new volume can be mounted.  If a particular SFS
volume is contained on a removable disk, it is a good idea to unmount the
volume if the disk in the drive is changed, although mounting a new volume will
automatically unmount the old volume.  The unmount operation can also be
performed using a quick-unmount hotkey which the SFS driver checks for (see
below).  Like the `status' and `information' command, the `unmount' command can
either apply to individual mounted volumes which are specified by their drive
letter, or to all volumes if no drive letter is given.

Unmounting a volume also signals the SFS driver software to write all data
still held in system buffers to disk and to erase any information it still
holds in memory.  It is therefore good practice to always unmount volumes as
soon as they are no longer in use in order to destroy any sensitive information
which may still be held by the SFS driver or in a system buffer.  For example
to unmount all currently mounted volumes the command would be:

  mountsfs unmount

To unmount the volume currently mounted as F: the command would be:

  mountsfs unmount f:

A faster way to unmount all volumes is to use the quick-unmount hotkey which
the SFS driver checks for and accepts in place of the standard unmount command.
This can be used both as a convenience to quickly and easily unmount all SFS
volumes, or as a safety feature to allow encrypted volumes to be instantly
unmounted if there is a danger of the data on them being compromised (this
option is generally unavailable under Windows - see the section
"Incompatibilities" below).

If no hotkey is currently set (either from a previous use of the mountsfs
command or through the use of the `HOTKEY=' option when the SFS driver is
loaded), mountsfs will install a default quick-unmount hotkey which is a
combination of the left and right shift keys.  On most keyboards these keys are
fairly large and easy to reach during normal typing.  When both shift keys are
pressed and released, all mounted SFS volumes will be unmounted as if a normal
unmount command had been issued via mountsfs, and a single beep will sound to
indicate that the unmount was successful.

Occasionally this default hotkey combination may clash with other software, or
it may be desirable to use another hotkey combination.  This can be set with
the `hotkey=' option, which may be used to specify any combination of the left
shift key, right shift key, control key, alt key, and a letter key[3].  The
keys are specified in the following manner:

    Alt key        = `alt'          Control key     = `ctrl'
    Left shift key = `leftShift'    Right shift key = `rightShift'
    Letter key     = `a'...`z'

Key combinations should be separated by hyphens, `-'.  The key names are not
case sensitive and can be given in upper or lower case, or a mixture of both.
If an unknown key name is used or the key names are not separated with hyphens,
mountsfs will complain:

  Error: Bad quick-unmount hotkey format

For example, to specify the use of the left shift and right shift keys as the
quick-unmount hotkey (the usual default setting), the command used in the
previous example would be changed to:

  mountsfs hotkey=LeftShift-RightShift vol=secure

To use the Control, Alt, and Z keys as the quick-unmount hotkey the command
would be:

  mountsfs hotkey=ctrl-alt-Z vol=secure

The hotkey value can also be altered without mounting any volumes.  This will
merely update the current hotkey without making any other changes.  For example
to set the right Shift, Control, and I keys as the quick-unmount hotkey (a
rather unwieldy combination), the command would be:

  mountsfs hotkey=rightshift-CTRL-I

Finally, the hotkey can also be specified when the SFS driver is loaded. More
details on this are given in the section "Advanced SFS Driver Options" below.

If the hotkey unmount is performed while the driver is accessing a volume, the
disk access will complete before the volume is unmounted.

The SFS driver can also automatically unmount volumes if they have not been
accessed for a certain amount of time.  This option is useful if there is a
chance that an interruption may call you away from a system with mounted SFS
volumes allowing others access to the encrypted data, or can simply be used as
a general safety precaution to automatically unmount the volumes after a
sizeable period of inactivity (this option is unavailable under Windows - see
the section "Incompatibilities" below).  However, care should be taken to allow
a large enough safety margin for the timeout, as having a volume take itself
offline five seconds before work is saved to it can be annoying.

When volumes are mounted using mountsfs, the time until they are automatically
unmounted can be set with the `timeout=' option, which is used to specify the
delay in minutes until the unmount takes place.  By default, no auto-unmount
timer is set.  For example, using the previous mount command but to have all
volumes automatically unmounted after 15 minutes of inactivity the command
would be:

  mountsfs timeout=15 vol=secure

The timeout period must be between 1 and 30,000 minutes (this means the upper
timeout limit is around three weeks).  If a timeout value of less than 1 minute
or greater than three weeks is given, mountsfs will exit with the error
message:

  Error: Timeout value must be between 1 and 30,000 minutes

If no accesses are made to any volumes within the given time period, the
volumes will be automatically unmounted.  Like the case when a hotkey unmount
is made, a single beep will sound to indicate that the unmount has taken place.

If the timed unmount is performed while the driver is accessing a volume, the
disk access will complete before the volume is unmounted.

Finally, if all is OK, mountsfs will print a short summary message for the
action taken.  For example if the command given was one to unmount all volumes,
with two volumes F: and G: of which only F: was currently mounted, the summary
would be:

  Volume F: has been unmounted
  Volume G: is already unmounted

Footnote [1]: Some versions of SFS will automatically know the users name when
              a volume is mounted.  Unfortunately the DOS version isn't one of
              these.

Footnote [2]: The driver checks for a disk change when a disk read or write
              attempt is made rather than whenever DOS performs a general disk
              check, as DOS may perform up to half a dozen consecutive disk
              checks before doing anything, which leads to a significant loss
              in performance.

Footnote [3]: The letter key is based on the US keyboard since the SFS driver
              must check for keyboard scan codes rather than actual character
              codes, which can differ slightly for some keyboards.


Advanced SFS Driver Options
---------------------------

The SFS driver supports several advanced options which can be used to customize
the operation of SFS.  These include the ability to mount SFS volumes
automatically when the driver is loaded, and the ability to change the
quick-unmount hotkey, the auto-unmount timeout, and the password prompt used
when automounting volumes.


Automounting SFS Volumes

SFS volumes can be automatically mounted when the system is started up rather
than having to be mounted through the mountsfs program.  This can be specified
using the `/AUTOMOUNT=identification number' option when the SFS driver is
loaded, in conjunction with the 8-digit volume identification number displayed
by mksfs when the encrypted volume is created or by using the `mountsfs
information' command.  The volume identifier is used to tell the SFS driver
which volume to load.  If the volume allows multiuser access, only the volume
administrator can automount it.  Normal volume users must follow the standard
volume mount procedure using mountsfs.  The operation of shared SFS volumes is
explained in more detail in the section "Sharing SFS Volumes Between Multiple
Users" below.

For example if mksfs displays the volume identifier `530A17FD' for a particular
volume then the command to automount this volume would be:

  DEVICE=SFS.SYS /AUTOMOUNT=530A17FD

If an incorrect volume identifier is given, the driver will display

  Error: Invalid automount ID, skipping automount

and skip the automount procedure.  If the volume identifier is correct, the
driver will locate the required volume on the disk and try to read in the
information needed to process it.  If this information cannot be read or is
incorrect, the driver will display:

  Error: Invalid SFS volume information, skipping automount

and skip the automount procedure.  If all is correct the driver will ask for
the password exactly as mountsfs would:

  Please enter password (10...100 characters), [ESC] to quit:

At this point a password in the given length range can be entered.  For
security reasons the password is not echoed to the screen.  Any typing errors
when entering the password can be corrected with the backspace key.  The Esc
key can be used to quit.  The software will check for a password longer than
the maximum of 100 characters or an attempt to backspace past the start of the
password, and beep a warning when either of these conditions occur.  Up to
three attempts at entering a correct password are allowed before the automount
is skipped.  If the Esc key is pressed the SFS driver will print:

  Aborted at user request

and skip the automount procedure.  Otherwise, once the password has been
entered, the SFS driver will process it and, if an incorrect password is
detected, will print:

  Error: Incorrect password, skipping automount

Otherwise the encrypted volume will be auto-mounted ready for use, with the
drive letter being the next available DOS drive.  In general the automount
procedure is the same as the one which mountsfs uses, except that the full
functionality of mountsfs is not available during the automount.  Once the
volume has been mounted and after the usual SFS installation message has been
displayed, the driver will display the DOS drive on which the encrypted volume
is mounted.  For example if the volume was available as drive G: the message
would be:

  Encrypted volume is now mounted as drive G:

If multiple volumes are to be automounted then then automount ID's should be
given in the order in which the mounts are to take place.  For example if a
second SFS volume with the volume identifier `4850414B' were to be automounted
then the previous example would change to:

  DEVICE=SFS.SYS /AUTOMOUNT=530A17FD /AUTOMOUNT=4850414B

As more volumes are mounted, the driver will automatically increase the mount
point allocation until the maximum number of 5 mount points has been reached.
If an attempt is made to automount more than 5 volumes, the driver will print:

  Error: No more disk units available for automount

and skip the automount procedure.


Setting the Quick-Unmount Hotkey Value

When a volume is mounted, the quick-unmount hotkey is by default set to a
combination of the left and right shift keys.  However, like the mountsfs
`hotkey=' option, the SFS driver supports user-defined hotkeys with the
`/HOTKEY=quick-unmount hotkey' command.  This may be used to specify any
combination of the left shift key, right shift key, control key, alt key, and a
letter key, in the following manner:

    Alt key        = `alt'          Control key     = `ctrl'
    Left shift key = `leftShift'    Right shift key = `rightShift'
    Letter key     = `a'...`z'

Key combinations should be separated by hyphens, `-'.  The key names are not
case sensitive and can be given in upper or lower case, or a mixture of both.
If an unknown key name is used or the key names are not separated with hyphens,
the SFS driver will complain:

  Error: Bad quick-unmount hotkey format

For example, to specify the use of the left shift and right shift keys as the
quick-unmount hotkey (the usual default setting), the command used in the
previous example would be changed to:

  DEVICE=SFS.SYS /AUTOMOUNT=530A17FD /HOTKEY=LEFTSHIFT-RIGHTSHIFT

To use the Control, Alt, and Z keys as the quick-unmount hotkey without
automounting any volumes the command would be:

  DEVICE=SFS.SYS /HOTKEY=CTRL-ALT-Z


Changing the Automount Password Prompt

In some environments it may be undesirable to alert others to the fact that
disk encryption is being used.  Using the /SILENT option with the driver
removes most indications of the presence of SFS, but if volumes are automounted
the appearance of the password prompt may still give things away.  To correct
this problem, the SFS driver supports user-definable prompts with the
`/PROMPT=user-prompt' command.  This may be used to specify any single-word
prompt, or, if the prompt is surrounded by quotation marks `"', any combination
of characters until another `"' is encountered.  For example to make the SFS
automount procedure appear like a network login, the previous automount example
might be changed to:

  DEVICE=SFS.SYS /SILENT /PROMPT=Login: /AUTOMOUNT=530A17FD

Instead of the usual password prompt, the driver would now display:

  Login:

when the password was required.

If a prompt containing multiple words is required, the prompt itself would be
surrounded with quotation marks:

  DEVICE=SFS.SYS /SILENT /PROMPT="Please log on:" /AUTOMOUNT=530A17FD

To print a line break as part of a prompt, the escape code '\n' may be used,
allowing prompts to be split over multiple lines, or simply to have blank lines
as part of the prompt.  An extended form of the above prompt, split over two
lines, could be given as:

  DEVICE=SFS.SYS /SILENT /PROMPT="Network logon\nPlease enter password:"
                         /AUTOMOUNT=530A17FD

which would be printed as:

  Network logon
  Please enter password:

The order in which these arguments are given is important, since an option only
takes effect once the driver has processed it.  If the /PROMPT option is given
after the /AUTOMOUNT option, the driver won't use the new prompt until after
the automount has taken place.  This can be used to allow multiple independant
prompts when several volumes are mounted, so that in the following example:

  DEVICE=SFS.SYS /SILENT /PROMPT="Local server logon: " /AUTOMOUNT=130D2C17
                         /PROMPT="Printer server logon: " /AUTOMOUNT=2A1102D3

the prompt "Local server logon: " would be used for the first volume to be
automounted and the prompt "Printer server logon: " would be used for the
second volume to be automounted.


Changing the Automount Read/Write Access Status

Write access to an automounted volume can be disabled in the same manner as
using the `mountsfs +r' options would (more information on read-only access to
SFS volume is given in the section "Mounting an SFS Volume" above).  For
example to automount the volume used in the previous example read-only the
command would be:

  DEVICE=SFS.SYS /READONLY /AUTOMOUNT=530A17FD

Like the automount /PROMPT option, the /READONLY option must be given before
the /AUTOMOUNT which it is to affect.

Read/write and readonly access to multiple automounted volumes can be
selectively turned on and off using the /READWRITE and /READONLY commands.  A
/READWRITE or /READONLY command applies for all automounts which follow it
until another /READWRITE or /READONLY command is encountered.  For example to
mount the first volume in the previous example read-only and the second one
with normal write access the command would be:

  DEVICE=SFS.SYS /READONLY /AUTOMOUNT=530A17FD /READWRITE /AUTOMOUNT=4850414B


Setting the Auto-unmount Timeout value

The auto-unmount timeout value functions just like the mountsfs `timeout='
option, and is used to tell the SFS driver to unmount volumes automatically if
they have not been accessed for a certain amount of time.  The time until
volume are automatically unmounted can be set with the `/TIMEOUT=' option,
which is used to specify the delay in minutes until the unmount takes place.
This option can only be used in conjunction with the `/AUTOMOUNT=' option, and
by default no auto-unmount timer is set.

Using the previous automount example, but to have volumes automatically
unmounted after 15 minutes of inactivity, the command would be:

  DEVICE=SFS.SYS /AUTOMOUNT=530A17FD /TIMEOUT=15

The timeout period must be between 1 and 30,000 minutes (this means the upper
timeout limit is around three weeks).  If a timeout value of less than 1 minute
or greater than three weeks is given, mountsfs will exit with the error
message:

  Error: Timeout value must be between 1 and 30,000 minutes

If no accesses are made to any volume within the given time period, all volumes
will be automatically unmounted.  Like the case when a hotkey unmount is made,
a single beep will sound to indicate that the unmount has taken place.


Changing the Characteristics of an SFS Volume
---------------------------------------------

Once an SFS volume has been created, various characteristics of the volume and
the entire volume itself can be altered using the chsfs program.  This allows
the SFS volume password, volume name, and volume serial number to be changed,
allows SFS volumes to be quickly deleted, and allows the reversion of SFS
volumes to their original unencrypted form.

The chsfs program is run in the following manner:

  chsfs [newpass] [newvol=<new volume name>] [newserial=<new serial no>]
        [delete] [convert] [vol=<volume name>] [<drive>]

Since all arguments are named, they can be given in any order.  The order shown
here is merely an example.

In general the volume name would be specified with the `vol=' option.  For
example if the volume name was "Secure disk volume" then the command would be:

  chsfs <command> vol=secure

The volume name can be in upper or lower case, and the full name need not be
given.  chsfs will match whatever part of the name is given to any SFS
volume names found until it finds a match.

Alternatively, if the SFS volume to be accessed is on a removable disk, the
drive letter can be specified instead of the volume name.  For example if the
disk drive was A: then the command would be:

  chsfs <command> a:

In order to find all available SFS volumes on all disks, the `mountsfs info'
option can be used as outlined in the section "Mounting an SFS Volume" above.

The basic characteristics of the SFS volume can be changed with the `newpass',
`newserial', and `newvol' commands, which set a new password, new serial
number, and new volume name respectively.  These commands can each be used
individually, or two or even all three may be used together (although they
can't be used in conjunction with the `delete' or `convert' options).  Their
usage is in general similar to their use with mksfs.  `newpass' takes no
arguments and will prompt for the original password and then the new password,
after which it will change the volume password from the original to the new
one.  `newserial' takes as an argument the new serial number to use for the
volume'  `newvol' takes as an argument the new volume name.  For example to
change the name of the SFS volume "Personal data" to "Letters" and the serial
number to 1234, the command would be:

  chsfs vol=personal newvol=Letters newserial=1234

If the newpass option is used, chsfs will first ask for the old poassword:

  Please enter old password (10...100 characters), [ESC] to quit:

After verifying that the password is correct, chsfs will ask for the new
password:

  Please enter new password (10...100 characters), [ESC] to quit:

Like mksfs, chsfs will then ask for this password a second time for safety.

Once the details for the new volume name, serial number, or password have been
obtained and the changes made to the volume, chsfs will display a message
indicating the changes made.  For the above example the message would be:

  Volume characteristics successfully updated.

  New volume name is `Letters'.
  New volume serial number is `1234'.

Note that chsfs doesn't perform the checking for duplicate or nonexistant
volume names and serial numbers which mksfs does.  This is to allow the safe
choices forced by mksfs to be subsequently overridden using chsfs if
required[1].

Changes to the SFS volume itself are made using the `convert' and `delete'
commands.  `convert' converts a volume back to its original unencrypted form,
and `delete' deletes it entirely, leaving behind what appears to the operating
system as an unformatted disk filled with random noise.

Since converting or deleting a volume while it is mounted is rather dangerous,
chsfs checks whether the volume to be converted or deleted is currently
mounted.  If it is, it will prompt:

  Warning: This volume is currently mounted.  Do you wish to unmount it
           and continue [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.  If a 'N' response is entered, the volume can be unmounted using
mountsfs or the quick-unmount hotkey before chsfs is re-run.

The delete option will first print the name and creation date of the SFS volume
to be deleted.  At this point the exact name and date of the volume should be
checked to ensure that this is indeed the one to be deleted.  In this example
the volume information will be displayed as:

  Encrypted volume is `Incriminating evidence', created 04/11/93

chsfs will now prompt for the password in the usual manner.  It uses this to
check that access to the volume is legitimate, and is needed for chsfs to
acquire various pieces of information it needs to perform the deletion.  The
program will then prompt:

  Warning: The deletion operation will permanently destroy all data on this
           volume.  Are you sure you want to continue with the deletion [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

If chsfs is told to continue, it will perform multiple overwrite passes over
the SFS volume header (which contains all the information needed to access the
volume), printing a progress report as it performs the overwriting:

  Overwriting: Pass 1

In total chsfs will perform 30 separate overwrite passes which have been
selected to provide the best possible chances of destroying data for various
disk encoding schemes (the exact details are given in the section "Deletion of
SFS Volumes" below).  Once the multiple overwrites have completed, chsfs will
print an informational message about the deletion operation:

  Encrypted volume `Incriminating evidence' has been destroyed

If the volume is on a fixed disk, you may wish to reboot your machine to make
the newly-deleted volume visible to DOS.  Volumes on floppy disks will
automatically be visible.  Since the disk volume is now filled with random
garbage, it will need to be formatted in the same way an unformatted disk would
be before it can be used by DOS.

The convert option will, like the delete option, first print the name and
creation date of the SFS volume to be converted.  At this point the exact name
and date of the volume should be checked to ensure that this is indeed the one
to be converted.  In this example the volume information will be displayed as:

  Encrypted volume is `Disk data', created 07/12/93

chsfs will prompt for the encryption password exactly as mksfs did when it
originally created the SFS volume, and will then prompt:

  Warning: You are about to convert this volume from an encrypted SFS one to
           a normal DOS one.  Are you sure you want to continue with the
           conversion [y/n]

At this point a response of 'Y' will continue and a response of 'N' will exit
the program.

Like mksfs, chsfs will then begin converting the disk.  As it processes the
volume, it prints a progress bar going from 0% complete to 100% complete.  The
conversion process will take a few minutes on most disks, and is somewhat
slower than a standard disk formatting procedure which only writes a very small
amount of data to the start of the disk, whereas chsfs has to read, decrypt,
and write the entire disk volume.

As the conversion progresses, the progress bar will gradually fill up until it
shows that the conversion is complete.  Once this has finished, chsfs will
display the message:

  Encrypted volume `Disk data' has been converted to a normal DOS volume.

The converted volume is now ready to be used as a normal DOS disk again. If the
volume is on a fixed disk, DOS will still think it is an encrypted SFS one
rather than a normal DOS one.  It is recommended that you reboot your machine
at this point to clear any memories of the old volume from the system, as DOS
will not be able to see the converted volume until the reboot takes place.  As
a reminder, chsfs will display:

  You may wish to reboot your machine to update the status of the volume,
  which will become available as a standard DOS disk.

before exiting.  If the volume is on a removable disk, no reboot is necessary
and chsfs will simply print:

  The volume is now available as a standard DOS disk.

Footnote [1]: This makes the (possibly incorrect) assumption that the chsfs
              user knows what they are doing.


Sharing SFS Volumes Between Multiple Users
------------------------------------------

At times it may be necessary to share a single encrypted SFS volume between
multiple users.  For instance several individuals may require access to a
volume containing confidential business correspondence as part of their
day-to-day duties.  Usually this would require using a common password which is
known to every member of the group of people who require access.  The need to
share passwords is a serious weakness, as the inability to chose individual,
unique passwords increases the chances that a simple, easy-to-remember (and
easy-to-guess) password is chosen, or that at least one person writes it down
if it is too hard to remember.

SFS solves this problem by allowing each member of the group access to an
encryped volume under their own individual password.  The allocation of access
rights to a volume is controlled by an administrator who can grant or revoke
access as required.  The administration process is handled by the adminsfs
program, which is run in the following manner:

  adminsfs [adduser=<user name>] [deluser=<user name>]
           [chuser=<user name>] [showuser=<user name>] [showall]
           [validfrom=<DDMMYY>] [validto=<DDMMYY>] [userfile=<user file>]

Since all arguments are named, they can be given in any order.  The order shown
here is merely an example.

[!!!! That's all there is at the moment.  adminsfs is still being checked
      out by beta-testers and parts of it are still under review.  If anyone
      has any suggestions for it, let me know !!!!]


Creating Compressed SFS Volumes
-------------------------------

Creating a compressed drive inside an SFS volume provides, apart from the usual
benefit of increasing the apparent disk space, some additional security against
an attack by breaking up the very regular standard filesystem structure
containing large quantities of known data at known locations into a compressed
filesystem whose structure and contents are much harder to guess.

The instructions given here are for Stac Electronics "Stacker"[1], although it
should be possible to do the same thing with other reasonably advanced disk
compressors.  Stacker should be installed in the usual manner onto a mounted
volume.  The Stacker driver can then be loaded in two ways, either from
CONFIG.SYS onto an automounted SFS volume, or at a later point (which, however,
means that it loads an extra copy of the command interpreter).  It is also
possible to load the driver from CONFIG.SYS without activating a compressed
drive, and activate it later.  This avoids the need to automount an SFS volume
at startup.

As SFS uses whatever drive letters DOS allocates to it, the stacked drive will
take over the drive letter used by the SFS volume rather than swapping drive
letters for the stacked and normal drive as it usually does.  This shouldn't
provide any problems, the compressed and encrypted drive will simply replace
the encrypted drive.

Footnote [1]: Specifically, Stacker 3.1


WinSFS - Using SFS with Windows
-------------------------------

WinSFS is a prototype of the Windows version of SFS, and currently runs as a
front-end for mountsfs, which means that the mountsfs program must be either in
the DOS path or in the Windows directory for WinSFS to work.  WinSFS also needs
the Visual Basic library VBRUN200.DLL in order to run.  This file is publicly
available from a number of sources.

When run, WinSFS will display a window containing a list of SFS volumes
available to be mounted, a list of currently mounted volumes, and an icon bar
which is used to control WinSFS.  These icons perform the following functions:

  Cross icon        : Exit WinSFS
  Disk icon         : Mount an SFS volume
  Crossed disk icon : Unmount an SFS volume
  Information icon  : Display detailed information on an SFS volume
  Write icon        : Enable read/write access on an SFS volume
  Crossed write icon: Enable read-only access on an SFS volume


Mounting a Volume with WinSFS

To mount an SFS volume, click on the volume name in the "Available volumes"
window, and then click on either the "Mount volume" icon or the "Mount" button
(eventually this function will also be available by dragging the volume name
and dropping it into the "Mounted" list).  WinSFS will ask for the volume
password, and then mount the volume.  Once the volume is mounted, its name will
disappear from the "Available volumes" list and appear in the "Mounted" list).


Unmounting a Volume with WinSFS

To unmount an SFS volume, click on the volume name in the "Mounted" window, and
then click on either the "Unmount volume" icon or the "Unmount" button
(eventually this function will also be available by dragging the volume name
and dropping it into the "Available volumes" list).  WinSFS will unmount the
volume, and its name will disappear from the "Mounted" list and appear in the
"Available volumes" list).


Getting Information on a Volume with WinSFS

To get detailed information on a volume, click on its name, and then either
click the right mouse button, or select the "Information" icon.  This will
bring up a window giving extra information on the volume such as the creation
time, serial number, size, and automount ID.


Setting a Volume's Read/Write Access with WinSFS

To change the read/write status of an SFS volume, click on its name in the
"Mounted" window, and then click on either the "Read-only" or "Read/write" icon
in the icon bar to change its access status.


Command Summary
---------------

This section serves as a quick-reference for the options available with the
various SFS programs.  The available options for mksfs, mountsfs, chsfs, and
adminsfs are:

MakeSFS - Make Secure Filesystem

  -c = Perform a confidence test on the volume to be encrypted without
       actually encrypting it
  -o = Override the disk boot record sanity check - may be necessary for
       some unusual disk formats
  -t = Test the integrity of the MDC/SHS encryption code used in SFS

  multiuser       = Allow multiuser access on the volume to be created

  vol=<volume name>      = Specify the name of the volume to be created
  serial=<serial number> = Specify the serial number of the volume to be created
  <drive letter>         = Specify the letter of the drive to create the
                           encrypted volume on

MountSFS - Mount Secure Filesystem

  +r  = Mount the encrypted volume with read-only access
  +rw = Mount the encrypted volume with read/write access (default)

  info          = Show brief information on all available SFS volumes
  information   = Show detailed information on all available SFS volumes
  status        = Show information on mounted volumes only
  unmount       = Unmount the volume

  hotkey=<hotkeys>    = Set the quick-unmount hotkey combination
  timeout=<timeout>   = Set the auto-unmount timer value in minutes
  user=<username>     = Specify the user name for a volume with multiuser access
  userfile=<filename> = Specify the path to the information file associated with
                        a volume which allows multiuser access
  vol=<volume name>   = Specify the name of encrypted volume to mount
  <drive letter>      = Specify the drive letter of the volume to mount
                        (For volumes on floppy disks only)

ChangeSFS - Change Secure Filesystem

  newpass               = Set a new volume password
  newvol=<volume name>  = Specify the new volume name
  newserial=<serial no> = Specify the new volume serial number

  delete    = Delete SFS volume
  convert   = Convert volume back to unencrypted form

  vol=<volume name>   = Specify the name of the encrypted volume to change
  <drive letter>      = Specify the drive letter of the volume to change
                        (For volumes on floppy disks only)

AdminSFS - Administrate SFS User Database

  adduser=<user name> = Add a new user with the given name to the database
  deluser=<user name> = Remove user with the given name from the database
  chuser=<user name>  = Change user database entry for the named user
  showuser=<user name>= Show access information for a given user
  showall             = Show access information for all users

  validfrom=<DDMMYY>  = Set date after which access for a user is allowed
  validto=<DDMMYY>    = Set date at which a users access expires

  userfile=<filename> = Specify the path to the user information file


Incompatibilities
-----------------

Over the years a variety of strange hardware and software setups have been
created in order to get around some of the shortcomings of the PC hardware and
DOS (and occasionally other operating systems) software.  Since SFS accesses
the disk at a level below that normally used by the operating system, it will
bypass special options like compressed volumes and non-local networked drives,
and won't recognise nonstandard hardware like drives with more than 1024
cylinders which require special software patches in order to work with DOS.
For example, SFS will recognise the uncompressed volumes used by Stacker and
DoubleSpace, but won't see the compressed volumes as these are an illusion
created in software and visible only to DOS.  It is therefore not possible to
encrypt compressed volumes (there would be very little point, as encryption
would render the data completely uncompressible), although it is possible to
create a compressed volume inside an encrypted volume (this is covered in the
section "Creating Compressed SFS Volumes" above).


Checking for Problems with mksfs

If your system has an unusual setup, or if you're worried about what SFS may
do, you can use a special option with the mksfs command to perform a check on
the drive which is to be encrypted.  This option also bypasses a number of the
usual checks SFS performs relating to duplicate volume names, anonymous
volumes, and so on, to allow all types of volume arrangements to be checked.

If the `-c' option is specified along with the drive letter, mksfs will (if the
volume in question is a fixed disk) first display technical information on all
available fixed disk volumes, so that the command:

    mksfs -c e:

would produce the following output:

  Drive partition information follows:

  Ph Bt Dr Cyl. Head Sec. Cyl. Head Sec.  Size  ID Type
  -- -- -- ---- ---- ---- ---- ---- ---- ------ -- ----
   0  N  C    0    1    0  379   15   39 121600 06 DOS (16-bit FAT, >= 32M)
   0  Y  -  380    0    0  383   15   39   1280 0A OS/2 boot manager
   0  N  D  384    1    0  594   15   39  67200 06 DOS (16-bit FAT, >= 32M)
   0  N  E  595    1    0 1022   15   39 136640 06 DOS (16-bit FAT, >= 32M)
                                                   This would be the SFS disk

This information is only displayed for fixed disks, as floppy disks don't
contain this information.  The values in the various columns are Ph = physical
drive number, Bt = bootable flag, Dr = DOS drive letter, Cyl,Head,Sec =
partition start, Cyl,Head,Sec = partition end, Size = size in kbytes, ID =
partition ID byte, and Type = partition type.  The proposed SFS partition will
be marked as such.  If you don't know what these values mean, don't worry -
this option is mainly useful in providing technical information for those who
want it.

In addition, mksfs may display specific information about the drive on which
the SFS volume is to be created.  Typically the message will be something like:

  The drive is a WDC AC2420 with a dual ported multi-sector
  cacheing 256K buffer which supports high-speed direct access.

This indicates that the drive will work with a faster direct-access version of
the SFS driver.  This is still being tested, and should provide a noticeable
performance improvement over the current version.

Once all drives have been checked, more specific information on the actual
volume in question is displayed:

  Volume will be checked on fixed drive E:
  This drive has a capacity of 136.6 MB and is labelled `Data disk'
  Are you sure you want to check this volume [y/n]

As with the usual mksfs process, typing 'Y' will continue with the volume check
and typing 'N' will exit.  If you choose to continue, mksfs will first perform
an initial disk confidence test which consists of some general checks on the
volume layout to make sure its format is valid, and will then perform a read
confidence test in which it reads random disk blocks and compares them with the
data reported by the operating system.  If any errors are encountered, it will
print a diagnostic message before continuing.  If all is OK, the sequence of
messages will be:

  Performing disk confidence test...
  Performing read confidence test...
  [various test-in-progress messages]
  Confidence test successfully concluded

If there are problems, the diagnostic message will give more information on the
nature of the problem.  Once the test has concluded, an error count will be
displayed.  In either case, mksfs will exit after the tests have concluded
without creating the encrypted volume.  If used with the `-c' option, mksfs
will never modify any information on disk, whether the tests are successful or
not.  This is important, as it allows a confidence test to be performed before
an encrypted volume is created.


Problems with Windows

The timed auto-unmount option and quick-unmount hotkey option are generally
unavailable under Windows as Windows disables the standard keyboard and timer
handling when it runs[1].  In order to unmount a volume from within Windows,
the mountsfs program must be run explicitly.  The one exception to this rule is
that if a quick-unmount hotkey is set from within a DOS session then it will
remain available (but only within the DOS session) while that particular DOS
session is active.


Problems with Other Software

The Mitsumi CDROM device driver, if installed before another block driver like
SFS, will mistakenly try to use the drive letter allocated to the other driver
as its own one.  There have been reports of other CDROM drivers (in particular
the Sony one) which display similar traits (CDROM drivers are strange beasts
which have rather special requirements).  The DTC SCSI driver has a similar
problem in that it grabs more drive letters than DOS allocates to it, which
means that any block drivers loaded after it will be allocated drive letters by
DOS which are already being used by the SCSI driver.  The solution to this
problem is to make sure that the SFS driver is loaded before any problematic
CDROM or SCSI drivers by placing the DEVICE=SFS.SYS line before the one which
loads the CDROM or SCSI driver in the CONFIG.SYS file.

The KEYB driver incorrectly handles the keyboard interrupt, which locks out the
SFS driver's quick-unmount hotkey handling if the `HOTKEY=' option is used at
the time the driver is loaded.  If the `HOTKEY=' option is *not* specified when
the SFS driver is loaded, but is set later (after the KEYB driver has been
loaded) using mountsfs, everything works fine.

Some (now very rare) device drivers and TSR's will destroy the contents of
32-bit registers when they are activated, which means that the data in the SFS
driver will become invalid from one machine instruction to the next.  There
have been reports of older versions of the PC-Kwik cache and Novell's
non-dedicated file server version 2.2 doing this.  A program to detect and
possibly fix this problem is:

    garbo.uwasa.fi:/pc/turbopas/trash.zip

Some of the Borland software development tools don't handle DOS critical errors
very well (they hang either when the error occurs or soon afterwards).  Since
trying to access a non-mounted volume is treated by DOS as an error, it may
cause programs like the IDE and the debugger to hang.  Trying to read a floppy
drive without a disk in the drive, and any other action which causes a DOS
critical error, can have the same effect.


Problems with hardware

Some floppy drive and system BIOS combinations aren't terribly reliable.  It
has been reported that a laptop using the Phoenix 1.01 BIOS gives a multitude
of disk errors when encrypting a disk using mksfs.  The exact error type is
uncertain since the error code returned when the disk access fails is an
undefined value.  The Award 3.03 BIOS when used with some floppy drives also
causes problems, especially with newer versions of DOS (version 6.0 and up),
which may have great trouble reliably writing disks.  Microsoft's suggested
solution to the problem is a BIOS upgrade.

Footnote [1]: Windows virtualizes the keyboard and timer interrupts and locks
              out SFS.  Although it is possible to bypass this, it must be done
              from within Windows itself, which is not possible for a device
              driver like SFS.


Authentication of SFS Software
------------------------------

There have been several occasions in the past when fake versions of software
have been distributed.  Sometimes these fake release are even wrapped up in a
nice-looking "security envelope" guaranteeing their authenticity.  With
encryption software like SFS it is all too tempting for an opponent to simply
create and distribute a compromised version of SFS rather than try to break the
SFS encryption itself.  In order to avoid any problems in this respect, the
distributed SFS driver and executables are accompanied by a digital signature
which can be used to verify that it is indeed an official version.

In order to check the authenticity of the particular version of SFS, you will
need the PGP encryption package, and my public key, which is included in the
standard PGP distribution.  My key is signed by Philip Zimmermann, the original
author of PGP, and several members of the PGP development team.  First, my key
should be checked for authenticity with the command:

  pgp -kc "Peter Gutmann"

When it performs the key check, PGP should display the following signatures:

  Type bits/keyID     Date    User ID
  pub  1024/997D47 1992/08/02 Peter Gutmann <pgut1@cs.aukuni.ac.nz>
  sig!      E722D9 1992/11/26   Branko Lankester <lankeste@fwi.uva.nl>
  sig!      997D47 1992/10/11   Peter Gutmann <pgut1@cs.aukuni.ac.nz>
  sig!      7C02F9 1992/09/07   Felipe Rodriquez <nonsenso@utopia.hacktic.nl>
  sig!      1336F5 1992/09/05   Harry Bush <Harry@castle.riga.lv>
  sig!      67F70B 1992/09/02   Philip R. Zimmermann <prz@sage.cgd.ucar.edu>

There may be other signatures on there, but these are the ones from the PGP
development team and are the most important ones.  Version 2.1 and up of PGP
can, in addition, generate a key fingerprint for a key.  This can be calculated
with the command:

  pgp -kvc "Peter Gutmann"

PGP should display the following:

  pub  1024/997D47 1992/08/02 Peter Gutmann <pgut1@cs.aukuni.ac.nz>
            Key fingerprint = 7C 6D 81 DF F2 62 0F 4A  67 0E 86 50 99 7E A6 B1

If the keyID or key fingerprint for my key differs from the one shown above or
the signatures don't check out, then the key is a probably a fake and shouldn't
be trusted.  Assuming the key is in order, the authenticity of the device
driver and the support software can be checked with:

  pgp sfs.sig sfs.sys
  pgp <program>.sig <program>.exe

where sfs.sig and <program>.sig are the digital signatures included with SFS as
distributed.  For example to check the authenticity of the mksfs program type:

 pgp mksfs.sig mksfs.exe

When it performs the check, PGP should display:

  Good signature from user Peter Gutmann <pgut1@cs.aukuni.ac.nz> .
  Signature made <date of signature>

If PGP reports a bad signature then the executable shouldn't be trusted.  A
new, hopefully untouched, version can be obtained from any archive site, BBS,
or system which carries the standard SFS distribution, or it can be obtained
directly from the author.


Applications
------------

Apart from the simple use of SFS for personal and business data privacy, there
are a number of other possible applications for which it can be used.  Some of
these are listed below.


Secure Information Exchange

If a communications channel is available between two systems which use SFS,
confidential data can be transferred from one encrypted SFS volume to the other
by using encryption on the communications channel.  For example a businessman
whose work involves a lot of travel could read data off the SFS volume on his
portable computer and encrypt it as it is sent via modem to his place of work.
At work the data could be decrypted and written to another SFS volume.  The
only time the data is available in unencrypted form is while it is being read
off the SFS volume and re-encrypted for transmission, which represents a
minimal risk as interrupting the transmission will involve stopping the program
which will (presumably) contain error handlers which erase any sensitive
information from memory.

Using a package like PGP (Pretty Good Privacy) or PEM (Privacy-Enhanced Mail)
in conjunction with SFS allows the secure distribution of information through
an online service like a computer bulletin board.  The online system can
retreive the public key of the person requesting the information, read the
required data off the SFS volume into the encryption program where it is
encrypted with the recipients public key, and transmit it.  At the other end
the recipient decrypts the data with their private key and writes it straight
onto their own SFS volume.  Again, the amount of time in which unencrypted data
is available is minimal, and properly implemented software will destroy any
sensitive information if interrupted in any way.


Defence in Depth

With the increasing strength of cryptographic software which is becoming
available to the public, means of compromising encryption security which don't
involve breaking the encryption itself are becoming more and more desirable.
This may involve things like creating fake versions of the encryption software
which have trapdoors in them and planting them in a victims system, planting
versions which save the entered password somewhere and then restore the
original unaltered copies, or similar tricks.  This means that for maximum
security it is necessry to not only protect the password, but also to protect
the encryption software itself, and any software which interacts with it, and
anything which interacts with that, ad nauseum.  If several encryption and
security packages are used, every one of these must be protected separately.

By using SFS, some degree of protection is offered against malicious
manipulation, since an attacker must first get to the software stored on an SFS
volume in order to compromise it.  Storing other security-related software on
an encryption volume takes it out of the reach of any attack, but makes the SFS
software itself more of a target for an attack.  Eventually this problem can be
reduced somewhat through the use of SFS encryption hardware, which is currently
under (very gradual) development.  Another possibility is to store duplicate
copies of the SFS software on an encrypted volume which is initially mounted
read-only.  The versions on the SFS volume can be compared (using software also
stored on the SFS volume) with the unencrypted versions, and if they are
identical to the reference versions, write access to the volume can be enabled
and the volume used as normal.  Another possibility is to simply store
checksums or digital signatures for the SFS programs on the encrypted volume,
and only write-enable it if the checksums or signatures check out.

Using SFS for Virus Protection

SFS can be used as a form of virus protection for large collections of
computers by using it to create a centralised entry point to the system for all
data.  Consider a company operating 1,000 separate machines.  Normally this
would require 1,000 copies of a virus scanner to be installed and updated every
few months as new viruses appear.  In addition, use of the scanner on every one
of the 1,000 machines would have to be enforced rigorously.

An alternative is to install SFS on each of the machines, and make a policy
that only SFS-encrypted disks will be used within the company.  Then a single
scanner can be installed on a single machine, and all disks brough in from the
outside scanned and encrypted on that machine.

If every computer is initially virus-free, and all disks are SFS-encrypted,
then there are two possible means of attack for a virus.  The first is to
infect a file or a disk when it is outside the company.  However as disks
originating from within the company are encrypted, no files (or, indeed,
anything) are visible on it, so there is nothing for a virus to infect (in
fact, DOS won't even recognise the disk as being formatted).  All disks
originating from outside the company have to be processed by the single
controlled computer before they can be used, meaning that any virus on a
non-company disk should be picked up before the disk is encrypted.

Alternatively, a boot sector virus could infect an SFS-encrypted disk.
However, if an attempt is made to use the infected disk (which involves
mounting it), the mount will fail as the boot sector will contain the virus
rather than the SFS volume header.  The person who tried to mount the volume
will assume the disk has not been "converted" yet, and will bring it to the
machine used for processing the disks.  At this point the virus can be found by
the scanner.

This procedure isn't totally error free.  It won't work if there may already be
viruses present on one or more of the machines before SFS is installed.  In
addition, an SFS disk whose volume header is overwritten by a virus is probably
damaged beyond repair.  However it does provide a reasonable amount of
protection, and has the pleasant side effect of keeping all the company records
secure against unauthorized access attempts.