New:	Removed DEVICE,UNIT,BAUD from icon tooltype
	Added gadgets to prefs: serial device, unit, baud, PAR/Serial

Icon ToolType defaults:
	BUTTON=ON	- all but VT-3000
	TBC1=TBC 1 \
	TBC2=TBC 2  \__ not in V-Scope or router
	TBC3=TBC 3  /
	TBC4=TBC 4 /
	ROUTER1=Ch-1
	ROUTER2=Ch-2
	ROUTER3=Ch-3
	ROUTER4=Ch-4
	ROUTER5=Ch-5
	ROUTER6=Ch-6
	ROUTER7=Ch-7
	ROUTER8=Ch-8
	OPTION=ON|OFF	- TBC-IV only

Command line works the same as tooltypes with additions:

	FILE=<filename>  - Use a file to set TBC's/V-Scope and then exit
	NOSCREEN

	(quotes are needed if there is a space in the argument i.e. "TBC1=TBC 1")


ARexx specifications for the TBC-IV

Address: TBC

Command summary:

Option board commands

Command         Argument(s)				Result
~~~~~~~         ~~~~~~~~~~~				~~~~~~
CHNR		[ OFF | ON ]				OFF or ON
LUNR		[ OFF | ON ]				OFF or ON

CAV		[ BETACAM | MII ]			BETACAM or MII
FILTER		[ COMB | NOTCH ]			COMB or NOTCH


Command         Argument(s)				Result
~~~~~~~         ~~~~~~~~~~~				~~~~~~
TBC		[ 1-4 | MASTER | ALL ]			[ 1-4 | ALL ]
UNITY		<no args>
INPUT		[ COMPOSITE/NTSC | SVIDEO/SVHS ]	[ COMPOSITE | SVIDEO ]
FREEZE		[ ON | OFF ]				[ ON | OFF ]
VIDEO		70.0 to 130.0				70.0 to 130.0
BLACK		-22.5 to +37.3				-22.5 to +37.3
CHROMA		50.0 to 150.0				50.0 to 150.0
HUE		-45.0 to +45.0				-45.0 to +45.0
HPOS	
HORIZONTAL	-1.00 to +1.00				-1.00 to +1.00
COARSE		-4.47 to +4.33				-4.47 to +4.33
SUB		0.0 to 180.0	(was FINE in III)	0.0 to 180.0
RED		-40.0 to +40.0				-40.0 to +40.0
BLUE		-40.0 to +40.0				-40.0 to +40.0
RECALL		1 to 10
STORE		1 to 10
STROBE		0 to 127				0 to 127
FMODE		[ FRAME | FIELD | STROBE | FILM ]	<<- returns same
UNDO		<no args>
QUIT		<no args>
LOAD		<name> (will be "S:TBCIV.Defaults" if no name given)
SAVE		<name> (will be "S:TBCIV.Defaults" if no name given)
BURST		[ OFF | ON ]				OFF or ON
COMBfilter	[ OFF | ON ]				OFF or ON
FIELD		1 to 3					1 to 3
FORCEblack	[ OFF | ON ]				OFF or ON
GMODE		[ INT | EXT ]				INT or EXT
HOTSWITCH	[ OFF | ON ]				OFF or ON
MONO		[ OFF | ON ]				OFF or ON
TERMINATION	[ OFF | ON ]				OFF or ON
VBLANK		[ NARROW | WIDE ]			NARROW or WIDE
VERSION 	<no args>				[ PersonalTBC-IV Vx.x ]
YCDELAY 	horiz vert				number number
KEYINPUT	[ ON | OFF ]				OFF or ON
KEYMODE 	[VIDEO|BLACK|CHROMA|HUE|HORIZ|BLUE|RED] <<-returns one

PROCAMP 	[1-10] [video black chroma hue horiz blue red] <<- returns same

TOFRONT 	<no args>	pops to front/closes switcher
TOBACK		<no args>	pops screen to back
TOSWITCHER	<no args>	opens switcher if it's running
TOPROCAMP 	<no args>	swicthes to proc amp screen
TOBALANCE	<no args>	switches to balance screen
TOWB		<no args>	pops workbench to front

WAIT		<numbers of frames>

SEND		For test purposes only (sends binary data)
		  i.e. SEND 'F06700013030F7'x

SERDEV		[name.device] (defautl: serial.device)		name.device
SERUNIT 	[number] (default: 0)				number
SERBAUD 	[ 9600 | 31250 ]				9600 or 31250
SERPAR		[ OFF | ON ]					OFF or ON


V-Scope
~~~~~~~
ANALIZER	[VECTOR|WAVE|OVERLAY|SPLIT] [1H|2H]	<<- returns same
EXCITER 	[NORMAL|FREEZE|PEAK|VARIABLE]		<<- returns same
RESPONSE	[ FLAT | LOWPASS ]			[ FLAT | LOWPASS ]
RATE		[ 2 to 127 ]				2 to 127
SUPERIMPOSE	[ ON | OFF ]				[ ON | OFF ]


Router
~~~~~~
ROUTER		[1 to 8]	Current router
INPUT4		[1 to 4]	Set 4x1 input
INPUT8		[1 to 8]	Set 8x1 input
BUS		[4 or 8]	Set BUS output
BNC		[4 or 8]	Set BNC output