LAN-LINK Version 2.32 PAGE 1 




                   LAN-LINK Copyright (c) 1988 - 1994 by G3ZCZ
                               All Rights Reserved 

                               Joe Kasser W3/G3ZCZ
                                    POB 3419
                                  Silver Spring
                               Md., 20918, U.S.A.
                              Voice (301) 593 6136
                             Data BBS (301) 593 9067
                           Internet jkasser@cap.gwu.edu

                            _______
                       ____|__     | (tm)
                    --|       |    |-------------------
                      |   ____|__  | Association of
                      |  |       |_| Shareware
                      |__|   o   |   Professionals
                    -----|   |   |---------------------
                         |___|___|   MEMBER































        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 2 


                                Table of Contents

        Appendix 1 Introducing LAN-LINK ........................ 2
         LAN-LINK PROGRAM HIGHLIGHTS............................ 4
         Getting Started ....................................... 7
         Bringing LAN-LINK Up the First Time ................... 8
         Using the Quick Menu .................................. 9
         Connecting to Other Stations .......................... 9
         Using Different TNCs .................................. 9
         LAN-LINK Memory Requirements ..........................10
         PC to TNC Communications ..............................10
         LAN-LINK Runs Open Loop ...............................10
         In Case of Problems ...................................10
         Logbooks ..............................................11
         How To Get an Update ..................................11
         Starting LAN-LINK in a Non Packet Mode ................11
         Using LAN-LINK with a PacketCluster ...................12
         Using ANSI Color for Transmitting Text Color Files ....13

        Appendix 2 LAN-LINK Features, Menus and Commands ...... 14
         1.0 LAN-LINK MESSAGE HANDLING FEATURES ................14
            1.1 Answering Machine ..............................14
            1.2 Mail Beacon (Annunciator) ......................14
            1.3 How to Leave a Message .........................15
         2.0 LAN-LINK WINDOWS ..................................15
         3.0 HOT KEYS ..........................................19
            3.1 Alt-A Alert Call (Packet) & AMTOR ARQ Call/Talk 19
            3.2 Alt-B Send Break/AMTOR Changeover ..............19
            3.3 Alt-C Call/Connect to Someone ..................19
            3.4 Alt-D Disconnect or Receive ....................21
            3.5 Alt-E Enter Call ...............................22
            3.6 Alt-F Flush TNC Buffer .........................22
            3.7 Alt-H Help Information for Function Keys .......22
            3.8 Alt-J Jump to DOS ..............................22
            3.9 Alt-K PacketCluster DX Alert....................22
            3.10 Alt-L Log Contact .............................22
            3.11 Alt-M Message Scan ............................22
            3.12 Alt-N Next Stream .............................23
            3.13 Alt-O Turn Robot On ...........................23
            3.14 Alt-P Turn Printer ON/OFF .....................23
            3.15 Alt-Q Call QRZ ................................23
            3.16 Alt-R Retry Call/Connect ......................23
            3.17 Alt-S Scan Log ................................24
            3.18 Alt-W :QRA: ...................................24
            3.19 Alt-X Exit to DOS .............................24
            3.20 Alt-Y Zap PacketCluster/RTTY Transmit "RY"s ...24
            3.21 Alt-Z Zap PBBS ................................24
            3.22 Alt-= Toggle Miscellaneous Flag ...............26
            3.23 End "> +?" [Over] .............................26
            3.24 PgUp Scrollback (Scrolls back incoming text) ..27


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 3 


            3.25 The Home Key ..................................27
            3.26 The Down Arrow Key ............................27
            3.27 Shift/Baudrate Control Keys ...................28
            3.28 Control-Z (^Z) ................................28
            3.29 Control T (^T) ................................28
         4.0 FUNCTION KEYS .....................................28
            4.1 Capture to Disk Toggle (F1) ....................29
            4.2 Send Brag Tape and Talk (F2) ...................29
            4.3 Transmit Callsign Sequence (F3) ................29
            4.4 Send Brag Tape (F4) ............................30
            4.5 Show Packet "MH" list and Point and Shoot 
                                     Connect (F5)...............30
            4.6 Auto CQ Call (F6) ..............................30
            4.7 Activate Type Ahead Buffer/AMTOR Relink (F7) ...31
            4.8 Disconnect, Disengage or Receive (F8) ..........32
            4.9 Put TNC in CMD Mode (F9) .......................32
            4.10 Put TNC in CONVERSE/Transmit/AMTOR FEC (F10) ..32
            4.11 Alternate Function Keys .......................33
            4.12 Shift Function Keys ...........................33
            4.13 Control Function Keys .........................33
         5.0 THE MAIN MENU .....................................34
            5.1 The Quick Menu .................................34
            5.2 Auto CQ ........................................35
            5.3 Send Brag Tape .................................35
            5.4 Call Someone ...................................35
            5.5 Log Menu .......................................35
            5.6 Change Communications Mode .....................35
            5.7 Call CQ ........................................35
            5.8 Send/Talk File .................................35
            5.9 QRZ ............................................36
            5.10 Send/Talk LAN-LINK Files 001..010 .............36
         6.0 THE PBBS/PacketCluster MENU .......................36
            6.1 Download Text Files ............................36
            6.2 Download Binary File (Xmodem) ..................37
            6.3 Download Binary File (Ymodem) ..................37
            6.4 Zap PacketCluster ..............................37
            6.5 Zap PBBS .......................................37
            6.6 Turn PacketCluster Mode ON/OFF .................37
            6.7 Send DX Alert ..................................38
            6.8 Clear All Search Flags .........................38
            6.9 Set All Search Flags ...........................38
            6.10 Set All CW Search Flags .......................38
            6.11 Set All SSB Search Flags ......................38
            6.12 Set/Clear Individual Search Flags .............38
            6.13 Set/Clear Current Band Search Flags ...........38
         7.0 THE CALL MENU .....................................39
            7.1 Alert Call .....................................39
            7.2 ReMember Path ..................................40
            7.3 Call CQ ........................................40
            7.4 Show Contents of Call Directory ................40


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 4 


            7.5 Target Call ....................................40
            7.6 Auto CQ ........................................41
            7.7 Toggle DX Flag .................................41
            7.8 Zap PBBS on Next Mail Beacon ...................41
         8.0 EDIT MENU .........................................41
            8.1 Edit Brag Tape .................................43
            8.2 Edit Call Directory File .......................44
            8.3 Edit Any Other File ............................44
            8.4 Answer Capture-to-disk (Ctdsk) File
                                      (Split Screen) ...........44
            8.5 Answer Incoming Messages (Split Screen) ........44
            8.6 Leave Note for Someone .........................44
            8.7 Edit Capture-to-Disk file ......................45
            8.8 Edit Two Files (Split Screen) ..................45
            8.9 Edit Configuration File ........................45
            8.10 Edit LAN-LINK.001 through LAN-LINK.010 Files ..45
            8.11 Pick Capture-to-disk File to Edit .............45
            8.12 Pick Message File to Edit .....................45
            8.13 Leave Messages on your local PBBS .............46
            8.14 Edit Incoming Message .........................46
            8.15 Edit LAN-LINK.OUT File ........................46
            8.16 Edit LAN-LINK.DMO File ........................46
            8.17 Pick dEmo File to Edit ........................46
         9.0 EVENT/CLOCK MENU ..................................46
            9.1 Set Alarm ......................................47
            9.2 Connect ........................................47
            9.3 Display Event ..................................47
            9.4 Periodic Event .................................47
            9.5 Turn Robot ON/OFF ..............................47
            9.6 Turn Contest ON/OFF ............................47
            9.7 Turn Time Display ON/OFF .......................47
            9.8 Cancel Event ...................................47
            9.9 Zap PBBS .......................................47
         10.0 FILES MENU .......................................48
            10.1 Send Brag Tape ................................48
            10.2 File Directory ................................49
            10.3 Erase File ....................................49
            10.4 Pick Capture-to-disk (Ctdsk) file to View .....49
            10.5 Rename File ...................................49
            10.6 Send File .....................................49
            10.7 Send/Talk File ................................49
            10.8 Send Uppercase File ...........................49
            10.9 View File .....................................49
            10.10 View Capture-to-disk (Ctdsk) File ............50
            10.11 View Incoming Message File ...................50
            10.12 Print File ...................................50
            10.13 View Color File ..............................50
            10.14 Turn Mode Files ON/OFF .......................50
            10.15 Turn eXpand Files ON/OFF .....................50
         11.0 HELP WITH FUNCTION KEYS ..........................50


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 5 


         12.0 JUMP TO DOS SHELL ................................51
         13.0 LAN-LINK MENU ....................................51
            13.1 :QBU: External Protocol Command ...............51
            13.2 :QBM: ASCII File ..............................52
            13.3 :QDB: ASCII File ..............................52
            13.4 :QIC: Page Operator ...........................52
            13.5 :QMH: Monitor Heard ...........................53
            13.6 :QRA: Who is "ON-LINE" ........................53
            13.7 :QRU: Messages ................................53
            13.8 :QSM: Message .................................53
            13.9 :QSP: Message .................................54
            13.10 :QTA: Messages ...............................54
            13.11 :QTR: Ask for Time ...........................54
            13.12 :QZD: Binary Files ...........................54
            13.13 :QZU: Binary Files ...........................55
            13.14 Demo Mode ....................................55
            13.5 Set Single/Dual PK-900/DSP 2232 In Windows.....55
         14.0 LOG MENU .........................................55
            14.1 Append From Another LAN-LINK Log ..............56
            14.2 Scan Log by Band ..............................56
            14.3 Change Logbook File ...........................56
            14.4 Delete Logbook File ...........................57
            14.5 Find Date .....................................57
            14.6 Purge Log .....................................57
            14.7 Help Function Keys ............................57
            14.8 Import From G3ZCZ's Contest Log ...............57
            14.9 Jump to an Entry ..............................58
            14.10 Pick a Log file ..............................58
            14.11 Pack a Logbook ...............................58
            14.12 Scan Log by Mode .............................58
            14.13 Create a New Logbook .........................58
            14.14 Print Log ....................................58
            14.15 Re-index a Logbook ...........................58
            14.16 Sort on Date + Time ..........................58
            14.17 Turn Update Disk ON/OFF ......................59
            14.18 Fuzzy Scan ...................................59
            14.19 Turn Secondary Search ON/OFF .................59
            14.20 Log Menu Function Keys .......................59
         15.0 MESSAGE MENU .....................................61
            15.1 PBBS Command Files ............................62
            15.2 Current Messages ..............................62
            15.3 View Message ..................................62
            15.4 Leave Note ....................................62
            15.5 Old Messages ..................................62
            15.6 Time Tag ......................................62
         16.0 TNC MENU .........................................63
            16.1 Set TNC Date/Time .............................64
            16.2 Flush TNC Buffer ..............................64
            16.3 Initialize TNC ................................64
            16.4 Show Calls Monitored List .....................65


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 6 


            16.5 Show Connect Status ...........................65
            16.6 Change CTEXT ..................................65
            16.7 Activate TNC Mailbox ..........................65
            16.8 Deactivate TNC Mailbox ........................66
            16.9 TNC Modem Menu.................................66
            16.10 Select Radio Port 1...........................66
            16.11 Select Radio Port 2...........................66
            16.12 Disable Radio Port 1..........................66
            16.13 Disable Radio Port 2..........................66
            16.14 Enable Radio Port 1...........................66
            16.16 Enable Radio Port 2...........................66
            16.17 Show ### Radio Port...........................66
         17.0 AMSAT-OSCAR MENU .................................67
            17.1 Full Duplex ON/OFF.............................67
            17.2 SAREX MENU ....................................67
            17.2.6 Set Attack Mode to Connect/CQ ...............69
            17.3 SAREX Orbiter Features ........................69
         18.0 PARAMETER MENU ...................................72
            18.1 Turn Beacon Mode ON/OFF .......................72
            18.2 Clear Connect Counter .........................73
            18.3 TNC Custom Line (TNC Parameter) ...............74
            18.4 Turn Beacon Control ON/OFF ....................76
            18.5 Turn Command Echo ON/OFF ......................76
            18.6 Change Keyboard Beep Count ....................76
            18.7 Set Message Count .............................77
            18.8 Turn Node Drop Link ON/OFF ....................77
            18.9 Turn Printer ON/OFF ...........................77
            18.10 Turn QTC Snatch ON/OFF .......................77
            18.11 Turn :QSP: Relay Flag ON/OFF .................78
            18.12 Turn Sound ON/OFF ............................79
            18.13 Turn Contest Mode ON/OFF .....................79
            18.14 Turn DCD Flag ON/OFF .........................80
            18.15 Turn PBBS Snatch ON/OFF ......................80
            18.16 Turn Time Id. ON/OFF .........................81
            18.17 Turn Automatic Capture-to-Disk Flag ON/OFF ...81
            18.18 Change PBBS Parameters .......................81
            18.19 Change Callsigns .............................82
            18.20 Change Directories ...........................83
            18.21 Enter Common Calls ...........................84
            18.22 Change File Names ............................84
            18.23 Change LAN-LINK Parameters ...................84
            18.24 Change PC Communications Parameters ..........88
            18.25 Change Colors ................................89
            18.26 Change SAREX Parameters ......................92
            18.27 Update Configuration File ....................93
            18.28 Verify Changes ...............................93
            18.29 Change Scan Words ............................93
            18.30 Turn Miscellaneous Flag ON/OFF ...............93
            18.31 Change Band/Mode .............................95
            18.32 Zap PBBS on Next Mail Beacon .................95


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 7 


            18.33 PBBS Zap, Don't Disconnect After Sequence ....95
            18.34 Control Send of LAN-LINK.OUT .................95
         19.0 Q Codes [NC/L] ...................................95
         20.0 COMMUNICATIONS MODES .............................96
            20.1 VHF PACKET ....................................96
            20.2 HF PACKET .....................................96
            20.3 ASCII (RTTY) ..................................96
            20.4 BAUDOT (RTTY) .................................96
            20.5 MORSE (CW) ....................................97
            20.6 AMTOR (STANDBY) ...............................97
            20.7 AMTOR (MONITOR) ...............................97
            20.8 PACTOR (STANDBY) ..............................97
            20.9 PACTOR (MONITOR) ..............................97
            20.10 SIGNAL .......................................98
            20.11 NAVTEX .......................................98
            20.12 G-TOR  .......................................98
            20.13 MANUAL .......................................98
         21.0 TERMINAL MODE MENU ...............................98
            21.1 Packet Terminal Menu ..........................98
            21.2 AMTOR Terminal Menu ..........................103
            21.3 Baudot Terminal Menu .........................104
            21.4 ASCII Terminal Menu ..........................106
            21.5 CW Menu ......................................107
            21.6 Pactor Terminal Menu .........................108
         22.0 EXIT TO DOS .....................................109
         23.0 THE ELMER MENU ..................................109
            23.1 Change ELMER File ............................109
            23.2 Turn ELMER ON/OFF ............................109
            23.3 Load State Table (ELMER.QSO) .................109
            23.4 Pick File to Edit ............................110
            23.5 Edit State Table (ELMER.QSO) .................110
            23.6 Show State Table .............................110
         24.0 RADIO MENU ......................................110
            24.1 Select VFO A/B................................110
            24.2 Set Mode......................................111
            24.3 Turn Flag QSY ON/OFF or N/A ..................111
            24.4 Read VFO Frequency............................111
            24.5 Set VFO Frequency.............................111
            24.1 24.6 Speak Frequency..........................111

        Appendix 3 LAN-LINK Disk Files ........................112
         1.0 LAN-LINK.EXE .....................................112
         2.0 LAN-LINK.SYS .....................................112
            2.1 CTEXT Line ....................................115
            2.2 ELMER Flag ....................................115
            2.3 PC Port 4 Custom Address ......................115
            2.4 PC Port 4 Custom IRQ ..........................115
            2.5 VHF Stream Switch Character ...................115
            2.6 HF Stream Switch Character ....................116
            2.7 TNC Error Message .............................116


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 8 


            2.8 Connect Timeout Delay .........................116
            2.9 ELMER Configuration File ......................116
            2.10 Expand Transmitted Files Flag ................116
            2.11 First PacketCluster Command ..................116
            2.12 Second PacketCluster Command .................116
            2.13 TNC Mailbox ON Command .......................116
            2.14 TNC Mailbox OFF Command ......................117
            2.15 VHF Maxframe Command .........................117
            2.16 HF Maxframe Command ..........................117
            2.17 Inhibit VHF Logging Flag .....................117
            2.18 Inhibit HF Logging Flag ......................117
            2.19 Printer Permanent Flag .......................117
            2.20 Log Disk Update Flag .........................117
            2.21 Secondary Log Flag ...........................117
            2.22 Auto Answer Flag .............................117
            2.23 Ctdsk File Disk Update Flag ..................118
            2.24 Default CW Speed .............................118
            2.25 Secondary Logbook ............................118
            2.26 BBS List Command .............................118
            2.27 BBS List Mine Command ........................118
            2.28 BBS Custom Command ...........................118
            2.29 BBS Bye Command ..............................118
            2.30 Start Up Packet Terminal Mode ................118
            2.31 Page Time (:QIC: Seconds) ....................119
            2.32 PacketCluster DX Alert Tone CW Dit time ......119
            2.33 Packet Cluster DX Alert Tone CW Note .........119
            2.34 Mode File Flag ...............................119
            2.35 BAUDOT Color Change Text String ..............119
            2.36 Dual Window Flag .............................119
            2.37 TNC String for Modem 9600 baud ...............119
            2.38 TNC String for Modem 1200 baud ...............119
            2.39 TNC String for Modem RTTY ....................120
            2.40 TNC String for Modem 300 baud ................120
            2.41 TNC String for Modem RTTY and 1200 baud ......120
            2.42 TNC String for Modem 300 baud and 1200 baud ..120
            2.43 TNC String for Modem Fuji ....................120
            2.44 Delay after a command line ...................120
            2.45 Radio ........................................120
            2.46 Radio Port ...................................120
            2.47 Radio Port baud rate .........................120
            2.48 Radio Port Bits ..............................121
            2.49 Radio Port Stopbits ..........................121
            2.50 Radio Port Parity ............................121
            2.51 Radio Address ................................121
            2.52 Flag QSY .....................................121
            2.53 Flag DX Alert Prefix Check ...................121
            2.54 Band parameters for DX Alert message 
                                     Log search ...............121
            2.55 Modes for DX Alert message log search ........122
            2.56 TNC Parameters ...............................122


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 9 


         3.0 *.RUN ............................................122
         4.0 *.DBF (HF.DBF and VHF.DBF) .......................122
         5.0 LAN-LINK.DIR .....................................122
         6.0 CONFIG.SYS .......................................123
         7.0 *.MBX ............................................123
         8.0 *.BBS ............................................124
         9.0 LAN-LINK.001 - LAN-LINK.010 ......................125
         10.0 QBU-RX.BAT ......................................126
         11.0 QBU-TX.BAT ......................................126
         12.0 LAN-LINK.QTA ....................................126
         13.0 QZ*.BAT .........................................126
         14.0 ELMER.QSO .......................................127
         15.0 LAN-LINK.OUT ....................................127
         16.0 *.DMO ...........................................127

        Appendix 4 Local Area Network Capability ..............128
         1.0 LAN Protocol (G3ZCZ Version) .....................128
         2.0 Message Format ...................................129
         3.0 ASCII File Uploading/Downloading .................129
         4.0 Path Determination to a DX station ...............130
         5.0 Binary File Transfers ............................131
         6.0 Requirements for Transfer Protocols ..............131
         7.0 The Zmodem Protocol ..............................132
         8.0 The PCZ Zmodem Package ...........................132
         9.0 BASIC NC/L DICTIONARY ............................133
            9.1 :QBM: .........................................133
            9.2 :QDB: .........................................134
            9.3 :QMH: .........................................134
            9.4 :QSM: .........................................134
            9.5 :QSP: .........................................134
            9.6 :QRA: .........................................134
            9.7 :QRT: .........................................134
            9.8 :QRU: .........................................134
            9.9 :QNO: .........................................135
            9.10 :QJG: ........................................135
            9.11 :QRV: ........................................135
            9.12 :QSL: ........................................135
            9.13 :QTA: message ................................135
            9.14 :QTC: Message List ...........................135
            9.15 :QBU: External Protocols .....................136
            9.16 :QZU: Zmodem Binary File Upload ..............136
            9.17 :QZD: Zmodem Binary File download ............136
            9.18 :QIC: Page Operator ..........................136
            9.19 :QTR: Ask for Time ...........................136

        Appendix 5 Using Different TNCs .......................137
         1.0 TNC2 (MFJ 1270) ..................................137
         2.0 TNC1 (HK-4040) ...................................137
         3.0 Kantronics KPC-2 .................................137
         4.0 Kantronics KAM ...................................138


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 10 


         5.0 PK-232 ...........................................138
         6.0 MFJ 1278 .........................................138
         7.0 Heath HK-21 ......................................139
         8.0 PK-900 and DSP 2232 ..............................139

        Appendix 6 Anomalies and Bugs .........................140
         1.0 Command/Converse Mode Anomalies ..................140
         2.0 Buffer Messages in AMTOR Beacon CQ Mode ..........140
         3.0 FEC +? Responses in AMTOR Beacon CQ Mode .........140
         4.0 Using a Monochrome Monitor .......................140
         5.0 The Packet Conference Mode .......................140
         6.0 Packet Conference Mode Disconnects ...............141
         7.0 Strange Events ...................................141
         8.0 *** DISCONNECTED .................................141
         9.0 *** CONNECTED ....................................141
         10.0 Greek Characters and Other Garbage in the 
                                     Incoming Screen ..........142
         11.0 Dumb TNC ........................................142
         12.0 Intermittent Lockup .............................142
         13.0 Automatic Functions Don't Work ..................142
         14.0 BBS Zap Failure .................................142
         15.0 LAN-LINK Forgets the Band/Power Information .....143
         16.0 Zmodem Binary Transfer Problems .................143

        Appendix 7 Updates, Revision History ..................144

        Appendix 8 ELMER An Expert System Based on a Finite 
                                     State Machine ............145
         1.0 INTRODUCTION .....................................145
            1.1 Expert Systems ................................146
            1.2 The User Interface ............................146
            1.3 The Knowledge Base ............................146
            1.4 The Inference Engine ..........................146
            1.5 Features of an Expert System ..................146
            1.6 Using an Expert System ........................147
            1.7 The Semantic Network ..........................147
            1.8 A State Machine ...............................148
            1.9 The User Perception ...........................148
            1.10 ELMER ........................................148
            1.11 Responses to an Input ........................148
            1.12 Syntactic Analysis ...........................149
            1.13 Programming ELMER ............................149
         2.0 The State Table (ELMER.QSO) File .................150
            2.1 The Directory Path to the ELMER Text Files ....150
            2.2 The Start Up File .............................150
            2.3 Window Colors .................................150
            2.4 The ELMER Initial State .......................151
            2.5 State Machine Parameters ......................151
            2.6 The State Machine File ........................152
            2.7 Example of Programming the State Table ........152


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        LAN-LINK Version 2.32 PAGE 11 


         3.0 The Stand Alone Version Status Window ............153
         4.0 The Stand Alone Menu .............................153
            4.1 Edit Any File .................................153
            4.2 Load State Table (ELMER.QSO) ..................153
            4.3 Pick File to Edit .............................154
            4.4 Edit State Table (ELMER.QSO) ..................154
            4.5 eXit to DOS ...................................154
            4.6 Show State Table ..............................154

        Appendix 9 PCZ Binary file Transfers ..................155

        Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ.....168
         1.0 PC-HAM 3.52 ......................................168
         2.0 STARTREK The Computer Program ....................168
         3.0 WHATS-UP 1.30 ....................................169
         4.0 ELMER 1.00 .......................................170
         5.0 BASIC PACKET RADIO ...............................170

        Appendix 11 How shareware Works .......................172

        Appendix 12 LAN-LINK 2.32 REGISTRATION FORM ...........174

        INDEX .................................................175





























        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 2


                         Appendix 1 Introducing LAN-LINK

        LAN-LINK is distributed as a Shareware product. You may freely 
        copy and share the product for non commercial use, with your 
        friends, associates and other radio amateurs. If you decide to 
        use the product, become a registered user by completing the 
        registration form in Appendix 12, and sending it (or a copy), and 
        $45.00 or equivalent in foreign currency to the author 
        (Mastercard and Visa accepted). All checks should be drawn on US 
        banks. Canadians, please use postal money order. Upon receipt of 
        your registration, you will receive one free update disk, 
        telephone and mail (electronic and regular) support. If you are 
        not satisfied with the program after registering it, your money 
        will be refunded no questions asked, for up to 30 days from the 
        date your registration was acknowledged.

        European Radio Amateur users may register (30.00 Pounds Sterling, 
        includes V.A.T.) and obtain support from Terry Dansey at 
        ReadyCrest Ltd., PO Box 75, Chatham, Kent, ME5 9DL, England. 
        ReadyCrest Ltd. accepts credit cards (Access, Visa, MasterCard 
        and Eurocard). Telephones: Voice 44 (0) 634-687168, FAX 44 
        (0)634- 687178, Data (BBS) 44 (0)634-200931.

        LAN-LINK may not be sold or distributed with another product 
        without the express written permission of Joe Kasser, G3ZCZ. Joe 
        Kasser, G3ZCZ will only support unmodified copies of this 
        software. 

        Potential Commercial Users please contact Joe Kasser directly for 
        modifications and/or details of Site licensing.                    






















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 3


        LAN-LINK is a Personal Packet Terminal Program for the TNC1, 
        TNC2, KPC-2, and, most of all, a smart multi-mode digital 
        communications controller for the KAM, MFJ1278, DSP-2232, PK-900 
        and the PK-232. LAN-LINK is designed to optimize the configura-
        tion of the TNC in each communications mode and to provide some 
        smart terminal features. It is designed to allow anyone to use 
        and get the most out of their packet TNC as well as from the PK-
        232, the MFJ1278, and the KAM for Morse, ASCII, BAUDOT, AMTOR, 
        Pactor as well as Packet Radio communications without having to 
        keep the manual handy. 

        LAN-LINK is a sophisticated program. In its basic state it allows 
        you to use the TNC in an optimal manner. It configures the TNC 
        (it types the commands) for you to maximize the communications 
        efficiency in the communications mode of your choice. That means, 
        for example, when working Packet on HF you need to program the 
        TNC parameters to different values than you would use on VHF to 
        make maximum use of the mode. One significant difference is the 
        length of the packet itself, for the longer it is, the greater 
        the probability of QRM destroying it. This program will adjust 
        the packet parameters for you.

        Since the computer is now involved, other features have been 
        added to simplify operation, and several features have been 
        automated. All these operations are performed using menus and 
        function keys as documented below. It will take a while to learn 
        how to use this program in a manner which suits you. Read this 
        document and have fun. After all, isn't that one of the purposes 
        of Amateur Radio.

        The LAN-LINK manual is organized by menu. It describes the 
        operation of each menu option and function key in each 
        Communications Mode. The manual tells you what LAN-LINK can do. 
        It does not tell you how to use LAN-LINK.

        Any Terminal Node Controller (TNC) is a complex piece of 
        equipment. It can operate in a Command Mode, in which you tell it 
        to do something, or in a Converse Mode in which you are using it 
        to talk to other stations. Many people confuse the two when first 
        getting on Packet. If you monitor the channels you will recognize 
        Command Mode TNC instructions on the air, and when you use the 
        TNC you will receive the "error" reply when you type something 
        thinking you are in the Converse Mode but are really in the Com-
        mand Mode. LAN-LINK is designed to make Packet operation simple 
        using Menus and high level (Function and Hot key combinations) 
        commands.

        Morse, ASCII, BAUDOT communications modes are HALF DUPLEX. One 
        station is transmitting at any time. You thus have to use the 
        Transmit-Converse and Receive-Disconnect function keys to turn 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 4


        the transmitter on and off respectively. 

        AMTOR is also HALF DUPLEX but has some of the attributes of full 
        duplex. In this Mode you control who is talking through software. 
        Only one station can send data at a time, but you can type 
        characters in to the buffer and they will be transmitted 
        automatically when the other station turns the QSO over to you. 
        Once you have linked with someone, you do not use the 
        Receive/Disconnect function until the QSO is over. 

        Both stations are communicating automatically thanks to the TNC. 
        If you want the other operator to respond type the "+?" key 
        sequence (or use the "End" Key). 

        Packet Radio communications on the other hand is a full duplex 
        mode of communications. Once you have connected with someone, you 
        do not use the Receive-Disconnect function until the QSO is over. 
        Both stations are communicating automatically thanks to the TNC. 
        If you want the other operator to respond type the ">" key 
        followed by the "Enter" Key. Better yet, use the "End" Key. 

        Morse, AMTOR, ASCII and BAUDOT are character mode communications 
        in that each character you type is sent as you type them. In 
        Packet Communications, the TNC stores them up and sends out a 
        burst or packet when you type the "Enter" Key or you type enough 
        characters to fill up a packet. Studies have shown that the human 
        attention span when sitting at the keyboard is of the order of 2 
        seconds. If you are in a keyboard to keyboard packet radio 
        connect, remember this and don't forget to use the "Enter" Key 
        frequently, especially before you stop to think about what to 
        send next.

        AMTOR, Pactor, and PACKET are full duplex modes of communica-
        tions. When you connect with someone, there is no need to use the 
        transmit and receive function keys. In fact you will have 
        problems if you do. Do not disconnect or break the link until the 
        QSO is over.

                           LAN-LINK PROGRAM HIGHLIGHTS

        *    First packet radio software to be flown in Space.
        *    Function key and Menu driven.
        *    Smart PacketCluster features, i.e. automatic QSY to the 
             frequency of a DX Alert (if in PacketCluster mode).
        *    Automatic search of HF logbook in response to a Packet-
             Cluster DX Alert Message. Customizable levels of 
             notification. Audio Notification of Prefix status.
        *    Start Up Communications mode is customizable.
        *    Start Up Packet terminal mode is customizable.
        *    Allows you to search through 2 logbooks for previous 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 5


             contacts.
        *    60 Different Bragtapes/files, 10 in each communications 
             mode.
        *    Automatic logbook entries for Pactor, Packet and Mailbox 
             Beacon Mode AMTOR Connects, semiautomatic logbook entries 
             for other modes. 
        *    Provides artificial intelligence in the shape of a second 
             operator (ELMER).
        *    Logbook file is dBASE compatible and can be processed by the 
             LOGBOOK Package of PC-HAM by G3ZCZ for indexed listings, 
             tracking of DXCC and other AWARDS, etc.
        *    Contest operation, sends standard message and automatically 
             increments QSO count.
        *    Automatic optimized configuration of the TNC for each commu-
             nications mode.
        *    All mode Function key "OVER" feature (End key).
        *    There are 10 files with fixed names (LAN-LINK.001 through 
             LAN-LINK.010) which may be viewed and transmitted by means 
             of function keys. They may also be edited from the Edit 
             Menu.
        *    Set up of TNC for AMSAT-OSCAR Telemetry reception.
        *    Time display and event scheduler.
        *    ASCII Text Editor.
        *    Customizable Colors.
        *    Access to the TNC Command Mode is provided in case the user 
             wishes to override any defaults.

                             In Packet Radio

        *    LAN message store and forward capability. 
        *    Automatic capture to disk of all packet radio connects.
        *    Automatic indication of the number of Packet connects. 
        *    Capable of automatic connect attempts to download a QTC from 
             another station in the LAN. 
        *    Capable of automatic connect attempts to a packet BBS to 
             download your incoming messages, when your callsign appears 
             on the BBS mail beacon annunciator.
        *    Capable of automatically requesting Bulletins on subjects 
             that interest you from your local PBBS.
        *    Digipeat monitoring and capture. 
        *    Alert signal to let you know when a predetermined call shows 
             up in a packet header on frequency. 
        *    Conference and Bridge modes in multi-connect situations.
        *    Path determination to DX station via :QMH:. 
        *    Indicator that a specific station designated as the "target" 
             call connected in Packet Mode, or linked to AMTOR Beacon or 
             Mailbox while you were away.
        *    Automatic NET/ROM and KA-Node path set up from directory 
             file.
        *    Selective answering machine and MAILBOX using NC/L command 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 6


             dialogue.
        *    Screen indication of connect by desired station (target 
             call).
        *    Automatic Beacon Mode CQ caller. 
        *    Automatic contest (DX-pedition) mode.
        *    Will call CQ repetitively and either work the connect and 
             keep going after disconnect or signal you when a reply is 
             received.
        *    Zmodem binary file transfer capability
        *    Customizable BBS Zap Commands.
        *    CTEXT File (LAN-LINK.OUT) which can be sent to all incoming 
             connects.
        *    ANSI Colors for Color "Brag Tapes".
        *    SAREX Attack mode lets you digipeat/CQ via the SAREX station 
             as well as try a connect. Use the CQ feature to digipeat via 
             MIR, and the connect for the Space Shuttle.
        *    Trigger to determine who else is on channel.
        *    Single keystroke Packet Cluster connect.

                                 In Pactor

        *    Smart Answering Machine.
        *    CTEXT File (LAN-LINK.OUT) which can be sent to all incoming 
             connects.
        *    ANSI Colors for Color "Brag Tapes".
        *    Automatic logging of connects.

                                  In AMTOR

        *    Automatic SELCAL determination.
        *    Automatic CQ caller. Will call CQ repetitively and signal 
             you when a reply is received. 
        *    LAN message store and forward capability. 
        *    Selective answering machine and MAILBOX using NC/L command 
             dialogue.
        *    Function key change from monitoring FEC CQs to QSOs in 
             progress (chirpcopy).
        *    Automatic Beacon Mode CQ caller.
        *    Automatic contest (DX-pedition) mode.
        *    Color changes between incoming and outgoing (echoed as sent) 
             text.

                           In MORSE/BAUDOT/ASCII

        *    Automatic CQ caller. Will call CQ repetitively and signal 
             you when a reply is received. 
        *    RTTY SELCAL.
        *    NAVY MARS RTTY file transmitting protocols.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 7


                              Getting Started

        MAKE A BACK UP COPY OF THE DISK, BEFORE YOU REMOVE THE WRITE 
        PROTECT TAB. If you are upgrading from a previous version of LAN-
        LINK, the 2.32 configuration files are NOT compatible with 
        earlier ones. If you are running 2.00, 2.10, 2.20, or 2.20B use the 
        UPGRADE program to save your current settings. If you have a 
        previous version, you have to go through the install sequence.

        Place the floppy disk in Drive A: Type "A:" (without the "") 
        followed by the "Enter" key so that you see the A:> prompt. The 
        floppy disk contains a batch file which will set up the correct 
        subdirectories on your hard disk. Type "SETUPLL", touch the 
        "Enter" key, and the batch file will go to work. 

        The Install program customizes the most often used parameters for 
        you. Section 18 of Appendix 2 describes each of the parameters. 
        Read it as you install LAN-LINK.

        Install first asks you for the TNC you are using, reply with the 
        number associated with your TNC. If you don't find your TNC 
        listed, try the TNC2 option. 

        The main things you need to change are: 

        Your Callsign
        Your SELCAL           (if you are using a Multi-mode TNC).
        PacketCluster Call    the callsign of your local PacketCluster.
        BBS Call              the callsign of your local BBS.

        If you have not already connected to your local BBS, skip the 
        next few parameters, and re-run install at some later time when 
        you know which answers to reply with, or change them from the 
        LAN-LINK Parameter menu. These parameters are:

        BBS Mail Trigger      text in your local PBBS mail beacon.
        Read Request          the command you send to the PBBS to read a 
                              message.
        Bulletin Read         the command you send to the PBBS to read a 
                              bulletin).
        BBS Subject           the PBBS prompt for the subject of a 
                              message you are sending.
        BBS Message           the PBBS prompt for the text of a message 
                              you are sending.

        The next few parameters set up the serial port between the PC and 
        the TNC. Read the TNC Manual to see what the manufacturer's 
        defaults are. These parameters are:-

        PC Com Port           A 0 disables serial I/O. Set to the Port 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 8


                              number you wish to use.
        PC Baud Rate          Enter the value you want to use.
        Data Bits             7 or 8. Note: 7 will inhibit binary trans-
                              fers.
        Parity Bit            Enter the correct letter.
        Stop bits             Use 1 unless the baud rate is 300 or less.

        Read Section 18 of Appendix 2 to learn what the remaining 
        parameters mean. You can change most of them, once you have 
        loaded LAN-LINK, by bringing up the Parameters Menu, and 
        following the prompts. 

                       Bringing LAN-LINK Up the First Time

        1    If you are upgrading from 2.00, 2.10 or 2.20, use the 
             UPGRADE program. Any other earlier version, or if this is 
             your first time, run the INSTALL program.
        2    Turn on the TNC.
        3    Load the program by typing LAN-LINK in the way you normally 
             load a program.
        4    WAIT until the program says it has initialized the TNC and 
             shows the band and power in the status window at the top of 
             the screen.
        5    If there is no battery in your TNC do what the TNC manual 
             tells you to do to synchronize the TERMINAL baud rate to 
             1200 baud.
        6    After LAN-LINK has loaded, use the Parameters Menu to change 
             anything you still need to customize. Use the "U" option to 
             save the updated file. After reading the rest of this 
             manual, you may want to change other defaults to set up LAN-
             LINK the way you like it.
        7    Use the "N" and "I" options in the TNC Menu to configure the 
             TNC. Then select the desired mode of operation from the 
             displayed menu by pressing the appropriate key. 
        8    Exit from LAN-LINK by using the Alt-X Key or the Esc Key 
             followed by the X Key.
        9    Reload LAN-LINK the same way you did before. This will load 
             the edited LAN-LINK.SYS file with the new settings. You are 
             now ready to use LAN-LINK. If this is your first time, try 
             the Quick Menu.
        10   If you are updating from previous versions the following 
             applies. The LAN-LINK.SYS configuration files are incompat-
             ible with any earlier version.

        If you have batteries in the TNC, make sure the TNC is set for a 
        terminal baud rate of 1200, and try to run the program. If you 
        see Greek characters or it doesn't work, remove the batteries and 
        try again. You can then replace the batteries and from then on 
        the program will be correct. Make sure you leave the TNC on when 
        you replace the batteries or your initialization will revert to 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 9


        the TNC default settings - the batteries are there to power the 
        TNC RAM while your primary power is off.

        If you have trouble with a PK232MBX, then, with LAN-LINK running, 
        turn the PK232MBX off, count to ten and turn it on again. Type 
        one * character. If that fails, repeat this a few times. If it 
        still fails, open the PK232 and remove the battery jumper. Count 
        to 10 slowly before replacing it and try again.

                              Using the Quick Menu

        The Quick Menu is designed for new users and provides the most 
        commonly used functions in a single Menu. You bring up the Quick 
        Menu by touching the "Escape" key to access the Main Menu and 
        then selecting the "A" option.

        The Quick Menu is described in Section 5.1 of Appendix 2.
         
                          Connecting to Other Stations

        LAN-LINK treats incoming connects and outgoing connects 
        differently. To connect to another station, Use the Alt-C hot 
        key, Function key 5, or bring up the Quick Menu using the "Esc A" 
        character sequence as described in Section 5.1, or by bringing up 
        the Call Menu via the "Esc C" character sequence. DO NOT TYPE "C 
        Call sign" in the command mode. If you do, the connect will still 
        take place (the TNC won't know if you or LAN-LINK issued the 
        command) but LAN-LINK will treat it as an incoming connect and 
        issue the "[ZCZ] LAN-LINK 2.32>" handshaking signal (if the LAN-
        LINK flag is in its default, or enabled state). If you connect to 
        a PBBS or a Node this way, you will get an error message back 
        from the PBBS or node, since it does not recognize LAN-LINK's 
        handshake.

        When you use the menu, Alt-C or F5 approach you can also make use 
        of the "path memory" feature in the LAN-LINK.DIR file.

                              Using Different TNCs

        There are differences between the command dialogue and the 
        features offered by the PK-232, PK-900, DSP 2232, TNC2 KAM, and 
        MFJ1278. LAN-LINK makes use of many of them. For example, the KAM 
        shows the HF and VHF packets as if they were separate streams. 
        LAN-LINK detects them and displays the different headers in 
        different colors. As this feature is not present in the PK-232, 
        LAN-LINK does not offer it for PK-232 users. From time to time, 
        as each manufacturer updates the firmware (EPROM) in the TNC, 
        LAN-LINK may be updated and new features added.

        LAN-LINK is normally loaded by typing LAN-LINK followed by the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 10


        "Enter" key. In this instance, LAN-LINK gets its configuration 
        information from the LAN-LINK.SYS file. LAN-LINK.SYS is the 
        default SYSTEM or configuration file. If you have more than one 
        TNC you may want to set up different configuration files for each 
        TNC. 

        To load LAN-LINK with the optional configuration file, type "LAN-
        LINK" followed by the name of the file (without the filetype) on 
        the command line then press the "Enter" Key. For example, if you 
        have a PK-232 and a TNC2 and occasionally use the TNC2, set up 
        the LAN-LINK.SYS file for the PK-232. Then type "LAN-LINK" to run 
        the program normally. On the rare occasions when you want to use 
        the TNC2, you may type "LAN-LINK TNC2" to run LAN- LINK with the 
        TNC2.SYS configuration file. Make sure you configure that 
        TNC2.SYS file before you put any signals on the air.

                          LAN-LINK Memory Requirements

        LAN-LINK 2.32 requires a minimum of 450k of RAM. You will need 
        more RAM if you wish to use the Editor. The Editor files will 
        each take a maximum of 64K additional RAM. If your memory is 
        marginal, you may get an error when you try to log a station or 
        edit a file/message. If you do not have enough memory working 
        from within LAN-LINK, you may use the EDITOR program from DOS.

                            PC to TNC Communications

        All communications between the computer and the TNC normally use 
        the 8 BIT NO PARITY and 1 stop bit RS-232 Serial Port 
        configuration. If you want to limit the character set to the 7 
        bit ASCII set, set the TNC parameters accordingly. The baud rate 
        defaults to 1200, but you may set it to 2400, 4800 9600 or even 
        19200 if your CPU clock is fast enough and the TNC will respond 
        correctly. 

                             LAN-LINK Runs Open Loop

        IF YOU USE LAN-LINK, YOU STILL MUST READ THE TNC MANUAL. WARNING 
        THIS PROGRAM OPERATES IN AN OPEN LOOP MODE. IT REMEMBERS WHAT 
        INSTRUCTIONS OR COMMANDS IT GAVE THE TNC. IF FOR SOME REASON, THE 
        TNC IS NOT SYNCHRONIZED TO THE PROGRAM YOU WILL NOT GET CORRECT 
        DISPLAYS ON THE SCREEN.

                               In Case of Problems

        In case you have problems, always check the default settings 
        using the "Verify Changes" option of the Parameters Menu. If you 
        work CW, read about the XMITOK flag, and set it for the way you 
        have wired your TNC to the radio. Problems can be caused by 
        incorrect settings of the TNC parameters. If all else fails, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 11


        (hard) reset the TNC. Make sure XFLOW and FLOW are OFF. 

                                    Logbooks

        LAN-LINK uses three dBASE 3 compatible logbook files. One is used 
        for VHF packet logging (VHF.DBF), the second for all HF modes 
        (HF.DBF) and a third designated as a secondary HF logbook. See 
        Appendix 2, Section 14 for more information.

                              How To Get an Update

        There are two ways to get an updated version, as follows. When 
        you register your copy of LAN-LINK, if this version is still 
        current, your registration will be acknowledged, and the 
        following upgrade will be sent to you automatically at the time 
        it is released (in this case, if you move, make sure you notify 
        me of your new address). If a later version exists at the time 
        that you register, it will be sent to you when your registration 
        is acknowledged and you will not be put on the list for an 
        automatic upgrade.

        If you are not on the list for an automatic upgrade (i.e., you 
        received a disk in the mail as a result of your registration), 
        then when you hear that a new release is out, do one of the 
        following:

        Send in $5.00 and remind me what size disk to send you.

        Download the new version from my land-line BBS or any place else 
        you find it (You do not need to reregister the upgrade in this 
        case).

        Get it from a friend (You do not need to reregister the upgrade 
        in this case).

        Collect together at least 300 kBytes of traffic on your local 
        VHF/UHF LAN by running LAN-LINK with the capture-to-disk 
        activated when you are not connected. If you can add to that, 
        connect to your local PBBS and dump all current bulletins with 
        full headers showing date/time into your capture-to-disk file. If 
        necessary compress the file (ZIP preferred). Send in the disk in 
        a mailer together with a label addressed to you, and sufficient 
        return postage, and the upgrade will be yours.

                     Starting LAN-LINK in a Non Packet Mode

        You may start LAN-LINK in a non packet mode, such as Pactor or 
        Baudot from the DOS command Line. If you wish to do so, the 
        format of the command is 'LAN-LINK SYSFILE MODE', where SYSFILE 
        is the name of the LAN-LINK.SYS file or its equivalent, and MODE 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 12


        is the letter used in the Communications Menu to put the TNC in 
        the particular mode (See Appendix 2 Section 20). For example, to 
        start LAN-LINK in AMTOR from DOS, type 'LAN-LINK LAN-LINK A'. To 
        start up in Pactor, type 'LAN-LINK LAN-LINK P'.If you are using a 
        different configuration file, such as HF.SYS, type 'LAN-LINK HF 
        A' or 'LAN-LINK HF P'. 

                       Using LAN-LINK with a PacketCluster

        Connect to the PacketCluster using the Alt-Y key. When the 
        connection is achieved, and the PacketCluster sends you a ">" 
        character at the end of a line of text, LAN-LINK will issue the 
        first cluster command, followed by the second one, to the Packet-
        Cluster and return to manual operation. The default commands are 
        "SHOW/WWV/1" command followed by a "SHOW/DX". Note: PacketCluster 
        is a specialized PBBS and conference node by Pavillion Software 
        for DX chasers.

        LAN-LINK also sets an internal PacketCluster Flag. When this flag 
        is set, LAN-LINK will interpret DX announcements, check your hf 
        logbook and alert you to the status of that prefix in both sound 
        and color. If you want LAN-LINK to react to the DX Alerts and 
        search your HF logbook, to see if you have QSLd or Worked or Need 
        the prefix, customize the Packet Cluster DX Alert Mode in line 
        112 of the LAN-LINK.SYS file to your liking. The parts of the DX 
        Alert message will be shown in different colors.

        Options in the PBBS/PacketCluster Menu allow you to customize the 
        check to set up which bands and which modes are checked. For 
        example if you never work the 160 Meter band, you may customize 
        LAN-LINK to ignore 160 Meter DX Announcements.

        The results of a logcheck show up at the end of the DX Alert 
        message. LAN-LINK also changes the current band (see status 
        window) to the band of the call shown in the DX alert.

        In the contest Mode, LAN-LINK checks the logbook for the 
        complete callsign.

        "B" means worked on the same band
        "W" means worked on another band 
        "Q" means that the callsign has been QSLd.

        In the non contest Mode, LAN-LINK checks the logbook for the 
        prefix (2 or 3 letters) of the callsign. 

        "W" means worked on the same band
        "w" means worked on another band and 
        "Q" means that the prefix has been QSLd on the same band
        "q" means the prefix has been QSLd on a different band.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 1 Introducing LAN-LINK Page 13



        In both contest and non contest modes, a check mark means the 
        logbook was checked and the prefix not found.

        You may use the Alt-G key to grab a DX Alert from the incoming or 
        scrollback windows. LAN-LINK will set the Radio to frequency and 
        post the call. This is similar to the action of F10.

        You can also enable an automatic QSY to the frequency of a DX 
        Alert via the Radio Menu.

               Using ANSI Color for Transmitting Text Color Files

        ANSI control codes are designed to allow you to control the 
        display at the other end of the link. LAN-LINK 2.32 reacts to 
        ANSI control codes including the color codes. This feature allows 
        you to send colorful bragtapes and other files using the text 
        mode graphics of the PC character set when operating packet, 
        Pactor or G-TOR.

        ANSI color codes are a sequence of characters beginning with the 
        'Escape' Character (represented as "Esc" or "^[") followed by a [ 
        character, one or two numbers follow and the sequence terminates 
        with the letter "m". Typical examples are 'Esc [37m' and 'Esc 
        [40m'. To save time, several codes may be combined using the 
        semi-colon character as in 'Esc [37;40m'.

        When transmitting lines of color, the ANSI control codes add 
        characters to the line, so your line will probably contain more 
        than 80 characters. Make sure you set the correct TNC parameter 
        (i.e. SCREENLN) to 255 to ensure that the TNC doesn't add extra 
        'CR/LF' codes to your picture and mess it up.




















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 14


                Appendix 2 LAN-LINK Features, Menus and Commands

        LAN-LINK provides an interface between you and the TNC. It works 
        in a client-server mode. It provides you with menus, and then 
        sends the TNC the commands that you would have had to type to 
        exercise the particular option. LAN-LINK also provides smart 
        features to smarten up your packet radio operations.

        This appendix contains a summary of the commands and menus 
        available to you in LAN-LINK. The commands are organized by Menu. 
        Some function keys provide you with short cuts so you don't have 
        to go through the entire menus. These function keys are described 
        below.

        1.0 LAN-LINK MESSAGE HANDLING FEATURES

        This section describes the mail box and message handling features 
        built into LAN-LINK.

        1.1 Answering Machine

        LAN-LINK contains an AMTOR (Robot beacon CQ mode only) and PACKET 
        Mode SMART "answering machine" facility. You can leave messages 
        on your disk (in the same directory as the LAN-LINK.* files, if 
        you are using a hard disk), for different stations. When someone 
        connects to you, if you left a message for him, he (or she or 
        even it as the case may be) and only that station will receive it 
        automatically. No one else will normally be able to download that 
        message. 

        1.2 Mail Beacon (Annunciator)

        To ensure that people know that you have left a message for them 
        a "MAIL for" list is loaded into your Packet Beacon and 
        transmitted every 30 minutes (Refer to the BTEXT command in the 
        TNC manual) as ":QTC:" followed by a list of calls. If no mail is 
        pending, or the only message in your system is one addressed to 
        you, the beacon transmissions are inhibited. This conforms to 
        good operating practice on crowded channels (at least inhibiting 
        the beacon does).

        The mail beacon in the Pactor, G-TOR, and AMTOR Modes is 
        transmitted as part of the beacon AUTOCQ message. It is 
        automatically updated when a message is transmitted. If you don't 
        set the beacon (see below) you will not transmit a mail beacon 
        text in your AMTOR CQ message.

        The Mail beacon text is set up either when you tell the computer 
        to set it up or when you disconnect a packet QSO from another 
        station. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 15



        In this manner you may update the list while the program is 
        running, for example, by using Borland's Sidekick or the included 
        Editor, to write a message, or preferably the NOTE feature. 

        Any station using LAN-LINK can be configured to automatically 
        attempt a connect (QTC-Snatch) when seeing their callsign in 
        someone else's LAN-LINK :QTC: beacon mail message list.

        If for some reason the message got lost (e.g. because the link 
        was marginal), :QSM: will get you a repeat of that message.

        1.3 How to Leave a Message

        You can use the "note" feature or type the message as a non-
        document file on the included Editor, or if you use another word 
        processor, you must leave the message as an ASCII text file. In 
        that case, you just name the message file as the callsign of the 
        station to whom you wish the message to be sent at connect time. 
        You must also give it the filetype of "OUT".

        For example, a message for G3ZCZ would be stored on the disk as a 
        file named "G3ZCZ.OUT", and similarly a message to 4X6AA would be 
        stored on disk as "4X6AA.OUT".

        Once the message has been sent, an entry to that effect will be 
        made in the LAN-LINK.RUN data capture file. The message file will 
        then be renamed and given the file extension ".OLD". At that time 
        any previously existing mail file with the file extension ".OLD" 
        will be deleted. This stops the addressee receiving the message 
        on successive connects if you can't delete it for some reason 
        (you forget) while at the same time, the message is still 
        available to you in case you need it.

        You should use a separate utility program if you want the calls 
        in the mail beacon sorted. You may, for example, wish to sort 
        them in alphanumeric order, or in the order of the date that they 
        were left in your answering machine.

        Incoming messages triggered by the QTC-Snatch will be left in a 
        message file named as YOURCALLSIGN.OUT, which can be scanned by 
        using the Alt-M Key combination. If you have non LAN-LINK 
        friends, train them to trigger the QTC-Snatch by simulating a 
        beacon, and prefixing and ending their text with lines containing 
        the ">" as the only character. Better yet, give them a copy of 
        LAN-LINK and tell them to use it and register it.

        2.0 LAN-LINK WINDOWS

        LAN-LINK displays information in different windows. The window at 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 16


        the top of the screen is the status window. The big blank window 
        in the center is the incoming text window. The lower third of the 
        screen is the outgoing text window. All outgoing text are echoed 
        in this window. The bottom line is a prompt window.

        The indicators in the status line depend on the state of the LAN 
        Link and are described in the sections that deal with the 
        functions they are associated with. Some typical status window 
        displays are shown below.

         2 Meters    2 Watts PACKET 1200 W [R] TRFC ->N4QQ
         20 Meters 100 Watts MORSE TEST[4]
         20 Meters 100 Watts PACKET 300 N TRFC
         CAPTURE TO DISK     PACKET 300 N [C1][Z] TRFC ->N4QQ

        If the automatic Capture-to-disk is turned off, a yellow bug will 
        be flashing on the left side of the line.

        If the Printer Flag is set, a yellow [P] will be flashing on the 
        left side of the line.

        If the miscellaneous flag is set, an asterisk "*" followed by two 
        numbers and a "]" will be displayed. The first number is the PBBS 
        Sequence State, the second is the Connect Sequence State. These 
        numbers reflect the internal state of LAN-LINK and should be 
        quoted when describing problems.

        If a message transfer is taking place, the callsign of the 
        station involved will be displayed.

        When the Capture-to-Disk is turned on, the words "CAPTURE TO 
        DISK" will be displayed. If it is turned off, the operating band 
        (Meters) and power (Watts) will be shown. If a Zap PBBS is in 
        operation, the Bulletin Request Count will then be shown in 
        square brackets ("[]").

        The communications mode will be shown next, it may be one of the 
        following;

        PACKET AMTOR AMTOR-(MAIL) AMTOR-FEC
        BAUDOT ASCII MORSE NAVTEX
        SIGNAL ???? DEFAULT {boot up}

        A flashing yellow musical note following the Communications Mode 
        indicates that the sound has been inhibited.

        The next number to be displayed is the RF communications 
        baudrate. The letter "W" or "N" indicates that the Wide shift or 
        the Narrow shift has been selected. A "down arrow" will be shown 
        if the shift is normal. If the shift is reversed a flashing 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 17


        yellow "up arrow" will be displayed.

        In the BAUDOT mode, "USOS" will be displayed if unshift- on-space 
        is selected.

        If the Contest Mode is selected, the word "TEST" will then be 
        displayed followed by the Contest QSO number in "[]".

        In certain Robot and AutoCQ states, namely while the computer is 
        waiting for a reply, a flashing cumulative CQ count will be 
        displayed next.

        If the RTTY SELCAL is active, the word "SELCAL" will be displayed 
        next.

        If the Navy MARS BAUDOT RTTY protocol is enabled, a "[n]" will be 
        displayed.

        In the packet and AMTOR Robot modes, if at least one station has 
        connected or linked, a flashing yellow "[C]" will be displayed 
        next. The number in the square brackets with the "C" is the 
        number of stations that have connected/linked. If the target call 
        station was one of those station, a happy face will also be 
        displayed in the square brackets.

        If at least one QTC snatch has taken place a flashing yellow 
        "[Q]" will be displayed next. The number in the square brackets 
        is the number of QTC Snatches that have taken place.

        In the packet communications mode, if a Zap PBBS, a QTC Snatch or 
        a PacketCluster Zap is in progress a flashing yellow "[Z]""will 
        be displayed next. However, if LAN-LINK is set to stay connected 
        when the sequence ends, the flashing indicator will be a "{Z}" 
        instead of "[Z]".

        In the packet or AMTOR communications mode, a "[R]" will be 
        displayed next if LAN-LINK is configured for store and forward 
        (:QSP:).

        In the packet and AMTOR communications modes, if the beacon mode 
        is enabled a "[B]" will be flashing yellow. If someone has 
        connected and sent a :QRT: sequence, the "[B]" will be flashing. 
        The "[B]" will be followed by a "[M]" if there are messages 
        pending. The number in the square brackets with the "[M]" is the 
        number of messages (*.OUT files) pending.

        In the packet communications mode, if the SAREX mode is enabled, 
        a "[S]" will be shown next. The "[S]" will be flashing while 
        capture to disk is in progress. If SAREX packets have been copied 
        a happy face will be displayed in the square brackets together 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 18


        with the "S". If the SAREX Orbiter robot is active a flashing 
        ">>" will be displayed.

        In the packet communications mode, if the digipeat Detect mode is 
        enabled, a "[D]" will be displayed next.

        In the packet communications mode, if connected and ELMER is 
        active, an "[E]" will be displayed. The number with the "E" shows 
        ELMER's state.

        In the packet communications mode, the terminal sub-modes are 
        then displayed as follows;

        SOLO This lets you only see messages addressed to you.
        CQ/B This lets you see beacons and CQ calls as well.
        TRFC This lets you see packets containing messages as well.
        EVRY This lets you see everything on channel, including the link 
             control packets.
        MAIL This lets you monitor packets from a specific station. In 
             the PK-232, you can do it without displaying the headers.

        Note each mode may not be available in each TNC.

        The next item to be displayed is a callsign, under the following 
        conditions: the call of the station connected with, will be 
        prefixed by a "*>" when connected, and by a "->" when a connect 
        request is in progress. If a disconnect is in progress, the 
        callsign will be replaced by a "$$$$". The callsign will be seen 
        as flashing when a connect is in progress.

        In the MAIL mode, the callsign of the station that you are 
        "reading the mail" on will be displayed. Otherwise, the callsign 
        displayed will be that of the one you are connected with.

        If an Alert Call has been entered, it will be displayed next. 
        Similarly, if a Target Call has been designated, the target call 
        will be displayed next. The display will be slightly different of 
        the calls have been heard/worked. A "!!>" before the flashing 
        call indicates that the Alert function is active. A "<->" before 
        the Alert Call signifies that packets to or from that call have 
        been heard on frequency. A smiling face in front of the call, 
        signifies that it has been worked. A "->" is displayed before the 
        Target Call.

        The next items to be displayed are the packet multi user mode 
        displays. If the conference bridge is up, a flashing yellow 
        bridge will be shown. If only the conference mode is set, the 
        letter "C" will be flashing, if the basic multi user mode is set, 
        the word "M" will be seen. The callsign will be prefixed by the 
        I/O channel number/letter, and will be in the color allocated to 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 19


        the traffic on that channel. The number shown after the flashing 
        letter is the number of streams that LAN-LINK thinks that you are 
        connected on.

        In the non packet modes, the callsign displayed will be that of 
        the station being worked (entered by the AMTOR robot, the 
        automatic CQ call recognition, or by the operator using the Alt-C 
        or Alt-E keys). In AMTOR, the SELCAL of the other station will 
        also be displayed sometimes, usually if you entered the call.

        An "[L]" will be displayed in the non packet modes when a 
        callsign is entered. The "[L]" will flash to remind you (to log 
        it) until the QSO is logged.

        3.0 HOT KEYS

        LAN-LINK contains a number of "Hot" keys to allow you to perform 
        common operations with a minimum of key strokes. The keys perform 
        related but slightly different tasks in each communications mode. 
        A list of those available is shown in Table 3-1. Should you 
        require any more hot keys, I suggest you use an external program 
        with a Keyboard Macro capability such as Borland's Superkey. 
        Consider the action of each key in detail.

        3.1 Alt-A Alert Call (Packet) and AMTOR ARQ Call/Talk

        In the Packet Communications Mode, this key combination performs 
        the same task as the Alert Call option in the Call Menu.

        In AMTOR, this key combination will attempt to send an ARQ call 
        to the desired station, transmit the callsign sequence when 
        linked and allow you to continue typing text (i.e. it will not 
        transmit the "+?" characters). Use this command option to log on 
        to an APLINK PBBS.

        3.2 Alt-B Send Break/AMTOR Changeover

        In the Packet Communications Mode, activating this key 
        combination sends a "BREAK" signal to the TNC. Use this key 
        combination to get out of the TNC's transparent mode.

        In the AMTOR Communications Mode, use this key combination to 
        force a changeover. You can type text into the outgoing buffer 
        and then force a changeover without losing that text.

        3.3 Alt-C Call/Connect to Someone

        This key combination works in almost the same manner in both the 
        packet and non packet communications modes as described in the 
        following sections.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 20



                           Table 3-1 LAN-LINK Hot Keys
        Hot Key                  Communications Mode
        _______________________________________________________________
                  Packet      AMTOR/Pactor/G-TOR   BAUDOT/ASCII    CW
        ____________________________________________________________________
        A    Set ALERT Call      ARQ Call/Talk      ------        ------
        ____________________________________________________________________
        B    Send 'Break to TNC'  Force Changeover  ------        ------
        ____________________________________________________________________
        C    Connect             ARQ Call            Call          Call
        ____________________________________________________________________
        D    Disconnect  Toggle Receive Modes   Receive Mode   Disengage Lock
        ____________________________________________________________________
        E    Enter Call   Enter Call and Selcal    Enter Call Enter Call
        ____________________________________________________________________
        F    Flush TNC Buffer (all communications modes)
        ____________________________________________________________________
        G    Grab Call and frequency (PacketCluster Flag set)
        ____________________________________________________________________
        H    Display function key Information Screen
        ____________________________________________________________________
        J    Jump to DOS (all communications modes)
        ____________________________________________________________________
        K    PacketCluster Spot
        ____________________________________________________________________
        L    Edit Log Entry (all communications modes)
        ____________________________________________________________________
        M    Scan Message (all communications modes)
        ____________________________________________________________________
        N    Next I/O Stream
        ____________________________________________________________________
        O    Turn Robot ON  Turn Robot ON            ------        ------
        ____________________________________________________________________
        P    Turn Printer ON/OFF (all communications modes)
        ____________________________________________________________________
        Q    call QRZ       call QRZ in FEC          call QRZ    call QRZ
        ____________________________________________________________________
        R    Retry Connect  Retry last Call (entered).
        ____________________________________________________________________
        S    Scan Logbook (all communications modes)
        ____________________________________________________________________
        W    :QRA:         ----------           -------         ------
        ____________________________________________________________________
        X    Exit to DOS (all communications modes)
        ____________________________________________________________________
        Y    Zap PacketCluster   ----------------    Transmit RY's -----           
        ____________________________________________________________________
        Z    Zap BBS    Drop Link after         Receive mode after 
                        after sending contents of buffer


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 21


        ____________________________________________________________________
        3           Set foreground color in outgoing text
        ____________________________________________________________________
        4           Set background color in outgoing text
        ____________________________________________________________________

        3.3.1 Non Packet Modes

        You use this key combination to call a station heard on the band. 
        In AMTOR the link request will be sent in the ARQ Mode to the 
        SELCAL of the desired station. (Note that this option sends the 
        "+?" after the callsign sequence).

        3.3.2 Packet Mode

        You use this key combination to attempt a connect with another 
        packet station. In a multiconnect situation the LAN-LINK will 
        auto-matically select a free I/O channel to try the connect. 

        3.3.2.1 Names, Handles and Paths: If you so desire, you can 
                 create a directory file (default name is LAN-LINK.DIR) 
                 and keep a list of names and calls. The computer will 
                 look up a name and call the station by its callsign. For 
                 example if you put "Joe G3ZCZ" as a line in the file, 
                 when you tell the computer to connect to Joe, it will 
                 try to connect to G3ZCZ. If you enter " 4X4HF 4X4HF V 
                 4X1AA, 4Z4ZB, 4X4IL" on a line in the file, you only 
                 need to type "4X4HF" to set up the correct connect path. 

                 You can also use this feature to automate a NET/ROM 
                 and/or a KA-Node path connection. 

        3.3.2.2 Loop Backs: In the Packet Communications Mode, if you 
                 want to loop back through someone else you would have to 
                 type "C YOURCALL VIA OTHERCALL" to the TNC. For example 
                 if I wanted to loop back through 4X6AA, I would have to 
                 type the command "C G3ZCZ VIA 4X6AA" to the TNC.

                 In LAN-LINK you just have to enter the "/" character 
                 followed by the call of the station you want to loop 
                 back through. For example if I wanted to loop back 
                 through 4X6AA, I just need to enter "/4X6AA" as the call 
                 to connect to at the correct prompt, and LAN-LINK will 
                 tell the TNC to try to connect to G3ZCZ via 4X6AA, 
                 namely issue the command "C G3ZCZ VIA 4X6AA" to the TNC.

        3.4 Alt-D Disconnect or Receive

        This key combination performs the same task as Function Key 8 
        (F8) EXCEPT in MORSE and AMTOR. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 22



        In the Morse communications mode, this key disengages the receive 
        speed lock in the PK-232 to unlock the PK-232 from the last 
        signal copied. It lets you lock onto another signal faster.

        In AMTOR this key toggles the receive mode between ARQ and FEC 
        signals (QSO's in progress and CQ calls).

        3.5 Alt-E Enter Call

        This key combination lets you enter the call of any station 
        calling you into the program. If you type the Enter Key in 
        response to the prompt, you can later use Function Key (F3) to 
        transmit the sequence "DE YOURCALL". You may also use the Retry 
        feature to call that station.

        In AMTOR, you use the feature to enter the callsign and SELCAL of 
        the station you are listening to and may want to call later.

        3.6 Alt-F Flush TNC Buffer

        This key combination performs the same task as the Flush TNC 
        Outgoing buffer option in the TNC Menu.

        3.7 Alt-H Help Information for Function Keys

        This key combination lets you display a brief reminder of the 
        action of each hot key. It performs the same function as the "H" 
        option in the Main Menu.

        3.8 Alt-J Jump to DOS

        This key combination lets you "Jump to a DOS Shell". It performs 
        the same function as the "J" option in the Main Menu.

        3.9 Alt-K PacketCluster DX Alert

        This key combination initiates the PacketCluster DX Alert sequence 
        described in the BBS Menu. 

        3.10 Alt-L Log Contact

        This key combination appends the callsign for the current QSO to 
        the Log. 

        3.11 Alt-M Message Scan

        This key combination performs the same task as the Message Scan 
        choice in the Message Menu. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 23


        3.12 Alt-N Next Stream

        In the Packet Communications Mode, if you are using the multiple 
        connect capability of LAN-LINK, this key combination prompts you 
        to change I/O streams, and display the state of the I/O streams, 
        showing which ones were last used to send or receive something. 
        To change I/O streams, move the cursor to the desired stream then 
        push the "Enter" Key. The calls in the Next Stream window update 
        when stations connect and disconnect. In the event of the window 
        not being correct, you may manually enter or delete calls using 
        the "Insert" Key to enter a call, and the "Delete" Key to remove 
        a call.

        The data about the streams will be shown in the same colors as 
        the multi-stream text colors.

        3.13 Alt-O Turn Robot On

        This key combination performs the same function as the Set ROBOT 
        option in the AMTOR Terminal Menu. The hot key combination 
        however, is active in both the Packet and AMTOR communications 
        modes.

        This function key also puts the Packet and AMTOR Contest 
        operation into automatic.

        3.14 Alt-P Turn Printer ON/OFF

        This key combination performs the same function as the toggle 
        printer on/off option in the Parameter Menu. 

        3.15 Alt-Q Call QRZ

        This key combination transmits the sequence "QRZ QRZ QRZ DE 
        YOURCALL" and turns the transceiver back to receive. In AMTOR, it 
        sends the sequence in FEC and adds the SELCAL.

        3.16 Alt-R Retry Call/Connect

        This key combination allows you to retry a connect that for some 
        reason did not go through the first time. It saves wear and tear 
        on your fingers particularly if the desired connect path is via a 
        number of digipeat relays or through a number of Nodes.

        In the non packet modes, it allows you to retransmit a call to 
        another station without having to re-enter the call.

        If you have previously used the "Enter Call" feature to put a 
        callsign in the program when you hear that station, you can use 
        the Retry command to call him later when the QSO in progress 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 24


        terminates. 

        3.17 Alt-S Scan Log

        This key combination performs the same function as the Scan 
        option in the LOG Menu.

        3.18 Alt-W :QRA:

        In the Packet Communications Mode, this key combination performs 
        the same task as the "W" option in the LAN-LINK menu. It puts the 
        TNC in the converse mode, sends a ":QRA:" and returns the TNC to 
        the command mode.

        3.19 Alt-X Exit to DOS

        This key combination performs the same task as the Exit to Dos 
        choice in the Main Menu. It exits the program and returns you to 
        DOS. 

        3.20 Alt-Y Zap PacketCluster/RTTY Transmit "RY"s

        In the Packet Communications Mode, this key combination first 
        prompts you with the callsign of the PacketCluster. If you enter 
        a callsign, the entered callsign will become the new Packet-
        Cluster call. LAN-LINK then issues a connect request to the 
        PacketCluster. In the RTTY communications mode, this key 
        combination causes a sequence of "RY"s to be transmitted.

        3.21 Alt-Z Zap PBBS

        In the Packet Communications Mode, the Alt-Z key initiates a PBBS 
        Mail Snatch. You use this key if you connect to a PBBS before you 
        hear its beacon, or if you have disabled the PBBS Mail Snatch 
        feature. If you are connected to a PBBS, the key must be used 
        BEFORE the first ">" is received. The first ">" triggers the 
        sequence. If you have already received that first ">", send the 
        PBBS any command, and the sequence should begin when the PBBS 
        signals that it has completed processing that command. If you are 
        not connected, LAN-LINK will first try to connect to the PBBS, 
        then perform the sequence.

        When you use this command you will be asked if you want to upload 
        or download. If you want to download, just push the "Enter" Key. 
        A Download (Mail from the PBBS to you) will automatically be 
        followed by an Upload if the *.BBS file exists.

        The download default sequence performed by the PBBS Mail Snatch 
        is as follows:



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 25


                   RM   To read your messages, (Configurable)
                   L    To let you know what is new on the PBBS,
                   LM   To list ALL your messages on the PBBS,
                   B    To log you off the PBBS.

        LAN-LINK will wait for the ">" as the last character of the line 
        of text being received from the PBBS, before issuing the next 
        command in the sequence. Your messages will be placed in a 
        message file YOURCALL.OUT as if someone else had left a message 
        for you.

        The "RM" may be customized in the LAN-LINK.SYS file to "RN" or 
        "VM" depending on the software in your local PBBS, and, on your 
        preference.

        During the time that the PBBS is responding to the "L" command 
        with a list of new messages, LAN-LINK is scanning the lines 
        containing the messages to see if it finds one containing a Scan 
        Word. If it does it will queue a request to download that 
        message. The line of text will also be displayed in a color that 
        matches the colors those scan words are shown in the window 
        generated by exercising option W in the Parameter Menu.

        The PBBS Mail Snatch can be initiated in two ways. It can be 
        initiated when your incoming screen displays a "Mail" beacon 
        (received from your local PBBS) with your call in the first line 
        following the header, or by LAN-LINK's Zap PBBS function (this 
        key combination). The automatic PBBS Zap will not take place if 
        LAN-LINK is in the multi-user mode.

        In the event of a PBBS Mail-Snatch, if the *.BBS file exists for 
        that PBBS, the file will be processed and the contents sent to 
        the PBBS. Thus if you don't get a chance to send the mail before 
        LAN-LINK downloads the mail from the PBBS, it will send it for 
        you. 

        When the PBBS has accepted the commands the name of the file is 
        changed from "*.BBS" to "*.n", where "n" is a number increasing 
        sequentially each time the function is performed from a base 
        value set up in the LAN-LINK.SYS file. For example, the file name 
        KE8X.BBS will be changed to KE8X.001 the first time it happens. 
        In this way, you will have a copy of the outgoing file on your 
        disk until you choose to delete it.

        In the real world however, message formats are nonstandard, and 
        can contain any set of characters. The algorithm developed here 
        transmits the next line in the *.BBS file when LAN-LINK sees a 
        "trigger" character string unless one of the "inhibitor" 
        character strings is also present on the line of the message text 
        received by LAN-LINK.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 26



        These "trigger" character strings are ">" (as the last character 
        of the line of text), and the customizable ones such as "Enter", 
        "Subject", "Sj:" and "Msg:". The "inhibitor" character strings 
        are "R:", "<" and "Message" ("R:" as in routing headers and "<" 
        and "Message" as in Message-Id: <message number> in message 
        headers).

        This should cover most simulated manual PBBS message reading 
        (WA7MBL and W0RLI/VE3GYQ) and avoid false triggering due to ">"s 
        showing up in message and routing headers.

        When LAN-LINK finishes processing the *.BBS file, it will send a 
        "B" command to the PBBS to terminate the session. This PBBS Zap 
        feature is designed to minimize the time you spend connected to 
        the PBBS by allowing you to scan the message list when automat-
        ically receiving your mail, prepare your replies, and download 
        requests off-line and then later read the incoming messages or 
        files without tying up the PBBS. For this reason, it thus 
        disconnects you from the PBBS. You can, however, override the 
        automatic disconnect command for the duration of the connection 
        using the "F" option in the Parameter Menu.

        3.22 Alt-= Toggle Miscellaneous Flag

        This key combination performs the same function as the "+" option 
        in the parameters menu.

        3.23 End "> +?" [Over]

        In the Packet Communications Mode this command sends your 
        callsign followed by the ">" and "Carriage Return, Line Feed" 
        character combination. You may use this to signal "OVER" in a 
        packet contact.

        In the AMTOR Communications Mode this command sends the "+?" 
        sequence of characters which is the software "OVER" signal. LAN-
        LINK will change colors when it recognizes the '+?' in the 
        incoming window.

        In the Pactor Communications Mode this command sends the "=>" 
        sequence of characters and switches the link to allow the other 
        station to send. LAN-LINK will change colors when it recognizes 
        the '=>' in the incoming window.

        In the MORSE and RTTY (BAUDOT and ASCII) communications modes, 
        this command lets you transmit the "KN" sequence and returns you 
        to the Receive Mode. LAN-LINK will change colors when it 
        recognizes the 'KN' in the incoming window. In these modes there 
        is no standard for signaling 'over'. The 'KN' sequence may show 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 27


        up in text (i.e. in the word KNOW) or in a callsign (i.e. G9KNA) 
        and cause a color change. If this "random" color change bothers 
        you in BAUDOT, change line 114 in the LAN-LINK.SYS file from KN 
        to some other pair of characters that should not show up in 
        normal text.

        If you have typed something into the "type ahead buffer" and then 
        press this key, the contents of the buffer will be transmitted 
        followed by the turnover command.

        For example, if you are 4X6AA, and you are working G3ZCZ, then 
        you would use Function Key 3 (F3) to transmit the sequence "G3ZCZ 
        de 4X6AA" and this key to send "over" and revert to receive. 

        3.24 PgUp Scrollback (Scrolls back incoming text)

        This key lets you repeat the display of up to 412 lines of 
        incoming text which has scrolled out of the incoming window. You 
        may print it or capture it to disk during the repeat. 

        The bottom line menu displays your options when showing the 
        scroll back information. Use the "Escape" key to terminate the 
        Scrollback Mode.

        You can save the contents scrollback buffer displayed on the 
        screen by turning the "Capture-to-Disk" on, and then writing text 
        to the window. Anything written will be captured. If the Capture-
        to-disk is ON before or during scrollback, you will get two 
        copies of the text in the file.

        3.25 The Home Key

        The Home Key will clear the window screen that the cursor happens 
        to be in at the time that the key was depressed, and will then 
        position the cursor at the top left hand corner of that window.

        3.26 The Down Arrow Key

        The Down Arrow Key toggles the Normal/Reverse Sideband command in 
        all communications modes except MORSE. The sideband is depicted 
        in the status window by the "Up" and "Down" arrows. If the "Down" 
        Arrow is showing, you are set for Lower Sideband (LSB) which is 
        the one normally used.

        If you set your transceiver to LSB, you will be set correctly for 
        all modes. If you have reversed the sidebands, a flashing "Up" 
        Arrow will be displayed. For CW operation you may set your rig to 
        the CW position and ignore the sideband setting. If you use FSK, 
        just set it so that it works for you.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 28


        3.27 Shift/Baudrate Control Keys
         
        The following keys are used to control the Shift (Wide or narrow) 
        and the Radio link baudrate in the BAUDOT and ASCII 
        communications modes. In the BAUDOT and ASCII communications 
        modes all baud rates supported by the PK-232 may be selected.

        3.27.1 RIGHT ARROW: This key speeds up the baud rate. In the CW 
                 communications mode, the right arrow increases the CW 
                 speed by 1 wpm.

        3.27.2 LEFT ARROW: This key slows down the baud rate. In the CW 
                 communications mode, the left arrow decreases the CW 
                 speed by 1 wpm.

        3.27.3 UP ARROW: This key toggles the shift from Wide shift (850 
                 Hz) to Narrow shift (170 Hz) and back. If you are using 
                 a KAM, it will also pass through the 425 Hz shift 
                 position.

        3.27.4 DELETE: This key toggles the USOS command (RTTY only). 

        The state of each of the above commands are displayed in the 
        status window at the top of the screen. If USOS is active, "USOS" 
        will be shown. The shift is shown as "W" or "N" for wide or 
        narrow respectively. 

        3.28 Control-Z (^Z)

        This key combination is used in the Packet Communication Mode to 
        signal the end of a file or message, when loading messages into 
        another LAN-LINK system or into a PBBS. In the AMTOR Communica-
        tions Mode, it is automatically translated into the sequence " 
        :EOF: +? " which can be used to terminate a message being stored 
        in another LAN-LINK AMTOR mailbox. 

        3.29 Control T (^T)

        This key combination inserts the date-time-text string into the 
        outgoing buffer. A typical example is "11-Mar-93 01:39".

        4.0 FUNCTION KEYS

        Function keys are used to perform operations common to all 
        communications modes, or to allow fast performance of a function 
        without having to go through several layers of menus. The action 
        of each of the function keys is described in the following 
        sections. The function key number corresponds to the paragraph 
        number, namely 4.1 refers to Function Key 1 (F1), etc.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 29


        4.1 Capture to Disk Toggle (F1)

        This key toggles the "capture-to-disk" command. When the 
        "capture-to-disk" is active, all incoming text (including "Echo 
        as sent" outgoing text) is stored on a disk (floppy or hard) in a 
        file called "YYMMDD.RUN" where YY is the last two digits of the 
        year, MM the month and DD the day (E.G. 900824.RUN). If this file 
        does not exist the first time that LAN-LINK is loaded, it is 
        created. From that time on, for the rest of that day, successive 
        activations append new data to the contents of the file.

        Each time the command is activated a datestamp (or timetag) will 
        be written to the file.

        When a Packet station connects "capture-to-disk" will be 
        activated automatically unless you instruct LAN-LINK not to do so 
        with the Capture-to-disk flag. Packet connects will thus be 
        recorded in their entirety automatically unless you turn off the 
        "Capture-to-disk" during the course of the QSO. "Capture-to-disk" 
        will be stopped at disconnect time.

        You may later edit the file at your convenience with your 
        favorite word processor or the included Editor. However, if your 
        word processor can only handle files smaller than 64k, make sure 
        that the "capture-to-disk" file remains smaller. You can do this 
        by renaming the file to something like "LAN-RUN.001". LAN-LINK 
        will automatically close the "capture-to-disk" file when you 
        terminate the program and return to DOS.

        You can make Capture-to-disk active when you scroll back. You can 
        use this feature to save data that has already scrolled by the 
        window. 

        4.2 Send Brag Tape and Talk (F2)

        This command lets you transmit the Brag Tape (Default LAN- 
        LINK.TXT). In the non packet modes, it will leave the transmitter 
        on after sending the file. In the packet mode it will send a ^Z 
        after sending the file to notify the recipient that the file is 
        complete.

        4.3 Transmit Callsign Sequence (F3)

        This command lets you transmit the following sequence OTHERCALL 
        DE YOURCALL. For example, if you are 4X6AA, and you are working 
        G3ZCZ, then this command would transmit the sequence "G3ZCZ de 
        4X6AA". You may use this key at the start and end of a 
        transmission in any mode except Packet.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 30


        4.4 Send Brag Tape (F4)

        This command lets you transmit the Brag Tape (Default LAN-
        LINK.TXT). In the non packet modes, it will turn the transmitter 
        off after sending the file.

        4.5 Show Packet "MH" list and Point and Shoot Connect (F5)

        This command lets you see what calls the TNC has heard recently 
        on the Packet channels. You can see up to 18 callsigns, with the 
        date and time they were last logged by the TNC. Refer to the "MH" 
        command in the TNC manual for the particulars of the display.

        The MH list shows up in a special window and freezes until you 
        depress any key. While the list is frozen, LAN-LINK is not 
        monitoring received data, so don't freeze it too long. 

        When you activate F5, LAN-LINK redirects all data coming from the 
        TNC into the MHwindow. If the MH list is blank, or information 
        comes in from the TNC between the time you entered the command 
        and the time the list is sent back, subsequent text from the TNC 
        will show up in the MH window until the next "Cmd:" appears or 18 
        lines of text have been received.

        You can also use this command in a point and shoot method for 
        attempting a connect with a station you have heard. Bring up the 
        MH Window and move the cursor to the desired callsign. When the 
        cursor is positioned on any character in the call, press the 
        "Enter" Key and that call will be recognized as the callsign. If 
        the call is joined to the word "Cmd:" or the cursor is positioned 
        on a space or blank, the connect attempt will be inhibited.

        LAN-LINK has no way of knowing when the MH list is complete. 
        Consequently, it sends two commands to the TNC to implement this 
        feature. The "MH" command instructs the TNC to start sending the 
        MH List, the "ZCZ" command forces an error response from the TNC. 
        LAN-LINK uses the error response to close the MH Window.

        This command does not work on the TNC1.

        4.6 Auto CQ Call (F6)

        This command will send a CQ sequence, wait a presettable delay 
        and then repeat the CQ sequence until it receives your call back 
        from someone else. When it does so, it will alert you with a 
        Connect Alarm signal, reset the delay timer, and revert to the 
        normal or listening mode. In AMTOR it will revert to the mode in 
        which it is waiting for an ARQ call and is able to copy FEC 
        signals on frequency.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 31


        When the Automatic CQ sequence is in operation, an indication 
        will be shown in the status window. The indicator will be steady 
        while the transmitter is sending the CQ text, and will blink 
        while the receiver is listening for a reply.

        The time delay between calls is set using the "Q" command in the 
        Parameters Menu (Set CQ delay time). It is also set as a defined 
        default by you when you setup your LAN-LINK.SYS file.

        The automatic CQ command will only work in the TNC non packet 
        modes if the "Echo as Sent" parameter is set to "ON" per the LAN-
        LINK.SYS file. In other words, you must be able to see the CQ 
        text slowly echo in the incoming window for the command to work. 
        This is because the "K K K" (or "+?" in AMTOR) sequence is used 
        to arm the software to look for a reply.

        In AMTOR you will get the connect alarm only when the replying 
        station transmits the "+?" character combination.

        The check for the detection of your callsign and the connect 
        alarm sequence only occur after a line feed character has been 
        received.

        Under most conditions in AMTOR, many in RTTY, and some in MORSE, 
        LAN-LINK will recognize the callsign of the station answering 
        your CQ and display it in the status window. In the event that it 
        fails completely, the sequence "--?--" will show up in the status 
        window. Since the callsign recognition algorithm used just looks 
        for the first word following the "DE space" sequence and assumes 
        that it has the callsign, be careful to check it when operating 
        under QRM conditions. You can override the automatic call 
        selection with the Enter Callsign command in the Call Menu.

        The automatic CQ sequence is canceled when an incoming call is 
        detected (only if the Beacon or Robot-Mailbox Mode is not 
        selected), if you push the disconnect command key, the "End" key, 
        F3, or if you change communications modes.

        4.7 Activate Type Ahead Buffer/AMTOR Relink (F7)

        This key is not available in the Packet Communications Mode. It 
        also functions somewhat differently in the AMTOR and other 
        communications modes as described in the following sections.

        4.7.1 Activate Type Ahead Buffer

        The use of this key sets LAN-LINK to the "Type Ahead" Mode. This 
        is necessary for the PK-232 only, the KAM and the MFJ1278 have 
        the feature built in. Any characters then typed at the keyboard 
        will be placed into the TNC transmit buffer. The contents of the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 32


        buffer will be transmitted over the air when the transmit command 
        is invoked with Function Key 10 [F10]. 

        This feature allows you to "type ahead" as you can enter text 
        into the transmit buffer while viewing incoming words in the 
        INPUT window in the screen. Any characters typed from the 
        keyboard will be echoed in the OUTGOING window on the screen.

        4.7.2 AMTOR Relink

        If you return to the Command Mode when linked to another station 
        in AMTOR, use this key to get back to the Converse Mode. If the 
        link times out, you can try to relink with this key if you have 
        entered the SELCAL of the other station.

        4.8 Disconnect, Disengage or Receive (F8)

        This function key returns the station to the receive communi-
        cations (TNC command) mode. It may also be used to abort the 
        automatic CQ sequence. If you use it to abort a CQ sequence while 
        the transmission is in progress, you may also want to flush the 
        PK-232 transmit buffer by using the Flush command in the TNC Menu 
        or the Alt-F hot key combination.

        In a multi-connect situation the program will prompt you to tell 
        it which I/O channel to disconnect.

        In AMTOR this command key toggles LAN-LINK between the Chirpcopy 
        Mode (listening to a QSO in progress) and monitoring FEC 
        transmissions (CQ calls).

        4.9 Put TNC in CMD Mode (F9)

        This command puts the TNC into the Command Mode. At this time, 
        the program is transparent and acts as a dumb terminal (except 
        for placing incoming and outgoing text in the relevant windows). 
        You use this Mode for overriding any of the TNC default 
        conditions.  (See I told you that you had to read the TNC 
        manual).

        4.10 Put TNC in CONVERSE/Transmit/AMTOR FEC (F10)

        This command places the TNC into the transmit or Converse Mode. 
        The transmitter is turned on and the contents of the transmit 
        buffer are transmitted. In the non packet communications modes, 
        the outgoing characters will be echoed back from the TNC and 
        displayed in the INCOMING window on the CRT as they are 
        transmitted on the air. In the AMTOR communications modes, this 
        key puts the TNC in the FEC Mode and turns the transmitter on.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 33


        4.11 Alternate Function Keys

        These keys transmit the files with the fixed names LAN- LINK.001 
        through LAN-LINK.010 (the suffix number corresponds to the 
        function key). These files must be located in the same sub-
        directory as the LAN-LINK.EXE program. The transmitter is left on 
        when the file has been sent.

                         4.11.1 Send/Talk file LAN-LINK.001
                         4.11.2 Send/Talk file LAN-LINK.002
                         4.11.3 Send/Talk file LAN-LINK.003
                         4.11.4 Send/Talk file LAN-LINK.004
                         4.11.5 Send/Talk file LAN-LINK.005
                         4.11.6 Send/Talk file LAN-LINK.006
                         4.11.7 Send/Talk file LAN-LINK.007
                         4.11.8 Send/Talk file LAN-LINK.008
                         4.11.9 Send/Talk file LAN-LINK.009
                         4.11.10 Send/Talk file LAN-LINK.010

        If the Mode File Flag is set (see 10.14), the file names will 
        change according to the modes.

        In the non packet communications modes, the transmitter is left 
        on when the file has been sent. In AMTOR, the changeover 
        character pair (+?) is not sent.

        4.12 Shift Function Keys

        These function keys show the contents of the files with the fixed 
        names LAN-LINK.001 through LAN-LINK.010 (the suffix number 
        corresponds to the function key). These files must be located in 
        the same sub-directory as the LAN-LINK.EXE program.

                         4.12.1 Show contents of file LAN-LINK.001
                         4.12.2 Show contents of file LAN-LINK.002
                         4.12.3 Show contents of file LAN-LINK.003
                         4.12.4 Show contents of file LAN-LINK.004
                         4.12.5 Show contents of file LAN-LINK.005
                         4.12.6 Show contents of file LAN-LINK.006
                         4.12.7 Show contents of file LAN-LINK.007
                         4.12.8 Show contents of file LAN-LINK.008
                         4.12.9 Show contents of file LAN-LINK.009
                         4.12.10 Show contents of file LAN-LINK.010

        If the Mode File Flag is set (see 10.14), the file names will 
        change according to the modes.

        4.13 Control Function Keys

        These function keys show the first lines of the files with the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 34


        fixed names LAN-LINK.001 through LAN-LINK.010 (the suffix number 
        corresponds to the function key). These files must be located in 
        the same sub-directory as the LAN-LINK.EXE program. 

        If the Mode File Flag is set (see 10.14), the file names will 
        change according to the modes.

        5.0 THE MAIN MENU

        When you press the "Escape" Key, the Main Menu shown in Figure 5 
        appears on your screen and provides you with a number of choices 
        as described in the following sections. Type in the single letter 
        to make your choice.

                               Figure 5 Main Menu

                                 A Quick Menu
                                 B PBBS Menu
                                 C Call Menu
                                 D eDit Menu
                                 E Event/Clock Menu
                                 F Files Menu
                                 H Help with Function keys
                                 J Jump to DOS Shell
                                 K Lan-linK Menu
                                 L Log Menu
                                 M Message Menu
                                 N TNC Menu
                                 O AMSAT-OSCAR Menu
                                 P Parameter Menu
                                 Q Q Codes [NC/L]
                                 R Radio Menu
                                 S communicationS Mode Menu
                                 T Terminal Mode Menu
                                 X eXit LAN-LINK
                                 Z Elmer Menu

        Different options will show up in each menu depending on the 
        connect state (in packet) or the type of TNC that you are using. 
        For example, if you are using a TNC that only supports packet, 
        the non packet menus will not be seen. The PBBS Menu is only 
        active when you are connected to another station.

        5.1 The Quick Menu

        The Quick Menu shown in Figure 5.1 is designed for new users and 
        provides the most commonly used functions in a single Menu. Type 
        in the single letter to make your choice. Each option is 
        described below.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 35


                            Figure 5.1 The Quick Menu

                                 A Auto CQ        
                                 B Send Brag Tape     
                                 C Connect to Someone 
                                 I Initialize PK232   
                                 L Log                
                                 M Change Mode        
                                 Q Call CQ            
                                 S Send File          
                                 T Send File/Talk     
                                 Z QRZ                
                                 1..0 Send/Talk 1..10 

        5.2 Auto CQ

        This option initiates the automatic CQ sequence in which LAN-LINK 
        sends out a CQ call, listens for a reply, and if none is 
        received, sends out another CQ call, and so on, ad infinitum. It 
        is the same as using Function Key 6 (F6).

        5.3 Send Brag Tape

        This option transmits the Brag Tape is the same as using Function 
        Key 2 (F2).

        5.4 Call Someone

        This option is used when you want to call or connect to another 
        station. 

        5.5 Log Menu

        This option invokes the logbook.

        5.6 Change Communications Mode

        This option invokes the Communications Mode Menu. You use it to 
        change TNC communications modes.

        5.7 Call CQ

        This option is used to initiate a single CQ call.

        5.8 Send/Talk File

        This option is used to send a file. When the file has been sent, 
        the transmitter will stay on. This option performs the same 
        function as Function Key 4 (F4).



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 36


        5.9 QRZ

        This option is the same as using Alt-Q Function Key (Alt-Q).

        5.10 Send/Talk LAN-LINK Files 001..010

        This option is used to transmit the contents one of the LAN- LINK 
        buffer files. You select the number, LAN-LINK does the rest. The 
        option is the same as that provided by the Alternate Function 
        Keys.

        6.0 THE PBBS/PacketCluster Menu

        The PBBS menu shown in Figure 6 gives you smart file transfer 
        capabilities with a PBBS. The menu is only active when you are 
        connected to another packet station. Type in the single letter to 
        make your choice.

                               Figure 6 PBBS Menu
                                 D Download Text File           
                                 X Download Binary File (Xmodem)
                                 Y Download Binary File (Ymodem)
                                 C Zap PacketCluster
                                 P Zap PBBS
                                 K Turn PacketCluster Mode OFF
                                 D Send DX Alert
                                 1 Clear All Search Flags
                                 2 Set All Search Flags
                                 3 Set All CW Search Flags
                                 4 Set All SSB Search Flags
                                 5 Set/Clear Individual Search Flags
                                 6 Set/Clear Current Band Search Flags


        6.1 Download Text Files

        This option lets you download a text file from the PBBS into a 
        separate text file on your disk. Enter the full PBBS download 
        command at the prompt line.

        To download a file from a W0RLI PBBS such as FILENAME.TYP in the 
        "A" sub-directory you'd enter "DA FILE- NAME.TYP". To download 
        the same file from the PACKET sub-directory of a WA7MBL PBBS 
        you'd enter the command "D \PACKET\FILENAME.TYP".

        If you use the "D" command to download a text file, it will end 
        up in a separate file on your disk ONLY IF a file of the same 
        name does not exist on your drive. If a file with the selected 
        name already exists on your disk drive you will get an error 
        message. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 37



        6.2 Download Binary File (Xmodem)

        This option lets you download a binary file from the PBBS or 
        other packet station using the Xmodem protocol into a separate 
        text file on your disk. You have to configure the Xmodem Receive 
        Batch file before you use this command.

        When you use this command, you first have to tell the PBBS the 
        name of the file you are going to download, and then bring up 
        this option to tell LAN-LINK that a binary file is on its way. 
        LAN-LINK uses an external binary file transfer protocol to do the 
        actual file.

        6.3 Download Binary File (Ymodem)

        This option lets you download a binary file from the PBBS or 
        other packet station using the Ymodem protocol into a separate 
        text file on your disk. You have to configure the Ymodem Receive 
        Batch file, before you use this command.

        When you use this command, you first have to tell the PBBS the 
        name of the file you are going to download, and then bring up 
        this option to tell LAN-LINK that a binary file is on its way. 
        LAN-LINK uses an external binary file transfer protocol to do the 
        actual file.

        6.4 Zap PacketCluster

        This option is the same as the Alt-K function key.

        6.5 Zap PBBS

        This option is the same as the Alt-Z function key.

        6.6 Turn PacketCluster Mode ON/OFF

        This option turns the PacketCluster Mode ON and OFF. If the flag 
        is on LAN-LINK will scan the incoming lines for a DX Alert 
        message. 

        You may monitor a PacketCluster in the TRAFFIC mode. When a 
        DX Alert shows up, it is sent to each connected station in turn. 
        LAN-LINK will only interpret the first one. 

        LAN-LINK displays the parts of the DX Alert message in different 
        colors. The colors correspond to the Multi String Colors, shown 
        in the color option in the Parameter Menu.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 38


        6.7 Send DX Alert

        This option is the same as the Alt-K function key. Use it AFTER 
        you have made the contact.

        If you have a valid Radio, LAN-LINK will read the frequency from 
        the Radio. If not, LAN-LINK will prompt you to enter the 
        frequency. LAN-LINK will then prompt for the call of the DX 
        Station, and will assume that you want to send the call of the 
        one you have just logged.

        6.8 Clear All Search Flags

        This option clears all the band search flags. LAN-LINK will not 
        check any bands. These options are provided for fast temporary 
        changes when working a contest.

        6.9 Set All Search Flags

        This option sets all the band search flags. LAN-LINK will check 
        every band.

        6.10 Set All CW Search Flags

        This option sets all the CW band search flags. LAN-LINK will 
        check every CW band.

        6.11 Set All SSB Search Flags

        This option sets all the SSB band search flags. LAN-LINK will 
        check every SSB band.

        6.12 Set/Clear Individual Search Flags

        This option prompts you to set or clear each flag for each band

        6.13 Set/Clear Current Band Search Flags

        This option allows you to set or clear the search flags for the 
        band you are operating on. Use this option and the "clear all" 
        option in a contest to change settings when changing bands.

        Notes:
        1: Use the Update option in the Parameter Menu to save the state 
           of the individual flags permanently.
        2: Set the debug flag on, to verify the prefix, if you are think 
           LAN-LINK is incorrect in its searches.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 39


        7.0 THE CALL MENU

        The call menu is used to enter calls, either to call/connect/link 
        a station or to remember a call or path. Each time you are 
        prompted for a call, LAN-LINK will remember the previous 15 calls 
        and you may use the Up and Down arrows to move the cursor to a 
        remembered call. If you wish to capture a call from the incoming 
        text window, push Function Key 10 (F10) to enter the incoming 
        text window and move the cursor to the desired callsign. When the 
        cursor is positioned on any character in the callsign, push the 
        "Enter" Key and that word will be recognized as the callsign. Any 
        characters joined to the call (such as a ".") will be picked up 
        as part of the call. If the cursor is positioned on a space or 
        blank, the connect attempt will be inhibited.

        In AMTOR, whenever you are asked to enter a callsign, LAN-LINK 
        will prompt you with its guess at the SELCAL. If you agree with 
        it, just press the "Enter" Key, if you disagree, enter your 
        choice over the prompt version.

        The Call Menu is communications mode sensitive. It gives you 
        different choices in each communications mode. In the packet 
        communications mode it provides the choices shown in Figure 7.1. 
        In AMTOR, it provides the choices shown in Figure 7.2. Type in 
        the single letter to make your choice.

        7.1 Alert Call

        This option toggles the Alert call feature ON and OFF. If it is 
        off, you are prompted for the call to be monitored, and, if it is 
        on, it is turned off. The toggle is set when you enter a 
        callsign, and cleared when you depress the "Enter" Key instead of 
        a callsign.

                      Figure 7.1 The Packet Mode Call Menu

                                 A Alert Call
                                 D Show Directory
                                 M ReMember Path    
                                 P Packet Cluster
                                 T Target Call   
                                 Q Call CQ  
                                 U aUto CQ   
                                 ! Zap PBBS [on Beacon]








        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 40


                         Figure 7.2 AMTOR Mode Call Menu

                                 D Show Directory
                                 Q Call CQ 
                                 U aUto CQ
                                 X Turn DX ON

        The Alert call will be shown flashing in the status window when 
        in the disconnected state.

        The Alert call feature is used in the Packet Communications Mode 
        when disconnected and the terminal set for "TRFC" or "CQ/BEACON". 
        LAN-LINK will scan the packet headers received from the TNC, and, 
        when it sees a packet originated (or digipeated if the MRPT 
        parameter in the TNC is set to "ON"), by the station whose call 
        you have entered as the "Alert" call, it will sound an alarm at 
        the console. The line containing the packet header will also be 
        displayed in the Alert call color. If the terminal is set for 
        "CQ/BEACON" the Alert will only sound if the specified station 
        transmits CQ or BEACON packets.

        7.2 ReMember Path

        You may use this option to put an entry in the LAN-LINK.DIR file. 

        7.3 Call CQ

        You use this command key to call CQ. In the Packet Communications 
        Mode, the TNC will transmit a line of text along with the CQ 
        packet. The line of text is in line 3 of the LAN-LINK.SYS file.          
        In the AMTOR Communications Mode, your SELCAL will be transmitted 
        along with the CQ call in the FEC Mode.

        7.4 Show Contents of Call Directory

        This option displays the contents of the call directory file 
        (LAN-LINK.DIR). Use this option to verify the contents of the 
        file.

        7.5 Target Call

        This option toggles the Target call feature ON and OFF. If it is 
        off, you are prompted for the callsign to be detected. If it is 
        on, it is turned off. The toggle is set when you enter a 
        callsign, and cleared when you press the "Enter" Key instead of a 
        callsign.

        The Target call feature is used in the Packet Communications Mode 
        when disconnected. LAN-LINK will monitor the stations connecting 
        to you. When it sees a connect by the station which you have 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 41


        entered as the "Target" call, it will set the flashing Connect 
        Count display to show a "happy face". The Target call will be 
        shown flashing in the status window when in the disconnected 
        state.

        7.6 Auto CQ

        This option is the same as Function Key 6 (F6).

        7.7 Toggle DX Flag

        LAN-LINK allows you to call either "CQ" or "CQ DX". If this flag 
        is set, all CQ calls will be to "CQ DX". If it is cleared, all CQ 
        calls will be plain CQ's. 

        7.8 Zap PBBS on Next Mail Beacon

        This option causes LAN-LINK to Zap your local PBBS next time it 
        beacons with a list of calls for which it has Mail. You set this 
        option active when you want to upload a set of messages, or are 
        not sure if there are any messages waiting for you on the PBBS. A 
        typical situation is where there are a lot of NTS messages 
        stacked up in the PBBS.BBS file waiting to go. This parameter 
        will be reset when the connect goes through, so if the Zap 
        attempt failed, it will try again on the following Mail beacon. 
        This will not work in the Multi-user mode.

        8.0 EDIT MENU

        LAN-LINK contains an ASCII text editor suitable for files less 
        than 64k in size. It is based on Borland's Turbo Pascal Editor 
        Toolbox and the commands are compatible with Sidekick and 
        Wordstar. Each time you invoke the editor, LAN-LINK checks that 
        enough RAM exists to contain the file to be edited (64k per 
        file). If you do not have enough RAM, LAN-LINK will give you a 
        "Heap Error" message.

        LAN-LINK 2.32 is supplied with an external editor. Run this from 
        DOS and you will be able to edit larger files. Make sure you put 
        the EDITOR.EXE file in the LAN-LINK subdirectory.

        The Edit Menu is shown in Figure 8-1. Type in the single letter 
        to make your choice.

        A summary of the commands used in the Editor is presented in 
        Figure 8-2. The ^ sign in front of a character identifies that 
        character as a "Control" character. To activate it, hold down the 
        Control key AND the character key. Some of the commands require 
        two keystrokes. Use ^P to embed a control character in the text. 
        For example, if you are creating a file containing commands to be 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 42


        sent to the TNC, to enter a Control-C character into the file, 
        use the ^P^C sequence of keystrokes.

                            Figure 8-1 The Edit Menu

                                 A LAN-LINK.OUT
                                 B LAN-LINK.TXT               
                                 D LAN-LINK.DIR               
                                 E Pick dEmo File to Edit
                                 F Any other File             
                                 G Incoming Message           
                                 K Answer Capture-to-disk file
                                 L Leave Messages >> N4QQ  
                                 M Answer Incoming Mail    
                                 N Leave Note              
                                 O Pick OUT File to Edit   
                                 P Pick Ctdsk File to Edit 
                                 R Capture-to-disk file    
                                 S LAN-LINK.SYS            
                                 T Two Files               
                                 Z LAN-LINK.DMO
                                 1,2 - 0 LAN-LINK.001 - 010

                      Figure 8-2 Summary of Editor Commands

                    F10 Switch Windows (if more than one window open)
                    Backspace Delete left char
                    Del       Delete Char      
                    Enter     New line
                    Ins       Toggle Insert mode
                    PgUp      Move cursor up one page
                    PgDn      Move cursor down one page
                    ^A Move cursor left one word
                    ^C Move cursor down one page
                    ^D Move cursor right one character
                    ^E Move cursor up one line
                    ^F Move cursor right one word
                    ^G Delete one character
                    ^H Delete left one character
                    ^I Tab
                    ^L Find/replace next occurrence
                    ^P Insert a control character into the text
                    ^M New line
                    ^N Insert line
                    ^R Move cursor up one page
                    ^S Move cursor left one character
                    ^T Delete one word after cursor 
                    ^V Toggle insert mode
                    ^W Scroll up
                    ^X Move cursor down one line


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 43


                    ^Y Delete line at cursor
                    ^Z Scroll down
                    ^K^B Mark beginning of block
                    ^K^C Copy block to position of cursor
                    ^K^D Save file and exit edit 
                    ^K^H Hide block marker
                    ^K^K Mark end of block
                    ^K^Q Abandon file and exit edit
                    ^K^R Read file into screen
                    ^K^T Mark single word as block
                    ^K^V Move block to position of cursor
                    ^K^W Write block to disk file
                    ^K^Y Delete block
                    ^K 1..9 Set marker 1 .. 9
                    ^Q^A Find text and replace
                    ^Q^B Move to beginning of block
                    ^Q^C Move to end of file
                    ^Q^D Move to right of line
                    ^Q^E Move to top of window
                    ^Q^F Find text
                    ^Q^I Toggle autoindent mode
                    ^Q^K Move to end of block
                    ^Q^R Move to top of file
                    ^Q^S Move to left of line
                    ^Q^X Move to bottom of window
                    ^Q^Y Delete to end of line
                    ^Q 1..9 Jump to marker 1..9

        The following options can be set in the Find/Find and Replace 
        (^Qf and ^Qa) operations.

                    # locates #th occurrence
                    G global replace
                    N replace without Y/N question
                    U ignore upper case/lower case
                    W match whole words only

        While you are using the editor, LAN-LINK can't receive and 
        process characters from the TNC. All other features are inhibited 
        or locked out. Thus if someone connects to you, the TNC will know 
        but LAN-LINK will not. Be warned!!! 

        The Edit menu allows you to call up the various files for editing 
        as follows.

        8.1 Edit Brag Tape

        This option allows you to create and edit the Brag Tape File 
        (LAN-LINK.TXT).



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 44


        8.2 Edit Call Directory File

        This option allows you to create and edit the Call Directory File 
        (LAN-LINK.DIR).

        8.3 Edit Any Other File

        This option allows you to create and edit any other file.

        8.4 Answer Capture-to-disk (Ctdsk) File (Split Screen)

        This option allows you to edit the capture-to-disk file and reply 
        to incoming bulletins/messages in a split screen mode. The 
        contents of the incoming bulletins and messages will be displayed 
        in the top window, and the reply file in the lower window. 

        The reply file is assumed to be named according to the Zap 
        convention (*.BBS file). You will have to set up the replies/-
        outgoing messages as if you were typing them by hand.

        You put "SP Call @ PBBS" in the first line, then the "Subject of 
        the message" in the next. Enter the message, and end it with 
        ":EOF:" , "/ex" or "/EX" as the first word on a separate line. 
        For example, a message to me could take the form shown below.
               
                                SP G3ZCZ@N4QQ
                                Test
                                This is a test
                                73 your name
                                /ex

        8.5 Answer Incoming Messages (Split Screen)

        This option allows you to answer incoming messages in a split 
        screen mode. The contents of the incoming messages will be 
        displayed in the top window, and the reply file in the lower 
        window. The reply file is assumed to be named according to the 
        Zap convention (LOCAL-BBS.BBS file). Reply messages are set up as 
        described in Section 8.4.

        Use Function key 10 (F10) to switch windows. At this time you 
        cannot transfer text between windows.

        8.6 Leave Note for Someone

        In all modes you can leave a brief note (message) for another 
        station. When you invoke this option, you will be prompted for 
        the call of the station that you want to leave a note for. As you 
        enter the text it is stored on the disk in the usual format. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 45


        After you have left the note, if you are in the Packet Communi-
        cations Mode, press Function Key 8 (F8) or Alt-D to load the 
        callsign of the recipient into the beacon.

        When you leave a note, leave it for the root call of the 
        connectee, for example to leave a note for W3/G3ZCZ or G3ZCZ/W3 
        leave it for G3ZCZ, similarly to leave a note for WB8WKA-1 leave 
        it for WB8WKA. LAN-LINK is smart enough to extract the root call 
        from any callsign it links/connects with. 

        8.7 Edit Capture-to-Disk file

        This option allows you to edit the Capture-to-Disk file as long 
        as it is smaller than 64k.

        8.8 Edit Two Files (Split Screen)

        This option allows you to create and edit any two files. Use 
        Function Key 10 (F10) to switch windows. At this time you cannot 
        transfer text between windows.

        8.9 Edit Configuration file

        This option allows you to edit the Configuration File (LAN- 
        LINK.SYS).

        8.10 Edit LAN-LINK.001 through LAN-LINK.010 Files

        This option allows you to create and edit the 10 files (LAN-
        LINK.001 to LAN-LINK.010). Use the suffix number to access the 
        respective LAN-LINK.* file, use the number 0 to access the LAN-
        LINK.010 file. If the Mode File Flag is set (see 10.14), the file 
        names will change according to the modes.

        8.11 Pick Capture-to-disk File to Edit

        This option presents you with a directory window containing a 
        list of capture-to-disk files (YYMMDD.RUN). Move the cursor down 
        to the desired file and touch the "Enter" key. If you don't want 
        to edit any of them, then move the cursor down to a blank line. 
        If you have more files than one screen full, use the Pgdn (Page 
        Down) key to show the next screen full.

        8.12 Pick Message File to Edit

        This option presents you with a directory window containing a 
        list of message files (*.OUT). Move the cursor down to the 
        desired message file and touch the "Enter" key. If you don't want 
        to edit any of them, then move the cursor down to a blank line. 
        If you have more files than one screen full, use the Pgdn (Page 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 46


        Down) key to show the next screen full.

        8.13 Leave Messages on your local PBBS

        This option allows you to edit your LOCAL-BBS.BBS file in a 
        single window.

        8.14 Edit Incoming Message

        This option allows you to edit your incoming message file in a 
        single window.

        8.15 Edit LAN-LINK.OUT File

        This option allows you to edit the LAN-LINK.OUT file.

        8.16 Edit LAN-LINK.DMO File

        This option allows you to edit the Demo or Test file. This is a 
        file you can read into LAN-LINK and LAN-LINK treats it as if the 
        data came from the TNC. Use this option to test features and 
        custom settings.

        8.17 Pick dEmo File to Edit

        This option allows you to pick a demo file to edit.

        9.0 EVENT/CLOCK MENU

        LAN-LINK contains some time dependent features which allow you to 
        schedule events. These features are controlled from this 
        Event/Clock Menu shown in Figure 9. Type in the single letter to 
        make your choice.

                            Figure 9 Event/Clock Menu

                                 A Set Alarm               
                                 C Connect ?               
                                 D Display Event           
                                 P Periodic Connect ?      
                                 R Turn Robot ON/OFF       
                                 S Turn ConteSt ON/OFF     
                                 T Turn Time Display ON/OFF
                                 X Cancel Event            
                                 Z Zap PBBS

        To set a scheduled event, first select the event, then enter the 
        time. You may set the event to occur once a day, or once an hour. 
        If you wish the event to occur once an hour, enter an hour value 
        greater than 23 when asked to enter the hour. Each time the event 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 47


        occurs, the feature will be cleared.

        9.1 Set Alarm

        This option allows you to set an alarm clock.

        9.2 Connect

        This option allows you to set LAN-LINK to issue a call or connect 
        request at some later time.

        9.3 Display Event

        This option allows you to display the scheduled event.

        9.4 Periodic Event

        This option allows you to set a periodic connect request or call 
        event. You can set the start time, the end time and the time 
        interval between the connect/call attempts. The first connect 
        that goes through will clear the event scheduler.

        9.5 Turn Robot ON/OFF

        This option allows you to turn the AMTOR/Packet Robot on or off 
        at a fixed time.

        9.6 Turn Contest ON/OFF

        This option allows you to turn the AMTOR/Packet Automatic 
        Contester on or off at a fixed time. You will be prompted for the 
        time, a starting QSO number (in case you a restarting the 
        contest) and the Contest Text (in case you wish to change it).

        9.7 Turn Time Display ON/OFF

        This option allows you to turn the clock display on or off.

        9.8 Cancel Event

        This option allows you to cancel a scheduled event.

        9.9 Zap PBBS

        This option allows you to schedule a PBBS Zap at a predetermined 
        time (like in the middle of the night). You may for example set 
        it to attempt to connect to a PBBS at a fixed time or hourly at 
        any desired minute after the hour. Should the connect be made, 
        the event scheduler will be cleared and no further connect 
        attempts will be made.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 48



        10.0 FILES MENU

        The Files Menu is shown in Figure 10. Type in the single letter 
        to make your choice.

                            Figure 10 The Files Menu

                                 B Send Brag Tape              
                                 C View Color File
                                 D File Directory           
                                 E Erase File               
                                 F priNt File
                                 M Turn Mode Files ON/OFF
                                 N priNt Ctdsk File         
                                 P Pick Ctdsk File to View  
                                 R Rename File              
                                 S Send File                
                                 T Send/Talk File           
                                 U send Uppercase File     
                                 V View File                
                                 Y View Capture-to-disk File
                                 X Turn eXpand Files OFF
                                 Z View Messages           

        10.1 Send Brag Tape

        This command allows you to transmit a standard text file 
        historically known as a "Brag Tape". The default name of the brag 
        tape file is LAN-LINK.TXT, and it should be created with a word 
        processor in the non-document mode, or with LAN-LINK's editor.

        During the file transfer, the outgoing text will appear in the 
        Outwindow. If the text is long enough and fills the TNC buffer, 
        you will see it stop, and then continue when the TNC is ready to 
        accept more text. LAN-LINK uses hardware flow control not 
        software (^S/^Q).

        When you transmit a file you are returned to the receive mode 
        after the file is sent except in the Packet Communications Mode. 
        In the Packet Communications mode, when the file has been loaded 
        into the TNC the computer will add the ^Z character to the 
        outgoing text to signal to the recipient that the file transmis-
        sion is over. 

        The computer will signal you (using the bell character) when the 
        file has been loaded into the TNC. That is not the same as the 
        time that the TNC has transmitted the file, because the TNC 
        contains a character buffer. LAN-LINK dumps the file into the TNC 
        at the baud rate used between the PC and the TNC. The TNC, then 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 49


        transmits the file at the radio link data rate. Flow control is 
        used to regulate the passage of data between the various buffers 
        in the link.

        10.2 File Directory

        This command shows you the directory of the disk drive.

        10.3 Erase File

        This command allows you to erase or delete a file.

        10.4 Pick Capture-to-disk (Ctdsk) file to View

        This command allows you to view a *.RUN file. When you exercise 
        this command you will be presented with a list of capture-to-disk 
        files (YYMMDD.RUN). Move the cursor down to the one you want to 
        view and touch the "Enter" key to select it. Use this option, if 
        you must, on long files. On files containing less than 64k 
        characters, use the Edit Menu. 

        10.5 Rename File

        This command allows you to rename a file. You could for example 
        rename a document file to a "CALLSIGN.OUT" file so that someone 
        will receive it automatically next time they connect.

        10.6 Send File

        This option lets you transmit an ASCII file. In the non packet 
        modes, it will turn the transmitter off after sending the file. 
        In the packet mode it will send a ^Z character when the file is 
        complete.

        10.7 Send/Talk File

        This option lets you transmit an ASCII file. In the non packet 
        modes, it will leave the transmitter on after sending the file.

        10.8 Send Uppercase File

        This option lets you transmit an ASCII file and converts each 
        line of text in the file to UPPERCASE before transmitting it. The 
        file itself is not changed. In the non packet modes, it will turn 
        the transmitter off after sending the file.

        10.9 View File

        This option lets you view the contents of a file. Use it if you 
        must on long files. On files containing less than 64k characters, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 50


        use the Edit Menu. 

        10.10 View Capture-to-disk (Ctdsk) File

        This option lets you scroll forward through, or view, the 
        contents of the capture-to-disk file (YYMMDD.RUN) which you 
        specify by name. Use it if you must, on long files. On files 
        containing less than 64k characters, use the Edit Menu. 

        10.11 View Incoming Message File

        This option lets you view the contents the Incoming message file 
        (yourcall.OUT). Use it if you must, on long files. On files 
        containing less than 64k characters, use the Edit Menu. 

        10.12 Print File

        This option lets you print the contents of a text file. 

        10.13 View Color File

        This option allows you to view an ANSI color file in glorious 
        color. If you use the regular edit or file view options, you will 
        see the ANSI color control characters inside the file. Use this 
        option to check on your color editing.

        10.14 Turn Mode Files ON/OFF

        This option lets you change the state of the Mode File Flag. If 
        this flag is set, LAN-LINK will change the name of the LAN-
        LINK.001 to LAN-LINK.010 when you change modes. The name will 
        change to the mode followed by a number, i.e. BAUDOT.001 to 
        BAUDOT.002, or AMTOR.001 to AMTOR.002. This feature allows you to 
        use different files in different modes and still use the same Alt 
        key combination to transmit them. Thus, you can if you wish, set 
        up a Pactor file with all 128 characters, and an AMTOR file with 
        the AMTOR character set as MODE.002, (where MODE is the 
        communications mode) and transmit each using Alt-F2. If the Mode 
        File Flag is not set, then the file names never change.

        10.15 Turn eXpand Files ON/OFF

        This option lets you change the state of the eXpand File Flag. If 
        this flag is set, LAN-LINK will change the macro string beginning 
        with the # sign, to the equivalent text.

        11.0 HELP WITH FUNCTION KEYS

        This Main menu option will activate the HELP display which 
        presents you with a (very) brief reminder summary of the function 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 51


        and hot keys. This window will remain on display until a 
        character is typed at the keyboard.

        12.0 JUMP TO DOS SHELL

        This Main menu option allows you to enter a DOS shell. If you do 
        not restore the system to the directory which contains LAN-LINK 
        before you EXIT from the shell, LAN-LINK will do so for you.

        You may use the DOS shell while in QSO when you have loaded the 
        computer/TNC output buffers and output will continue to flow.

        To exit from the DOS shell back to LAN-LINK, enter the command 
        "EXIT". LAN-LINK will automatically return you to the correct 
        sub-directory.

        13.0 LAN-LINK MENU

        The LAN-LINK menu provides different options depending on whether 
        you are connected to another station or not. Figure 13.1 shows 
        options that are available when connected and the PAcketCluster 
        flag is not set. Figure 13.2 shows the menu when not connected. 
        In each case, type in the single letter to make your choice. 

        Each of the features (except the :QYU:) may also be performed 
        manually by typing the full sequence of Network Control Language 
        character strings. 

        13.1 :QBU: External Protocol Command

        This is a Sequence for external operations. It requires that the 
        batch file "QBU-TX.BAT" be present in the transmitting 
        (initiating) station, and the batch file "QBU-RX.BAT" be present 
        in the receiving station. When the QBU sequence is executed the 
        following occurs:-

                    Figure 13.1 LAN-LINK Menu When Connected
                                 9 Demo Mode
                                 B :QBU: Protocol   
                                 D :QZD: Binary File
                                 G :QIC: Page Operator
                                 H :QMH: Activity
                                 M :QBM: ASCII File 
                                 P :QSP: Message    
                                 Q :QDB: ASCII File 
                                 R :QTR: Ask for Time
                                 S :QSM: Message    
                                 T :QTA: Message    
                                 U :QRU: Messages   
                                 Z :QZU: Binary File


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 52



                  Figure 13.2 LAN-LINK Menu When Not Connected 

                                 9 Demo Mode
                                 W Who is "ON-LINE"

        The transmitting station sends a :QBU: The receiving station 
        sends a :QRV: and the amount of memory left on disk, enters the 
        transparent mode, jumps to dos and executes the batch file "QBU-
        RX.BAT". 

        Upon receipt of the :QRV:, the transmitting station then puts the 
        TNC in the transparent mode and jumps to Dos and executes the 
        batch file "QBU-TX.BAT". The batch file should exit and return to 
        LAN-LINK. LAN-LINK then exits the transparent mode.

        When the receiving station batch file finishes and returns to 
        LAN-LINK. LAN-LINK then exits the transparent mode and transmits 
        a :QSL: if the DOS Error level was 0 and a :QNO: error if it 
        wasn't. At this time both stations are back in the converse mode.

        You may use this technique for transmitting pure binary files 
        using external (to LAN-LINK) protocols). You may change the 
        default names of the batch files in the LAN- LINK.SYS 
        configuration file.

        13.2 :QBM: ASCII File

        You use this option to download an ASCII file from another LAN-
        LINK station. It is the same as manually typing ":QBM: FILENAME".

        13.3 :QDB: ASCII File

        You use this option to upload an ASCII file to another LAN- LINK 
        station. It is the same as manually typing ":QDB: FILENAME".                  
        Using this option saves you typing the file name twice.

        13.4 :QIC: Page Operator

        This command allows you to page the operator at the other LAN-
        LINK 2.1+ station. The sequence is:- you send :QIC: to another 
        LAN-LINK 2.1 station. Use the LAN-LINK Menu or type it by hand. 
        Upon receipt, LAN-LINK begins to page the operator if the sound 
        flag is on. At that time it sends you a :QRX: followed by a 
        number, i.e. ':QRX: 30'. The number is the number of seconds it 
        will page the operator. At the end of the paging sequence it will 
        send the prompt i.e. 'G3ZCZ>'. If the sound is inhibited it will 
        send ':QRX: QRT' to signal that it is in a silent configuration.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 53


        13.5 :QMH: Monitor Heard

        This command causes your copy of LAN-LINK to issue the :QMH: 
        command. When the other station's copy of LAN-LINK receives a 
        :QMH: command, it drops back to the TNC Command Mode and issues a 
        "MH" command to the TNC (except to a TNC1 which does not support 
        it). It stores the list received in a temporary buffer, and then 
        returns to the Converse Mode and transmits the list back to you.

        13.6 :QRA: Who is "ON-LINE"

        You use this option (when unconnected and monitoring the traffic 
        on a channel) to see who is "ON-LINE" on the LAN. It is the same 
        as going manually into the Converse Mode and transmitting an 
        unconnected packet containing the character string :QRA:. You may 
        also use the Alt-W function key to transmit the same sequence.

        13.7 :QRU: Messages

        The NC/L QRU command allows you to upload a number of messages to 
        the other station. You use it when you have messages pending on 
        your system and want to pass them to a third computer for storage 
        in the LAN, while you take your computer off-line.

        You use this option to begin the upload sequence to transfer 
        messages for a number of stations to another LAN-LINK station. It 
        is the same as manually typing :QRU:. 

        You can only use this option with a station which you have 
        previously designated as a store and forward mail box, for 
        specific stations. You must also have set up a CALLSIGN.MBX file 
        for that station.

        When the upload sequence is over, the computer sending the 
        messages will transmit the NC/L command word :QJG: to signal that 
        the sequence is complete. Should you receive it before you get 
        any messages, then there weren't any pending. 

        If you want to upload messages to another LAN-LINK system, 
        connect to it and type the sequence :QRU: followed by the "Enter" 
        character. That system will then respond to you as if the 
        operator there had initiated a QRU command.

        13.8 :QSM: Message

        You use this option to request a repeat of a message. It is the 
        same as manually typing ":QSM:".





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 54


        13.9 :QSP: Message
         
        You use this option to store a message on another LAN-LINK 
        station. It is the same as manually typing ":QSP: CALLSIGN".

        LAN-LINK contains store and forward routines for messages in a 
        Local Area Network (LAN). 

        When connected to another LAN-LINK station, you may use the NC/L 
        :QSP: command to leave a message at that station. This QSP 
        command automates that feature for you. It lets you just enter 
        the callsign of the station you wish to leave a message for. It 
        will then send the text sequence :QSP: <callsign>. The other LAN-
        LINK HOST station will either reply :QNO: followed by a number or 
        :QRV: <callsign>. The "QNO" message means that the other computer 
        cannot accept the message, the "QRV" message means that it is 
        waiting for you to send it.

        If you get the :QRV: reply, go ahead and type the message, or 
        send the text file containing the message. If you type the 
        message, use a Control-Z (^Z) character and carriage return to 
        terminate the message. (In AMTOR, LAN-LINK will translate the ^Z 
        to :EOF: +? to terminate the message). You will then receive 
        either a :QSL: from the other station meaning that the message is 
        accepted, or a :QNO: followed by a message that something went 
        wrong and the message was not stored. 

        13.10 :QTA: Messages

        If you have a bad path and your messages are not automatically 
        deleted by the other station after they have been sent to you, 
        you use this option to delete your message. It is the same as 
        manually typing ":QTA:".

        13.11 :QTR: Ask for Time

        This command allows you to get the date-time-text string from the 
        other LAN-LINK 2.1+ station. Don't confuse it with :QRT:.

        13.12 :QZD: Binary Files

        This command uses the external batch files to download a Binary 
        file from another LAN-LINK Station using the Zmodem Protocol. If 
        you attempt to download a file which exists in your computer, 
        LAN-LINK will use ZModem's "restore after interrupt" capability 
        to pick up the transfer at the point when (it assumes) the 
        transfer was interrupted. You must configure all four QZ*.BAT 
        files before trying to :QZD: as described in Section 24 (Install 
        takes care of the configuration in most instances).



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 55


        13.13 :QZU: Binary Files

        This command uses the external batch files to Upload a Binary 
        file to another LAN-LINK Station, making use of the Zmodem 
        Protocol. LAN-LINK will not let you upload a file to the other 
        system, if a file with that name already exists on the system. 
        This stops you overwriting existing files. If the link drops out 
        while you are uplinking a file, and you wish to try again later, 
        rename the file you are sending, then reconnect and try again. 
        Don't forget to :QSP: the other station and tell the operator 
        what happened. You must configure all four QZ*.BAT files before 
        trying to :QZU: as described in Section 24.

        13.14 Demo Mode

        Use this option to enter the demo mode, and simulate incoming 
        lines of text from a disk file.

        13.5 Set Single/Dual PK-900/DSP 2232 In Windows

        This option in only active for the PK-900 and DSP 2232. It allows 
        you to separate the incoming text from the two radio ports into 
        two windows. When operating hf/vhf the hf window is usually the 
        middle incoming window.

        14.0 LOG MENU

        LAN-LINK allows you to have up to 3 logbooks on-line. One is 
        designated as the HF logbook, the second is the VHF logbook, and 
        the last one is known as the Secondary Logbook. They can be 
        different or the same. 

        LAN-LINK performs automatic log book entries for Packet, Pactor 
        and AMTOR Beacon mode Connects, and semi-automatic log book 
        entries for other modes. The Log files are in dBASE 3 format and 
        can be processed by the DBASE Log book Package in PC-HAM for 
        indexed listings, tracking of DXCC and other AWARDS, etc. This is 
        ideal for special event stations and DX-peditions, for the whole 
        QSL process and further statistical analyses of their operation. 
        The structure of the logbook files are as shown in Table 14.

        The size of the COMMENTS field is a compromise. Each field is a 
        fixed size so that each log entry takes up a minimum of 62 
        characters worth of space on the disk even if all the character 
        space is unused. You may change the size of the field if you 
        wish, but to do that you will have to use dBASE. Note also, that 
        if you do make the comments field longer, the display will be 
        screwed up.

        For the logging feature to work, the logbook files must be 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 56


        present on the disk. 

                 Table 14 Structure of the Logbook Database File

        Field     Field Name       Type         Length
        1              DATE      Character      8
        2              TIME      Character      4
        3              BAND      Character      3
        4              CALL      Character      10
        5              RX        Character      3
        6              TX        Character      3
        7              MODE      Character      4
        8              POWER     Character      4
        9              QSLSENT   Character      1
        10             QSLRX     Character      1
        11             COMMENTS  Character      20

        When an AMTOR beacon mode, G-TOR, Pactor, or packet connect 
        occurs, the connect is automatically logged (if the automatic 
        logging feature is enabled). In the Packet Mode, the connect path 
        is placed in the comments section of the logbook entry. In the 
        non packet modes, the log data entry is set up for you with 
        default 599 values for the reports exchanged. 

        When you bring up the Logbook you will be shown the last screen 
        or page of log entries. The last entry will be highlighted. At 
        this time a number of function keys can be used, or you may 
        depress the "Escape" key to bring up the Main Log Menu. When you 
        bring up the Main Log Menu, it provides the choices shown in 
        Figure 14.1. Type in the single letter to make your choice.

        14.1 Append From Another LAN-LINK Log

        This option lets you append entries from another LAN-LINK 
        logbook. Use it after a contest, to merge the contest log into 
        the main logbook.

        14.2 Scan Log by Band

        This option lets you scan the logbook file and display QSOs made 
        on a particular band. 

        14.3 Change Logbook File

        This option lets you temporarily change the logbook file. If you 
        want to change it permanently, change it in the LAN- LINK.SYS 
        file. When you enter the new name, LAN-LINK will assume that it 
        is a filetype DBF. For example, if you have different logbooks 
        for different operations on-line, such as 4X.DBF or W8.DBF, you 
        only need answer "4X" in response to the question, to change to 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 57


        the 4X.DBF logbook. In accordance with the dBASE convention, you 
        cannot use any filetype other than DBF.

                            Figure 14.1 The Log Menu
                                 A Append from Another LAN-LINK Log
                                 B Scan Log by Band
                                 C Change Log
                                 D Delete Logbook
                                 F Find date
                                 G Purge Log
                                 H Help Function Keys
                                 I Import From G3ZCZ's Contest Log
                                 J Jump to an Entry
                                 K PicK Log
                                 L pack Logbook
                                 M Scan Log by Mode
                                 N Create New Blank Log
                                 P Print Log
                                 R Re-index Logbook
                                 T Sort on Date + Time
                                 U Turn Update Disk OFF
                                 Z fuZzy scan
                                 2 Turn Secondary Search OFF

        14.4 Delete Logbook File

        This option lets you delete both the logbook (.DBF) and its 
        associated index file (.NDX).

        14.5 Find Date

        This option lets you locate and move the highlight to entries for 
        a particular date. If no entries are found for the desired date, 
        the first entry after that date will be highlighted. You can also 
        scan for parts of a date, such as "90/01", for the first entry in 
        January 1990.

        14.6 Purge Log

        This command allows you to purge one callsign from the log. Use 
        it to delete the callsign of your local PBBS if the logbook file 
        gets too big.

        14.7 Help Function Keys

        This option brings up a menu listing the log mode function keys.

        14.8 Import From G3ZCZ's Contest Log

        This option lets you import logs from earlier releases of LAN-


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 58


        LINK (up to and including Version 1.56). It can also be used to 
        import a log generated by the Contest Program in PC-HAM.

        14.9 Jump to an Entry

        This option lets you jump to an entry by its record number. This 
        is the number displayed in the first column.

        14.10 Pick a Log file

        This command allows you to pick a *.DBF file. When you exercise 
        this command you will be presented with a list of log files 
        (*.DBF). Move the cursor down to the one you want to use and 
        touch the "Enter" key to select it. 

        14.11 Pack a Logbook

        This function key allows you to pack the logbook files. All 
        entries marked for deletion will really be deleted at this time.

        14.12 Scan Log by Mode

        This option lets you scan the logbook file and display QSOs made 
        using a particular mode. 

        14.13 Create a New Logbook

        This command allows you to create a blank logbook (*.DBF) file. 

        14.14 Print Log

        This command prints the contents of the logbook file in a 
        formatted manner to the printer. 

        14.15 Re-index a Logbook

        This command allows you to index logbooks that you have ported 
        over from other DBASE formats, or to re-index logbooks that have 
        had their index files damaged in some manner. 

        14.16 Sort on Date + Time

        This command allows to you create a new logbook from the current 
        one with the entries is sequential order sorted on date and time. 
        You use this option after entering old QSOs manually. Make sure 
        there is space on the disk for a temporary logbook before evoking 
        this operation.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 59


        14.17 Turn Update Disk ON/OFF

        If this parameter is set ON, LAN-LINK will close the logbook and 
        re-open it after every entry. If the parameter is set OFF, LAN-
        LINK saves a few entries in memory and only writes them to disk 
        when the buffer fills, or the logbook is closed. Setting the 
        parameter guarantees you will not lose any entries if the power 
        fails, at the expense of a slightly slower logging operation.

        14.18 Fuzzy Scan

        This option allows you to scan the callsign or the comment field 
        (your choice) for a character string. For example you could scan 
        the comments field for all entries with the word "Joe". You could 
        scan the callsigns for all calls with the suffix of "ZCZ".

        14.19 Turn Secondary Search ON/OFF

        This option allows you to turn the secondary search mode on and 
        off. If it is on, and if the secondary logbook exists, every time 
        you command a search of the logbook to find a prefix or callsign, 
        LAN-LINK will also search the secondary log. Use this feature if 
        you have more than one log, as a result of operating from more 
        than one location or for any other reason.

        14.20 Log Menu Function Keys

        The Function Keys shown in Figure 14.2 are active in the Log 
        book. The operation of each function key is described below.

                  Figure 14.2 Function Keys Active in Log book

                                 A  Append Entry
                                 E  Edit Log Entry
                                 H  Scan for Log Entry
                                 S  Scan for Call
                                 U  Toggle Delete Mark
                                 X  eXit Log Menu
                                Ins  Toggle Insert Mode
                                End  Show Last Page
                                Home Show First Page
                                PgUp Page Up
                                PgDn Page Down
                                Up   One Entry
                                Down One Entry

        14.20.1 Alt-A Append Entry 

        This function key allows you to manually append an entry to the 
        log. You can also use this command to enter the odd SSB contact 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 60


        into the logbook file. If you do, use the characters "SSB" or 
        "FM" for those voice modes to remain compatible with the rest of 
        the DBASE logbook package.

        When appending or editing an entry, LAN-LINK will automatically 
        enter the date, time, callsign of the other station, band, mode 
        and QSL information in upper case.

        The comments field in the LAN-LINK logbook file is restricted to 
        a maximum of 20 characters. If you try and enter more than 20, 
        the surplus will be ignored.

        14.20.2 Alt-E Edit Log Entry

        This function key allows you to edit the highlighted entry. Move 
        the cursor with the arrow keys, and end the edit process by 
        depressing the "Escape" key. 

        You may use the "QSL" entry to tag the fact that you have written 
        out or received a QSL card.

        14.20.3 Alt-H Scan Log by Call

        This function key allows you to scan the logbook by callsign 
        prefix for the callsign in the highlighted entry in the logbook. 
        This command displays the contents of the logbook file in a 
        formatted manner on the screen. It requests the callsign of the 
        log entry to be displayed. If you want to see entries for 
        particular callsigns or parts of a callsign, enter those 
        callsigns or the front parts of the callsign. Valid entries are 
        G, G3, G3Z etc. If you want to see every entry in the log, don't 
        use this command, use the Page Up and Page Down keys from the 
        Main Log menu.

        14.20.4 Alt-S Scan Log by Call

        This function key allows you to scan the logbook by callsign 
        prefix for the callsign entered with the Alt-C or Alt-E keys. 
        This command displays the contents of the logbook file in a 
        formatted manner on the screen. It requests the callsign of the 
        log entry to be displayed. If you want to see entries for 
        particular callsigns or parts of a callsign, enter those 
        callsigns or the front parts of the callsign. Valid entries are 
        G, G3, G3Z etc. If you want to see every entry in the log, don't 
        use this command, use the Page Up and Page Down keys from the 
        Main Log menu.

        14.20.5 Alt-U Toggle Delete Mark

        This function key allows you to mark an entry for deletion, or 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 61


        unmark it in case you change your mind. Entries marked for 
        deletion will be flagged by an "*" character next to the record 
        number.

        14.20.6 Alt-X eXit Log

        This function key lets you exit from the Logbook.

        14.20.7 Ins Toggle Insert Mode

        This function key allows you to turn the insert mode ON and OFF 
        for the edit/append functions.

        14.20.8 End Show Last Page

        This function key moves you to the last callsign on the last page 
        of the logbook.

        14.20.9 Home Show First Page

        This function key moves you to the first callsign on the first 
        page of the logbook.

        14.20.10 PgUp Move Up One Page

        This function key moves the display up one page of the logbook.

        14.20.11 PgDn Move Down One Page

        This function key moves the display down one page of the logbook.

        14.20.12 Up Arrow Move Up One Entry

        This function key moves the highlight up one entry in the 
        logbook.

        14.20.13 Down Arrow Move Down One Entry

        This function key moves the highlight down one entry in the 
        logbook.

        15.0 MESSAGE MENU

        The Message Menu is shown in Figure 15. Type the single letter to 
        make your choice.

                           Figure 15 The Message Menu
                                 B PBBS Command Files
                                 C Current Messages
                                 L Leave Note   


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 62


                                 N Print Message
                                 O Old Messages 
                                 T Time Tag     
                                 V View Messages

        15.1 PBBS Command Files

        This option shows you a list of the PBBS command files on the 
        default directory. In other words, all files with the file 
        extension of ".BBS". 

        15.2 Current Messages

        This option shows you a list of the outgoing messages that have 
        not been sent. In other words, all files with the file extension 
        of ".OUT". 

        15.3 View Message

        This feature allows you to view messages in the computer. After 
        depressing the key you will be prompted for INcoming or OUTgoing 
        (I/O) messages. If you request "I" (Incoming) messages you will 
        see the messages addressed to your callsign. If you request "O" 
        (for OUTgoing) you will be presented with a directory window 
        containing a list of messages. Move the cursor down to the 
        desired message, and touch the "Enter" key. If you don't want to 
        view any of them, then move the cursor down to a blank line. If 
        you have more messages than one screen full, use the Pgdn (Page 
        Down) key to show the next screen full.

        15.4 Leave Note

        This feature allows you to leave a note for another station on 
        the LAN in your system. It works using the editor in the manner 
        described in Section 8.
         
        15.5 Old Messages

        This feature shows you a list of the messages that have been 
        sent. In other words, all files with the file extension of 
        ".OLD".

        15.6 Time Tag

        This option is used to place a date time header on a message file 
        previously prepared by a word processor. The name of the file 
        must be in the format "CALLSIGN.OUT" (i.e. G3ZCZ.OUT). It 
        requests the callsign of the message file. It then opens a new 
        file, writes the header to the new file and copies the contents 
        of the original "*.OUT" file to the new one. When all is done, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 63


        the original filename is changed to "*.BAK" and the new one 
        becomes "*.OUT".

        16.0 TNC MENU

        The TNC Menu depends on the TNC. For example the MFJ1278 provides 
        the choices are shown in Figure 16-1. The PK-232 TNC menu is 
        similar as shown in Figure 16-2. The actual menu you see also 
        depends on the mode. In the non packet modes, the non packet 
        options will be locked out. For example, in the PK-232 Baudot 
        mode, the menu will appear as shown in Figure 16-3. 

        The DSP-2232 and PK-900 support simultaneous dual port operation. 
        LAN-LINK provides for support of this feature, so the TNC Menu 
        for those TNCs has additional options as shown in Figure 16-4.

                          Figure 16-1 MFJ1278 TNC Menu

                                 D Set MFJ1278 Date/Time     
                                 E Disable MFJ1278 Port      
                                 F Flush MFJ1278 Buffer      
                                 I Initialize MFJ1278        
                                 M calls Monitored List      
                                 S Show Connect Status       
                                 T Change cText              
                                 X Activate MFJ1278 Mailbox  
                                 Y Deactivate MFJ1278 Mailbox

                         Figure 16-2 The PK-232 TNC Menu

                                 D Set PK232 Date/Time     
                                 E Disable PK232 Port      
                                 F Flush PK232 Buffer      
                                 I Initialize PK232        
                                 M calls Monitored List    
                                 S Show Connect Status     
                                 T Change cText            
                                 X Activate PK232 Mailbox  
                                 Y Deactivate PK232 Mailbox

                    Figure 16-3 The PK-232 TNC Menu in BAUDOT

                                 D Set PK232 Date/Time
                                 E Disable PK232 Port
                                 F Flush PK232 Buffer
                                 I Initialize PK232  

                    Figure 16-4 The PK-900 TNC Menu in Packet

                                 D Set PK900 Date/Time


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 64


                                 E Disable PK900 Port
                                 F Flush PK900 Buffer
                                 I Initialize PK900
                                 M calls Monitored List
                                 N PK900 Modem Menu
                                 S Show Connect Status
                                 T Change cText
                                 X Turn PK900 Mailbox ON
                                 Y Turn PK900 Mailbox OFF
                                 1 Select Radio Port 1
                                 2 Select Radio Port 2
                                 3 Disable Radio Port 1
                                 4 Disable Radio Port 2
                                 5 Enable  Radio Port 1
                                 6 Enable  Radio Port 2
                                 7 Show ## Radio Port

        Whichever menu is displayed, type in the single letter to make 
        your choice.

        16.1 Set TNC Date/Time

        This feature puts the TNC into the Command Mode and loads the 
        date into it from the computer time of day clock. This command 
        does not work on the TNC1.

        16.2 Flush TNC Buffer

        This option is used to flush LAN-LINK's incoming or outgoing text 
        buffer and that of the PK-232, PK-900 or DSP 2232. When used with 
        other TNCs it will only flush contents (if any) of the buffers in 
        the PC. If you flush the incoming buffer, you will only flush the 
        buffer in the PC. Any characters still in the TNC buffer will 
        still come through. If that happens, bring up the function but 
        wait a while before activating it.

        16.3 Initialize TNC

        This feature sets up the defaults for the TNC from the file LAN-
        LINK.SYS. If you have put batteries in the TNC, you should 
        normally only have to run this command when you first power up 
        the TNC or change the batteries. However, the batteries must be 
        removed initially since they are there to retain the default 
        settings of the TNC (particularly the PK-232). Once the 
        initialization is complete, you can replace the batteries but 
        leave the TNC on since the battery provides power to the RAMs 
        after the TNC power is turned off.

        The function will also set the date and time within the TNC from 
        the PC computer clock, and, when it has loaded the configuration 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 65


        file, may prompt you to set the TNC Terminal mode. If you are 
        using a TNC1 or a TNC2, it will not prompt you because it assumes 
        that they only operate on VHF packet. If you are using a KPC-2, 
        you may select "H" or "V", and of course, if you have a PK-232, 
        you may choose any of the options.

        16.4 Show Calls Monitored List

        This option performs the same operation as Function Key 5 (F5). 

        16.5 Show Connect Status

        When you are in the Packet Communications Mode, this command lets 
        you see the state of the connection. It will show you if there 
        are any unacknowledged packets en route to the other station. If 
        you have been sending text, it is advisable to use this command 
        before you disconnect, to ensure that all the data has been 
        received and acknowledged by the other party. You may use this 
        command in either the TNC Command or the TNC Converse Mode.

        In a multi-connect situation, it will show you the status on all 
        the I/O channels. 

        You may also use this command to reset the status window display 
        after a relink or any other event which was not reflected in the 
        status window.

        16.6 Change CTEXT

        This feature allows you to change the message that will be 
        received by another packet station when it connects to you. Refer 
        to the CTEXT command in the TNC manual.

        16.7 Activate TNC Mailbox

        The mailbox in your TNC provides a convenient way for people to 
        leave you a message when your PC is switched off or is in use for 
        something other than packet radio. If you do choose to make use 
        of the personal PBBS in the mailbox, make sure that you have a 
        battery in the TNC. You will have to interrogate the mailbox in 
        the command mode to view any messages. Type the commands listed 
        in your TNC manual.

        This menu option allows you to activate the personal mailbox 
        built into your TNC to read any messages stored in it, or, before 
        shutting down, if you have not set the shut down mode to 5.

        To save your local full service PBBS SYSOP some hassles, it is 
        strongly recommended that you let LAN-LINK do your outgoing and 
        incoming message and bulletin store and forwarding. Use the "L" 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 66


        option in the Edit menu to enter any messages off-line, the "M" 
        and "K" options in the Edit menu to answer any incoming messages 
        or comment on any bulletins. Once the messages are written into 
        the LOCALPBBS.BBS file, let the PBBS Zap take care of 
        transferring the messages to the PBBS. 

        16.8 Deactivate TNC Mailbox

        This option allows you to deactivate the personal mailbox built 
        into your TNC.

        16.9 TNC Modem Menu

        This option applies to the PK-900 and DSP 2232. It interrogates 
        the TNC and displays list of the modems in the TNC.

        16.10 Select Radio Port 1

        This option applies to the PK-900 and DSP 2232. It sets outgoing 
        text to Radio Port 1.

        16.11 Select Radio Port 2

        This option applies to the PK-900 and DSP 2232. It sets outgoing 
        text to Radio Port 2.

        16.12 Disable Radio Port 1

        This option applies to the PK-900 and DSP 2232. It disables all 
        input from Radio Port 1.

        16.13 Disable Radio Port 2

        This option applies to the PK-900 and DSP 2232. It disables all 
        input from Radio Port 2.

        16.14 Enable  Radio Port 1

        This option applies to the PK-900 and DSP 2232. It disables all 
        input from Radio Port 1.

        16.16 Enable  Radio Port 2

        This option applies to the PK-900 and DSP 2232. It disables all 
        input from Radio Port 1. You might want to use it to temporarily 
        disable the vhf port when receiving an ANSI color picture on the 
        HF port.

        16.17 Show ## Radio Port



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 67


        This option applies to the PK-900 and DSP 2232. It displays the 
        current TNC connect and radio port status.

        17.0 AMSAT-OSCAR MENU

        This menu allows you to configure the KAM, MFJ1278, or the PK-232 
        to copy signals from AMSAT-OSCAR Spacecraft telemetry beacons 
        depending on the TNC. The following options are available.

                                D Full Duplex ON/OFF
                                S SAREX Menu 

        Type in the single letter to make your choice.

        17.1 Full Duplex ON/OFF

        This option allows you to turn the FULLDUPLEX parameter in the 
        TNC ON and OFF. Set it to OFF (default) when working a station 
        simplex (same uplink and downlink frequencies) i.e. MIR. Set 
        FULLDUPLEX to ON when working a station duplex (different uplink 
        and downlink frequencies) i.e. SAREX and Fuji-OSCAR 20.

        17.2 SAREX MENU

        This menu shown in Figure 17-1, is only active in the Packet 
        Communications Mode. It is designed for use with the Shuttle 
        Amateur Radio Experiment (SAREX), MIR, and the packet radio 
        Microsats, or any terrestrial station you want to connect with as 
        soon as they appear on frequency. Apart from the Attack Mode, it 
        can also be used as a diagnostic LAN tool for monitoring LAN 
        traffic. 

                           Figure 17-1 The SAREX Menu

                                 A Set Attack Mode ON
                                 C Set SAREX Call
                                 D Edit SAREX Capture File
                                 L Turn SAREX Capture ON
                                 M set Attack Mode Connect/CQ
                                 Z Turn Zap MIR-1 ON
                                 0 Multiple User Connects

        17.2.1 Attack Mode ON/OFF

        If the Attack Mode is set, this option will cause LAN-LINK to 
        issue a connect request to the SAREX Call whenever a packet sent 
        to or from it is heard. The mode, is cleared when the connect is 
        made (and does not retry out) or when the "A" option is selected 
        a second time, or when the Alert Call is cleared. If this mode is 
        enabled, the Alert/SAREX Call prefix shown in the Status Window 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 68


        will indicate accordingly.

        A happy face will be displayed next to the ">" before the call 
        once the connect has been achieved.
                         
        Be careful using this feature, as it has the potential to cause a 
        great deal of QRM. It can also be cleared by another station 
        connecting to you and telling you to ":QRT:".

        In the SAREX configuration you are listening on one channel while 
        transmitting on an other. If this feature is used on a simplex 
        channel (everyone transmits and listens on the same channel) 
        aimed at a DX-pedition or the MIR space station, there is a 
        potential lockout mode, in which any one station sending a 
        connect request to the desired/SAREX call will trigger the other 
        ones on frequency who will in turn trigger the first. If this 
        pile up situation occurs, I hope the DX-station will QSY and 
        leave the automatic stations to do their thing. IN any event, if 
        you use this feature and cause QRM, anyone can connect to you 
        with the callsign of the DX station (as a pirate) and shut you 
        down. You will then not get the coveted DX QSL.

        17.2.2 Change SAREX Call

        This option lets you temporarily change the SAREX call. 

        17.2.3 SAREX Packets Capture to Disk ON/OFF

        This option allows you to configure LAN-LINK to capture to disk 
        any packets addressed to or from the SAREX callsign. A "[S]" will 
        be displayed in the status window when this option is active. The 
        capture to disk file is opened by a packet header containing the 
        SAREX call, and closed by another packet header not containing 
        the call. When the file is open, the "[S]" will blink. Packet 
        headers are considered to be lines with a ">" character in them. 
        LAN-LINK thus considers both of the lines below as packet 
        headers.

                                     N4QQ*>G3ZCZ
                                     N4QQ PBBS>

        If you use this feature for monitoring PBBS traffic, the PBBS 
        prompt lines ("E.G. N4QQ PBBS>") will not be captured to disk. Do 
        not get your SYSOP to remove the ">" from the prompt line, or the 
        ZAP feature will then not work.

        A happy face will be displayed in the "[S]" after the SAREX call 
        has been heard.

        If you want to see an ORBITER menu, temporarily change the SAREX 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 69


        call to be the same as your call and bring up the AMSAT-OSCAR 
        Menu.

        17.2.4 Edit SAREX Capture-to-disk File

        This option lets you edit the SAREX Capture-to-disk file as long 
        as it is less than 64 kBytes.

        17.2.5 Zap SAREX ON/OFF

        This option combines the "Set SAREX Attack Mode" and the "SAREX 
        Packets Capture to Disk ON/OFF" options in one fast operation.
         
        17.2.6 Set Attack Mode to Connect/CQ

        This option allows you to configure the SAREX Attack mode to 
        digipeat or CQ via the SAREX station as well as to try for 
        connect. Use the CQ feature to digipeat via MIR, and the connect 
        for the Space Shuttle. If the Attack Mode is set, LAN-LINK will 
        either try for a connect or send an unproto packet containing the 
        CQ text. If you want it to go through the SAREX Callsign you must 
        configure the UNPROTO parameter in the TNC. For example, to 
        attempt a digipeat via R2MIR, set 'UNPROTO CQ via R2MIR' from the 
        command mode.

        17.3 SAREX Orbiter Features 

        This was the menu as seen by WA4SIR in orbit on STS-35. You need 
        the SAREX ROBOT EPROM for this menu to actually do anything to 
        the TNC. The EPROM may be available from The Radio Amateur 
        Satellite Corporation (AMSAT) for DX-pedition use. Other options 
        which control LAN-LINK parameters may be used without the SAREX 
        ROBOT EPROM.

        In the Orbiter mode, LAN-LINK does not scan incoming text for the 
        "*** CONNECTED" and "*** DISCONNECTED" messages when the SAREX 
        Robot is active. This inhibits the bells and the capture-to-disk. 
        It also means that the Robot must be OFF for any :Q: code uploads 
        or downloads to occur.

        17.3.1 Status Window Display

        A flashing ">>" appears in the status window when the SAREX robot 
        is active. The SAREX Configuration boots up assuming that the 
        SAREX Robot is active (Default).

        17.3.2 Alt-O Function key

        The Alt-O Function Key brings up the Orbiter menu. This is a 
        faster route than the "Esc O" sequence.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 70



        17.3.3 The Metabeacon

        The Metabeacon is loaded from the contents of one of the META.00n 
        files. These files may be created by the LAN-LINK editor. When 
        loading, LAN-LINK will insert a pass character (^V) into the text 
        before a carriage return, so as not to end the packet before at 
        least 240 characters, and not more than 255 characters have been 
        output to the TNC. The maximum number of characters that can be 
        loaded into the Metabeacon is 1776. The maximum number of packets 
        in a Metabeacon is 7. You can also force a hard carriage return 
        or "end of packet" in the Metabeacon by inserting the "\" 
        (backslash) character, which will not be transmitted, into the 
        text.

        17.3.4 SAREX Orbiter Menu

        The following commands are active in the Orbiter Menu.

        17.3.4.1 Activates Beacons/SAREX Robot: This option activates the 
                 SAREX Robot and loads the Meta Beacon. This command is 
                 designed for use when the SAREX is returned to the 
                 regular frequency.

        17.3.4.2 Set QRZ/QSL Beacon Interval: This command allows you to 
                 change the beacon timer.

        17.3.4.3 Set SAREX Call: This command allows you to change the 
                 SAREX call. Don't use this command on orbit (it's for 
                 ground use only).

        17.3.4.4 Turn SAREX ROBOT OFF: The Robot must be turned ON and 
                 OFF this way to synchronize LAN-LINK to the TNC. When 
                 the Robot is turned OFF the following commands are sent 
                 to the TNC by LAN-LINK.

                  USERS 1
                  |A
                  RO OFF
                  CMSG OFF
                  NO OFF

        17.3.4.5 Set SAREX ROBOT Heard Count: This command lets you set 
                 the Heard Count number.

        17.3.4.6 Show I/O Status: Shows the callsign of the station 
                 connected on each stream, the SAREX Robot state, the 
                 number of USERS, the beacon timer value, the metabeacon 
                 timer value and the CTEXT.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 71


        17.3.4.7 ChecK Count: Shows both heard and worked counts.

        17.3.4.8 List Heard Calls: Lists the callsigns of the last few 
                 stations heard.

        17.3.4.9 Load Metabeacon: This command loads the Metabeacon. You 
                 will be prompted for a text file number in the META.00n 
                 series. Enter a number 1-9 corresponding to META.001-
                 META.009. The 0 value is for file META.010. Note the 
                 delays after loading the file to allow the TNC to 
                 stabilize.

        17.3.4.10 Show Worked Calls: Shows the last 35 or so callsigns 
                 worked.

        17.3.4.11 Turn SAREX ROBOT ON: The SAREX Robot must be turned ON 
                 and OFF via the menu. When the Robot is turned ON the 
                 following commands are sent to the TNC by LAN-LINK.

                  USERS 9
                  CONOK ON
                  CMSG ON
                  RO ON
                  NO ON

        17.3.4.12 Stop Metabeacon: This command stops the metabeacon 
                 transmission. When activated, the contents of the beacon 
                 are dumped to the UNPROTO address (default SAREX) by the 
                 TNC, rather like a regular PBBS dumping packets when a 
                 user disconnects abnormally.

        17.3.4.13 Set Metabeacon Interval: This command allows you to set 
                 the metabeacon timer. It will be loaded into the TNC the 
                 next time that the metabeacon is loaded. Even though 
                 loaded into the TNC immediately, it does not take effect 
                 till then.

        17.3.4.14 Set SAREX ROBOT Worked Count: Lets you set the starting 
                 number.

        17.3.4.15 Set Connect TeXt: This is the text (CTEXT) that will be 
                 transmitted to an incoming station when the ROBOT mode 
                 is off. This option lets you set up a new text string to 
                 go with the QSO number.

        17.3.4.16 Selects Silent Mode: This command turns off the 
                 beacons, the SAREX Robot and also stops the metabeacon. 
                 This command is designed to be used just before any 
                 prearranged packet activity.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 72


        17.3.4.17 Restart TNC: This command RESTARTs the TNC, loads the 
                 date from the computer's clock and turns the "EC OFF". 
                 It seems to have no effect on the SAREX ROBOT and 
                 counters, but does kill the metabeacon.

        17.3.4.18 Capture QSL/QRZ Calls: This command initiates the log-
                 to-disk operation. It turns the capture-to-disk "on" and 
                 sends the following commands to the TNC:- "DA", "SERW", 
                 "SERH","MW", "MH". When the calls have stopped 
                 scrolling, use Function key 1 to turn the capture-to-
                 disk off.
        18.0 PARAMETER MENU

        A typical Parameter Menu is shown in Figure 18. The colors used 
        for the option letter differentiate between those options that 
        are "remembered" in the SYS file and those that are only set 
        temporarily for the session. Type in the single letter to make 
        your choice.

                       Figure 18 A Typical Parameter Menu

         A Send of LAN-LINK.OUT is ON   0 Change Band & Power
         B Beacon/Robot Mode is OFF     1 Change PBBS/PacketCluster Parameters
         C Clear Connect Count          2 Change Callsigns
         D Digipeat Detect is OFF       3 Change Directories
         E Command Echo is ON           4 Enter Common Calls
         F BBS Zap Drop Link is ON      5 Change File Names
         I Packet Beacon Control is ON  6 Change LAN-LINK Parameters
         L Automatic Ctdsk is ON        7 Change PC Communications Parameters
         M Set Message Count            8 Change Colors
         N NODE Drop Link is OFF        9 Change SAREX Parameters
         P Printer is OFF
         Q QTC Snatch is ON             U Update LAN-LINK.SYS
         R :QSP: Relay Flag is ON       V Verify Changes
         S Sound is ON                  W Change Scan Words
         T Contest Mode is OFF          Z Time Id. is OFF
         X DCD Flag is OFF              ! Zap PBBS On Next Beacon is OFF
         Y PBBS Snatch is ON            + Misc. Flag is OFF

        18.1 Turn Beacon Mode ON/OFF

        This command toggles the beacon option for the automatic CQ 
        caller in the AMTOR, Pactor, G-TOR and Packet Communications 
        Modes. When it is active a "[B]" will be flashing in the status 
        window. In this mode, the Automatic CQ sequence will resume after 
        the AMTOR link is dropped or a Packet Communications Mode 
        disconnect. 

        In the Beacon Mode, the last few logbook entries will be 
        displayed in the logbook window which overlays the outgoing text 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 73


        window at the bottom of the screen.

        In the Packet Mode, the CTEXT message is the only transmission 
        from you that the other station will receive, so make it good and 
        don't forget to set "CMSG ON".

        In the AMTOR Mailbox/Beacon Mode, the contents of the LAN-
        LINK.TXT file will be transmitted to the station who called you. 
        The capture-to-disk will then be turned on to record one 
        transmission from that station. The QSO will then be logged to 
        the logbook file. Don't forget to check the entries in the 
        logbook and text in the LAN-LINK.RUN files in case the computer 
        made a mistake in recognizing the call sign of the other station.

        The Beacon mode is designed to encourage people to QSY off the 
        crowded HF packet channels. Do not use it on a crowded HF channel 
        or on an active VHF channel. If you do, you will soon find that 
        other stations have set their TNCs to ignore your packets, and 
        you will not work anyone. You will just be a source of QRM and 
        will be known as such.

        The Beacon mode is also designed for robot beacons on the higher 
        frequencies. For example, if you leave it running on 6 or 10 
        meters, you never know when a short opening will allow a QSO with 
        some part of the world, a DX contact you would otherwise have 
        missed. Don't leave it running on 20 Meters when the band is wide 
        open. Further applications are in meteor scatter and other 
        "exotic" communication modes.

        If you are using the Beacon Mode in a special event station or 
        DX-pedition you may type characters into the transmit buffer, 
        while the other station is sending to you. When he, she, or even 
        it, turns it back to you, you will transmit those characters 
        before the sign-off sequence. 

        In all communications modes, the robot may be shut down by 
        stations connecting to you and telling you to QRT.

        18.2 Clear Connect Counter

        You use this option to reset the PACKET and AMTOR Beacon Mode 
        "connect has taken place indicator" and QTC Snatch counters. 
        These are the flashing "[C]" and "[Q]" displays in the status 
        window. Whenever someone else connects or links up to you the 
        "[C]" display will be incremented. The number shown with the "C" 
        is the number of connects that have taken place since the 
        Indicator was last reset. If a "happy face" is flashing along 
        with the connect count, your "target station" was amongst those 
        connecting. The "[Q]" indicator alerts you to the fact that LAN-
        LINK tried to connect to another station after recognizing your 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 74


        call in a mail beacon. Both are reset by this option. If you are 
        monitoring Packet traffic on a channel, you may not notice that a 
        connect has previously taken place. These indicators alert you to 
        check the contents of the Incoming mail file ("yourcall.OUT") for 
        any incoming messages.

        If the "Q" count is much greater than the "C" count, you may be 
        copying a beacon from a station that you cannot connect with 
        directly.

        18.3 TNC Custom Line (TNC Parameter)

        This line has different effects depending on which TNC you are 
        using. To set the line, add the numbers up for the parameters you 
        want, and put the total in line 32. 

             18.3.1 All TNC's

             TNC Sync shift (128) 
             LAN-LINK normally ensures that the Transmitter and Receiver 
             data sense are in phase. This presupposes AFSK operation. If 
             you are running FSK and need them out of phase, set this 
             byte to 128. If this line includes the number 128, LAN-LINK 
             will NOT set the receiver shift when you change modes.

             Zap Stay Up (64) 
             If you include the number 64 in this line, LAN-LINK will 
             default to staying connected to a PBBS when the Zap sequence 
             ends. Use this parameter setting if the messages contain a 
             lot of ">" characters at the end of lines and LAN-LINK is 
             faked into thinking the messages ended prematurely.

             TNC initialize Date (32) 
             LAN-LINK normally sets the time of day clock in the TNC from 
             the PC during initialization. If you don't want LAN-LINK to 
             set the TNC time of day clock, include the value 32 in this 
             line.

             18.3.2 PK-232, PK-900 and DSP 2232

             PK-232 Digipeat Display Flag (1) 
             Set this line to 1 to activate this feature, 0 to inhibit 
             it. If the Digipeat Display is active, any signals digi-
             peated through you will be stored to the LAN-LINK.RUN file 
             and a "beep" will be sounded for each packet being 
             digipeated. The status window will also contain a "[D]".

             PK-232 Converse Mode Default (2) 
             LAN-LINK runs the PK 232 is command mode in the RTTY an CW 
             modes. Function key 7 (F7) allows you to set the PK 232 into 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 75


             the converse mode. The MFJ 1278 and KAM operate in the 
             Converse mode in all communications modes. If you set this 
             bit to 2, LAN-LINK will run the PK-232 in the converse mode 
             in all modes, and you will not need to use F7 to enter the 
             converse mode before transmitting.

             PK-232 Serial Port Initialization (4) 
             If this bit is set to 4, LAN-LINK will assume there are no 
             batteries in the PK-232 and issue the '* * *' sequence to 
             the PK-232 on start up. If this bit is not set, LAN-LINK 
             will assume the PK-232 contains batteries and will not try 
             to synchronize the PC to PK-232 serial port. 

             This feature was removed from LAN-LINK in 2.00 in response 
             to numerous users who had batteries in their PK-232's and 
             didn't want to see the initialization sequence. Then came 
             the complaints from the users who didn't have batteries in 
             their PK-232's.

             PK-232 XMITOK Flag (8) 
             In the CW communications mode, you may have to change the 
             value of the PK-232 XMITOK Parameter depending on how you 
             connect the PK-232 to your transmitter. This LAN-LINK 
             parameter determines if LAN-LINK instructs the PK-232 to 
             turn the XMITOK PK-232 parameter on and off when entering 
             and leaving the CW communications Mode. You may temporarily 
             change the value of the XMITOK Flag in the CW menu to set 
             things up.

             As an example, to configure LAN-LINK to initialize the PK-
             232 serial port (4) and default to the Converse Mode (2), 
             Set this parameter to 4+2 or 6.

             18.4.2 KAM

             KAM Set LFADD (2) 
             If this bit is set, LAN-LINK will send a 'LFADD ON' command 
             to the KAM when you enter the BAUDOT communications mode, 
             and send a 'LFADD OFF' command when you exit that mode to 
             another one.

             KAM Pre 3.0 EPROM (4) 
             If your KAM contains an EPROM with a Revision number of less 
             than 3.0, then set this bit. LAN-LINK will issue NODE 
             commands when selecting SOLO mode. You must set this bit if 
             you plan to use the mailbox in the KAM, or the traffic on 
             frequency will fill the memory in the KAM, and people will 
             not be able to leave you any messages. 




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 76


             18.4.3 MFJ 1278

             MFJ Radio Port (1) 
             This bit allows MFJ users to set the default radio port for 
             VHF. Set this bit to 1 to assign Radio 1 to VHF (Radio 2 to 
             HF). Set this bit to 0 to assign Radio 2 to VHF (Radio 1 to 
             HF). 

             MFJ Echo ON/OFF Flag (2) 
             Some versions of the MFJ firmware require 'ECHO ON' in 
             AMTOR. IF bit 2 is set, LAN-LINK will command 'ECHO ON' 
             before entering AMTOR, and will command 'ECHO OFF' when 
             leaving AMTOR, if you switch modes via the Menu.

             MFJ AMTOR Converse Flag (4)
             This bit configures the MFJ to send the CONVERSE Command 
             when someone connects in the AMTOR Mode.

        18.4 Turn Beacon Control ON/OFF

        This option toggles the LAN-LINK Handshake features. When they 
        are on (default), the Connect handshake message 

                            [ZCZ] *** LAN-LINK 2.32>

        will be transmitted on incoming connects. The beacon text and 
        time will be controlled by LAN-LINK as a function of the messages 
        you have posted on your system. When they are off, LAN-LINK does 
        not do anything to your beacon, nor does it transmit the 
        handshake.

        18.5 Turn Command Echo ON/OFF

        This option toggles the LAN-LINK "Command ECHO flag" ON and OFF 
        (not the ECHO parameter in the TNC). If the Command Echo flag is 
        set, the commands and (contents of) files LAN-LINK sends to the 
        TNC will be displayed in the outgoing window. Set this flag to 
        see how LAN-LINK commands the TNC in the different modes.

        18.6 Change Keyboard Beep Count

        LAN-LINK counts the number of characters entered on a line at the 
        keyboard. When it gets to a preset value it will beep, signaling 
        you to start a new line. If you have the Word wrap option set, it 
        will also automatically insert a "carriage return/line feed" 
        character sequence into the outgoing text for you. This option 
        changes the value that the keyboard beep counter is compared with 
        to sound the audio signal. 




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 77


        18.7 Set Message Count

        As an alternative to Function Key 8 (F8) or Alt-D, using this 
        option will also load a QTC "Mail" list into your Packet Communi-
        cations Mode Beacon and initiate a beacon transmission every 30 
        minutes (Refer to the BTEXT command in the TNC manual). If no 
        messages are present, or the only message is to you (incoming or 
        snatched), beacon transmissions are inhibited. This conforms to 
        good operating practice on crowded Packet channels.

        18.8 Turn Node Drop Link ON/OFF 

        When connecting via a Node, the normal way of operating is to 
        disconnect if the connect attempt fails. You may configure the 
        Node connect attempt flag to stay connected at the node where the 
        failure occurred. Use the normal mode when trying to get through 
        on a known path, and the stay alive mode when exploring Node 
        circuits.

        18.9 Turn Printer ON/OFF 

        This option toggles the printer ON and OFF. When the printer is 
        turned on, any incoming data will be printed in real time. If you 
        intend to print files received at 1200 baud in the Packet 
        Communications Mode, use a print spooler or you may lose data. 
        The printer is automatically turned off in the Packet Mode when a 
        disconnect occurs.

        18.10 Turn QTC Snatch ON/OFF 

        This option toggles the QTC Snatch flag ON and OFF. If the QTC 
        Snatch flag is enabled, LAN-LINK scans the contents of packets 
        appearing in the Inwindow on the screen while the terminal is 
        disconnected. Should it recognize the three text strings "LAN- 
        LINK", ":QTC:", and "YOURCALLSIGN" in the contents of a packet, 
        it will then issue a connect request to the callsign of the LAN-
        LINK station that originated the beacon transmission. If the 
        connect is made, the other station will send you the message 
        automatically which LAN-LINK will "capture to disk". The connect 
        will time out and terminate a few minutes later.

        The normal connect request will be made DIRECT to the station. If 
        you expect messages from stations you can only connect with via a 
        digipeater, place the path in your LAN-LINK.DIR directory file. 
        It should be there anyhow if you connect to the station 
        regularly. For example, if you expect messages from 4Z4ZB whom 
        you can only work if digipeated via 4X1AA then place an entry 
        like "4Z4ZB 4Z4ZB V 4X1AA" in the LAN-LINK.DIR file.

        The QTC Snatch leaves your messages in a message file 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 78


        YOURCALL.OUT. It is triggered by the first ">" in the initial 
        connect response of "LAN-LINK 2.00R>" and terminated by the 
        "over" at the end of the message e.g. G3ZCZ/W8>. If you train 
        stations not using LAN-LINK who want to leave you messages to 
        trigger your QTC-Snatch, by transmitting the following un- 
        addressed packet

                            LAN-LINK :QTC: YOURCALL

        your system will connect to them. (For example to leave a message 
        for me, they would send 

                            LAN-LINK :QTC: G3ZCZ

        as an un-addressed packet [in Converse Mode when not connected, 
        or in their beacon text].)

        If they then send you a ">" on a line by itself, followed by the 
        message itself, and terminated by another ">" as the last 
        character of the line, the message will end up in a message file 
        rather than in the LAN-LINK.RUN file and you can scan it fast 
        using Alt-M (Message Scan Menu Options). It goes without saying 
        that the message itself should not contain the ">" character at 
        the end of a line. If it does, by the way, the first part of the 
        message will be in the message file, while the remainder will be 
        in the LAN- LINK.RUN file.

        18.11 Turn :QSP: Relay Flag ON/OFF 

        This option toggles the Store and forward Message Relay 
        Capability of your system ON and OFF. If the Message Relay 
        Capability is active (toggled on), any one who connects can store 
        a message in your system using the ":QSP: CALLSIGN" NC/L command. 
        If the Message Relay Capability is not active anyone who attempts 
        to ":QSP:" a message will receive a ":QNO: error" message. The 
        status display window will show a "[R]" when the Message Relay 
        Capability is active. The default state for the Message Relay 
        Capability is loaded from the LAN-LINK.SYS file.

        When the Store and forward capability is active, the suffix "R" 
        will be added to the "[ZCZ] *** LAN-LINK 2.32". i.e., "[ZCZ] *** 
        LAN-LINK 2.32R" message received by anyone connecting to your 
        system to notify them that they can store messages. In this 
        manner they don't have to try to leave a message and then get 
        ":QNO:" error message to find out that the feature is toggled 
        off.

        Remember, if you configure your computer to store and forward 
        messages, you have a moral obligation to deliver them.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 79


        18.12 Turn Sound ON/OFF 

        This option toggles the sound ON and OFF. If the sound is off, a 
        flashing indicator will be displayed in the Status Window. When 
        the sound is toggled on again, a chime will sound to verify the 
        audio.

        18.13 Turn Contest Mode ON/OFF

        This option first toggles the Contest Mode. If the Contest Mode 
        is active, the word "TEST" and the number of the next QSO will be 
        displayed in the status window. When the Contest Mode is toggled 
        on, this command prompts you to set the starting QSO number, and 
        the standard message that will be transmitted as part of the 
        exchange of messages during the contest. The QSO number will be 
        incremented each time you log a contact. 

        The contest feature is toggled off the next time you select this 
        feature.

        While these features do give you some semiautomatic contest 
        operation by using command keys, there is no checking of 
        callsigns for duplicates built into the program. You may do that 
        by using the Alt-S hot key. 

        In a contest, you enter the callsigns and call the other station 
        in the normal manner, then use the "End" Key to transmit the 
        exchange (QSO number and standard text). LAN-LINK will only 
        transmit the contest text in this manner. If you want to add a 
        "K" or "KN", you will need to put it in the contest text string. 
        It is also advisable to use a different log file for each contest 
        to cut down the search time. The contest QSO number increments 
        each time you log the QSO (Alt-L). 

        You may put the Contest Mode into automatic if you are operating 
        AMTOR or packet. To do so, use the Alt-O function key.

        The following special character sequences can be entered in the 
        contest text string. 

        18.13.1 ##

        A "##" will be replaced by the QSO number when the text is 
        transmitted. 

        18.13.2 #1 

        A "#1" will be replaced by the callsign of the station being 
        worked in the contest text string. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 80


        18.13.3 #T

        A "#T" will be replaced by the date and time as read from the PC 
        time-of-day clock and converted to Universal Coordinated Time 
        (UTC). A sample time text is "03-Mar-92 03:13".

        For example, use the following entries for the following 
        contests;

         "##1 UR ##A" ... in the Sweepstakes,
         "5905" ... in the WAZ,
         "59 MD" ... in the ARRL DX, and
         "59 ##" ... in the WPX.

        As an example, if I (W3/G3ZCZ) am in the Sweepstakes contest, and 
        my Contest text line is,
         "##1 UR ##A W3/G3ZCZ 68 MDC". 
        If the next QSO number is 345, and I am working KW3C, when I 
        touch the "End" key, LAN-LINK would transmit the following line 
        "KW3C UR 345A W3/G3ZCZ 68 MDC".

        18.14 Turn DCD Flag ON/OFF 

        If you are using a PK-232 then this flag should be set to ON. If 
        you are using a KAM, this flag should be set to OFF. If you are 
        using another TNC, and if you can set the TNC so that pin 8 on 
        the RS-232 interface changes state when connected, do so, and set 
        this flag to ON. If you can't, then set this flag to OFF. If this 
        flag is OFF, the multiple-connect modes will not work so don't 
        attempt to invoke them. If this flag is OFF, the words "*** 
        CONNECTED" and "*** DISCONNECTED" when seen in the LAN may cause 
        spurious apparent connects and disconnects in LAN-LINK. 

        18.15 Turn PBBS Snatch ON/OFF 

        When the PBBS Mail Snatch is enabled, and a PBBS sends a packet 
        announcing "Mail", if your callsign is in the first line of that 
        message, LAN-LINK will issue a connect request (again via the 
        path in LAN-LINK.DIR) to that PBBS. When connected, it will act 
        as if you have initiated a Zap PBBS command. The Zap counter will 
        be incremented each time a PBBS Mail Snatch takes place.

        If the PBBS Mail beacon has an extra line in it (between the 
        header and the list of calls) as follows, the PBBS Mail snatch 
        will not work. 

        On the other hand, if N4FG is monitoring the LAN, and a message 
        is posted for any callsign containing the character string "N4FG" 
        such as N4FGA, N4FG will respond to the message. This gives rise 
        to a lock out situation, because N4FG will respond to the beacon, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 81


        go through the sequence described in the Zap PBBS section and 
        disconnect. The beacon message will not be cleared because it was 
        not read, so the next mail beacon from the PBBS will contain the 
        call N4FGA, and N4FG will once again respond to it.

        Should you be unlucky and happen to be in this situation, disable 
        the PBBS Snatch flag and set a Periodic Event to Zap your PBBS 
        sometime in the middle of the night. Alternatively, when you come 
        into the shack and the PBBS is in use, set the "Zap PBBS on Next 
        Mail Beacon" parameter to ON.

        18.16 Turn Time Id. ON/OFF

        This option allows you to determine if the callsign sequence 
        transmitted using Function key 3 (F3) will contain a date/time 
        stamp. If the Id. is set ON a date/time stamp will be 
        transmitted.

        18.17 Turn Automatic Capture-to-Disk Flag ON/OFF 

        This option allows you to turn the automatic "capture-to-disk" 
        feature ON and OFF.

        18.18 Change PBBS Parameters 

        This sub-menu allows you to change the PBBS Parameters, as 
        described in the following paragraphs.

        18.18.1 Local PBBS Callsign

        This option lets you change the call of the local PBBS. This is 
        the call that LAN-LINK will show in the prompt for the "Zap" 
        command.

        18.18.2 Mail-Snatch Trigger Word

        You can set the Mail-Snatch Trigger in the PBBS Mail beacon. Most 
        PBBSs use word "Mail" and a string of calls to indicate the 
        presence of messages. If your PBBS uses something else, you may 
        customize LAN-LINK on this line to tell it what word your PBBS 
        uses. This word is case sensitive. If your PBBS uses "QTC" 
        instead of "Mail", you may end up calling yourself if you 
        disconnect while traffic is flowing on the LAN.

        18.18.3 Read Request Command

        This is the command LAN-LINK issues to the PBBS during a Zap 
        sequence to request your mail. The default value is "RM" for Read 
        Mine. On a WA7MBL type PBBS you may change it to "VM" for a 
        Verbose Read of the full packet headers. On a W0RLI PBBS you may 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 82


        change it to RN to only request new messages. If you do change 
        it, use the "V" option in the Parameters Menu to make sure it is 
        correct. If it isn't correct, the Zap PBBS feature will not work.

        18.18.4 Read Bulletin Request Command

        This is the command LAN-LINK issues to the PBBS during a Zap 
        sequence to read bulletins identified by the scan words. The 
        default value is "R" for Read. For a Verbose Read of the full 
        packet headers on a WA7MBL type PBBS, change it to "V"; on a 
        W0RLI type PBBS change it to "RH".

        18.18.5 PBBS Subject String

        When you enter a message into a PBBS, you first use the "S" 
        command. The PBBS then sends you a reply asking you for some 
        information about the PBBS; typically the subject of the message. 
        When you have entered the subject, the PBBS then asks you for the 
        rest of the message. This line is used in the Zap sequence and is 
        a unique word seen in the text that the PBBS sends you asking for 
        the subject.

        18.18.6 PBBS Message String

        When you enter a message into a PBBS, you first use the "S" 
        command. The PBBS then sends you a reply asking you for some 
        information about the PBBS; typically the subject of the message. 
        When you have entered the subject, the PBBS then asks you for the 
        rest of the message. This line is used in the Zap sequence and is 
        a unique word seen in the text that the PBBS sends you asking for 
        the text of the message.

        18.19 Change Callsigns 

        This sub-menu allows you to change the Callsign and AMTOR SELCAL, 
        as described in the following paragraphs.

        18.19.1 Callsign

        The default callsign is G8BTB. Please do not use G8BTB. Replace 
        G8BTB with yours. This is the callsign that will be used in the 
        non packet modes. You may use "portable designators" such as 
        G3ZCZ/A, G3ZCZ/W3, W3/G3ZCZ or G3ZCZ/4X, which you cannot do in 
        Packet. 

        This is the call that will be monitored for in the Digipeat 
        Monitoring Mode. In this Mode, which is toggled on and off by the 
        selection of the "D" Option included in the Parameter Menu (PK-
        232 only), if someone uses you as a digipeater while you are not 
        connected to anyone else, the event will be logged to disk. This 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 83


        Mode will only work if your callsign as stored in this line is a 
        valid (uppercase only) packet callsign. 

        For example, in the PK-232, if the callsign is G3ZCZ then the 
        sequence >G3ZCZ> will be recognized as a digipeat and the event 
        logged. Thus 4X6AA*>G3ZCZ>4Z4ZB would be logged as a digipeat 
        event. 

        Store your callsign using UPPERCASE characters if you want the 
        "DIGIPEAT DETECT" option to work (i.e. G3ZCZ). If you use lower 
        case (i.e. g3zcz), recognition will never take place. The TNC 
        displays all callsigns in upper case in the non packet communica-
        tions modes.

        If you are using an SSID (e.g. G3ZCZ-8) in the Packet 
        Communications Mode, you should enter the whole call INCLUDING 
        the SSID.

        18.19.2 The SELCAL

        This is your AMTOR SELCAL. LAN-LINK will try to guess it and 
        prompt you with a SELCAL configured for your callsign. If you 
        want a different one, overwrite the prompted version.

        If you are not using a PK-232 or KAM or the MFJ1278, you don't 
        have to change anything, but the SELCAL line must still be in the 
        Configuration file.

        18.19.3 The PacketCluster Call

        This option allows you to change the default PacketCluster Call 
        without connecting to it.

        18.20 Change Directories 

        This sub-menu allows you to change the Directories used by LAN-
        LINK, as described in the following paragraph.

        18.20.1 Capture-to-disk files Directory

        This is the drive and directory that LAN-LINK will put the *.RUN 
        capture-to-disk files. Note: the last "\" MUST be present if you 
        are using a different sub-directory.

        18.20.2 QBM Download Directory

        This is the directory the :QBM: command will search to find a 
        file to be downloaded. The default directory for the files is 
        \LAN-LINK\FILES\. Note: the last "\" MUST be present.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 84


        18.21 Enter Common Calls

        Each time you call another station, LAN-LINK remembers it (up to 
        the last 16). When you update the SYS file, those calls will be 
        saved to disk. You can use this option to add calls, delete calls 
        or edit calls in the list. Use the "Delete" key to delete a call.

        18.22 Change File Names

        This sub-menu allows you to change the default file names used by 
        LAN-LINK, as described in the following paragraphs.

        18.22.1 VHF Logbook File (VHF.DBF)

        This is the name of the file to be used as your VHF Packet 
        logbook. 

        18.22.2 HF Logbook File (HF.DBF)

        This is the name of the file to be used as your HF logbook. It is 
        used for all HF modes, including HF packet.

        18.22.3 Path Directory File (LAN-LINK.DIR)

        This is the name of the file used as your call directory. 

        18.22.4 Brag Tape (LAN-LINK.TXT)

        This is the name of the file used as your brag tape. 

        18.22.5 QBU Upload File Name (QBU-TX.BAT)

        This is the name of the batch file used to initiate a QBU. 

        18.22.6 QBU Download File Name (QBU-RX.BAT)

        This is the name of the batch file used when a :QBU: command is 
        received from a remote station. 

        18.23 Change LAN-LINK Parameters

        This sub-menu allows you to change the LAN-LINK Parameters, as 
        described in the following paragraphs.

        18.23.1 Change CQ Text

        This feature allows you to change the contents of the CQ text 
        message string. This is the message string that is transmitted 
        along with the CQ call. Think of this message as a CQTEXT line. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 85


        18.23.2 Set CQ Delay Time (Seconds)

        This option allows you to change the time (seconds) that the LAN-
        LINK waits for a response after a CQ call until the following one 
        is transmitted. The default value (in minutes and seconds) is 
        loaded from the LAN-LINK.SYS file. 

        18.23.3 Set CQ Delay Time (Minutes)

        This option allows you to change the time (minutes) that the LAN-
        LINK waits for a response after a CQ call until the following one 
        is transmitted. The default value (in minutes and seconds) is 
        loaded from the LAN-LINK.SYS file.

        18.23.4 Set Connect Time Timeout (Minutes)

        This option allows you to change the time (minutes) that the LAN-
        LINK waits for a response in a packet connect before issuing a 
        Disconnect command. The default value is loaded from the LAN-
        LINK.SYS file. 

        18.23.5 Set Number of Lines in a Non-Contest CQ Call

        This option allows you to change the number of lines in a non-
        contest CQ call from the default value of 3 to any number you 
        wish. The default value is loaded from the LAN-LINK.SYS file. 

        18.23.6 Keyboard Beep Character Count

        When your typing at the keyboard gets to a point where you may 
        overrun the normal line length, LAN-LINK issues a beep to remind 
        you to touch the "Enter" key. This option allows you to change 
        the number of characters you can type in a line before the beep 
        sounds. Note the beep will not sound if the sound flag is 
        inhibited.

        18.23.7 Word Wrap Mode

        This option allows you to change the word wrap mode. It is really 
        more of a "force carriage return" parameter, rather than "word 
        wrap". There are four options as follows:

        18.23.7.1 Off: Word wrap is off.

        18.23.7.2 AutoCR: LAN-LINK will insert an "Enter" character for 
                 you into the outgoing text when you enter the first 
                 space character after the beep has sounded.

        18.23.7.3 Word: LAN-LINK will hold all entered text until you 
                 either type a space character or touch the "Enter" key. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 86


                 At that time LAN-LINK will send the word to the TNC.

        18.23.7.4 Line: LAN-LINK will hold all entered text until you 
                 either touch the "Enter" key or the beep sounds. At that 
                 time LAN-LINK will send the word to the TNC.

                         Set this parameter value as follows, 
                         0 = OFF, 
                         1 = AutoCR, 
                         2 = Word, 
                         3 = Line.

        18.23.8 Set Shut Down Mode (QRT Flag)

        This option allows you to customize the shut down and start up 
        sequences of the TNC as described in the following sections. If 
        the Shut down mode is not set to 1, you also have the option to 
        customize the packet terminal mode.

        18.23.8.1 State 0: On shut down, turns the TNC into a VHF Digi-
                 peater and turns CONOK OFF (CFROM NONE for the PK-232). 
                 In this condition the TNC will reject connect requests. 
                 On start up turns CONOK or CFROM on.

        18.23.8.2 State 1: Does not send any commands to the TNC on shut 
                 down or start up.

        18.23.8.3 State 2: On shut down, sends CMSG ON to the TNC. On 
                 start up, sends CMSG OFF to the TNC.

        18.23.8.4 State 3: On shut down, turns on the mailbox in the TNC. 
                 On start up turns off the mailbox.

        18.23.8.5 State 4: On shut down, turns on the mailbox in the TNC 
                 and puts the TNC into the SOLO Mode so that the internal 
                 buffer in the TNC does not fill with on-the-air traffic. 
                 On start up turns off the mailbox.

        18.23.9 Set Default Users

        This option allows you to set the maximum number of multiple 
        users that can be connected to your TNC at the same time, and to 
        configure the default start up mode of the program. If this 
        parameter is set to 1, LAN-LINK will configure itself to the 
        single user mode, and set the maximum number of users to 9. If 
        this parameter is set to any number other that 1, LAN-LINK will 
        assume that value to be the maximum number of allowed connects, 
        and configure itself in the Multiple user Mode (equivalent to the 
        TNC Menu Option 0).



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 87


        18.23.10 Set UTC Offset

        This parameter contains the difference in hours between Universal 
        Co-ordinated Time (UTC) and your local time. For example, if you 
        are located on the east coast of the U.S.A., and it is winter, 
        you are in the Eastern Standard Time (EST) Zone, which is 5 hours 
        behind UTC. In this case, the value of the UTC Offset parameter 
        is 5. Don't forget to change this parameter when the clocks are 
        adjusted each spring and autumn.

        18.23.11 VHF Packet Length

        This option allows you to change the default VHF packet length. 
        The TNC has a maximum permissible value of 255. Set the parameter 
        to 127 or 255.

        18.23.12 HF Packet Length

        This option allows you to change the default HF packet length. 
        The default value of about 30 seems to be optimal. 

        18.23.13 Beacon Time

        This option allows you to change the default beacon time. The KAM 
        requires a value in minutes, all other TNCs in tens of seconds. 
        Use good operating practice and don't beacon too often. Every 30 
        minutes on a well used channel is more than enough.

        18.23.14 Custom Prompt before "Over"

        This option allows you to add a word or two (up to 20 characters) 
        before the ">" in packet or the "+?" in AMTOR. If you are working 
        an AMTOR APLINK PBBS, clear this feature by changing it to a 
        space character.

        18.23.15 Packet Cluster DX Alert Mode

        This parameter determines the action LAN-LINK takes when you are 
        connected to a PacketCluster, and a DX Alert message shows up. 
        The states are 0, 1, 2, or 3.

        If it is 0, LAN-LINK takes no action at all. In all other states, 
        LAN-LINK splits the prefix from the DX callsign, searches the HF 
        logbook for the prefix and posts a message in the status window 
        (in the Alert Call color) as follows: Prefix, Logbook Status, DX 
        callsign. The logbook status shows up as 'Q' for QSLd, 'W' for 
        worked and '?' for not in log. You can configure LAN-LINK to 
        generate an audible alarm for each condition to save you 
        monitoring the screen. If the Sound is inhibited, the audible 
        alarm will also be inhibited. The visual display and audio alarms 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 88


        are controlled by this parameter as shown below.

        State     QSLd (Q)            Worked (W)          Not in Log (?)
          0       No Action           No Action                No Action
          1       Audio + Display     Audio +Display      Audio + Display
          2       Display             Audio + Display     Audio + Display
          3       Display             Display             Audio + Display

        You can customize the CW tone and speed, by changing the states 
        of the "Packet Cluster DX Alert Tone CW Dit time" and "Packet 
        Cluster DX Alert Tone CW Note" parameters in the LAN-LINK.SYS 
        File.

        In this version of LAN-LINK, the prefix scan is simple minded, so 
        set this parameter to 3 to get used to it, then set it to 1.

        18.24 Change PC Communications Parameters

        This sub-menu allows you to change the Communications Parameters 
        between the PC and the TNC, as described in the following 
        paragraphs.

        18.24.1 The Communications Port

        This is the default Communications port. The default value is 1. 
        You may set it at any value between 1 and 4. If you only have one 
        serial port in your PC, set the parameter to "1" even if your 
        card is configured as Com2. LAN-LINK will ALWAYS assume Com1 for 
        a single card. If you use a different port instead of Com1, and 
        plan to do binary transfers, don't forget to customize the 
        QZ*.BAT files.

        The default Com3 and Com4 default PC port values are as follows.

        Port  Address(Hex)            Address (Decimal)     IRQ
        Com3       3E8                      1000             4
        Com4       2E8                       744             3

        If you set the port number to 0, LAN-LINK will not accept or 
        transmit any character to the serial port. All other features 
        will work.

        18.24.2 The Terminal Baud Rate

        This Parameter tells LAN-LINK what baud rate the TNC is set to. 
        This is the baud rate on the RS-232 line between the TNC and the 
        PC. Valid baud rates for LAN-LINK are 300, 1200, 2400, 4800, 9600 
        and 19,200. If you specify something else LAN-LINK will default 
        to 1200. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 89


        You may experience problems when using baud rates greater than 
        1200. It depends on the CPU clock rate, any TSR's in the PC, and 
        the I/O card in the PC. LAN-LINK scans the incoming text 
        constantly, something which requires time. My PK-232, when used 
        with my XT Clone at 10MHz, does not like baud rates faster than 
        2400, and sometimes not even that. The PK-232 seems to drop the 
        first character of some lines at 4800 baud. Use 1200 until you 
        have tested, and are sure that a faster one will work.

        This program has been tested on a TNC2 and an MFJ1278 using a 
        terminal baud rate of 9600 baud and worked correctly. It also 
        works correctly with a KAM at 2400 Baud.

        If you use a different rate instead of 1200, and plan to do 
        binary transfers, don't forget to customize the QZ*.BAT files.

        18.24.3 TNC Data Bits

        You can set the number of data bits on the RS-232 line between 
        the PC and TNC to 7 or 8. Use 7 with a TNC2 if you have problems 
        with Greek characters. Set this value to either 7 or 8.

        18.24.4 TNC Parity

        Use this parameter to set the Parity bit on the RS-232 line 
        between the PC and TNC. Enter the letter corresponding to the 
        desired parity. N = None, O = Odd, E = Even, M = Mark, S = Space.

        18.24.5 Number of TNC Stop Bits

        You can set the number of stop bits on the RS-232 line between 
        the PC and the TNC to 1 or 2. Use 1 at all terminal (not packet) 
        baud rates except 300. Set this value to 1 or 2.

        18.25 Change Colors

        This option lets you change the default colors. A display of all 
        of the combinations is shown on the left side of the screen. You 
        will then be prompted to sequence through each window/message 
        color that can be customized. Enter the number shown in the 
        combination window followed by the "Enter" key to set a value. If 
        you don't wish to make a change, just press the "Enter" Key.

        The following identifications are made to the color choices:

        18.25.1 OutWindow Color

        This is the color of the text (typed at the keyboard) in the 
        outgoing window.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 90


        18.25.2 StatusWindow Color

        This is the color of the Status Window.

        18.25.3 PromptWindow Color

        This is the color of most of the menus.

        18.25.4 LogWindow Color

        This is the color of the text in the log window.

        18.25.5 InWindow Color

        This is the color of the text in the window showing the incoming 
        characters.

        18.25.6 ScrollBack Window Color

        This is the color of the text in the Scroll back window.

        18.25.7 MHWindow Color

        This is the color of the text in the monitor heard calls (MH) 
        window.

        18.25.8 Alarmwindow Color

        This is the color of the text in the Error and Alarm window.

        18.25.9 BottomWindow Color

        This is the color of the text in the prompt line at the bottom of 
        the screen.

        18.25.10 Emphasis Color

        This is the color of the emphasized text in the Menu windows.

        18.25.11 Prompt Color

        This is the color of the prompt text in the Menu windows.

        18.25.12 Option Color

        This is the color of selected option text in the Menu windows.

        18.25.13 Connected Text Color

        This is the color of the text in the incoming window when 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 91


        connected in the packet communications modes.

        18.25.14 Computer Color

        This is the color of the computer generated text in the outgoing 
        window when the Command Echo Flag option is enabled.

        18.25.15 VHF Header Color

        This is the color of the VHF Header lines in the Incoming window 
        when not connected.

        18.25.16 HF Header Color

        This is the color of the HF Header lines in the Incoming window 
        when not connected.

        18.25.17 Alert Call Color

        This is the color of the packet header lines containing the Alert 
        call in the Incoming window when not connected. It is also the 
        color of the non-permanent Parameter Menu prompts.

        18.25.18 Outgoing Text Color

        This is the color of the outgoing text echoed in the Incoming 
        window in the AMTOR Communications Mode.

        18.25.19 Multi I/O Stream Color[1]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 1.

        18.25.20 Multi I/O Stream Color[2]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 2.

        18.25.21 Multi I/O Stream Color[3]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 3.

        18.25.22 Multi I/O Stream Color[4]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 4.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 92


        18.25.23 Multi I/O Stream Color[5]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 5.

        18.25.24 Multi I/O Stream Color[6]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 6.

        18.25.25 Multi I/O Stream Color[7]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 7.

        18.25.26 Multi I/O Stream Color[8]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 8.

        18.25.27 Multi I/O Stream Color[9]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 9.

        18.25.28 Multi I/O Stream Color[10]

        This is the color of the text lines in the Incoming window in the 
        Multiconnect Mode when connected to I/O stream 10.

        When you change the colors, LAN-LINK does not overwrite all 
        existing windows. If you want to be sure of seeing the changed 
        colors, save the color changes using the Update option, and then 
        exit from and reload LAN-LINK. 

        18.26 Change SAREX Parameters 

        This sub-menu allows you to change the SAREX Ground Station 
        parameters, as described in the following paragraphs.

        18.26.1 SAREX CallSign

        This is the callsign of the SAREX station.

        18.26.2 Change SAREX Capture to Disk File

        This option lets you change the name of the SAREX Capture- to-
        disk file. Don't change file names while "capture-to-disk" is in 
        progress (when a flashing "[S]" in present in the status window), 
        or the old one will stay open and may not close properly when 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 93


        LAN-LINK is terminated, resulting in data loss.

        18.27 Update Configuration File

        Use this option to save the changes (permanently) in the 
        configuration file (LAN-LINK.SYS). Activate it twice to see most 
        of the changes.

        18.28 Verify Changes 

        This feature lets you display how LAN-LINK was configured by the 
        LAN-LINK.SYS file. It also displays the state of any flags you 
        have set/reset if they are not already shown in the Status window 
        or Parameter Menu. 

        18.29 Change Scan Words 

        In the ZAP PBBS feature you can ask the program to scan the lines 
        read from the PBBS and if it sees any of the scan words in the 
        line, it will queue a request for that bulletin by number. You 
        can only set 16 such Scan words (should be enough) and request up 
        to 255 messages/bulletins at a time. 

        Color in the scan words. The colors shown in the Scan Word window 
        match the colors the lines containing those scan words are 
        written in during a BBS Zap. The colors are the multi stream 
        colors.

        Use the "Delete" key to delete a word from the list.

        Words that show up in the PBBS prompt line cannot be used as scan 
        words. For example, if your PBBS prompts you with

                             N4QQ PBBS> 

        then "N4QQ" and "BBS" should not be used as Scan Words. 
        Don't leave a blank line in the Scan Word section of the 
        configuration file.

        18.30 Turn Miscellaneous Flag ON/OFF

        The Miscellaneous Flag performs several different functions in 
        the different Communications modes as follows.

        18.30.1 All Modes:- Debug or state-sequence numbers

        Shows two debug or state-sequence numbers in left hand corner of 
        the status window in the format N-M]. N is the BBS State and M is 
        the Communications State. These are used to figure out what went 
        wrong in the automatic sequences. If an automatic sequence fails 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 94


        to work, set the miscellaneous flag, and observe the state in 
        which LAN-LINK seems to hang. It will be waiting for something, 
        and you should get a clue as to what, from Table 18.30.1. BBS 
        State (N) numbers are shown in Table 18.30.1-A and the 
        Communications states are shown in Table 18.30.1-B. 

                           Table 18.30.1-A BBS States

        1    Connected to BBS waiting for first '>'
        2    Receiving incoming messages
        3    Receiving list of new messages
        4    Receiving your messages (in case missed some)
        5    Custom command (i.e. KM)
        6    LAN-LINK QTC Snatch in progress
        7    Receiving Mail going to YOURCALL.OUT
        8    :QDB: waiting for QRV/QNO
        9    :QDB: sending file waiting for QSL/QNO
        10   AUto UPload Opening BBS.BBS command file
        11   AUto UPload sending one line command
        12   AUto UPload sending subject line of message
        13   AUto UPload sending message
        14   AUto UPload waiting for last '>' before disconnecting
        22   Receiving file
        25   Packet cluster connect waiting for first '>'
        26   Packet cluster connect waiting for first '>' 

                      Table 18.30.1-B Communications States

        0    Disconnected packet mode or normal non packet mode.
        1    Connected in packet mode
        2    Trying to connect in packet mode
        3    Trying to disconnect in packet mode
        4    Sending mail file in packet mode
        5    ARQ called someone, or in QSO
        6    Connected in autocq mode
        7    Calling autocq in packet
        8    Sending file in autocq
        9    Waiting for reply in autocq packet
        10   Autocq non packet sending CQ message
        11   Autocq non packet waiting for reply
        12   SELCAL waiting for ZCZC or YOURCALL
        13   SELCAL waiting for NNNN
        14   Autocq AMTOR sending bragtape
        15   Autocq AMTOR receiving message
        16   Autocq AMTOR requesting repeat of his_call
        17   Autocq MFJ1278/KAM waiting for 73 to complete and sign off
        21   QRU mode packet
        22   Calling someone in pactor
        25   AMTOR sending :QQQ: response
        26   QRU mode packet


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 95



        18.30.2 BAUDOT Mode:- Navy MARS Protocol Verify

        When the flag is set, and the BAUDOT Navy MARS option is enabled, 
        the character string ":CR:" will be displayed in the outgoing 
        window each time a carriage return character is received in the 
        incoming window. Similarly, every time a line feed character is 
        received, a ":LF:" will be displayed in the incoming window. 

        You may use this feature to verify that another station is 
        sending files using the correct protocol. If you do, make sure 
        that you tell the PK-232 not to add a line feed to incoming 
        carriage returns by setting the ALFD parameter to OFF in the Com-
        mand Mode. You will have to set "ALFD ON" again when you change 
        to other communications modes, or all incoming lines will 
        overwrite each other.

        18.31 Change Band/Mode

        This option is used to set the band and radio mode without 
        invoking the Log Menu. You can use it when changing bands on HF 
        before logging a new QSO. The value is not remembered when you 
        shut LAN-LINK down, unless you log the QSO.

        18.32 Zap PBBS on Next Mail Beacon

        This parameter causes LAN-LINK to Zap your local PBBS next time 
        it beacons with a list of calls for which it has Mail.

        18.33 PBBS Zap, Don't Disconnect After Sequence

        This parameter stops LAN-LINK from issuing the automatic 
        disconnect when the Zap sequence is over. You can set it during 
        the Zap sequence. Use it to stop the disconnect if the sequence 
        gets out of sync with the messages, or if there is something 
        interesting you wish to do to the PBBS. This parameter resets 
        when the Zap sequence terminates.

        18.34 Control Send of LAN-LINK.OUT 

        THe LAN-LINK.OUT file is a file that you can configure LAN-LINK 
        to transmit to an incoming connect (packet, AMTOR, Pactor and G-
        TOR modes). Think of this file as a CTEXT File. If this flag is 
        set, the file will be transmitted. If this flag is OFF, the file 
        will not be transmitted. Use this file as a welcome or help file 
        to other stations when using LAN-LINK in a special event station.

        19.0 Q Codes [NC/L]

        This option displays help information about the use of the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 96


        Network Communications Language (NC/L) "Q" codes.

        20.0 COMMUNICATIONS MODES

        This menu allows you to change the communications mode of the 
        TNC. If your TNC hardware cannot support those modes, don't 
        bother to try them. This is software not hardware, and in spite 
        of what people tell you, software can't do everything. The commu-
        nications modes shown in Figure 20 are available. Type in the 
        single letter to make your choice. While the KAM ports are set, 
        and the MFJ-1278 ports are defaulted in LAN-LINK (1 = VHF, 2 = 
        HF), don't forget that YOU HAVE to select the correct radio port 
        on the PK-232.

                    Figure 20 PK-232 Communications Mode Menu

                                 V VHF PACKET
                                 H HF PACKET
                                 A AMTOR (STANDBY)
                                 B BAUDOT (RTTY)
                                 C MORSE (CW)
                                 M AMTOR (MONITOR)
                                 P PACTOR (STANDBY)
                                 Q PACTOR (MONITOR)
                                 S ASCII (RTTY)
                                 N NAVTEX
                                 G SIGNAL/G-TOR
                                 X Manual

        20.1 VHF PACKET

        This is the 1200 baud VHF Packet Mode. LAN-LINK will optimize the 
        TNC link parameters for this mode.

        20.2 HF PACKET

        This is the 300 baud HF Packet Mode. LAN-LINK will optimize the 
        TNC link parameters for this Mode.

        20.3 ASCII (RTTY)

        This is the ASCII RTTY Mode. LAN-LINK will configure the TNC 
        parameters for this Mode at 110 baud.

        20.4 BAUDOT (RTTY)

        This is the BAUDOT RTTY Mode. LAN-LINK will configure the TNC 
        parameters for this Mode at 45 baud.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 97


        20.5 MORSE (CW)

        This is the CW Mode. LAN-LINK will configure the TNC parameters 
        for this Mode at the default CW speed (20 for the PK-232 and MFJ-
        1278, 10 wpm for the KAM).

        In this Mode the ALT-D Key will disengage the receive speed lock 
        inside the PK-232 to facilitate locking onto another signal and 
        Function Key 8 (F8) will turn the transmitter off.

        LAN-LINK has a flag in the configuration file that lets you 
        configure the XMITOK parameter in the TNC. This flag allows you 
        to set XMITOK to "OFF" when you enter the CW communications mode, 
        and turn it "ON" again when you exit from the CW communications 
        mode.

        20.6 AMTOR (STANDBY)

        When you select the AMTOR Standby Mode you are placed into the 
        "Standby Receive" Mode. If you are in AMTOR Standby Mode, you 
        will not be able to display signals of the Chirpcopy Mode (which 
        means that you will not be able to display a QSO in progress).

        The Alt-D Key and Function Key 8 (F8) both toggle between the 
        AMTOR STANDBY and MONITOR communications modes.

        20.7 AMTOR (MONITOR)

        If you want to read the mail on an existing AMTOR QSO in 
        progress, select the AMTOR (MONITOR) or Chirpcopy Mode. 

        The Alt-D key and Function key 8 (F8) both toggle between the 
        AMTOR STANDBY and MONITOR communications modes.

        20.8 PACTOR (STANDBY)

        When you select the Pactor Standby Mode you are placed into the 
        "Standby Receive" Mode. If you are in Pactor Standby Mode, you 
        will not be able to display signals from a QSO in progress.

        The Alt-D Key and Function Key 8 (F8) both toggle between the 
        Pactor STANDBY and MONITOR communications modes.

        20.9 PACTOR (MONITOR)

        If you want to read the mail on an existing Pactor QSO in 
        progress, select the Pactor STANDBY or Chirpcopy Mode. 

        The Alt-D key and Function key 8 (F8) both toggle between the 
        Pactor MONITOR and STANDBY communications modes.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 98



        20.10 SIGNAL

        Use this option to select the PK-232 SIGNAL Mode. Read the PK-232 
        documentation carefully to understand how this mode works. Once 
        the PK-232 has identified the digital signal it is tuned to, use 
        the Communications Mode Select Menu a second time to select the 
        relevant mode and then set the baud rates and shift to display 
        the data if necessary.

        20.11 NAVTEX

        Use this option to select the NAVTEX Mode. Read the TNC 
        documentation carefully to understand how this Mode works. 

        20.12 G-TOR

        If you are using a KAM, you may use this option to select the G-
        TOR Mode. Read the TNC documentation carefully to understand how 
        this Mode works. If you are not using a KAM, this option will not 
        show up on your menu.

        20.13 MANUAL

        This option selects the HF logbook and copies the previous mode 
        entry in subsequent logging. Use this mode to log SSB or FM 
        contacts when monitoring the PacketCluster and working stations 
        spotted therein.

        21.0 TERMINAL MODE MENU

        This menu allows you to set the Terminal Configuration Mode. The 
        Terminal Menu provides different choices depending on which 
        communications mode you have selected.

        21.1 Packet Terminal Menu

        The Packet Terminal Mode of operation will be shown in the Status 
        window at the top of the screen. If you are reading the mail on a 
        station, the callsign of that station will be shown next to the 
        word "MAIL". If you are connected to someone, the call (and path) 
        will be shown prefixed by the "*>" sequence.

        In the Packet Communications Mode, you are presented with the 
        choices shown in Figure 21.1. Type in the single letter to make 
        your choice. 

        21.1.1 Change Packet Baud Rate

        In the PACKET Mode you may change the RF baud rate between 300, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 99


        600, 1200 and 2400 baud. While LAN-LINK allows these baud rates, 
        the TNC may not.

        21.1.2 CQ/Beacons

        In this Mode, you will see CQ and BEACON packets on the channel. 
        This Mode only works on the PK-232 and the KAM.

                        Figure 21.1 Packet Terminal Menu
                                 B Change Packet Baud Rate
                                 C CQ/Beacons  
                                 E Everything  
                                 I Information 
                                 L Turn MCON ON 
                                 M Read the Mail          
                                 O Turn Meta Beacon ON    
                                 S Just My Station (Solo) 
                                 T All Traffic            
                                 0 Multiple User Connects 
                                 F Turn Conference ON     

        21.1.3 Everything

        You can set the TNC Mode to "Everything", i.e. show all packets 
        on the LAN.

        21.1.4 Read the Mail

        You can read the mail on a PBBS or other station and get 
        bulletins without connecting to that station yourself. You use 
        this Mode to do so. You will be prompted for the call whose 
        packets you wish to monitor. Remember to enter the call of the 
        station sending the packets, not the call of the one receiving 
        them. This mode only works without showing the packet headers on 
        the PK-232. On the other TNCs the headers will also be displayed.

        You can also use this command to monitor both sides (read the 
        mail) on a QSO on a busy packet channel.

        You may want to turn the Digipeat Data Display Mode off when 
        reading the mail.

        21.1.5 Just My Station (Solo)

        In this Mode, you will only see messages addressed to you. You 
        will only get messages from people who connect to you. 

        21.1.6 All Traffic

        In this Mode you will see all of the data packet traffic on 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 100


        channel. You can use this Mode to check that the TNC is working. 

        21.1.7 Information Packets 

        In this Mode you will see all of the packet traffic on channel 
        that contain information. You can use this Mode to check that the 
        TNC is working. 

        21.1.8 Single User Connects

        This is the normal one-on-one Mode of operation (USERS 1).

        21.1.9 Multiple User Connects

        When you are in a Multiple Connect Mode, an asterisk will be 
        shown in the status window next to the word "PACKET". Each I/O 
        stream will show up in the Inwindow in a different color.

        LAN-LINK supports two multiple connect modes, Individual and 
        Conference.

        An extract of an actual "off the air" CRT display (showing 
        received text only) in a multi-user mode is shown below. Each 
        line of text as received by the TNC is prefixed (by the PK-232) 
        with the I/O channel number and callsign of the station its 
        connected with.

         1:4X4IL: *** CONNECTED to 4X4IL via 4X4IC, 4X6JP
         0:4X4IC: joe do u read?
         2:4Z4ZB: *** CONNECTED to 4Z4ZB
         1:4X4IL: Look for me on PR via 4X6JP 73s and Shalom.
         2:4Z4ZB: GE JOE I WILL DIS THEN U CAN GO VIA THE REP>
         1: *** DISCONNECTED: 4X4IL via 4X4IC, 4X6JP
         0:4X4IC: UNPROTO CQ
         2:4Z4ZB: GO AHEAD BOYS...DE ALON..>
         0:4X4IC: 
         2: *** DISCONNECTED: 4Z4ZB

        This is the normal Multi-connect Mode as described in the TNC 
        manual. Here you are connected to up to 10 stations and will send 
        different traffic to each of them. Each time you wish to send 
        something to a particular station, you must select the I/O 
        channel the station is connected on before typing the text or 
        sending the file.

        The default stream change character for all TNCs in the VHF 
        multiple connect modes is "|" ($7C). In the KAM, it is "\" on HF 
        and "|" on VHF. They are both on the same key but one is in the 
        shift case. Be careful on HF as the "\" shows up in file 
        directories and confuses the computer. These values can be 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 101


        customized. However to do so, they must be customized both in 
        LAN-LINK and in the TNC at the same time.

        You select the I/O channel using the Alt-N key and moving the 
        cursor to the desired stream, or by typing the "|" character 
        followed by (in the TNC) the channel letter/number. For example 
        to do it manually, if you are connected to G8BTB on I/O channel 0 
        and to G3ZCZ on I/O channel 1, then to talk to G8BTB you would 
        type "|0" before any text, and similarly to send something to 
        G3ZCZ you would type a "|1" before the text you"re going to send 
        me. If you are not using a PK-232, read the TNC manual to deter-
        mine if the I/O streams are identified by numbers or by letters. 
        The TNC2 standard configuration uses letters ("|A" etc.).

        Use the Alt-N key and move the cursor up and down to select the 
        I/O channel automatically.

        21.1.10 Conference

        In the Conference Mode on the other hand, everything that you 
        type at the keyboard is automatically transmitted to each station 
        that you are connected with. Thus if you are linked to two 
        stations each line will be packeted twice by the TNC. You don't 
        have to worry about sending the wrong thing to the wrong person, 
        as they will all get the stuff. 

        You enter this Mode by selecting the "F" option in the Terminal 
        Menu. You terminate this Mode by selecting the "1" option.

        You connect in the usual manner using Alt-C or the Connect Option 
        in the Call Menu. You must wait for a connection to be 
        established, or to time out, before attempting to connect to the 
        next station. If you do not, you will get an error message back 
        from the TNC.

        In the Conference Mode, as the same text is transmitted on all 
        I/O channels, the throughput will be reduced. Slow down your 
        typing speed or use short packets. Should you check the link 
        status or call monitored list, you may not be able to get back 
        into the Converse Mode if you have too many packets outstanding. 
        If that happens, wait a while and then try to set the Converse 
        Mode with Function Key 10 (F10). You may have to try it a few 
        times, depending on how good your links are.
                         
        Don't try to send a file in the conference mode, it is not 
        designed for it. Keep the packets short (use short lines). Be 
        also warned that if you use the conference bridge on bad links 
        (such as crowded HF channels, or VHF/UHF channels with lots of 
        retries, the keyboard may seem to lock up. This is because LAN-
        LINK has to wait for space to appear in the TNC buffer before it 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 102


        can output the text.
            
        The Conference Mode will only work in the PK-232 if DCDCONN is 
        set to ON. So if you are using a PK-232, LAN-LINK will do it for 
        you when you enter the Conference Terminal Mode in case you 
        forgot or/and haven't set the LAN-LINK.SYS file to include the 
        line "DCD ON". At the same time set LAN-LINK.SYS default states 
        to show the calls of other stations on each incoming line in the 
        Multiconnect modes (read the TNC manual on how to do this).

        The Conference Mode will only work in the TNC2 if DCDCONN is 
        jumpered so that Pin 8 of the RS-232 Interface changes state when 
        you connect to someone else. If you get error messages and see 
        the characters "|J" on your screen, then the jumper probably 
        isn't set. The Conference Mode does not work on the TNC1. 

        In the Conference Mode, if any one of the stations disconnects, 
        the TNC will return to the Command Mode, and you must use 
        Function Key 10 (F10) to return to the Converse Mode before you 
        type another character of text.

        21.1.10 Conference Bridge ON/OFF

        This option toggles the Conference Bridge ON and OFF. In the 
        Bridge Multiconnect Mode you are acting as a central switch. You 
        can link together up to 10 stations in one multi-way connection. 
        In this Mode any packets arriving on any stream are echoed to all 
        other streams that you have "connects" on except the one that 
        they came in on. Anything you type will be sent to all connected 
        streams.

        In this manner, all stations will not see their own text echoed 
        back. Each line of text output by LAN-LINK in this Mode will 
        contain the callsign of the station originating the packet. Your 
        packets will contain your call as entered in line 1 of the LAN- 
        LINK.SYS file. Thus for example, if your call was KB8RP/4X and 
        normally shows up in the packet header as KB8RP here it will show 
        in the data as KB8RP/4X.

        Just remember that the Bridge puts out a lot of packets, so do 
        multi-way connects on a quiet frequency. You must be in the 
        Conference Mode to turn the bridge on, and any disconnect will 
        take the bridge down. Should that happen, toggle it on again. A 
        bridge will be shown in the status window whenever the Conference 
        Bridge is up.

        21.1.11 Turn Metabeacon ON/OFF

        This option lets you turn the LAN-LINK Metabeacon ON and OFF. 
        LAN-LINK provides you with a metabeacon, that gives you the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 103


        capability to transmit a long beacon message at periodic 
        intervals. The Metabeacon is loaded from the contents of one of 
        the LAN-LINK.00n files. These files may be created by the LAN-
        LINK editor. When loading, LAN-LINK will insert a pass character 
        (^V) into the text before a carriage return, so as not to end the 
        packet before at least 240 characters, and not more than 255 
        characters have been output to the TNC. The maximum number of 
        characters that can be loaded into the Metabeacon is 1776. The 
        maximum number of packets in a Metabeacon is 7. You can also 
        force a hard carriage return or "end of packet" in the Metabeacon 
        by inserting the "\" (backslash) character, which will not be 
        transmitted, into the text.

        The frequency of Metabeacon transmissions is the same as that of 
        the automatic CQ timer.

        The MetaBeacon is designed for special event stations. PLEASE do 
        not abuse it.

        21.2 AMTOR Terminal Menu

        In the AMTOR Communications Mode, you are presented with the 
        choices shown in Figure 21.2. Type in the single letter to make 
        your choice.

                             Figure 21.2 AMTOR Menu

                                 L Force LETTERS Case      
                                 K Turn SELCAL ON/OFF   
                                 R Set ROBOT/Mailbox       
                                 W CW Identification       
                                 Z Set ROBOT Infinite Delay

        21.2.1 Force LETTERS Case

        This option lets you force the PK-232 receiver to the letters 
        case if for some reason you appear to be in the numbers case. It 
        will return you to the Converse Mode. 

        If your TNC allows you to use a control character (^L) to force 
        the letters case, you don't need to go through all these menu 
        layers to do the job.

        21.2.2 SELCAL ON/OFF

        This command key toggles the SELCAL feature ON and OFF. When the 
        SELCAL is activated, as shown in the status window, the incoming 
        text from the TNC is scanned. When either the letters "ZCZC" or 
        "your callsign" (as entered in line 1 of the LAN- LINK.SYS file) 
        is received, the "capture-to-disk" is turned on. All subsequent 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 104


        text will be stored in the LAN-LINK.RUN file until the letters 
        "NNNN" are received. At that time the "capture-to-disk" is turned 
        off.

        21.2.3 Set ROBOT/Mailbox

        This option lets you turn on the Mailbox during a regular AMTOR 
        QSO so that the other station can leave a message or download a 
        file remotely. You must only use it when the other station is 
        sending text.

        21.2.4 CW Identification

        This option only works on the PK-232, PK-900 and DSP 2232. You 
        use it to send a CW identification (CWID). The CWID is sent in 
        the FEC Mode. The CWID consists of the sequence "DE YOURCALLSIGN" 
        where YOURCALLSIGN is that entered into the PK-232 as "MYCALL".

        You use this feature if your license requires you to identify in 
        Morse code as well as in the operating mode. 

        21.2.5 Set ROBOT Infinite Delay

        You use this option to prevent the Robot from ever transmitting 
        when not linked. In the normal manner, the Robot counts down the 
        CQ delay parameter, and, when it gets down to 0, puts a CQ call 
        on the air. If the Infinite Delay is set, the CQ call will be 
        inhibited. This option thus puts the Robot into an indefinite 
        wait mode where it thinks it has sent out a CQ call and is 
        waiting for a reply.

        You would use this Mode if you want to set up a MailBox on a 
        known frequency for some group or organization.

        21.3 Baudot Terminal Menu

        In the Baudot Communications Mode, you are presented with the 
        choices shown in Figure 21.3. Type in the single letter to make 
        your choice.

        21.3.1 Set Baud Rate

        This feature allows you to set a desired communications baud rate 
        directly. You will be prompted to enter the desired rate. Use 
        this command to avoid having to shift through too many intermedi-
        ate states, if for example, you want to make a direct change from 
        45 to 100 baud.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 105


                             Figure 21.3 BAUDOT Menu

                                 B Set Baud Rate    
                                 F Select Shift     
                                 N Turn NAVY MARS Message Protocol ON
                                 U USOS OFF         
                                 K Turn SELCAL ON/OFF   
                                 W CW Identification

        21.3.2 Select Shift

        This feature lets you select Wide (850 Hz) or narrow (170 Hz) 
        shift directly. The PK-232 will copy 170 Hz signals using its 
        internal 200 Hz circuitry. If you have a KAM, you may also select 
        the Commercial Shift (425 Hz).

        The shift is displayed in the status window at the top of the 
        screen. It is shown as "W"", "N" or "C" for wide, narrow or 
        commercial respectively. 

        21.3.3 NAVY MARS Message Protocol

        The Navy MARS option toggles the Navy MARS Mode ON and OFF. When 
        the Navy MARS option is active, an "[N]" will be displayed in the 
        status window, and the feature performs the protocol described 
        below.

        21.3.3.1: Any Carriage Return or Enter (CR) from the keyboard is 
                  sent as CR, CR. (two sequential CR characters.
        21.3.3.2: In a file transmission lines are terminated by a CR, 
                  CR, LF (Line Feed) sequence.
        21.3.3.3: In a file transmission, blank lines are sent as a LF 
                  (without a CR).
        21.3.3.4: In a file transmission, a plus sign "+" in the file is 
                  replaced by a sequence of 12 "letters" characters. 
                  There can be more than one + sign on a line.
        21.3.3.5: In a file transmission, the sequence "NNNN" is trans-
                  mitted followed by a sequence of 12 "letters" charac-
                  ters. There can only be one "NNNN" sequence on a line.

        21.3.4 USOS ON/OFF

        This option toggles the Unshift on space (USOS) feature ON and 
        OFF. When the USOS is on, the TNC reverts to the letters shift 
        each time a "space" character is received. It helps when 
        displaying noisy copy.

        If USOS is active, "USOS" will be shown in the status window at 
        the top of the screen. 



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 106


        21.3.5 SELCAL ON/OFF

        This command key toggles the SELCAL feature ON and OFF. When the 
        SELCAL is activated, as shown in the status window, the incoming 
        text from the TNC is scanned. When either the letters "ZCZC" or 
        "your callsign" (as entered in line 1 of the LAN-LINK.SYS file) 
        is received, the "capture-to-disk" is turned on. All subsequent 
        text will be stored in the LAN- LINK.RUN file until the letters 
        "NNNN" are received. At that time the "capture-to-disk" is turned 
        OFF.

        You may use this feature when monitoring commercial RTTY 
        broadcasts to record news and other information, or when calling 
        CQ to start recording all incoming text and keep the QSO on disk.

        You may use Function Key 1 (F1) to turn the capture to disk 
        permanently on to override the automatic turnoff if you wish.

        21.3.6 CW Identification

        This option is used to send a CW identification. You use this if 
        your license requires you to identify in Morse Code as well as in 
        the operating mode. 

        The identification consists of the sequence "DE YOURCALLSIGN" 
        where your callsign is that entered into the TNC as "MYCALL".

        21.4 ASCII Terminal Menu

        In the ASCII Communications Mode, you are presented with the 
        choices shown in Figure 21.4. Type in the single letter to make 
        your choice.

                             Figure 21.4 ASCII Menu

                                 B Set Baud Rate    
                                 F Select Shift     
                                 K Turn SELCAL ON   
                                 W CW Identification

        21.4.1 Set Baud Rate

        This feature allows you to set a desired communications baud rate 
        directly. You will be prompted to enter the desired rate. Use 
        this command to avoid having to shift through too many intermedi-
        ate states. For example, if you want to make a direct change from 
        110 to 1200 baud.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 107


        21.4.2 Select Shift

        This feature lets you select Wide (850 Hz) or narrow (170 Hz) 
        shift directly. The PK-232 will copy 170 Hz signals using its 
        internal 200 Hz circuitry. If you have a KAM, you may also select 
        the Commercial Shift (425 Hz).

        The shift is displayed in the status window at the top of the 
        screen. It is shown as "W", "N" or "C" for wide, narrow or 
        commercial respectively. 

        21.4.3 SELCAL ON/OFF

        This command key toggles the SELCAL feature ON and OFF. When the 
        SELCAL is activated, as shown in the status window, the incoming 
        text from the TNC is scanned. When either the letters "ZCZC" or 
        "YOURCALLSIGN" (as entered in line 1 of the LAN-LINK.SYS file) is 
        received, the "capture-to-disk" is turned on. All subsequent text 
        will be stored in the LAN-LINK.RUN disk file until the letters 
        "NNNN" are received. At that time the "capture-to-disk" is turned 
        off.

        You may use Function Key 1 (F1) to turn the capture to disk 
        permanently on to override the automatic turnoff if you wish.

        21.4.4 CW Identification

        This option is used to send a CW identification. You use this if 
        your license requires you to identify in Morse code as well as in 
        the operating mode. 

        The identification consists of the sequence "DE YOURCALLSIGN" 
        where your callsign is that entered into the TNC as "MYCALL".

        21.5 CW Menu

        In the CW Communications Mode, you are presented with the Menu 
        shown in Figure 21.5. Type in the single letter to make your 
        choice.

                               Figure 21.5 CW Menu

                                 L Lock to Receive Signal
                                 S Set Morse Speed   
                                 U Unlock Morse Speed
                                 X Turn XMITOK Flag ON 

        21.5.1 Lock to Receive Signal

        This option locks the TNC to the speed of the incoming CW signal.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 108



        21.5.2 Set Morse Speed

        This option lets you set the CW speed.

        21.5.3 Unlock Morse Speed

        This option unlocks the TNC from the incoming CW signal. It 
        performs the same task as the Alt-D option keys. It is used to 
        speed up capture of a new signal or to break the lock when the 
        TNC appears to have locked up at the wrong speed.

        21.6 Pactor Terminal Menu

        Pactor applies to the KAM and PK-232 only, assuming they contain 
        Pactor firmware. In the Pactor Communications Mode, you are 
        presented with the choices shown in Figure 21.6. Type in the 
        single letter to make your choice. Do not use any of these 
        options when linked to another station or you may drop the link.

        21.6.1 AUTO BAUD

        This option configures the TNC to switch between 100 and 200 baud 
        on the HF Pactor link as determined by propagation Conditions.

                             Figure 21.6 Pactor Menu

                                 0 AUTO BAUD
                                 1 Force 100 BAUD
                                 2 Force 200 BAUD
                                 H Enable Huffman
                                 K Disable Huffman

        21.6.2 Force 100 Baud

        This option forces the TNC to use 100 baud on the HF Pactor link 
        as determined by propagation Conditions.

        21.6.3 Force 200 Baud

        This option forces the TNC to use 200 baud on the HF Pactor link 
        as determined by propagation Conditions. This option is only 
        available for the KAM.

        21.6.4 Enable Huffman

        This option enables Huffman compression of the transmitted text.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 109


        21.6.5 Disable Huffman

        This option disables Huffman compression of the transmitted text.

        22.0 EXIT TO DOS

        When you exit the program and return to DOS, if the Shut down 
        (QRT) flag is set to 0, the TNC is put into the VHF default mode 
        in which it rejects calls from any other stations. (Read about 
        the CFROM and/or CONOK command in the TNC manual). You can, if 
        you wish, leave the TNC powered, and, if you also leave the VHF 
        radio powered up, you will be active as a digipeater, but at the 
        same time anyone trying to connect with you will receive a "busy 
        signal". The MBX command (Reading the Mail) is also cleared at 
        this time.

        If you want to leave the TNC set up to accept messages when LAN-
        LINK is not active, customize the shut down state as described in 
        the Section 18.23.

        23.0 THE ELMER MENU

        ELMER is a smart server or second operator feature described in 
        Appendix 7. The ELMER Menu presents you with the choices shown in 
        Figure 23. Type in the single letter to make your choice.

                            Figure 23 The ELMER Menu

                                 C Change ELMER File
                                 E Turn ELMER ON/OFF
                                 L Load ELMER.QSO   
                                 P Pick File to edit
                                 S Edit ELMER.QSO  
                                 T show state Table

        23.1 Change ELMER File

        This option allows you to change the ELMER state table file.

        23.2 Turn ELMER ON/OFF

        This option allows you to turn ELMER ON and OFF. If the ELMER 
        state table file (ELMER.QSO) is not present, you will not be able 
        to activate ELMER.

        23.3 Load State Table (ELMER.QSO)

        This option allows you to reload the state table. The name of the 
        state table will appear in the menu.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 110


        23.4 Pick File to Edit 

        This option allows you to pick and edit, a file with the default 
        filetype of "TXT".

        23.5 Edit State Table (ELMER.QSO) 

        This option allows you to edit the state table.

        23.6 Show State Table  

        This option allows you to see the contents of the state machine. 
        It is used in debugging the logic to ensure that the contents of 
        the table match what you thought you put into it. A typical set 
        of contents appears as shown in Figure 23.1. The keywords have 
        been capitalized and set to 15 characters wide. None existent 
        characters have been represented as periods.

                      Figure 23.1 Typical ELMER State Table

           L   C   N  R   E      KEYWORD    U       FILE
           0   1   2  0   0 WHAT........... 0 *               
           1   2   3  0   0 ENGLISHMAN..... 0 *               
           2   2 100  0   0 SYSTEMS........ 0 *               
           3   3   4  0   0 DOING.......... 0 *                  
           4   4   1  0   0 COUNTRY........ 0 ME-USA.TXT
           5   1   1  0   0 EQUIPMENT...... 0 PK232COM.TXT    


        24.0 RADIO MENU

        The Radio Menu provides you with the capability to exercise the 
        interface to a Kenwood Radio. The options available are shown in 
        Figure 24-1. Type the single letter to make your choice. All 
        commands will be ignored if the radio is not enabled. The radio 
        interface is automatically enabled at LAN-LINK initialization 
        time.

                       Figure 24-1 The Kenwood Radio Menu

                                 F Select VFO A/B
                                 M Set Mode
                                 Q Turn Flag QSY ON/OFF or N/A
                                 R Read VFO A Frequency
                                 S Set Frequency
                                 V Speak Frequency

        24.1 Select VFO A/B

        This option sets the VFO that will be interrogated or set by LAN-


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 2 Page 111


        LINK.

        24.2 Set Mode

        This option sets the radio mode (USB, LSB, FM, CW etc.). You will 
        be prompted to supply the mode.

        24.3 Turn Flag QSY ON/OFF or N/A

        This option set the QSY Flag as follows:

        N/A  Radio is not enabled.
        ON   QSY to the frequency of a DX Alert (if in PacketCluster 
             mode).
        OFF  Don't QSY in response to a DX Alert.

        24.4 Read VFO Frequency

        This option reads and displays the frequency of the selected VFO.

        24.5 Set VFO Frequency

        This option sets the frequency of the selected VFO. You will be 
        prompted to supply the frequency.

        24.6 Speak Frequency

        This option sends a command to the radio to announce the 
        frequency of the selected VFO. If the radio is equipped with a 
        voice annunciator the radio will announce the frequency. If the 
        radio is not equipped in such a manner, the command will be 
        ignored.




















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 112


                         Appendix 3 LAN-LINK Disk Files

        The following disk files are associated with the LAN-LINK 
        program.

                   LAN-LINK.COM
                   LAN-LINK.SYS
                   *.RUN
                   LAN-LINK.LOG
                   LAN-LINK.DIR
                   CONFIG.SYS
                   *.MBX
                   *.BBS
                   LAN-LINK.001 .. LAN-LINK.010
                   QBU-RX.BAT
                   QBU-TX.BAT
                   LAN-LINK.QTA
                   QZ*.BAT
                   ELMER.QSO
                   LAN-LINK.OUT
                   *.DMO

        The "*" represents a "wildcard" character in the manner of DOS. 
        Consider each file in turn.

        1.0 LAN-LINK.EXE

        This is the program. You activate it from DOS by typing the word 
        "LAN-LINK" followed by "ENTER" in the normal manner of invoking 
        DOS commands.

        2.0 LAN-LINK.SYS

        This file contains the configuration information for both the 
        program and the TNC. Use the customization options in the 
        parameters menu to make any changes not taken care of in the 
        INSTALL program.

        The contents of the default file together with an item (line) 
        number are shown below.

         1. Callsign
         2. Selcal 
         3. CQ Text
         4. CTEXT Line
         5. ELMER Flag
         6. CQ Delay (seconds)
         7. CQ Delay (minutes)
         8. :QSP: Message Relay Flag
         9. PC Serial Communications Port Number


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 113


         10. TNC Type
         11. PC to TNC Baud Rate
         12. VHF Log Book File 
         13. HF Log Book File 
         14. GMT Offset
         15. Path Directory File name
         16. Brag Tape File name
         17. PBBS Snatch Mail Trigger Word
         18. QTC Snatch Flag
         19. PBBS Snatch Flag 
         20. Shut Down Mode (QRT Flag)
         21. PC to TNC Data Bits
         22. PC to TNC Parity Bit
         23. PC to TNC Stop Bits
         24. DCD Flag
         25. QBM Download Sub-directory 
         26. Run File Directory Path
         27. PBBS Read Request Command
         28. Local PBBS Callsign
         29. SAREX Callsign
         30. SAREX Capture to Disk File name
         31. PacketCluster Call
         32. TNC Specific Parameters
         33. Node Drop Link Flag
         34. Sound Flag
         35. Display Computer Generated Commands Flag
         36. Date/timestamp in Call Sequence Flag
         37. Keyboard Character Beep value (number of characters).
         38. :QBU: Receiving Station Batch file (QBU-RX.BAT)
         39. :QBU: Originating Station Batch file (QBU-TX.BAT)
         40. Capture-to-disk Flag
         41. Beacon Control/LAN-LINK handshake Flag
         42. Read Bulletin Character
         43. PBBS Subject String
         44. PBBS Message String
         45. VHF Paclen
         46. HF Paclen
         47. Beacon Time
         48. Number of CQ Lines
         49. Word wrap 
         50. PC Port 4 Custom Address 
         51. PC Port 4 Custom IRQ
         52. VHF Stream switch character
         53. HF Stream switch character
         54. TNC Error message
         55. Connect Timeout Delay
         56. Custom Prompt
         57. ELMER Configuration File
         58. Expand Transmitted File flag
         59. Input Message Base Count


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 114


         60. Default users
         61-88. Custom Colors
         89. First PacketCluster Command 
         90. Second PacketCluster Command 
         91. TNC Mailbox ON Command
         92. TNC Mailbox OFF Command
         93. VHF Maxframe Command
         94. HF Maxframe Command
         95. Inhibit VHF Logging Flag  
         96. Inhibit HF Logging Flag
         97. Printer Permanent Flag 
         98. Log Disk Update Flag 
         99. Secondary Log Flag 
        100. Auto Answer Flag 
        101. RUN File Disk Update Flag
        102. Default CW Speed
        103. Secondary Logbook
        104. BBS List Command
        105. BBS List Mine Command
        106. BBS Custom Command
        107. BBS Bye Command
        108. Start Up Packet Terminal Mode
        109. Page Time (:QIC: Seconds)
        110. Packet Cluster DX Alert Tone CW Dit time
        111. Packet Cluster DX Alert Tone CW Note
        112. Packet Cluster DX Alert Mode
        113. Mode File Flag
        114. BAUDOT Color Change Text String
        115. Default RTTY Baud Rate
        116. Dual Window Flag
        117. TNC String for Modem 9600 baud packet
        118. TNC String for Modem 1200 baud packet
        119. TNC String for Modem RTTY 
        120. TNC String for Modem 300 baud packet
        121. TNC String for Modem RTTY and 1200 baud packet
        122. TNC String for Modem 300 baud and 1200 baud packet
        123. TNC String for Modem Fuji 
        124. Delay after a command line 
        125. Radio
        126. Radio Port
        127. Radio Port baud rate 
        128. Radio Port Bits
        129. Radio Port Stop Bits
        130. Radio Port Parity
        131. Radio Address
        132. Flag QSY 
        133. Flag DX Alert Prefix Check
        134. start of band parameters for DX Alert message log search
        135. * end of band parameters; modes for DX Alert message log 
             search 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 115


        136. Start of Scan Words (MUST HAVE AT LEAST ONE)
        137. * end of Scan Words
        138. Start of Common Calls (MUST HAVE AT LEAST ONE)
        139. * end of Common Calls
        140. Remaining TNC start up Commands.

        The contents of each line are described in the section of the 
        Parameters menu which deals with customizing them. The others, 
        described below, can only be changed by using the Editor. The 
        remaining lines contain commands to the TNC. For further informa-
        tion about them refer to the TNC manual. LAN-LINK assumes 
        different defaults (in some instances) to those set in the TNC. 
        The LAN-LINK.SYS file contains only those that are different to 
        the TNC default reset state. 

        2.1 CTEXT Line

        This parameter is the CTEXT line changed in the TNC Menu.

        2.2 ELMER Flag

        This parameter is the ELMER Flag. If it is a "1", ELMER is primed 
        for activity. ELMER is only active in the Packet communications 
        mode, when you are connected to another station. If the ELMER 
        flag is a "0", or the ELMER state table file is not present in 
        the default directory, LAN-LINK will never activate ELMER.

        2.3 PC Port 4 Custom Address 

        This parameter is the decimal value of the address of your Port 
        4. Use this parameter if you are using a non standard Serial I/O 
        card. Configure the PC Port to 4. The PC default address for Com4 
        is 2E8 (hex) or 744 (decimal).

        2.4 PC Port 4 Custom IRQ

        This parameter is the decimal value of the IRQ of your Port 4. 
        Use this parameter if you are using a non standard Serial I/O 
        card. Configure the PC Port to 4. The PC default IRQ for Com4 is 
        3.

        2.5 VHF Stream Switch Character

        This parameter is the VHF stream switch character. If you wish to 
        change it, you must enter the ASCII representation in this line, 
        and the equivalent stream switch command in the LAN-LINK.SYS 
        file.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 116


        2.6 HF Stream Switch Character

        This parameter is the HF stream switch character. If you wish to 
        change it, you must enter the ASCII representation in this line, 
        and the equivalent stream switch command in the LAN-LINK.SYS 
        file. The KAM is currently the only TNC that has different HF and 
        VHF stream switch characters.

        2.7 TNC Error Message

        This parameter is the error message your TNC generates. The PK-
        232 generates "?What?". Others may generate "EV?" or "?EH".

        2.8 Connect Timeout Delay

        This parameter is the time, in minutes, LAN-LINK lets you stay 
        connected to another packet station, after the receipt of the 
        last incoming character.

        2.9 ELMER Configuration File

        This parameter is the name of the default ELMER Configuration 
        file. It is changed through the ELMER Menu.

        2.10 Expand Transmitted Files Flag

        The Flag tells LAN-LINK to scan the outgoing text when a file is 
        transmitted and perform the same conversions it does to the 
        contest text. You can insert the '##', "#1' and "#T" parameters 
        in the files to transmit, your call sign, the other station's 
        call, and the time of day. Set this parameter to 1 to enable the 
        feature, 0 to disable it.

        2.11 First PacketCluster Command

        This parameter is the first command (up to 20 characters) LAN-
        LINK sends to the PacketCluster after receiving a ">" character 
        at the end of line from the PacketCluster.

        2.12 Second PacketCluster Command 

        This parameter is the second command (up to 20 characters) LAN-
        LINK sends to the PacketCluster after receiving a ">" character 
        at the end of line from the PacketCluster.

        2.13 TNC Mailbox ON Command

        This parameter is the command (up to 15 characters) your TNC 
        expects to turn its internal mailbox ON.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 117


        2.14 TNC Mailbox OFF Command

        This parameter is the command (up to 15 characters) your TNC 
        expects to turn its internal mailbox OFF.

        2.15 VHF Maxframe Command

        This parameter is the command (up to 15 characters) your TNC 
        expects to set the VHF MAXFRAME parameter.

        2.16 HF Maxframe Command

        This parameter is the command (up to 15 characters) your TNC 
        expects to set the HF MAXFRAME parameter.

        2.17 Inhibit VHF Logging Flag

        When set to 1, automatic VHF Logging is disabled.

        2.18 Inhibit HF Logging Flag

        When set to 1, automatic HF Logging is disabled.

        2.19 Printer Permanent Flag

        When clear (set to 0), if you leave the printer on during a 
        packet connect, it will stop printing when you disconnect. This 
        stops the printer generating lots of garbage. If you set this 
        parameter to 1, the printer will not stop printing when you 
        disconnect.

        2.20 Log Disk Update Flag

        If this flag is set to 1, LAN-LINK writes each log entry to disk 
        as you enter it. If this flag is not set (=0), LAN-LINK writes 
        the log entry to a buffer and updates the disk when the program 
        is terminated. Set the flag ON to ensure that rare DX contact is 
        logged, Set it OFF for speed, or if power dropouts are not a 
        problem in your area.

        2.21 Secondary Log Flag

        If this Flag is set to 1, LAN-LINK allows you to search both the 
        current log book and a secondary logbook for the call of a 
        station.

        2.22 Auto Answer Flag

        If this flag is set to 1, AND you have a LAN-LINK.OUT file on 
        your system, LAN-LINK will transmit the contents of the LAN-


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 118


        LINK.OUT file to every incoming connection. 

        2.23 Ctdsk File Disk Update Flag

        If this flag is set to 1, LAN-LINK will close the capture-to-disk 
        file (YYMMDD.RUN) between received messages. If the flag is not 
        set, LAN-LINK will close the file when all messages have been 
        received, or a DISCONNECT takes place.

        2.24 Default CW Speed

        This is the default CW speed for the multi-mode TNC (KAM, PK-232 
        or MFJ1278).

        2.25 Secondary Logbook

        This is the name of the secondary logbook.

        2.26 BBS List Command

        This is the BBS List Command. The default value is 'L'.

        2.27 BBS List Mine Command

        This is the BBS List Mine Command. The default value is 'LM'.

        2.28 BBS Custom Command

        This is a configurable BBS List Command. The default value is 
        'KM'. 

        2.29 BBS Bye Command

        This is the BBS Bye Command. Change this parameter when the 
        default 'B' command only drops you to the Node.

        2.30 Start Up Packet Terminal Mode

        This is the Packet Terminal Mode when LAN-LINK is first 
        activated. Set this to the letter corresponding to the terminal 
        mode you like being in. See Section 21.1. Use the corresponding 
        letter, as shown in Table 2.30.

                        Table 2.30 Start Up Terminal Mode

        Letter    Mode                              Actions
        I         INFO lets you only see packets containing information.
        S         SOLO lets you only see messages addressed to you.
        C         CQ/B lets you see beacons and CQ calls as well.
        T         TRFC lets you see packets containing messages as well.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 119


        E         EVRY lets you see everything on channel, including the 
                       link control packets.

        2.31 Page Time (:QIC: Seconds)

        This is the number of seconds the system pages the operator in 
        response to a QIC command, if the sound is turned on.

        2.32 PacketCluster DX Alert Tone CW Dit time

        This is the time period for 1 dit sound in the PacketCluster 
        audible DX alert message. 

        2.33 Packet Cluster DX Alert Tone CW Note

        This is the tone for the PacketCluster audible DX alert message.

        2.34 Mode File Flag

        If this flag is set, LAN-LINK will change the name of the LAN-
        LINK.001 to LAN-LINK.010 when you change communications modes. 
        The name will change to the mode followed by a number, i.e. 
        BAUDOT.001 to BAUDOT.002, or AMTOR.001 to AMTOR.002.

        2.35 BAUDOT Color Change Text String

        This is a pair of characters that LAN-LINK will scan text 
        appearing in the incoming window for. When LAN-LINK recognizes 
        the pair, it will change colors. This parameter is customizable 
        to allow you to override apparent random changes of color, since 
        there is no agreed standard way for signaling 'over' in BAUDOT.

        2.36 Dual Window Flag

        This flag applies to the PK-900 and DSP 2232 only. If this flag 
        is set, LAN-LINK separates out the text streams coming from each 
        port and directs them to two separate windows. If the flag is 
        reset, the text streams are combined into a single incoming 
        window.

        2.37 TNC String for Modem 9600 baud

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working 9600 baud packet.

        2.38 TNC String for Modem 1200 baud

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working 1200 baud packet.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 120


        2.39 TNC String for Modem RTTY 

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working HF RTTY.

        2.40 TNC String for Modem 300 baud

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working 300 baud HF packet.

        2.41 TNC String for Modem RTTY and 1200 baud

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working simultaneous HF RTTY 
        and VHF 1200 baud packet.

        2.42 TNC String for Modem 300 baud and 1200 baud

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for simultaneous HF 300 baud 
        packet and 1200 baud VHF packet.

        2.43 TNC String for Modem Fuji 

        This item applies to the PK-900 and DSP 2232 only. This is the 
        command used to select the modem for working Fuji 1200 baud PSK 
        packet.

        2.44 Delay after a command line 

        This item is the number of milliseconds to wait between sending 
        lines to the TNC output buffer.

        2.45 Radio

        This item is the name of the Radio. Kenwood has been tested, Icom 
        may work (coded but not tested). If this is not set to Kenwood or 
        Icom, the Radio functions are disabled.

        2.46 Radio Port 

        This item is the serial port for the Radio (1 to 4). If set to 0, 
        the Radio functions are disabled.

        2.47 Radio Port baud rate 

        This item is the serial port baud rate for the Radio. Check the 
        correct value in the Radio manual.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 121


        2.48 Radio Port Bits 

        This item is the number of data bits on the serial port for the 
        Radio. Check the correct value in the Radio manual.

        2.49 Radio Port Stop Bits

        This item is the number of stop bits on the serial port for the 
        Radio. Check the correct value in the Radio manual.

        2.50 Radio Port Parity

        This item is the parity value on the serial port for the Radio. 
        Check the correct value in the Radio manual.

        2.51 Radio Address 

        This item is ignored for Kenwood radios. For Icom, it is the 
        decimal value of the radio address. Check the correct value in 
        the Radio manual.

        2.52 Flag QSY 

        This flag determines of LAN-LINK tunes the radio to the frequency 
        of the PacketCluster DX Alert message automatically.

        2.53 Flag DX Alert Prefix Check

        This flag determines how LAN-LINK responds to a DX Alert message. 
        If the flag is set, LAN-LINK checks to see of the prefix is in 
        the log.

        2.54 Band parameters for DX Alert message log search

        These lines contain the band, reference frequency (Hz), low and 
        high band search flags. They can be changed via the Radio Menu. 
        Typical values are:

                                10, 28300000.0,Y,Y
                                12, 24930000.0,Y,N
                                15, 21200000.0,Y,Y
                                17, 18110000.0,Y,Y
        LAN-LINK checks the frequency of the DX Alert message to see if 
        it matches on in these lines. If it does, then LAN-LINK compares 
        the frequency with the value on the corresponding line to 
        determine if the DX Alert frequency is higher or lower than the 
        reference frequency. 

        If the frequency is lower than the reference, and the low band 
        search flag is "Y", LAN-LINK will check to logbook to see if the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 122


        prefix is in the log.

        Similarly, if the frequency is higher than the reference, and the 
        high band search flag is "Y", LAN-LINK will check to logbook to 
        see if the prefix is in the log.

        If LAN-LINK does not find a match, the check mark is displayed.

        2.55 Modes for DX Alert message log search 

        This line marks the end of the band parameters for DX Alert 
        message log search with the *. It then contains the 
        communications modes corresponding to the low and the high parts 
        of the band. Typical values are:

                                *,CW,SSB
        2.56 TNC Parameters

        The remaining lines contain parameters loaded into the TNC at 
        initialization.

        If you are not using a TNC1 you MUST set the HEADERLN parameter 
        to ON. The packet headers and the text of the packets must show 
        up on your screen on separate lines. You must also have the "Echo 
        as Sent" feature set ON ("EAS ON" for PK-232 and "XM" ON " for 
        the KAM).

        3.0 *.RUN

        These files contain incoming data from the TNC recorded while the 
        "capture-to-disk" function was active. LAN-LINK names them as 
        YYMMDD.RUN automatically (YY = Year, MM = Month, DD = Date, i.e. 
        920903.RUN is a file for 3 Sept 1992).

        4.0 *.DBF (HF.DBF and VHF.DBF)

        These file contain the log entries. They are Dbase 3 and 4 
        compatible. The format of the logbook file is the same as that 
        used by the LOGBOOK package of the PC-HAM software package, with 
        a little additional space for comments.

        5.0 LAN-LINK.DIR

        This is the directory file as described in Appendix 2, Section 
        6.1.2. You use it to store names, handles, NET/ROM, TheNet, KA-
        Node, ROSE or digipeat paths as well as name/callsign relation-
        ships. Sample lines are shown below.





        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 123


         Joe G3ZCZ
         Alon 4Z4ZB V 4X6AA
         Milt 4X6AA
         LR 4X6LR
         hf-il 4x4hf v 4z4zb 4x4il
         hf-rj 4x4hf v 4z4zb 4z4rj
         K1HTV ELK v WB4APR-5! SNJ3! NNJ! WMA! SCCT!K1HTV
         w9tnn-2 jrw !% w3eax-7 !& w9tnn-2

        You create this file with the Editor or by using your word 
        processor in its non-document mode. You must leave at least one 
        space character between the first (key) word and the connect 
        path. When you type in the key word, the program does not care 
        about upper or lower case. 

        You may also use the "reMember Path" option in the Call Menu to 
        make entries in this file.

        If you already have a YAPP.DIR or a PK232COM.DIR file just rename 
        it to LAN-LINK.DIR and add any NET/ROM and/or KA-Node paths. 

        All path entries in LAN-LINK.DIR must be on a single 80 column 
        line.

        6.0 CONFIG.SYS

        You must have a CONFIG.SYS file on the boot disk if you are going 
        to use the disk logging features. This file must contain the line 

        FILES = 20.

        See the DOS manual for more information about the CONFIG.SYS 
        file.

        7.0 *.MBX

        These are the files associated with the stations you have 
        designated as LAN store and forward mailboxes. Other stations can 
        only :QRU: with you if you have designated them as QRU stations 
        and have a "CALLSIGN.MBX" file on your disk. For example, if you 
        want to use 4Z4ZB as a store and forward mailbox, you will have 
        to create an ASCII file called 4Z4ZB.MBX using Editor, or the 
        non-document mode of your word processor. In this file you will 
        put a list of the call signs of the stations 4Z4ZB can connect 
        with reliably. For example, if you want 4Z4ZB to be able to store 
        messages from you to 4X6AA, 4X6LR, G3ZCZ, ON8IK, F0WN,and G8BTB, 
        you would put those call signs in the file, one call on a line as 
        follows.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 124


         4X6AA
         4X6LR
         G3ZCZ
         ON8IK
         F0WN
         G8BTB

        When the QRU function is invoked either by you manually or by 
        4Z4ZB connecting to you and sending you the command :QRU:, any 
        message files present on your system addressed to any of those 
        stations (E.G. G3ZCZ.OUT and ON8IK.OUT) will be transferred from 
        you to 4Z4ZB just as if you had tried to :QSP: the messages 
        manually or as if G3ZCZ or ON8IK had connected directly to you. 
        The file names on your system will be changed to *.OLD.

        You must create one file for each designated store and forward 
        station, i.e. 4Z4ZB.MBX, G3ZCZ.MBX etc.

        8.0 *.BBS

        These are LOCAL-BBS.BBS AUTO-Upload Command files. Each file is 
        named for the callsign of the BBS that you wish to access. It 
        must have exactly the name as the callsign of the BBS. If the BBS 
        is W9TNN-1 the name of the file must be W9TNN-1.BBS, or if the 
        BBS is 4Z4ZB then the file must be called 4Z4ZB.BBS. The file 
        must be an ASCII file. that means the word processor must be used 
        in the non-document mode to create it.

        This file contains the command sequence that you would have typed 
        at the keyboard if you were accessing the BBS manually. The ONE 
        difference is that the text of a message you are uploading with 
        the S command must be followed by the character strings ":EOF:" 
        or "/EX" (on a separate line) as illustrated by the example 
        below.

        If you use the "D" command to download a text file, the file will 
        end up in a separate file on your disk ONLY IF a file of the same 
        name does not exist on your drive.
                         
        Do delete "read" mail from your local PBBS. Don't clutter the 
        PBBS's disk with your read mail. The "LM" command is built into 
        LAN-LINK to remind you of what you have out there. 

        The PBBS "S" command (including its variations such as "SP") is 
        the only multiple line command allowed. You can put all the 
        single line commands such as "D", "H", "?", "L", and "R" in the 
        PBBS.BBS file.

        A "multiple command" is defined in this instance as a command 
        which allows you to enter multiple lines before the PBBS will 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 125


        send back a ">" character (i.e. one that the PBBS tells you to 
        type in text and terminate it with the Control-Z (^Z) character).

        A typical message could be as shown below.

        SP G3ZCZ @ N4QQ
        LAN-LINK
        I think it is great. However, why don't you change the 
        following...... (add your comments here).
        73 de your name
        :EOF: {last line may also be "/EX"}
         k 1234
         d \net\lan-link.doc
         s g8btb
         Test Message
         This is a test message.
         :EOF:
         lm
         r 567
         r 593

        9.0 LAN-LINK.001 - LAN-LINK.010

        These are 10 different text files with fixed names. They can be 
        transmitted using the Alternate function keys. Their contents can 
        be viewed using the Shift function keys. In all cases the 
        function key to use for a particular file corresponds to the 
        number in the file suffix. For example, use Alt/Shift Function 
        Key 3 (Alt-F3) to transmit/view file LAN-LINK.003. You may also 
        use the Edit Menu to edit and/or create the files.

        In case you forget what you put in each of the files, LAN- LINK 
        allows you to take a peek into all of them at the same time. Use 
        Control Function key 1 (Control-F1) to look at the first line of 
        all the LAN-LINK.001 - LAN-LINK.010 files and the Brag Tape.

        If the Mode File flag is set, LAN-LINK changes the files as you 
        change modes. You thus have 10 files in EACH mode, accessible via 
        the same set of control function keys. The file names are shown 
        below.

        COMMUNICATIONS MODE Mode Flag                FILE NAMES 
        All                 OFF            LAN-LINK.001 to LAN-LINK.010
        Packet              ON             LAN-LINK.001 to LAN-LINK.010
        AMTOR               ON             AMTOR.001 to AMTOR.010
        BAUDOT              ON             BAUDOT.001 to BAUDOT.010
        ASCII               ON             ASCII.001 to ASCII.010
        CW                  ON             MORSE.001 to MORSE.010
        Pactor              ON             PACTOR.001 to PACTOR.010
        G-TOR               ON             G-TOR.001 to G-TOR.010


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 126



        10.0 QBU-RX.BAT

        This is the command or batch file used in the :QBU: originating 
        station.

        11.0 QBU-TX.BAT

        This is the command or batch file used in the :QBU: receiving 
        station.

        12.0 LAN-LINK.QTA

        You can leave a message on your system for someone else in a file 
        named CALLSIGN.OUT. When the station with that callsign connects 
        to you, the message will be sent, and the filename will be 
        changed from CALLSIGN.OUT to CALLSIGN.OLD. This is fine as long 
        as the path between the stations good. If the path is marginal, 
        it is possible that your station will transmit the message and 
        change the filename, but the link will drop out before the 
        message is received at the other station. If the other station 
        does not connect to you and :QSM:, the message may get lost. If 
        this situation occurs, you can tell LAN-LINK that there is a bad 
        path between you and that station, and not to change the file 
        names without an explicit :QTA: instruction from that other 
        station. You do this by putting the call of the station(s) having 
        a bad path in an ASCII file called LAN-LINK.QTA. Put one call on 
        each line in the form

        N9BE
        G8BTB

        You must use the root call of the station without an SSID. that 
        means, if the station is N9BE-4, just put N9BE in the file.

        LAN-LINK will automatically acknowledge incoming messages from 
        stations with callsigns in the LAN-LINK.QTA file with a ":QTA:".

        13.0 QZ*.BAT

        As any LAN-LINK station can either receive or originate a :QZD: 
        and a :QZU: command, LAN-LINK uses four batch files to control 
        Zmodem transfers. These files are as follows.

        QZU-RX.BAT Batch file implemented after receipt of :QZU:
        QZU-TX.BAT Batch file implemented after transmission of :QZU:
        QZD-RX.BAT Batch file implemented after receipt of :QZD:
        QZD-TX.BAT Batch file implemented after transmission of :QZD:

        Each LAN-LINK user must configure the QZ*.BAT files for their 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 3 Page 127


        systems. The port number in the batch file should be set to the 
        PC I/O Port used. The data rate in the batch file should be set 
        to the data rate used between the PC and the TNC, NOT the data 
        rate used on the radio link.

        For example, the default QZU-RX.BAT file of
           "pcz 1 1200 rz %1" should be changed to
           "pcz 2 1200 rz %1" if you are have interfaced your TNC to Port 
        2 on your PC. If, the baud rate between the TNC is 2400 baud, the 
        file should be changed to "pcz 2 2400 rz %1".

        Each of the four batch files have to be customized for each user 
        who is not using PC Port Com1 and 1200 baud between the PC and 
        their TNC. The INSTALL program takes care of that chore. The high 
        level of customization required here is because different Zmodem 
        implementations require different sequences of instructions and 
        LAN-LINK does not want to limit you to a specific one.

        14.0 ELMER.QSO

        This is the state table (configuration file) for ELMER. The 
        contents of the file are as described in Appendix 8. If this file 
        is not present in the same sub-directory as LAN-LINK, you will 
        not be able to activate ELMER.

        15.0 LAN-LINK.OUT

        This file will be transmitted to all incoming connects (except 
        when in the multi user mode), if the file is present, and if the 
        Auto Answer flag is enabled. You can think of this file as a 
        CTEXT File.

        16.0 *.DMO

        These files are demonstration or test files. When LAN-LINK is put 
        into the Demo Mode (LAN-LINK Menu), LAN-LINK treats the lines of 
        text read from these files as if they came in from the TNC via 
        the serial port. Use these files for demonstrations and/or tests 
        of different features.













        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 128


                    Appendix 4 Local Area Network Capability

        VHF Packet radio systems can be considered as part of a Local 
        Area Network (LAN) in which messages can be left by one station 
        in the computer belonging to a second station. At HF the same is 
        true, but the area becomes greater. The basic problem here is 
        that people can only send and receive messages to or from you 
        when you are on-line. To compensate for this, BBS stations were 
        developed which allowed both messages and bulletins to be stored 
        by anyone for later retrieval.

        LAN-LINK allows you to store messages in your computer so as to 
        use it as an automatic answering machine. By storing the messages 
        in a file called by the name of callsign, with the file extension 
        ".OUT", anyone connecting to the computer will get their message 
        without having to request it. LAN-LINK also extends that concept 
        to cover the eventuality of you wanting to take your computer 
        off-line for some reason. You may now load the message into any 
        other computer you can connect to using elements of the Q code 
        adapted to the High Level Network Communications Language (NC/L) 
        first proposed in my book Software for Amateur Radio, (Book 
        number 1560) published by TAB Books, Blue Ridge Summit, Pa. 17214 
        U.S.A. 

        1.0 LAN Protocol (G3ZCZ Version)

        The protocol is as follows. When connected to someone who has 
        their LAN-LINK configured as a host, if you want to store a 
        message on that system, you use "QSP". You send the other station 
        ":QSP: CALLSIGN" where "CALLSIGN" is the callsign of the station 
        that the message is for, not the callsign of the host station in 
        whose computer you are storing the message. [Note use only one 
        space character after the :QSP:].

        For example if you want to store a message for 4Z4ZB in 4X6AA's 
        computer which is configured as a LAN-LINK Store and Forward 
        system, you would first connect to 4X6AA and then send the 
        command as ":QSP: 4Z4ZB". Better still use :QSP: option in the 
        Lan-Link Menu to automate the sequence.

        The computer at 4X6AA will respond either with a statement saying 
        that it is ready for you to go ahead, or send a message saying 
        that it can't comply. If it is ready you get a positive reply 
        which will take the form :QRV: CALLSIGN which if you know the Q 
        code, means "I am ready to accept a message for CALLSIGN".

        At this time you may go ahead and send the message. If you type 
        the message at the keyboard, you may use either a Control-Z (^Z) 
        character or the character sequence ":EOF:" followed by a 
        carriage return (the "Enter" key) to terminate the message. If 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 129


        you have first written the message into a text file you may then 
        send it using the "Send File" option of the Files Menu and the 
        termination sequence is automatic.

        Once you have completed the message, the other (host) computer 
        will either reply that the message has been successfully stored 
        or give you an error message.

        If the message is stored and ready to be sent next time the 
        addressee connects to that computer, you will see the message 
        :QSL: on your screen. If something went wrong, you will get back 
        a negative message taking the form :QNO: followed by a number. 
        The number tells you why the operation failed.

        2.0 Message Format

        The message is stored just as if you had left it in your system 
        (except that a header is added identifying the time of reception 
        and the call of the sending station). It will contain a header 
        showing the date and time it was received and your callsign. 
        Should a message for that station already be in the system, yours 
        will be appended to it. In the event your upload is aborted, the 
        amount of text received before the abort occurred will be stored 
        as the message.

        When you disconnect from the other LAN-LINK host station, its 
        mail beacon will be updated.

        Once the message is loaded in the host, it can only be deleted by 
        the operator of the host station. When the addressee connects to 
        the host and receives the message, the file type will change from 
        ".OUT" to ".OLD". Note QTA stations require positive confirmation 
        of receipt of message for the renaming to take place.

        3.0 ASCII File Uploading/Downloading

        There comes a time when you want to leave a file on your system 
        for someone to download later. You can do this by using NC/L to 
        control the transfer. You must leave the file in the file 
        download sub-directory defined in the LAN-LINK.SYS FILE (default 
        value is C:\LAN-LINK\FILES). You must first create the sub-
        directory, if it does not exist. The station who wants the 
        message then asks for it using :QBM: FILENAME.TYP. They do not 
        need to use the full sub-directory path. They must, however, 
        leave a single space character between :QBM: and the filename. In 
        AMTOR the Mailbox must be turned on for remote functions.

        For example, you have the latest ARRL DX bulletin, and you want 
        to pass it on. You could pass it to selected people by copying 
        the file to individual messages with the filetype ".OUT", e.g. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 130


        4X6AA.OUT, 4Z4ZB.OUT or even G3ZCZ.OUT if you want me to get it, 
        which wastes a lot of disk space.

        On the other hand you could tell people that the file was 
        available for downloading, either in the CTEXT connect message 
        line which everyone gets when connecting to you by configuring 
        LAN-LINK accordingly, or in individual (".OUT") messages.

        If you include the following in your CTEXT message 

                           "ARRLDX.015 now available"

        people will know that to download it, they just have to type the 
        line ":QBM: ARRLDX.015" (one space character between :QBM: and 
        the file name) to get the file. LAN-LINK is not designed as a 
        BBS, however, if you copy the contents of the \LAN-LINK\FILES 
        sub-directory into a file called DIR (USE DIR > DIR in DOS), 
        anyone can get a list of the files you have stored in it for 
        downloading by typing :QBM: DIR. Since they do not get the real 
        directory, just what was in it at the time you copied it into the 
        file "DIR", you may keep "hidden" files in this sub-directory. 
        You may thus leave a file for someone to download, tell them that 
        its there by leaving them a message (which they will get 
        automatically when they connect) and no one else connecting will 
        know that it is there.

        If you want to upload a file, ":QDB:" allows you to upload text 
        or ASCII files.

        If you use the "lan-linK" option of the Packet Terminal Menu, 
        LAN-LINK will automate the QDB and QBM features for you.

        4.0 Path Determination to a DX station

        If you want to establish a digipeat path to a station somewhat 
        out of your direct range, you need to know which of the stations 
        that you can connect to can hear that desired DX station. If you 
        could get a call monitored (MH list) from the stations that you 
        connect to, you would be able to see if the station you are 
        connected to has heard your desired DX station. 

        LAN-LINK uses the :QMH: command to request such a list. When LAN-
        LINK receives a :QMH: command, it drops back to the TNC Command 
        Mode and issues a "MH" command to the TNC (except to a TNC1 which 
        does not support it). It stores the list received in a temporary 
        buffer, and then returns to the Converse Mode and transmits the 
        list back to the station it is linked to.

        By judicious use of :QMH: you can determine paths to other 
        stations. Note however, that just because one station can hear 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 131


        another station, it does not mean that it can work it. For 
        example, the station you are connected to may be using a power 
        level of 1 watt or so, while the station 200 miles away that it 
        heard was using 100 watts. Test the path yourself, or/and leave a 
        message asking how reliable the connect path between those two 
        stations is.

        If you and a small group use a non standard packet channel for 
        inter-group communications, you may also use the :QMH: function 
        to find out who the station you are connected with, has heard 
        recently, when you first sign on the LAN channel.

        5.0 Binary File Transfers

        In the PC world most binary file transfers seem to be taking 
        place using the YAPP protocol built into the YAPP user terminal 
        program and the BBS software written by Jeff Jacobsen, WA7MBL. As 
        Jeff stated in the documentation, YAPP was written to provide a 
        terminal program for use in testing the WA7MBL BBS code. However 
        for many radio amateurs, YAPP was their first terminal program.

        The YAPP binary transfer protocol is similar to the Xmodem 
        protocol used on telephone line BBSs. In order to transmit a 
        file, the sending station breaks the file down into blocks of 
        characters. Each block is transmitted in sequence. After a block 
        has been transmitted, the sending station waits for the receiving 
        station to acknowledge that block and verify that it was received 
        without errors. 

        When two stations are alone on a frequency, they can transfer 
        data quite quickly. So back in 1986 when YAPP was written, it 
        provided the few hams using packet radio with a binary file 
        transfer capability. Today, however, the situation is different. 
        In most urban areas, each packet radio channel is occupied by 
        many stations, and the requirements for binary file transfers are 
        somewhat different.

        6.0 Requirements for Transfer Protocols

        The AX.25 protocol provides for a basic verification that packets 
        have been received error free. If the binary file transfer 
        protocol could establish the connection, start sending blocks, 
        and then keep sending data until one of three things happen; the 
        link drops out, the receiving station signals that some of the 
        data were received with errors, or the whole file is transmitted 
        correctly. 

        If the whole file is transmitted, then the sending station just 
        has to wait for an acknowledgment from the receiving station that 
        the file was received. If the circuit is busy with several 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 132


        stations on the channel, or the path goes through one or more 
        Nodes, there will be varying delays in the delivery time of the 
        packets. By not having to acknowledge each block of data, the 
        file can get through much faster than it would have, in the case 
        in which each received block has to be individually acknowledged.

        If the link drops out, it would be nice if the computers, could 
        determine how much of the file was received, then pick up the 
        transmission at that point next time they link up.

        If the receiving station signals that some data were received in 
        error, the sending station should then begin to retransmit from 
        the start of the error.

        7.0 The Zmodem Protocol

        This situation is not unique to the amateur radio packet network. 
        It is also present in the commercial packet switching 
        environment, and the Zmodem protocol was developed to provide the 
        capabilities described above. Zmodem thus seems to be an almost 
        ideal binary file transfer protocol for use on radio amateur 
        packet channels, and is incorporated in LAN-LINK 2.00+. 

        LAN-LINK uses the :QZD: and :QZU: commands to provide the 
        capability to remotely download and upload binary files. :QZD: 
        allows you to download a file from another station, while :QZU: 
        allows you to upload a binary file. :QZD: is configured so that 
        if the link drops outs during the transfer, when the connection 
        is once again established, a subsequent :QZD: for the same 
        filename, will cause the transfer to pick up where it left off 
        when the link dropped out. This feature is not allowed in the 
        upload :QZU: command to inhibit people from injuring files that 
        already exist on the other computer. Each command may be 
        initiated from either end of the link, but to gain the most from 
        the recovery capability, files should be downloaded by the 
        receiving station.

        8.0 The PCZ Zmodem Package

        LAN-LINK implements the Zmodem protocols using batch files in DOS 
        that call up external programs. This approach allows stations to 
        try different versions of Zmodem and experiment to find the 
        optimal one for their area. LAN-LINK comes with the (PCZ) Public 
        Domain implementation of the Zmodem, Ymodem, Xmodem, Xmodem-1K 
        and Sealink protocols by Drue Kennon and Gary Smith. 

        Since any LAN-LINK station can either receive or originate a 
        :QZD: and a :QZU: command, LAN-LINK comes with four default batch 
        files to control Zmodem transfers. These files are as follows.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 133


        QZU-RX.BAT Batch file implemented after receipt of :QZU:
        QZU-TX.BAT Batch file implemented after transmission of :QZU:
        QZD-RX.BAT Batch file implemented after receipt of :QZD:
        QZD-TX.BAT Batch file implemented after transmission of :QZD:

        Each pair of users can experiment with other protocols and Zmodem 
        implementations using the :QZD: and :QZU: commands after reading 
        the PCZ documentation. The :QBU: command can also be used if the 
        corresponding DOS batch files (QBU-RX.BAT and QBU-TX.BAT) are 
        created.

        LAN-LINK contains an output buffer to store data being output to 
        the TNC. The TNC contains a buffer which stores data about to be 
        sent on the radio link. In the normal course of events, the two 
        buffers fill up, so that the Zmodem package used by LAN-LINK may 
        think that all the data has been transmitted, when in fact there 
        are still characters left in the buffers, or the last packet has 
        not yet made it to the destination station. In this case, you may 
        see a message on your screen that the system has sent all the 
        data and is waiting for the final acknowledgment, while at the 
        same time you can see from the LEDs on the TNC that you still 
        have outgoing data in your system. Have patience and wait a while 
        to let the two systems synchronize.

        In the event that the link is bad and errors occur, this 
        buffering may cause problems which require some of the Zmodem 
        timing parameters to be changed. Should this situation arise, 
        read the Zmodem package documentation.

        The flexibility offered by the Zmodem protocol has many 
        advantages when used in a packet radio network. LAN-LINK 2.00+ 
        implements Zmodem by the use of an external public domain 
        protocol package which provides for the maximum degree of user 
        customization. This capability is provided at the cost of having 
        the individual user customize four batch files using the text 
        editor built into LAN-LINK.

        9.0 BASIC NC/L DICTIONARY

        Messages can be transferred into any other LAN-LINK computer you 
        can connect with using elements of the Q code adapted for the 
        purpose. NC/L command words are summarized in the following 
        paragraphs. There is no command word to request your message. To 
        receive your message, you do nothing. You will receive your mail 
        automatically when connecting/linking with a LAN-LINK station. 
        You cannot normally read messages addressed to another person.

        9.1 :QBM: 

        To download an ASCII file, send ":QBM: FILENAME.TYP". The 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 134


        FILENAME.TYP is the file you want. i.e. ":QBM: DIR".

        9.2 :QDB: 

        To upload ASCII files to another LAN-LINK system send ":QDB: 
        FILENAME.TYP". Files will be uploaded into the same sub-directory 
        as LAN-LINK, and will have a message header inserted at the top 
        of the file to allow the operator to know who uploaded the file. 
        If the operator then wants to make the file available for 
        downloading, he or she can move it to the \LAN- LINK\FILES sub-
        directory. The ".TYP" following the filename is optional. If you 
        attempt to upload a file which has the same name as one that 
        already exists on the remote system, you will receive an "error" 
        message. This command is the reverse of :QBM:.

        9.3 :QMH: 

        To request a call monitored list ("MH") from the LAN-LINK station 
        that you are connected with, send ":QMH:".

        9.4 :QSM: 

        To request a repeat of a message from a station using LAN- LINK, 
        send ":QSM:". This command will be valid as long as the host 
        station has not deleted the YOURCALL.OLD file on his disk. If the 
        file does not exist, you will receive a :QNO: "error" response.

        9.5 :QSP: 

        To leave a message, send ":QSP: callsign". The callsign is that 
        of the station you wish to leave a message for.

        9.6 :QRA:

        When disconnected, to see what stations (using LAN-LINK 1.53+) 
        are on the LAN, or which LAN-LINK stations have messages pending, 
        send ":QRA:". All LAN-LINK stations will reply with a mail beacon 
        within a few seconds. The Alt-W key implements this feature.

        9.7 :QRT: 

        To shut down a LAN-LINK AMTOR/Packet mode Mailbox or beacon 
        station which is causing QRM, link or connect to the station and 
        send ":QRT:".

        9.8 :QRU: 

        To upload messages from one LAN-LINK/PK232COM (1.38+) system to 
        your computer, send ":QRU:".



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 135


        You may only use the QRU function with stations designated as 
        Store and Forward mailboxes. Put a list of stations that you can 
        connect to reliably in your CALLSIGN.MBX file and send it to 
        other stations in your LAN also using LAN-LINK. They will then be 
        able to dump their mail messages on you and you on them. If they 
        do the same and send you their file, then you will be able to 
        send messages via them for stations that they can work.

        While QRU gives you the capability to bulk upload messages to 
        another station in your local area, when you take your machine 
        off line, it may also be used to transfer messages between two 
        LANs via well sighted gateway digipeaters.

        9.9 :QNO: 

        :QNO: and error message text is a response to a request. 

        9.10 :QJG: 

        :QJG: is a response to :QRU:. It confirms that the QRU sequence 
        is complete. There are no more messages pending.

        9.11 :QRV: 

        :QRV: callsign is a response to :QSP: callsign. The computer is 
        ready to send the message. End the message with a control Z (^Z) 
        character, or the sequence :EOF: 

        9.12 :QSL:

        :QSL: is a response to a command. It confirms receipt of message 
        to that callsign or that a file has been successfully uploaded 
        and stored to disk. It is also used to acknowledge receipt of a 
        ":QRT:" command.

        9.13 :QTA: message 

        If LAN-LINK receives :QTA: and a message exists for the 
        connecting station, LAN-LINK will change the filetype from "OUT" 
        to "OLD" and respond with a "QSL". If a message does not exist, 
        it will respond with a "QNO".

        9.14 :QTC: Message List

        If LAN-LINK receives :QTC: it will respond with the beacon text 
        showing the mail queue. :QTC: precedes a list of callsigns for 
        whom messages are stored up on a computer. It is used in Packet 
        Beacon transmissions or AMTOR Beacon mode CQ calls. 




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 4 Page 136


        9.15 :QBU: External Protocols

        This feature is supplied to allow experimentation with external 
        protocols.

        9.16 :QZU: Zmodem Binary File Upload

        :QZU: is used to implement an upload of a binary file from 
        another station using an external Zmodem protocol via the QZ*.BAT 
        files.

        9.17 :QZD: Zmodem Binary File download

        :QZD: is used to implement a remote download of a binary file 
        from another station using an external Zmodem protocol via the 
        QZ*.BAT files. In the event that the link drops out during the 
        transmission, when the link is remade, and the :QZD: retried, the 
        transfer will pick up from the point at which it was interrupted, 
        if the batch files provided are used.

        9.18 :QIC: Page Operator

        Use :QIC: to page the operator at any LAN-LINK 2.10+ station. The 
        sequence is:- you send :QIC: to another LAN-LINK 2.10 station. 
        Use the LAN-LINK Menu or type it by hand. Upon receipt, LAN-LINK 
        begins to page the operator if the sound flag is on. At that time 
        it sends you a :QRX: followed by a number, i.e. ':QRX: 30'. The 
        number is the number of seconds it will page the operator. At the 
        end of the paging sequence it will send the prompt i.e. 'G3ZCZ>'. 
        If the sound is inhibited it will send ':QRX: QRT' to signal that 
        it is in a silent configuration.

        9.19 :QTR: Ask for Time

        The :QTR: command allows you to get the date-time-text string 
        from the other LAN-LINK 2.10+ station. Don't confuse it with 
        :QRT:.















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 5 Page 137


                         Appendix 5 Using Different TNCs

        The Packet Mode capabilities can be used on all TNCs. There are 
        minor differences in the command dialogue between different TNCs. 
        The dialogue differences affecting the operation of LAN-LINK are 
        built into the program and set when the TNC type is read from the 
        LAN-LINK.SYS file at the program load time. The non packet modes 
        will obviously result in error messages if attempted on a packet 
        mode only TNC.

        The following notes apply to different TNCs or digital 
        communications controllers.

        1.0 TNC2 (MFJ 1270) 

        The following functions do not work because the TNC does not 
        support them.

        All NON PACKET modes.
        Software controlled HF/VHF switching.
        Software controlled baudrate switching.
        CQ/BEACON Packet terminal mode.
        TNC Transmit Buffer flush.

        N2GNJ noticed that he needed "LC ON" when using a Tiny 2 EPROM 
        Version 2.0 in the MFJ 1270B to make the automatic snatch 
        features work.

        2.0 TNC1 (HK-4040)

        The Packet Communications Mode header colors are not supported in 
        LAN-LINK for this TNC.

        The following functions do not work because the TNC does not 
        support them.

        All NON PACKET modes.
        Day/Time functions. 
        MH and remote :QMH: functions. 
        MAIL Packet Terminal Mode. 
        CQ/BEACON Packet Terminal Mode.
        TNC Transmit Buffer flush.
        Conference and multiconnect modes.

        3.0 Kantronics KPC-2

        The Packet Communications Mode header colors are not supported in 
        LAN-LINK for this TNC.

        The following functions do not work because the TNC does not 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 5 Page 138


        support them.

        All NON PACKET modes.
        MAIL Packet Terminal Mode. 
        CQ/BEACON Packet Terminal Mode.
        TNC Transmit Buffer flush.

        4.0 Kantronics KAM 

        LAN-LINK switches colors when it sees the /V or /H following the 
        callsign in the packet header, or in the calls monitored ("MH") 
        list. If you are monitoring both HF and VHF simultaneously, the 
        colors will show you which radio you heard which signal on. If 
        the Mail-Snatch or the QTC-Snatch are triggered, LAN-LINK will 
        change modes and attempt the connect on the correct radio but 
        will not change the band/power information or the logbook to 
        reflect that change in the logbook or in the status window 
        display. Turn the DCD flag OFF for these automatic features to 
        work.

        The following functions do not work because the TNC does not 
        support them.

        TNC Transmit Buffer flush. 
        The SIGNAL Communications Mode.
        The Alt-D key in the MORSE Communications Mode.
        The AMSAT-OSCAR Menu does not allow UoSAT option, as the KAM does 
        not have 1200 baud ASCII capability.

        5.0 PK-232 

        Turn BBS OFF, if you want the Alert Call, packet communications 
        mode header colors, and Digipeat Detect features to work, 
        otherwise turn BBS ON.

        6.0 MFJ 1278 

        LAN-LINK assumes that the Radio 1 port is connected to the 
        VHF/UHF packet transceiver, and the Radio 2 port is connected to 
        the HF transceiver with the multi mode communications capability 
        (you may customize this however).

        The MFJ1278 suffers from one major deficiency as far as LAN-LINK 
        is concerned. The Echo-As-Sent only works in the AMTOR 
        Communications Mode. That means that you will not see the 
        contents of a file echo in the incoming window as the file is 
        being transmitted in the RTTY mode.

        The following functions do not work because either the TNC does 
        not support them or does not do so in a consistent manner.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 5 Page 139



        Pactor 
        Type Ahead Buffer
        TNC Transmit Buffer flush. 
        The SIGNAL Communications Mode.
        The AMSAT-OSCAR Menu does not allow UoSAT option. 
        CW Identification.

        7.0 Heath HK-21

        K3WGF noticed that his Heath HK-21 TNC didn't seem to have the 
        proper circuitry to support true DCD on pin 8 of the RS232 
        connector. Even though the pin was labeled DCD it didn't signal 
        properly. Set the DCD function in LAN-LINK to OFF to make the 
        Capture-to-Disk close out normally rather than continue to remain 
        engaged. 

        8.0 PK-900 and DSP 2232

        LAN-LINK supports dual windows, and some of the 
        communications modes. Otherwise, support is as if they were PK-
        232s. Sometimes, LAN-LINK may take a few characters to 
        synchronize windows.





























        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 6 Page 140


                          Appendix 6 Anomalies and Bugs

        This section discusses various anomalies and bugs.

        1.0 Command/Converse Mode Anomalies

        Since the Program has no way to check the command/converse mode 
        status of the TNC, you may see various "Cmd:" and other "error 
        messages" from the TNC when using the menus or function key 
        commands. Ignore them for now. If you get an error message, try 
        using the function key again.

        2.0 Buffer Messages in AMTOR Beacon CQ Mode

        In the AMTOR Beacon CQ Mode, if the other station drops the link 
        while you are recording the text, BEFORE the callsign has been 
        recognized as a valid callsign, LAN-LINK will time out before 
        logging the QSO and restart the CQ sequence. If someone else 
        calls in before the time-out has occurred, the text from both 
        stations should be captured to disk, but the log entry may not 
        show both stations. You should compare the callsigns in the 
        logbook with the "RUN" file for QSO purposes.

        LAN-LINK in the Beacon/Mailbox Mode, normally logs the contact at 
        the end of the line in which it recognized the callsign as a 
        valid callsign.

        3.0 FEC +? Responses in AMTOR Beacon CQ Mode

        In the AMTOR Beacon CQ or Mailbox mode, if another station sends 
        a +? in the FEC Mode, the beacon will attempt to send the LAN-
        LINK.TXT file. The PK-232 however is not in the Converse Mode at 
        that time and will interpret the text of the file as commands. If 
        by some chance, the text corresponds to a valid command the PK-
        232 will execute it and put the PK-232 in an unknown state and 
        you may not notice that it did. As such I recommend that the 
        first character of each line in the file LAN-LINK.TXT be a non 
        valid command character such as a number or a period (.) or 
        another punctuation sign.

        4.0 Using a Monochrome Monitor

        If you are using a monochrome monitor, the text you type into the 
        Outwindow may be fainter than the incoming text. This is because 
        of the default colors used. Change the colors using the Parameter 
        Menu.

        5.0 The Packet Conference Mode

        The Conference Mode has been tested on a PK-232, KAM, a SANYO 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 6 Page 141


        MBC-675 which has a clock speed of 4.7MHz and other PC clones 
        with faster clock speeds. If you have problems with intermittent 
        selection of I/O channels try slowing down your CPU clock. There 
        is a software delay loop in the program that is used to allow the 
        TNC time to switch I/O streams after receipt of the stream change 
        command. This delay is there because LAN-LINK tests for a connect 
        on each channel before outputting any text, so that it does not 
        send un-addressed packets on non connected I/O channels.

        6.0 Packet Conference Mode Disconnects

        Any Packet conference Mode disconnect returns the TNC to the 
        Command Mode, even if you remain connected to other stations.

        7.0 Strange Events

        If the TNC does not use an interrupt driven serial port you may 
        experience problems when using baud rates greater than 1200. The 
        PK-232 DOES NOT LIKE LAN-LINK to use RS-232 baud rates faster 
        than 2400, and sometimes not even that. Use 1200 until YOU have 
        tested and ARE SURE that a faster one will work. 
                         
        If you have any strange problems and are using an RS-232 terminal 
        baud rate between the PC and the TNC which is greater than 1200, 
        set the Terminal Baud Rate to 1200 and see if the problem goes 
        away.

        Make sure that your configuration is set the way you think it is. 
        Verify it using the Parameter Menu.

        You must have at least one common call or scan word in your SYS 
        file, or you will get errors when you update the SYS file.

        8.0 *** DISCONNECTED

        In the Packet Communications Mode, when you are connected to 
        someone and the TNC sends "*** DISCONNECTED" to the computer, 
        LAN-LINK thinks you have been disconnected and resets. This 
        normally only happens when a true disconnect occurs. However, if 
        the text shows up in the middle of a line being sent to you, it 
        will have the same effect. LAN-LINK will think that you have 
        disconnected if the DCD Flag is not set in the SYS file, and the 
        TNC does not use the DCD signal on pin 8 of the RS-232 interface.

        9.0 *** CONNECTED

        In the Packet Communications Mode, if you are monitoring traffic 
        on the LAN and someone sends a packet containing "*** CONNECTED", 
        LAN-LINK thinks you have been connected, if the DCD-Flag is not 
        set, and the TNC does not use the DCD signal on pin 8 of the RS-


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 6 Page 142


        232 interface. 

        10.0 Greek Characters and Other Garbage in the Incoming Screen

        If you see Greek characters in the Incoming screen you probably 
        have the wrong parity set in the TNC. First make sure that the 
        RS-232 baud rate is correct. If it is, take the batteries out of 
        it and reset it. If that fails, play with the parity. LAN-LINK 
        sets the serial port as configured in the TNC.SYS file for each 
        TNC. For example, for the PK-232 it is 8 bits, no parity. For the 
        TNC2, it is 7 bits. If you still can't get LAN-LINK to talk to 
        the TNC, set the interface to 7 bits in the configuration file.

        11.0 Dumb TNC

        If the TNC seems to respond to commands but is not sending 
        anything back, you may have one of two problems. You may have a 
        bad RS-232 cable with a wire disconnected. If the computer can 
        operate the TNC in another communications program, try to reset 
        the TNC, take the batteries out, etc. You may also have a not-so- 
        compatible PC. 

        12.0 Intermittent Lockup

        Watch out for flow control problems on the cable between the TNC 
        and the PC and between the PC and the Display. 

        Versions of LAN-LINK up to and including 1.55 used software 
        handshaking. Anytime the program received a Control-S (^S) 
        character from the TNC it waited until it subsequently received a 
        Control-Q (^Q). These characters can appear on the LAN in a 
        binary packet, either when binary file transfers are in progress, 
        or in a Inter NET/ROM message. To avoid this lockup, a line 
        containing "MFILTER 19" was added in the LAN-LINK.SYS file for 
        the PK-232 to make the TNC filter the ^S character out and not 
        pass it to LAN-LINK. LAN-LINK 1.56 and onward use hardware hand-
        shaking so this problem should not appear. However if the FLOW 
        and XFLOW parameters are not set to OFF in your TNC, LAN- LINK 
        can appear to lockup. Make sure that they are both set OFF in 
        your TNC.

        13.0 Automatic Functions Don't Work

        This usually happens with the KAM. Set the DCD Flag off, and the 
        automatic functions should work. Note that in this case the 
        multi-connect functions will not work.

        14.0 BBS Zap Failure

        If the BBS Zap hangs up in the middle of sending a message, the 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 6 Page 143


        probability is that the LAN-LINK is waiting for the PBBS to send 
        it a word it recognizes. You have probably not configured the 
        "PBBS Read Subject" and "PBBS Message" Strings (lines 43 and 44) 
        in the LAN-LINK.SYS File (See Appendix 2, Section 18.18).

        15.0 LAN-LINK Forgets the Band/Power Information

        LAN-LINK picks up the band and power information from the 
        logbook. You can set them via the "0" option in the Parameters 
        Menu. If the logbook is empty, LAN-LINK will not remember the 
        settings when it is switched off. Put at least one entry in each 
        logbook.

        16.0 Zmodem Binary Transfer Problems

        Some stations perform binary transfers with no problems, others 
        seem to have problems. If you are having problems with the binary 
        file transfers make sure:

        *    You have enough memory left over after loading LAN-LINK to 
             run the external communications protocol.
        *    The QZ*.BAT files have the correct port and baud rate 
             values.
        *    The TNC is set for 8 bit transfers.
        *    Both stations are using the same data rate between the PC 
             and the TNC.
        *    The TNC does not filter any characters out of the data 
             stream, i.e. MFILTER or the equivalent parameter in your TNC 
             is not set.
        *    Make sure you try the binary transfers via the LAN-LINK 
             menu.
        *    Read the PCZ Documentation file and set the Environmental 
             variables correctly.
        *    If all else fails, try a different external protocol.


















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 7 Page 144


                         Appendix 7 Updates, Revision History

        If you are updating from a previous version of LAN-LINK, the 
        following changes were made in recent versions of LAN-LINK.

        2.00 

        ELMER, Alt-W, word wrap, G option in Edit menu, Strswitch chars & 
        error_st in sys file, added. KAM cw/cmd bug fixed, AMTOR sets 
        narrow shift, connect timeout configurable, KAM RX/TX inv added, 
        bell filtered out of connectee/log call, KAM cw and other 
        parameter changes, log power/band picked up from log, custom 
        word[20] in prompt, Elmer added, event timer 2/6 reset change, MH 
        fire delay for KAM, ^T filtered out in all tncs, #T in contest 
        text, NAVTEX and navy MARS enabled for KAM/MFJ1278, flag_XMITOK 
        added, base count added to SYS file, CTEXT saved.

        2.10

        PACTOR (KAM, PK-232) added. Converted to TP6, Bug fixes Init: 
        7/8bits, log package changed, Elmer.qso loaded at start-up, Elmer 
        RUN commmand, BBS custom commands, Flag_Inhibit_Logging, Logging 
        package, FLAG_Printer_Perm, TNC_parameter, mode at start up, QIC, 
        QMH in menu, QTR, LAN-LINK.OUT, ANSI Colors, PacketCluster Log 
        Search mode added. ELMER resets on disconnect, MFJ1278 radio port 
        customzable, Shut down flag 5 deleted, BBS upload states changed.

        2.20

        Converted to TP7. Scan word colors, PacketCluster DX Alert 
        colorized. 2.2 was really a bug fix version for 2.10 which should 
        never have been released and was replaced within a few days.

        2.30

        Support for PK-900 and DSP 2232. Better ANSI support. G-TOR in 
        KAM. Manual Mode, Z and B options added to BBS Menu. Expanded 
        PacketCluster support. Demo option added in LAN-LINK Menu. Radio 
        Menu added for Kenwood and Icom (untested). EDIT.EXE and 
        UPGRADE.EXE external programs added.












        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 145


        Appendix 8 ELMER An Expert System Based on a Finite State Machine

        There are two versions of ELMER supplied with LAN-LINK. One is 
        built in for use in packet mode communications, when connected to 
        someone else. The second version is a stand alone version for use 
        in developing the text files and the logic. The stand alone 
        version lets you program and debug your own personal ELMER on 
        your own. The stand alone version is a separate product and 
        requires separate registration.

        Most initial amateur radio contacts (QSO) are somewhat 
        repetitive, in that they send the same information each time. In 
        digital mode communications hams don't type exactly the same 
        information in every QSO, but in general the information 
        exchanged is a subset of a standard set. Hams have noticed this 
        phenomenon and have each created and used files containing 
        standard information. This fact was noticed years ago, and the 
        first so called "brag tapes" were invented to serve that need 
        back when they were using teletypewriters and generated paper 
        tapes for the standard information.

        ELMER takes that concept a little further and provides expert 
        system. By parsing the incoming text, ELMER will recognize 
        certain words and transmit text files containing replies or 
        further questions, just as if the operator was at the keyboard.

        Hams can use this feature to build a smart server they can put 
        on-line on the LAN. The server will prompt people and will serve 
        an educational purpose. ELMER can be set up to teach people about 
        packet radio, license upgrades, or anything else. ELMER can also 
        be programmed to recognize different languages and hold a 
        conversation in those languages. In fact, apart from the 
        dedicated educational and informational server applications, 
        ELMER may be configured with such a variety of vocabulary files 
        so as to pass the Turing test in most typical amateur radio 
        digital mode conversations.

        1.0 INTRODUCTION

        ELMER is a program which allows you to build an expert system. It 
        uses the ELMER.QSO file to set up the state machine.

        The ELMER contains an array of words to be matched, current 
        states, next states, and files to be loaded.

        The ELMER starts up in an initial state. When a line of text is 
        received, it begins to match an array of words against the 
        incoming line of text. It starts matching the words in the order 
        that they are present in the array. It only matches words that 
        are enabled for the current state or for state 0. If it finds a 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 146


        match, it advances the next state, and if a valid file name is 
        present (and exists), will output that file. The ELMER will then 
        continue scanning the line of text from the point that the last 
        match was obtained. At the end of the line, it waits for the next 
        line.

        1.1 Expert Systems

        Before discussing ELMER, here's some information about expert 
        systems. An expert system contains knowledge about a particular 
        field to assist human experts or provide information to people 
        who do not have access to an expert in the particular field. It 
        is an information system that can pose and answer questions 
        relating to information borrowed from human experts and stored in 
        the system's knowledge base. Although they vary in design, most 
        expert systems have a user interface, a knowledge base, and an 
        inference engine.

        1.2 The User Interface

        The User Interface to the expert system is the way that the user 
        interacts with the system to extract information from the system.

        1.3 The Knowledge Base

        The Knowledge Base of an expert system contains both declarative 
        and procedural knowledge. The facts describing the situations, 
        events and objects are called declarative knowledge. Procedural 
        knowledge is the information about courses of action and the 
        rules governing the actions. There are various kinds of rules 
        that may be employed.

        1.4 The Inference Engine

        The Inference Engine controls how and when the information in the 
        knowledge base is applied. It determines how the rules in the 
        knowledge base are to be applied to the problem.

        1.5 Features of an Expert System

        The following list of features are desirable in any expert 
        system.

        1.5.1 Useful

        The system should meet a specific need.

        1.5.2 Usable

        The system should function so that even a novice computer user 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 147


        finds it simple to use. It should be able to respond to simple 
        questions.

        1.5.3 Educational

        The system should allow non experts to increase their expertise. 
        In a similar vein, the system should be able to explain the 
        reasoning behind its advice to allow the user to determine the 
        validity of the advice. 

        1.5.4 Adaptable

        The system should be able to learn new knowledge. 

        1.6 Using an Expert System

        Expert systems take the form of software packages residing on a 
        hardware platform (computer). The most common use of an expert 
        system is via a man-machine dialogue. The user types something at 
        the keyboard and the system replies. The user interface accepts 
        the input. The input is parsed in some manner. The inference and 
        knowledge engines process the user input in a predetermined 
        manner and an output appears. The parsing function may be a 
        simple pattern matching method commonly called keyword analysis, 
        or a more complicated function using syntactic analysis. Keyword 
        analysis is a logical function in which the presence of various 
        keywords are detected. When a keyword is found, the system 
        responds in the manner in which it has been programmed. For 
        example, if the system detects the words "the wx" in a question, 
        it may respond with " the wx here is sunny".

        In syntactic analysis, a sentence is analyzed according rules 
        which allow the system to respond differently to keywords which 
        appear in different sequences. For example, the system may 
        respond differently to the question "what is the wx" and "the wx" 
        if it recognizes those words in a sentence. 

        1.7 The Semantic Network

        The most general and oldest artificial intelligence scheme for 
        representing knowledge is the semantic network. A semantic 
        network is a collection of objects called nodes. The nodes are 
        connected together by links. Ordinarily, both the links and the 
        nodes are labeled. A drawing of a semantic network contains 
        bubbles to represent the nodes, and lines connecting the nodes to 
        represent the links. Both nodes and links are labeled. The 
        drawing looks just like a PERT or CP/M chart. It is also the 
        drawing used to represent a state machine.




        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 148


        1.8 A State Machine

        A state machine is a system that exists in several states. The 
        system makes a transition from one state to another as a result 
        of a stimulus. All states and transitions are defined at the time 
        the system is designed. The links in the semantic network are the 
        transitions in the state diagram.

        1.9 The User Perception

        The user perception of an expert system is that the system 
        appears to be in a rest state. It receives an input from the user 
        and enters a transition to a state in which it processes the data 
        it has just received. After processing the input, it generates an 
        output and returns to what seems to be the same rest state. In 
        reality, the two rest states (initial and final) are different.

        1.10 ELMER

        ELMER is an expert system for amateur radio. ELMER is based on a 
        finite state machine using table driven software. The declarative 
        knowledge is stored in the form of separate ASCII text and 
        command files. The procedural knowledge is stored in the state 
        table. The Data files in ELMER correspond to the Knowledge Engine 
        (and the Inference Engine). The State Tables correspond to the 
        Inference Engine. ELMER also contains an ASCII editor for text 
        files, and a tool to view the state table. These tools allow the 
        user to "teach" ELMER new knowledge.

        1.11 Responses to an Input

        ELMER has three kinds of reaction to a word match. It can do 
        nothing, output a test file, run a command or overlay a new state 
        table. ELMER's state table contains four entries:-

        1.11.1 Current State

        This is the state that the string match is performed in. ELMER 
        can have up to 63 different states.

        1.11.2 Next State

        This is the state that the ELMER will advance to if a string 
        match is found.

        1.11.3 Repeat Flag

        This is a flag to allow or disallow repeats. If it is a 0 repeats 
        are allowed. If it is a 1, they are not.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 149


        1.11.4 Command Flag

        This is a flag to tell the ELMER how to treat the file. If it is 
        a 0, load a text file; a 2, overlay the current state table with 
        the defined one.

        1.11.5 Keyword

        This is the text string to match in the syntactic analysis of the 
        input text. The text string can be up to 15 characters long and 
        can include spaces. The match is case insensitive, i.e. there is 
        no difference between upper and lower case.

        1.11.6 Data File

        This is a text file to be loaded or a new configuration file.

        1.12 Syntactic Analysis

        ELMER performs syntactic analysis on the input text in the manner 
        described below. ELMER performs a string match on the line of 
        received text against each keyword entry in the state table. 
        ELMER starts with the first entry. If a match is made, ELMER 
        changes state and performs the transient function defined by the 
        Command Flag. All words in the input text including the keyword 
        are then deleted. ELMER then continues the string match until 
        either the input line of text has been reduced to zero length, 
        or, the line of input text has been tested against all keywords 
        in the state table. 

        1.13 Programming ELMER

        Programming ELMER is simple. The knowledge base is broken out in 
        terms of states and transitions. States can be passive or active. 
        A passive state is one in which ELMER does nothing other than 
        accept/parse further input. An active state is one in which ELMER 
        loads and displays a text file containing information or shells 
        to DOS and runs an external program.

        ELMER contains a set of tools for programming and debugging 
        purposes. A state table for the procedural knowledge is drawn up 
        using pencil and paper and a large sheet of graph paper. The 
        built in text editor is then used to enter information into the 
        table. The individual text files containing the knowledge are 
        also created using the editor. The state table viewing tool is 
        used to check the entries. The state table loading capability is 
        used to exercise ELMER and verify the logic. Because the 
        procedural knowledge is contained in the state table, all sorts 
        of rules and linkages may be used.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 150


        2.0 The State Table (ELMER.QSO) File

        These are the contents of the ELMER.QSO file.

        2.1 The Directory Path to the ELMER Text Files

        This item is the directory path to the sub-directory containing 
        the ELMER text files. For example "c:\LAN-LINK\ELMER\" or 
        "c:\ELMER\" or just "c:", if you put them in the same sub-d-
        irectory as ELMER.EXE. If you do use a path you MUST have the 
        last "\" character at the end of the sub-directory name because 
        the program concatenates the directory path to the ELMER.

        2.2 The Start Up File

        This line is not used in LAN-LINK's ELMER. It is only used in the 
        stand alone version. It contains the name of the text file to 
        output the first time ELMER is invoked (if present);

        2.3 Window Colors

        These seven lines are only used in the stand alone version. They 
        are the numbers which correspond to the colors of the seven 
        different windows displayed on the screen of the stand alone 
        version, in the following order.

        2.3.1 Status Window Color

        The color of the window at the top of the screen.

        2.3.2 OutWindow Color

        The color of the window in which the replies are displayed.

        2.3.3 InWindow Color

        The color of the window in which your keystrokes are displayed.

        2.3.4 BottomWindow Color

        The color of the bottom line of the screen.

        2.3.5 Promptwindow Color

        The color of the window in which menus are displayed.

        2.3.6 Option Color

        The color of the highlighted characters in the menus and prompts.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 151


        2.3.7 Alarmwindow Color

        The color of the window in which error and alarm messages are 
        displayed.

        2.4 The ELMER Initial State

        This item is included to allow you to have different state 
        machines, each starting with a different state number.

        2.5 State Machine Parameters

        The next few lines contain the state machine parameters.

        2.5.1 Current State

        This is the state the string match is performed in. LAN-LINK 
        allows up to 63.

        2.5.2 Next State

        This is the state that the ELMER will advance to if a string 
        match is found.

        2.5.3 Repeat Flag

        This is a flag to allow or disallow repeats. "0" means that 
        repeats are allowed. "1" means they are not.

        2.5.4 Command Flag

        This is a flag to tell the ELMER how to treat the file as shown 
        below.

        Flag                Operation
        0    Load/display a text file. 
        1    Execute a BAT, COM, or EXE file.
        2    Overlay the current state table with the new one.

        2.5.5 Keyword

        This is the text string to match. It can be up to 15 characters 
        long and can include spaces. The match is case insensitive, i.e. 
        there is no difference between upper and lower case.

        2.5.6 Data File

        This is either a text file to be loaded or a command file to be 
        executed, depending on the state of the Command File Flag. An "*" 
        character defines a "do nothing" state in which the Data File is 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 152


        ignored.

        The two character sequence "#1" will cause ELMER to clear the 
        screen before displaying the rest of the text in the data file.

        2.6 The State Machine File

        An example of some state machine parameters is shown in this 
        typical extract from an ELMER.QSO file.

        1, 2,0,0,what,*
        2, 3,0,0,englishman,*
        3, 4,0,0,doing,*
        4, 1,0,0,country,me-usa.txt
        1, 1,1,0,equipment,pk232com.txt
        1, 1,0,0,wx,localwx.txt
        1, 5,0,0,kenwood,kenwood.txt
        5, 1,0,0,811,811.txt
        1, 1,0,0,hello,hello.txt
        0, 1,0,0,name,joe.txt

        An "*" character defines a "do nothing" state in which the Data 
        File is ignored.

        2.7 Example of Programming the State Table

        Consider a typical question that I get asked.

        "what's an englishman like you doing in this country ?"  

        followed by

         " The equipment here is ....."

        Assuming that the ELMER is in State 1, and that the first few 
        lines in the ELMER.QSO file are as shown above. The ELMER 
        recognizes the word "what" and advances to State 2. Since the 
        file name is an "*" character no file is sent. The ELMER then 
        recognizes the word "englishman" and advances to state 3. The 
        ELMER machine then recognizes the word "doing" and advances to 
        State 4. The ELMER then recognizes the word "country" advances to 
        State 1 and transmits the text file "me-usa.txt", because the 
        Command Flag is a 0. It then recognizes the word "equipment", 
        remains in State 1 and transmits my brag tape file called 
        pk232com.txt. Since the Repeat Flag is a 1, the ELMER will not 
        retransmit pk232com.txt should it once again recognize the word 
        equipment while in State 1.

        Since the ELMER scans sections of the line, the same effect will 
        be achieved if the incoming text had looked like :-


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 153



        "what's an englishman like you 
        doing in this country ?
        The equipment here is ....."

        You can only have 63 lines in any one state machine array. You 
        can define up to 64,000 different states. Each state must be an 
        integer. State 0 is a wild card state. This means that any word 
        in the array coded for state 0 will be matched against the 
        incoming text whichever state the machine is in. The entries in 
        the state machine file must end with a line that contains state 
        666. For example 

        666, end of file

        The number of lines in the array and the current state at the end 
        of each line scanned are shown in the status window.

        3.0 The Stand Alone Version Status Window

        The Status Window provides you with some diagnostic information 
        about the state machine. 

        C:        shows the current state.
        T:        shows the number of states (lines) in the state table.
        ELMER.QSO represents the name of the current state machine.

        4.0 The Stand Alone Menu

        You bring up the menu by touching the "Escape" character. You are 
        then presented with the options shown in Figure 8-4. To activate 
        an option touch the highlighted key.

                              Figure 8-4 ELMER Menu

                                 E Edit Any File    
                                 L Load ELMER.QSO   
                                 P Pick File to edit
                                 S Edit ELMER.QSO   
                                 X eXit to DOS      
                                 * Show State Table 

        4.1 Edit Any File

        This option allows you to edit text files using the LAN-LINK 
        compatible text editor.

        4.2 Load State Table (ELMER.QSO)

        This option allows you to reload the state table, or load a 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 8 Page 154


        different one. If a different state table is loaded, its name 
        will appear in the menu.

        4.3 Pick File to Edit 

        This option allows you to pick a file with the default filetype 
        of "TXT", and edit it.

        4.4 Edit State Table (ELMER.QSO) 

        This option allows you to edit the state table (configuration) 
        file.

        4.5 eXit to DOS       

        This option allows you to exit to DOS.

        4.6 Show State Table  

        This option allows you to see the contents of the state machine. 
        It is used in debugging the logic to ensure that the contents of 
        the table match what you thought you put in.






























        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 155


                      Appendix 9 PCZ Binary file Transfers

        LAN-LINK uses the PCZ public domain external protocol for binary 
        file transfers by shelling to DOS and executing the QZ*.BAT batch 
        files. The QZ*.BAT files are set up for you by the INSTALL 
        program. This appendix contains the documentation for PCZ as 
        supplied by the developers of PCZ, in case you have problems 
        making binary file transfers work in your system.

                      PCZ - A Public Domain implementation
                   Zmodem, Ymodem, Xmodem, Xmodem-1K, Sealink
                              for the IBM PC family

                 PcConnect Zmodem by Drue Kennon and Gary Smith

        PCZ is a public domain Zmodem implementation that will allow  
        users of communication software that does not implement internal 
        Zmodem to access it through an external program. It is a full-
        featured version of Zmodem, but does not have the large volume of 
        bells, whistles & options provided by Omen Tech's DSZ. However, I 
        do believe that it will be suitable for the average demanding 
        BBS'r.

        PCZ provides support for the basic Xmodem variants: Xmodem, 
        Xmodem-1K, Ymodem & SEAlink.

        The following is a description of how to start PCZ for file 
        transfers.

         LEGEND
               Data enclosed in "[" "]" are optional.
               Data enclosed in "<" ">" are required.

         Send Command line:
         PCZ <1-8> <300-19200> [m] [f] [d] [s] <s?> [r] [@]<filespec>

         Recv Command line:

         PCZ <[1-8]> <[300-19200]> [m] [f] [k] [d] [s] <r?> [r]
         [filespec]

         Ref:
                 1-8 - the number 1 - 4, -(8) << PS/2 >>
                 300-19200 - the number 300, 1200, 2400 etc...
                 m - front-end menu option (see MENU)
                 f - enable FOSSIL comm driver routines
                 k - rx keep aborted received files
                 d - disable video memory writes (use dos)
                 s - request enable Super_Z transfer mode (zmodem only)
                 r?,s?  - transfer type sz, rz, sx, rx etc...


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 156


                 r - resume/recover aborted transfer (zmodem only)
                 @ - command file transfer alert flag (SEAlink, Z,Ymodem)
                 filespec - file name w/extension {complete file spec 
                 allowed}     {drive:\path\filename.ext}

        Flags should be placed as shown for standardization purposes. 
        i.e. "f" before "d"; "d" before "k"; "rz,sz" before "r" etc...

        Due to the nature of the beast, no support is provided for a 
        default port & no default port speed is assumed.

        NOTE * See environment variables below for more on default 
        port/speed

        I personally never enter "port" or "speed", but always enter  
        their values. i.e. pcz 1 9600 f sz xxxxxxx.xxx The batch files 
        included reflect this method.

         "ZMODEM RECEIVE"

         << SINGLE >>

         PCZ 1 9600 rz myfile.ext - assume your specified file name.

         << BATCH >>

         PCZ 1 2400 rz - Receive ALL sender files.

         PCZ f d k rz r - Receive ALL sender files
                          assume PCZPORT & PCZSPEED values
                          use FOSSIL routines
                          use standard DOS screen output
                          KEEP all aborted files.
                          RESUME any incomplete previous files.
         one file mode:
         PCZ 1 9600 rz INFILE.ARC - Receives one file and names it
                 INFILE.ARC
         PCZ 1 9600 rz r INFILE.ARC - Recovery effort on file
                 INFILE.ARC

        NOTE * A word about command line switches might be in order here. 
        The switch flags " f, d, k " are global. That is they control PCZ 
        and not any particular protocol. The "r & s" switch is isolated 
        within zmodem, but is applied to both sender and receiver. If you 
        want PCZ's resume code enabled when sending a file then the 
        sender must specify "r" on the command line. Accordingly if the 
        receiver requests resumption of an aborted transfer, the sender 
        must have "r" specified or we won't resume anything. This was 
        requested by BBS Sysops who track download bytes, transfer points 
        etc... Probably so you aren't charged twice or the such like.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 157



         "ZMODEM SEND"

         << SINGLE >>

         PCZ 1 9600 sz OUTFILE.ARC - Send one file to receiver.

         << BATCH >>

        Create a TEXT command file with one complete file spec per line, 
        which includes drive and directory information for each file that 
        is not in the directory PCZ was called from.

         e.g. C:\MYDIR\THISFILE.ZIP

        There is NO limit to the number is allowed. Have no blank lines 
        in the file. Place the "@" symbol as the first character of the 
        filename.

        Pass it to PCZ on the command line as follows:

         PCZ 1 2400 sz @OUTFILE.TXT

        What you name the command file is your business. It simply must 
        be a standard ASCII file with no software or printer control 
        codes present.

        An alternative to creating the command file for sending 2 or 3 
        files may be used. Simply type the file names on the dos command 
        line separating each one with a space.

        Remember the receiver must be set to accept batch uploads or you 
        might be spinning your wheels. Some BBS packages are just now 
        coming on-line with batch upload features using PCZ. They 
        normally indicate (BATCH) if it is supported.

         BBS << BATCH >>

        One method for implementing batch uploads on a bbs is to use the 
        log file and examine the transfer status character. The first 
        character of each line in the log file denotes how the transfer 
        finished. A "1" for good transfer & "0" for a failed transfer.

        Armed with this information, simply setup to call PCZ in batch 
        receive mode. After PCZ has finished and your bbs code has 
        control, open the logfile and read in the line(s) of information. 
        You may now format a string to send the user about the status of 
        each file he/she sent, prompt for a file description etc..

        After you have dealt with each entry in the logfile, simply close 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 158


        the file and delete it. PCZ will create a new file for the next 
        transfer session. If you desire a continuous record of the 
        transfers then you should create your own and append each entry 
        you read from the pczlog to your continuous log file.

        The information below shows exact start positions for each piece 
        of data. The x's denote the length of each element, the first (x) 
        shows start position as PCZ will write it to the log.

        e.g. Below, the file size is 47877. PCZ will always write the 
        file size as a 7 character string which begins at position 21 in 
        the line. Hence, read from pos (21) to pos (27), trim any blanks 
        & convert to decimal value etc..
         Log extract w/char positions:
                  1 2 3 4 5
         1234567890123456789012345678901234567890123456789012345
         x xx xxxxxxxxxxxx xxxxxxx xxxxxx xxxx x
         1 sz PCZ40x.ZIP 47877 @ 2400 bps @ 237 cps 0

             6 7 8
         6789012345678901234567890
                 xxxxxxxxxxxxx
         errors Fri 10/5/1990

         "XMODEM VARIANTS"
        To receive files using any of the Xmodem variants, the format is:

              PCZ <port> <speed> rs filename - SEAlink receive
              PCZ <port> <speed> rs - SEAlink Batch receive
              PCZ <port> <speed> rx filename - Xmodem receive
              PCZ <port> <speed> r1 filename - Xmodem-1K receive
              PCZ <port> <speed> ry filename - Ymodem receive
              PCZ <port> <speed> ry - Ymodem Batch receive

        Remember the "k" option works for all of the receive modes. Hence 
        you can receive a file via SEAlink, have it abort on errors, and 
        then later RESUME the transfer using Zmodem.

        To send files using any of the Xmodem variants, the format is:

              PCZ <port> <speed> sx filename - Xmodem
              PCZ <port> <speed> s1 filename - Xmodem-1K
              PCZ <port> <speed> sy filename - Ymodem *
              PCZ <port> <speed> ss filename - SEAlink *

        * Refer to Zmodem Batch sending for batch transfers via Ymodem 
        and SEAlink

        NOTE: The bytes and cps rate reflect the actual number of bytes 
        sent to, or received from the IOBuffer as a transfer progresses. 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 159


        It does not necessarily reflect any specific "BLOCKSIZE". When 
        sending, as a transfer nears it's end, you will see the cps 
        decline. That's because PCZ uses buffered output vs a simple 
        "sector size" buffer. This will let you see actually how PCZ is 
        progressing in the transmission of data. In the best case "Full 
        Streaming Zmodem", you will see the time for actual file data; 
        worse case time will reflect the transmission of data headers and 
        block acks. It is different, but I hope everyone can appreciate a 
        more accurate account of what is happening inside the powerful 
        zmodem protocol.

        ** : The "Transfer Time" reflects PORT speed, (NOT MODEM) speed! 
        If speed conversion is being used, FORGET the transfer time.
         
         "ENVIRONMENT VARIABLES"

        PCZ supports several environment variables which can make setting 
        up a comm pkg. or BBS more "user friendly". These variables are 
        as follows and should be placed in the autoexec.bat file as I 
        have them shown here or modify the setenv.bat file included to 
        accommodate your system.

        "DRIVE" refers to the letters "A".."Z"

        "YOURDIR" refers to a complete directory specification.
                   i.e. \COMM\ARC\
        "YOUR.FIL" refers to a filename with extension that you want PCZ 
        to use vs it's default name.

         "DIRRX"

        set DIRRX=drive:\yourdir\

        This variable provides the ability for all your received files to 
        be placed in a single location. It is very useful for bbs 
        purposes as well as general comm program usage. If you specify a 
        directory spec on the command line, it will override DIRRX. 
        Therefore you can easily set the variable and then just forget 
        about it. If DIRRX isn't set and no spec. is given on the command 
        line, your receive file will be created in the current active dos 
        directory.

         "PCZLOG"

        set PCZLOG=DRIVE:\YOURDIR\

        In the log file's case, it specifies the directory you want your 
        PCZ.LOG file to be kept in. If "PCZLOG" is not found in the 
        environment then no log file is generated.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 160


         set PCZLOG=DRIVE:\YOURDIR\YOUR.FIL

        As an option to the log file name "PCZ.LOG" you may specify your 
        own filename in the filespec. This provides greater flexibility 
        with some bbs packages such as RBBS which expects it's own naming 
        convention to be used, and for multitasking environments etc... 
        If your "YOUR.FIL" exist, it overrides filename "PCZ.LOG" in all 
        cases.

         "PCZPORT"

         set PCZPORT=(1-8)

        PCZ will use the port number (1-8) as the default port.

         "PCZSPEED"

         set PCZSPEED=(300-19200)

        PCZ will use the speed (300-19200) as the default speed.

        NOTE ** If you specify the PORT or SPEED on the command line, it 
        will override a default set by the environment variables.
         "PCZDIR"

         set PCZDIR=DRIVE:\YOURDIR\

        If you experience any problems with PCZ not being able to access 
        it's overlay file, setting this variable will cure the problem. 
        DRIVE:\YOURDIR\ should point to the directory where you have 
        located PCZ.EXE

         IMPORTANT NOTE:
        NO SPACES are allowed when setting an environment variable!

         i.e. {WRONG}
         set PCZLOG = C:\COMM\ will not work.

         That's not my fault. It is just DOS....

         i.e. {ahhhh}
         set PCZLOG=C:\COMM\

         "PORT & IRQ"

        It has seemingly become necessary, instead of interrupt sharing, 
        to reassign Comm. PORT addresses and use seldom triggered IRQ 
        lines e.g. "5 & 7" to allow multiple "more than two" ports on one 
        machine. Efforts to support this trend have been successful with 
        PCZ. Referring back to our PCZPORT environment variable:


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 161



         set PCZPORT=1

        If you have reassigned your IO card addresses etc..., you can 
        force PCZ to comply with your wishes.

        Lets say you want to use PORT 3 @ 2E8h on irq 5. You set PCZPORT 
        in this manner.

         set PCZPORT=3,2E8,5
                     | | |
                     | | |____ IRQ line number
                     | |_______ PORT address
                     |__________ PORT number

        If you specify an invalid address or one your card isn't set for, 
        then PCZ will simply abort during it's port validation routine. 
        This method should provide the support needed for those who like 
        to match their wits against the cpu's.

         "Super_Z" (tm)

        Always in search for faster from fast. Super_Z takes zmodem to 
        the ragged edge! If you are one of the blessed, and enjoy 
        relatively noise free transmission lines, you should see an 
        increase of 2 to 3 % efficiency. XON/XOFF MUST be disabled and 
        the modem must pass these characters. You may activate Super_Z 
        via the command line switch "s". As is usually the case, Super_Z 
        can be called by the receiver or by the sender. That is to say, 
        that either can flag for Super_Z and if the remote version 
        supports Super_Z, we're doing it.

        Regarding noise, a seldom thought of fact is that just because 
        your local transmission lines are great to one place, someone 
        else's local lines may be the pits. A good example is.... When I 
        log on to the "Corner" from Texas on a "596" extension I rarely 
        ever get a line hit. When I use the "995" extensions I am prone 
        to hits anytime. A reverse situation might occur in your 
        particular area. It simply depends on the quality of any of the 
        many exchanges you might encounter. I can only hope you are one 
        of the lucky ones.

          "NETWORK SUPPORT"

        PCZ has been tested completely in a network environment. It will 
        allow multiple users to read the same file via use of DOS's 
        shareable attribute. It will also lock any files that it is 
        currently writing to. This has been tested using Novell Netware, 
        LAN Manager, and CBIS Network-OS.
         


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 162


         "MENU FRONTEND"

        Many fine programs exist which allow protocol engines to be 
        called from a communications package. In an effort to make PCZ 
        all the more user friendly, there is now a simple menu system 
        built into the program. It is controlled by the file PCZ.CFG 
        which is included in this zip file. Take a few moments to read 
        over it. It may be that it is just what you are looking for in 
        the way of a nice user interface. The design and layout of the 
        system is very simple and straight forward. You control the 
        options and protocols you wish to have active. PCZ.CFG comments 
        explain the various functions you can use. To use the menu system 
        simply call PCZ in the following manner.

         PCZ m

        Make your menu selections and complete the command line with your 
        filespecs.

         "FOSSIL SUPPORT"

        FOSSIL is an acronym for "Fido/Opus/SEAdog Standard Interface 
        Layer". This version of PCZ implements the use of FOSSIL 
        communications support. To date only one, "X00.SYS" driver has 
        been tested to work with PCZ. X00.SYS is a product of Raymond 
        Gwinn. It has proven itself in many environments and I recommend 
        it to you without reservation. X00.SYS was chosen because it 
        provides "FIFO" etc... support for the 16550 UART chip. My 
        internal routines support the chip but not all it's features. 
        Also X00.SYS provides enhanced ability to work in a multitasking 
        environment such as DeskView. If DeskView is active PCZ gives 
        idle processor time back to the cpu for smoother operations. For 
        a brief description of setting up X00.SYS on your system read the 
        enclosed file PCZFOSSL.DOC

        Making use of the driver with PCZ is as simple as adding "f" to 
        the command line. It should be placed after the baudrate in all 
        transfer types.

         i.e. PCZ 1 9600 f sz OUTFILE.ZIP

        When PCZ starts, it will check for the presence of the driver in 
        memory. If it is resident all will proceed as planned. If 
        however, the driver is not in memory, PCZ will gracefully shut 
        down with a message stating this fact. I gave careful thought to 
        jumping to the internal routines, but decided against it for a 
        couple of reasons. In some cases the ports may be scrambled which 
        will surely cause a system lockup on PCZ's part. A problem may 
        exist with the driver you are using, giving false info which 
        PCZ's routines would not like very much. A "dumb" terminal might 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 163


        have charge of things and not want another routine hanging 
        around, etc...

         "PHONE SUPPORT"

        Phone support can be provided when you require it, if you call 
        while I am home. I umpire for our local women's softball league 
        on Mon. & Tues. nights. I play golf on Wed. & Thurs. evenings. 
        Fri. night I do what Maureen tells me to do! Sat. is up for grabs 
        and Sun. morn & evenings I am in church. Please try me sometime 
        other than those mentioned ...... Seriously though, any night 
        (late) will be fine. Just try and make it before 10p.m. CST if 
        possible.

                                      Note from the author:

        Over the last year PCZ has received some very good reviews. More 
        users rely on the program for their transfers now than I thought 
        would ever be interested. For this I am especially grateful and 
        would thank each one if possible. Gary & I will continue to grow 
        with the needs of the BBS community. We ask for your continued 
        input and support, with our assurance that your IDEAS, "cheers & 
        jeers" are taken with sincerity.
                            Thanks
                            Drue

            History
            -------

         V1.01.88 - Initial release, no known bugs. Please report any 
        problems to Drue Kennon.

         V2.01.89 - Extended version that contains Xmodem, Xmodem-1K, 
        Sealink, and Ymodem Batch in addition to Zmodem. Also provides 
        full file sharing for use in networking environments.

         V2.11.89 - Fixed several reported bugs. Enabled hardware flow 
        control for use with MNP type modems. Enhanced port speeds up to 
        19.2k, and tightened some code for more efficient operation. 
        Properly set errorlevel 1 in event of transfer failure.

         V3.03.90 - Fixed a problem with SEAlink xfers not seeing the 
        last EOT. Batch sending for SEAlink per request. Enhanced some 
        screen data writes.

         V3.06.90 - Fixed a problem with SEAlink xfers created by making 
        the last fix. Zmodem command file name can't be fouled due to 
        misunderstanding the docs.

         NOTE:


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 164


        Unless forced into it by the users, I do not plan to support 7 
        bit data transfers. Nor can I figure why any IBM machined BBS 
        would? Did I miss something along the way?

         V3.08.90 - Got with the program and added support for FOSSIL 
        driver. e.g. Gwinn's Communications Controller, X00.SYS add "f" 
        to cmd line params for fossil). Removed internal support for 
        default port and speed which caused problems for multitaskers. 
        Defaults are now specified through environment variables. Added 
        environment variable for default receive dir. Reinstated environ-
        ment variable for pcz log file.

         V3.09.90 - By popular demand, namely "Gary", I added yet another 
        multitasker enhancement. Since the cpu is much faster than the 
        port, idle time occurs during output. This time is now "given 
        back" to the cpu, allowing the "other side" to operate smoother 
        and more efficiently.

         V3.10.90 - Some users mentioned that PCZ would wait forever in a 
        transfer if the carrier was lost. I couldn't dupe the problem, 
        but added several more checks nonetheless. The logfile has 
        changed so that you may specify a full filespec. including 
        filename for you logfile in the env. var. The first char of each 
        line in the file represents pass or fail. "0" = failed xfer "1" = 
        good xfer. Keep those cards and letters coming!

         V3.11.90 - ArrrrG! %#^^#%%@#*$(%*#$%($$%&*( the &*&^*&^ woes of 
        changes really &#$^& my &(&^#$.

         V3.12.90 - Forget 3.11.90 ever existed! Several routines got a 
        face lift! You should see more efficiency with this release. I 
        can't begin to go through the entire chase with you here, but I 
        need a new can of RAID! Seems there is never a total end with a 
        bug problem, in programming as well as the home! I must offer a 
        special word of thanks to Dick Melville from San Marino for his 
        the help with RBBS interface problems. Dick was an excellent BETA 
        Buster! And to Steve Clancy who finally helped me see there was 
        NO carrier on the line!

         V4.00.90 - {BETA} Version 4.00 represents a major revision 
        change to PCZ. As you have noticed, if you've used prior 
        versions, there are two PCZ files now instead of one. PCZ.EXE is 
        the global executable file and PCZ.OVR contains the actual 
        protocol functions. The decision to go with overlay functions was 
        made due to the fact that more Sysops are using PCZ with their 
        BBS's in a multitasking environment. Memory usage has been 
        drastically reduced. Additionally, each transfer type function 
        i.e. "sz,sx(1),ss,sy" & "rz,rx(1),rs,ry" is totally self 
        contained which simply means once the program loads and a 
        transfer type is called, no other overlay read is needed. The 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 165


        function completes and exits. Simply put; execution time has been 
        enhanced.

         V4.01.90 - {BETA} Dick & Steve
         V4.02.90 - {BETA} Dick & Steve
         V4.03.90 - {BETA} PcConnect, Dick & Steve
         V4.04.90 - {BETA} PcConnect
         V4.05.90 - Major revision V4.xx.90 released on the world!
         V4.06.90 - Some enhancements added here include; Super_Z (tm) by 
        PCý, offers enhanced transfer times when used with error  
        correcting modems and relatively noise free transmission lines. 
        No limit to the number of files allowed in a batch transfer 
        command file. Non-standard PORT, IRQ line assignments supported 
        via environment setup. Frontend menu system for comm package use. 
        PCZ is supplied as a ".EXE" file which when executed breaks it's 
        code out into overlays. The largest executable code segment will 
        run well inside of a 64k memory segment.

        Personal contact may be made by one of the following methods.

         Drue Kennon Gary J. Smith
         Rural Route #2 Box 54 6122 Cedar Wood Drive
         Center, TX. 75935 Columbia, MD 21044
         Voice 409-598-3809

                            The Programmer's Corner
               Home of
         "PcConnect" & "PCZ"

         Data/BBS: 301-596-1180 Data/BBS: 301-995-3744
                         Data/BBS: 301-621-4636

                           10 roll over lines in place
                           with over 1.5 gigabytes of
                           storage space

        DSZ, ZCOMM, Professional-YAM are Copyrights of Omen Technology 
        Inc, all rights reserved.

        X00.SYS Copyright (c) by Raymond L. Gwinn, All Rights Reserved.

        PCZ Copyright (c) by Drue Kennon, All Rights Reserved. 
        Super_Z(tm) is a trademark of PCý

        ** If you are the author of a communications package that has 
        zmodem implemented internally and would like to enable Super_Z in 
        you program for PCZ compatibility, look over SuperZ.Doc. If you 
        have any questions or problems then just drop me a line or call 
        and we will be glad to help you out.
         


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 166


                          The PCZ Menu Transfer System

        This is the PCZ.CFG file.

        ;To make use of this transfer menu system PCZ should be called in 
        the following manner.

        ;PCZ m <ENTER>

        ;We assume in this config file that you are using SETENV.BAT to 
        preset your PCZ parameters for PORT and SPEED. If this isn't the 
        case then simply add them on the protocol lines below in their 
        proper place. You should be able to see from the listings the 
        format used here. i.e.
        ;SEND    without the ";" begins send protocol block
        ;END     without the ";" end the protocol block

        ;The protocol goes on a line followed by the ":" char followed by 
        PCZ's command line options for that protocol. You will be 
        prompted to complete the command line with your filespec(s) once 
        the program is started etc... pretty simple huh?

        ;Simple yes! but simple minded as well, and if you fail to follow 
        these guidelines.... who knows what type of protocol you might be 
        trying to use for a transfer. Just to satisfy your cats curiosity 
        you may uncomment the first line after SEND. Run PCZ using "m" 
        menu option, select upload and see what happens. No your pc won't 
        bark but it might barf if you select "A" as your protocol type.

        ;The following represent the send parameters. Using the ";" at 
        the beginning on a line comment out any protocol you do not wish 
        to use during you file transfer sessions.

        SEND
        ;flag for beginning of send protocols

        ;TOSSIT:  sp  ;This is a curiosity test line

        ;XMODEM:  sx
        ;send a file using xmodem

        ;X1K:     s1
        ;send a file using xmodem 1k blocks

        ;YMODEM:  sy
        ;send a file using ymodem with file header information

        ZMODEM:  s sz
        ;send a file using Super_Z zmodem



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        APPENDIX 9 PCZ 4.06.90 Nov. 27, 1990 Page 167


        SEALINK: ss
        ;send a file using sealink

        END
        ;end of send protocols

        :The following represent the receive parameters.

        RECEIVE
        ;flag for beginning of receive protocols

        ;XMODEM:  rx
        ;recv a file using xmodem

        ;X1K:     r1
        ;recv a file using xmodem 1k blocks

        ;YMODEM:  ry
        ;recv a file using ymodem with file header information

        ZMODEM:  s rz
        ;recv a file using Super_Z zmodem

        SEALINK: rs
        ;recv a file using sealink

        END
        ;end of receive protocols

        ;You may add any of the other command line switches you wish to 
        the above. They are

        ; "f" use FOSSIL
        ; "d" no direct screen writes
        ; "k" keep all aborted downloads

        ;Thanks and have fun!















        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ, Page 168


              Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ

        1.0 PC-HAM 3.52

        PC-Ham contains the following suite of programs.

        1.1 LOGBOOK

        Full blown logging package. With automatic check of logs for 
        awards such as DXCC. Allows you to recall any entry by call sign 
        within seconds. Indexed displays, QSLing, Contest mode QSLing 
        (prints the lot) and lots more. Although written in dBASE3 the 
        package contains a compiled version (LOGBOOK.EXE), so you don't 
        need dBASE to run it. The source code is ONLY given to registered 
        users. It can convert your exported LAN-LINK.LOG file to LAN- 
        LINK.DBF to put this package to work. Ideal for DX-peditions or 
        for DX robot users to handle QSLing and log statistics.

        1.2 CONTEST

        Keeps Dupes in memory, logs QSO's to disk in format which can be 
        processed by the LOGBOOK package. Now compiled in Turbo BASIC, 
        source code is supplied so that you can modify the program to 
        meet your requirements.

        1.3 CQSS

        Sweepstakes game compiled in Turbo BASIC. Work the ARRL 
        Sweepstakes contest on your computer. You are located just 
        outside Washington DC. A propagation model is built in to the 
        program. This program is REQUIRED training for all sweepstakes 
        operators. Earlier version of the program is described in detail 
        in Software for Amateur Radio by Joe Kasser G3ZCZ, published by 
        TAB Books, Blue Ridge Summit, PA. 17214.

        1.4 WHATSON

        Predict HF Propagation for given days. Contest mode with printout 
        to whole world at hourly intervals. Needs BASIC.

        2.0 STARTREK The Computer Program

        An ideal task for the beginner to learn a language on, is a 
        simulation game which is written to run on a computer that the 
        beginner has access to. For in that case, there is complete 
        control of all inputs and outputs. This kind of game (in which 
        the player makes decisions based on the information available to 
        him or her available at the time), can be made sufficiently 
        sophisticated and complex so as to make writing it an adequate 
        challenge for anybody.


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ, Page 169



        The techniques used in writing a good game are the same that 
        programmers use in professional activities. Writing a good game 
        poses a challenge that allows you to develop good habits and 
        techniques for programming and also allows you to learn a 
        language in an interesting manner. By taking an orderly approach 
        to the game design, complex operations may be clearly understood 
        and converted to computer code with the aid of a language 
        reference manual, irrespective of the language being used.

        This product teaches the techniques for writing such a game using 
        the STARTREK game as an example, and the BASIC language as the 
        programming language in which to write the code.

        Registration fees.

        Single Copy $15.00
        10 - 50        Copies $12.00 per registered copy.
        50 - 100       Copies $10.00 per registered copy.
        100 +          Copies $8.00 per registered copy.

        3.0 WHATS-UP 1.30

        WHATS-UP is a tool for experimenting with orbital dynamics and 
        Telemetry Decoding and display Program for the UoSAT-OSCAR 2, 
        AMSAT-OSCAR 13, Fuji-OSCAR 20 and the AMSAT Microsat Spacecraft 
        (OSCARs 16, 17, 18 and 19). It is table driven via the 
        configuration files to allow maximum flexibility.

        WHATS-UP contains the following features:
        Can beacon [APRS] and/or automatically attempt a connect to 
        MIR/SAREX: Can automatically set Kenwood Radios to spacecraft 
        beacon frequency when satellite comes over your horizon: Can 
        automatically read the frequency from Kenwood Radios to a disk 
        file for Doppler frequency measurements: Can automatically 
        configure a PK-232 for each spacecraft data format: Reads 2 Line 
        and AMSAT format orbit element data files: Provides antenna 
        azimuth and elevation pointing data: Real time, Playback and Dumb 
        Terminal mode: Automatic logging of AOS in LAN-LINK compatible 
        logs for AOS time analysis: Automatic Capture-to-disk of raw 
        telemetry. Extracts telemetry channel data to a database or 
        spreadsheet readable file for further analysis: Link quality 
        measurement on packet telemetry: 

        Capability to print the raw telemetry as it is received: Up to 16 
        user configurable display pages (screens): You set the position 
        on the page (width of engineering unit field, and number of 
        decimal places) that a parameter is displayed at: Wild card page 
        (parameter shows up on all pages): Selectable display of 
        Engineering units or raw byte for each display page: Display of 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ, Page 170


        raw packets (i.e. STATUS) Color changes if a parameter value 
        changed between successive frames: Audio and visual alarms if a 
        telemetry value exceeds, falls below or falls outside a preset 
        limit value(s): Dumb split screen terminal mode (in the manner of 
        LAN-LINK): Customizable colors, PC to TNC baud rate, data parity 
        and stop bits: Default spacecraft configuration files: Time of 
        day clock display (in HH:MM:SS format). Real time analysis 
        requires a receiver and demodulator. Analysis of playback data 
        can be performed with just the computer and WHATS-UP. 

        If you would like a copy of WHATS-UP and have captured any 
        telemetry to disk, especially daytime or southern hemisphere 
        passes, please put them on a disk and send it in with your 
        request, a mailer and return postage. Don't let the individual 
        data files become too long. I suggest that you rename them every 
        day in the format YYMMDD.SC, such as 900824.D17, 900824.F20, etc.

        IF YOU ARE INTERESTED IN OSCAR AND SPACECRAFT TELEMETRY, THEN 
        THIS PROGRAM IS A MUST.

        4.0 ELMER 1.00

        ELMER is an Expert System Based on a Finite State Machine. There 
        are two versions of ELMER supplied with LAN-LINK. One is built in 
        for use in packet mode communications, when connected to someone 
        else. The second version is a stand alone version for use in 
        developing the text files and the logic. The stand alone version 
        lets you program and debug your own personal ELMER by yourself. 
        The stand alone version is a separate product and requires 
        separate registration.

        5.0 BASIC PACKET RADIO

        Basic Packet Radio explains how the computer can be used to 
        smarten up your use of packet. Not only does the book explain 
        packet radio, it comes with a full feature version of LAN-LINK 
        (for the PC) on disk and contains the manual for the program.

               The topics covered in the book are outlined below.

        Getting Started in Packet Radio, What Packet Radio Is, The Shared 
        Radio Channel, The Virtual Channel, The Equipment Needed to Hold 
        a Packet QSO, The TNC, TNC Modes, The Terminal Program.

        Connecting the PC to the TNC, Command Convention, Making the PC 
        Communicate with the TNC, Determining and Changing the State of a 
        Parameter, Setting the Carriage Returns and Line Feed Display 
        Controls, Flow Control, Connecting the TNC to the Radio, Delays 
        in the Transceiver.



        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 10 Other Products by Joe Kasser, W3/G3ZCZ, Page 171


        The Local Area Network, How TNCs Communicate, Controlling the 
        Display of Monitored Packets, Setting Your TNC to Display or 
        Ignore Packets, The Wireless LAN, Use of Packet Beacons, The 
        Alert Call, The Target Call, LAN Answering Machine, Mail Beacon 
        (Annunciator), Remote Beacon Shutdown.

        Connecting to Someone, Connecting to Other Stations the LAN-LINK 
        Way, The Point and Shoot (MH List) Way, Using the Call Menu, Loop 
        Backs, Names, Handles and Paths, Connecting via NET/ROM and 
        TheNet, Connecting via KA-Nodes, The SAREX Call and Working MIR.

        Extending the Range, Digipeating, Using NET/ROM and TheNet Nodes, 
        Using G8BPQ Nodes, Using KA-Nodes, Using MSYS Nodes, Using ROSE 
        Switches, Using LAN-LINK to Communicate via Nodes, Path 
        Determination to a DX Station, Finding Packet Signals, Using 
        Communication Satellites.

        The Packet Bulletin Board System, How to Connect to the PBBS, 
        Connected to the PBBS, Connected, But What Next ?, Telling it 
        Your Name, Getting Information about the PBBS Itself, The Command 
        Prompt Line, Changing the Prompt Line, Listing the Messages and 
        Bulletins, Reading Messages, Sending Messages, Sending Messages 
        Around the World, Sending a Bulletin, Forwarding Bulletins, 
        Sending NTS Traffic, The Parts of the NTS Message, Killing 
        Messages, Using LAN-LINK to Send NTS Traffic, Handling NTS 
        Traffic, Files, Talk to the SYSOP, Connecting Elsewhere via the 
        PBBS, Obtaining On-Line Help, Logging Off the PBBS, The F6FBB 
        PBBS Features, Automating Message Reading, Message Headers.

        The PacketCluster, Summary of commands and features, Smartening 
        Up PacketCluster Access With LAN-LINK.

        Other Applications of Packet, Data Base Servers, Using a REQFIL 
        Server, Using a REQDIR Server, Using a REQQTH Server, Electronic 
        Newspapers, Non Real-Time QSOs, Automatic Beacons, Robots and 
        Contests, Propagation Research, Transmission Control 
        Protocol/Internet Protocol (TCP/IP).

        This is a book to read once, then use as a reference over and 
        over again. If you decide you don't like the book, send it back 
        within 30 days for a swift refund.











        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 11 Page 172


                     Appendix 11 How Shareware Works

        The Association of Shareware Professionals (ASP) has established 
        standards for its members and for any organization which has "ASP 
        Approved" status. The ASP wants to make sure the shareware 
        principle works for you. If you are unable to resolve a problem 
        with an ASP member or organization (other than technical 
        support), the ASP may be able to help. Please write to 

                       The ASP Ombudsman, 545 Grover Road, 
                         Muskegon, MI. 49442-9427, USA.

        You are encouraged to copy the floppy disk and share it freely 
        with others. You have the luxury of trying out the product at 
        your own pace and in the comfort of your own home or workplace. 

        After you have used the material for a reasonable evaluation 
        period (30 days), you should either discontinue use of the 
        material or register your copy. Your support is important and 
        greatly appreciated. With it, Shareware authors are encouraged to 
        design and distribute new products. Without it, a great deal of 
        high quality, low cost software will cease to be available.

                                 Why pay at all?

        You receive support from the author. You receive a CURRENT copy 
        of the program. Your input and ideas help shape future products. 
        You have a sense of pride and ownership in having honestly 
        participated in the Shareware revolution. You help to keep 
        software prices down by supporting a distribution method which 
        doesn't depend on expensive advertising campaigns.

        Be aware of the following restrictions, designed to protect the 
        community of Shareware users and to prevent greedy people from 
        taking unfair advantage of the trust, hard work and good will of 
        Shareware authors. 

        1. No price or consideration may be charged for the material. 
           However, a distribution cost may be charged for the cost of 
           the diskettes, shipping and handling, not to exceed $6.

        2. The files and programs on the disks may not be modified or 
           deleted.

        3. The material cannot be sold as part of some other more 
           inclusive package.

        4. The material cannot be "rented" or "leased" to others.

        5. The end user must be told clearly in writing on the outside of 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 11 Page 173


           the package and in all advertising that the diskette(s) are 
           "Shareware."

        6. The package must contain a written explanation that the disk 
           is for evaluation purposes, and that an additional 
           "registration fee" is expected by the author, if the material 
           is used beyond an initial evaluation period.

        7. In the case of distribution via any telecommunications link, 
           the following must be done:
           * An error checking protocol must be used.
           * The individual files must be combined into, and transferred 
             in a library or archive format. 

        8. Shareware distribution is permitted only in the United States, 
           Canada, England, and Australia.




































        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Appendix 12 Page 174


                   Appendix 12 LAN-LINK 2.32 REGISTRATION FORM

        PLEASE COPY this form and MAIL to

        Joe Kasser G3ZCZ, P.O. BOX 3419, SILVER SPRING, MD 20918.

        CALL ________________ TODAY'S DATE ________________
        NAME ______________________________________________
        ADDRESS ___________________________________________
        ___________________________________________________
        CITY ______________________________________________
        STATE _________ POSTCODE ____________ TNC TYPE_____
        FIRMWARE REV ____ HOME BBS ______________
        DISK SIZE 5.25 _____ 3.5 ____ 

        Please register me as a user of LAN-LINK. I am currently using 
        LAN-LINK Version ______ which I obtained from _______. Please 
        send me the latest version of LAN-LINK or if a more recent one 
        does not exist at this time, QSL my registration and add my name 
        to the list to receive a free update when it becomes available.

        I also enclose an additional amount for evaluation copies of 
        ELMER _, WHATS-UP _, PC-HAM _ and Startrek TCP _ ($5 for 1 
        program, $15.00 for the set). If I like them, I plan to register 
        them in due course. 

        Basic Packet Radio Book (29.95)                   __.__
        Shipping for book $3.50 US/Canada, $6.00 overseas __.__
        LAN-LINK Registration ($45.00)                    __.__
        ELMER Registration ($45.00)                       __.__
        Evaluation software                               __.__
        ____________________________________
              Maryland Residents please add 5% sales tax. __.__

        Total Enclosed                                    __.__    

        MasterCard/Visa Number ___________________________Expires __/__

        My favorite operating modes are ________________________.

        Many additions come into LAN-LINK as a result of user 
        suggestions, so here's your chance to get some input in. Write 
        them on this piece of paper.









        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 175


                                INDEX

        Accessible, 125
        AFSK, 74
        Alarmwindow, 90, 151
        Alt-A, 2, 19, 59
        Alt-B, 2, 19
        Alt-C, 2, 9, 19, 60, 101
        Alt-D, 2, 21, 45, 77, 97, 108, 138
        Alt-E, 2, 19, 22, 60
        Alt-F, 2, 22, 32, 125
        Alt-F, 50
        Alt-G, 13
        Alt-H, 2, 22, 60
        Alt-J, 2, 22
        Alt-K, 2, 22, 37, 38
        Alt-L, 2, 22, 79
        Alt-M, 2, 15, 22, 78
        Alt-N, 2, 23, 101
        Alt-O, 2, 23, 69, 79
        Alt-P, 2, 23
        Alt-Q, 2, 23, 36
        Alt-R, 2, 23
        Alt-S, 2, 24, 60, 79
        Alt-U, 60
        Alt-W, 2, 24, 53, 134, 144
        Alt-X, 2, 8, 24, 61
        Alt-Y, 2, 12, 24
        Alt-Z, 2, 24, 37
        AMTOR, 2, 3,  7, 10, 3, 4, 5, 6, 12, 14, 16, 17, 19, 20, 21,  22, 
                 23, 26, 28, 30, 31, 32, 33, 39, 40, 47, 50, 54, 55,  56, 
                 72,  73,  76, 79, 82, 83, 87, 91, 94, 95, 96,  97,  103, 
                 104, 119, 125, 129, 134, 135, 138, 140, 144
        AMTOR-FEC, 16
        Announce, 111
        Announcements, 12
        Annunciator, 2, 5, 14, 111, 171
        Anomalies, 10, 140
        ANSI, 2, 6, 13, 50, 66, 144
        AOS, 169
        APLINK, 19, 87
        APRS, 169
        ARQ, 2, 19, 20, 21, 22, 30, 94
        ASCII, 5, 7,  9, 3, 4, 5, 6, 10, 15, 16, 20, 26, 28, 41, 49,  51, 
                 52,  96,  106, 115, 116, 123, 124, 125, 126,  129,  130, 
                 133, 134, 138, 148, 157
        ASP, 172
        Attempt, 15,  19, 21, 30, 39, 41, 47, 54, 69, 77, 80,  134,  138, 
                 140, 169
        Audio, 4, 76, 79, 87, 88, 170


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 176


        Auto, 3, 4, 8, 30, 35, 39, 40, 41, 94, 108, 114, 117, 127
        AUTO-Upload, 124
        AUTOCQ, 14, 17, 94
        AutoCR, 85, 86
        Autoexec, 159

        Battery, 8, 9, 64, 65
        BAUDOT, 7,  8, 3, 4, 6, 11, 16, 17, 20, 26, 27, 28, 50,  63,  75, 
                 95, 96, 104, 105, 114, 119, 125
        BBS, 1, 8, 9, 10, 2, 5, 6, 7, 11, 20, 22, 24, 25, 26, 41, 44, 46, 
                 62,  66, 72, 93, 94, 112, 114, 118, 124, 128, 130,  131, 
                 138, 142, 144, 156, 157, 159, 160, 163, 164, 165, 174
        BPQ, 171
        BTEXT, 14, 77
        Bulletin, 7, 16, 65, 82, 93, 113, 129, 171

        Callsigns, 6, 30, 59, 60, 71, 72, 79, 82, 83, 126, 135, 140
        Capture-to-disk,  4, 6, 11, 16, 27, 29, 42, 44, 45, 48,  49,  50, 
                 69,  72, 73, 81, 83, 92, 103, 104, 106, 107,  113,  118, 
                 122, 139, 169
        CFROM, 86, 109
        Checked, 12, 13
        Chirpcopy, 6, 32, 97
        Client-server, 14
        CLOCK, 4, 10, 34, 46, 47, 64, 72, 74, 80, 89, 141, 170
        Cluster, 8, 6, 12, 39, 87, 88, 94, 114, 119
        CMSG, 70, 71, 73, 86
        Colorized, 144
        COMMENTS, 55, 56, 59, 60, 122, 125, 162
        Compares, 121
        CONFIG, 9, 112, 123, 166
        CONOK, 71, 86, 109
        Contest, 4,  5, 6, 5, 6, 12, 13, 17, 23, 38, 46, 47, 56, 57,  58, 
                 72, 79, 80, 116, 144, 168
        Control-C, 42
        Control-F, 125
        Control-Q, 142
        Control-S, 142
        Control-Z, 3, 28, 54, 125, 128
        CONVERSE, 3, 10, 3, 24, 32, 52, 53, 65, 74, 75, 76, 78, 101, 102, 
                 103, 130, 140
        CQ, 3, 4, 6,  10, 6, 14, 17, 18, 19, 22, 30, 31, 32, 35, 39,  40, 
                 41, 67, 69, 72, 84, 85, 94, 99, 100, 103, 104, 106, 112, 
                 113, 118, 135, 137, 138, 140
        CQs, 6
        CQTEXT, 84
        CR, 13, 95, 105
        Ctdsk, 4, 8, 42, 44, 48, 49, 50, 72, 118
        CTEXT, 6, 7,  6, 63, 64, 65, 70, 71, 73, 95, 112, 115, 127,  130, 
                 144


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 177


        CW, 3, 7, 8,  10,  20, 27, 28, 36, 38, 74, 75, 88, 96,  97,  103, 
                 104,  105, 106, 107, 108, 111, 114, 118, 119, 122,  125, 
                 139, 144
        CWID, 104

        Date-time-text, 28, 54, 136
        Daytime, 170
        DBASE, 5, 11, 55, 57, 58, 60, 122, 168
        DCD, 6, 72, 80, 102, 113, 138, 139, 141, 142
        DCD-Flag, 141
        DCDCONN, 102
        DEmo, 4, 5, 42, 46, 51, 52, 55, 127, 144
        Demonstration, 127
        Demonstrations, 127
        Digipeat, 5, 6, 18, 23, 69, 72, 74, 82, 83, 99, 122, 130, 138
        Digipeater, 77, 82, 86, 109
        Directory,  3, 4, 10, 5, 14, 21, 39, 40, 44, 45, 48, 49, 51,  62, 
                 77, 83, 84, 113, 115, 122, 130, 150, 157, 159, 160
        Directs, 119
        Disconnect,  2, 3, 7, 4, 6, 14, 18, 20, 21, 23, 26, 29,  31,  32, 
                 65, 72, 77, 81, 85, 94, 95, 102, 117, 118, 129, 141, 144
        DMO, 4, 9, 42, 46, 112, 127
        Downlink, 67
        Download, 3,  9, 5, 11, 14, 24, 25, 26, 36, 37, 52, 54,  83,  84, 
                 104, 113, 124, 129, 130, 132, 133, 136, 156
        Dropouts, 117
        DSP, 5, 10, 3, 9, 55, 63, 64, 66, 67, 74, 104, 119, 120, 139, 144
        DSZ, 155, 165
        Dual, 5, 8, 55, 63, 114, 119, 139
        Duplex, 6, 3, 4, 67
        Duplicates, 79

        Echo, 6, 29, 31, 72, 76, 91, 122, 138
        Echo-As-Sent, 138
        Editor, 5,  10,  15, 29, 41, 42, 43, 48, 62, 70, 103,  115,  123, 
                 133, 148, 149, 153
        ELMER, 7, 8, 9, 10, 11, 5, 18, 34, 109, 110, 112, 113, 115,  116, 
                 127,  144, 145, 146, 148, 149, 150, 151, 152, 153,  154, 
                 170, 174
        Ended, 74
        Ensures, 74
        EOF, 28, 44, 54, 124, 125, 128, 135
        Equipped, 111
        EVENT, 4, 5, 23, 25, 31, 34, 46, 47, 55, 65, 68, 73, 81, 82,  83, 
                 95, 103, 129, 133, 136, 144, 163
        EXpand, 4, 8, 48, 50, 113, 116
        Expires, 174

        Faked, 74
        FEC, 3, 10, 6, 20, 22, 23, 30, 32, 40, 104, 140


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 178


        Flashing, 16, 17, 18, 19, 27, 40, 41, 69, 72, 73, 79, 92
        FSK, 27, 74
        Fuji, 8, 114, 120
        Fuji-OSCAR, 67, 169
        FULLDUPLEX, 67

        G-TOR, 7, 13, 14, 20, 56, 72, 95, 96, 98, 125, 144
        Garbage, 10, 117, 142
        Gateway, 135
        Grab, 13, 20
        Greek, 10, 8, 89, 142

        Header, 5, 25, 40, 62, 68, 80, 91, 102, 129, 134, 137, 138,  166, 
                 167
        HEADERLN, 122
        Huffman, 108, 109

        Icom, 120, 121, 144
        Incoming, 2, 4, 10, 5, 6, 9, 13, 15, 16, 25, 26, 27, 29, 31,  32, 
                 37, 39, 42, 44, 46, 50, 55, 62, 64, 65, 66, 69, 71,  74, 
                 76, 77, 89, 90, 91, 92, 94, 95, 102, 103, 106, 107, 108, 
                 116,  118, 119, 122, 126, 127, 138, 140, 142, 145,  152, 
                 153
        Interrogated, 110
        Interrogates, 66
        IRQ, 7, 88, 113, 115, 160, 161, 165

        KA-Node, 5, 21, 122, 123
        KAM, 9, 3, 9, 28, 31, 67, 75, 80, 83, 87, 89, 94, 96, 97, 98, 99, 
                 100, 105, 107, 108, 116, 118, 122, 138, 140, 142, 144
        KM, 94, 118
        KN, 26, 27, 79
        KPC, 9, 3, 65, 137

        Larger, 41
        LF, 13, 95, 105
        LFADD, 75
        LM, 25, 118, 124, 125
        Log-to-disk, 72
        Logcheck, 12

        Mail-Snatch, 25, 81, 138
        Marks, 122
        MARS, 6, 17, 95, 105, 144
        MBX, 9, 53, 109, 112, 123, 124, 135
        MCON, 99
        Metabeacon, 70, 71, 72, 102, 103
        Meter, 12
        MFILTER, 142, 143
        MFJ, 9, 10,  3, 9, 31, 63, 67, 75, 76, 83, 89, 94, 96,  97,  118, 


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 179


                 137, 138, 144
        MH, 3, 30, 53, 72, 90, 130, 134, 137, 138, 144, 171
        MHwindow, 30, 90
        Milliseconds, 120
        MIR, 6, 67, 68, 69, 169, 171
        MRPT, 40
        Multi-connect, 5, 32, 65, 100, 142
        Multi-mode, 3, 7, 118
        Multi-stream, 23
        Multi-user, 25, 41, 100
        MYCALL, 104, 106, 107

        NAVTEX, 7, 16, 96, 98, 144
        NET, 5, 21, 122, 123, 125, 142, 171
        NNNN, 94, 104, 105, 106, 107
        Node, 6, 3, 9, 12, 72, 75, 77, 113, 118
        NTS, 41, 171

        Outwindow, 48, 89, 140, 150
        Overseas, 174

        PacketCluster, 2, 3, 8, 4, 7, 12, 17, 20, 22, 24, 36, 37, 51, 72, 
                 83, 87, 98, 111, 113, 114, 116, 119, 121, 144, 171
        PACTOR, 7,  3, 4, 5, 6, 11, 12, 13, 14, 20, 26, 50, 55,  56,  72, 
                 94, 95, 96, 97, 108, 125, 139, 144
        PBBSs, 81
        PCý, 165
        PCZ, 9, 11,  127,  132, 133, 143, 155, 156, 157, 158,  159,  160, 
                 161, 162, 163, 164, 165, 166
        PCZDIR, 160
        PCZPORT, 156, 160, 161
        PCZSPEED, 156, 160
        PgDn, 42, 45, 59, 61, 62
        PgUp, 2, 27, 42, 59, 61
        Post, 13
        Prematurely, 74
        Presupposes, 74
        Printer, 2, 6, 8, 16, 20, 23, 58, 72, 77, 114, 117, 144, 157
        PromptWindow, 90, 150
        PSK, 120

        QBM, 5, 9, 51, 52, 83, 113, 129, 130, 133, 134
        QBU, 5, 9, 51, 52, 84, 113, 126, 133, 136
        QBU-RX, 9, 51, 52, 84, 112, 113, 126, 133
        QBU-TX, 9, 51, 52, 84, 112, 113, 126, 133
        QDB, 5, 9, 51, 52, 94, 130, 134
        QIC, 5, 8, 9, 51, 52, 114, 119, 136, 144
        QJG, 9, 53, 135
        QMH, 5, 9, 5, 51, 53, 130, 131, 134, 137, 144
        QNO, 9, 52, 54, 78, 94, 129, 134, 135


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 180


        QQQ, 94
        QRA, 2, 5, 9, 20, 24, 53, 134
        QRM, 3, 31, 68, 73, 134
        QRT, 9, 17, 52, 54, 68, 73, 86, 109, 113, 134, 135, 136
        QRU, 5, 9, 51, 53, 94, 123, 124, 134, 135
        QRV, 9, 52, 54, 94, 128, 135
        QRX, 52, 136
        QRZ, 2, 3, 20, 23, 35, 36, 70, 72
        QSL, 9, 52, 54, 55, 60, 68, 70, 72, 94, 129, 135, 174
        QSM, 5, 9, 15, 51, 53, 126, 134
        QSO, 7, 9, 10, 11, 4, 5, 14, 17, 19, 22, 23, 29, 32, 47, 51,  71, 
                 73,  79,  80, 94, 95, 97, 99, 104, 106, 109,  110,  112, 
                 127, 140, 144, 145, 150, 152, 153, 154, 170
        QSP, 5, 6, 9, 17, 51, 54, 55, 72, 78, 112, 124, 128, 134, 135
        QSY, 7, 8, 4, 13, 68, 73, 110, 111, 114, 121
        QTA, 5, 9, 51, 54, 112, 126, 129, 135
        QTC, 6, 9, 5, 14, 15, 17, 72, 73, 77, 78, 81, 94, 113, 135
        QTC-Snatch, 15, 78, 138
        QTR, 5, 9, 51, 54, 136, 144
        QYU, 51
        QZD, 5, 9, 51, 54, 126, 132, 133, 136
        QZD-RX, 126, 133
        QZD-TX, 126, 133
        QZU, 5, 9, 51, 55, 126, 132, 133, 136
        QZU-RX, 126, 127, 133
        QZU-TX, 126, 133

        Random, 27, 119
        Receive-Disconnect, 3, 4
        REQDIR, 171
        REQFIL, 171
        REQQTH, 171
        Reregister, 11
        Results, 12
        Retry, 2, 20, 22, 23, 67
        Reverse, 27, 134, 161
        Robot, 2, 4, 14, 17, 18, 19, 20, 23, 46, 47, 69, 70, 71, 72,  73, 
                 103, 104, 168
        Robot-Mailbox, 31
        RTTY, 2, 7, 8, 6, 17, 24, 26, 28, 31, 74, 96, 106, 114, 120, 138
        RY, 2, 24, 158, 164, 167

        SAREX, 6, 17, 18, 67, 68, 69, 70, 71, 72, 92, 113, 169, 171
        Scrollback, 2, 13, 27, 90
        SELCAL, 6,  7,  17, 19, 20, 21, 22, 23, 32, 39, 40, 82,  83,  94, 
                 103, 105, 106, 107, 112
        Separates, 119
        Simulate, 55
        Simultaneous, 63, 120
        SOLO, 18, 75, 86, 99, 118


        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994

        Index Page 181


        Speak, 7, 110, 111
        Spot, 20
        Spotted, 98
        SSID, 83, 126
        State-sequence, 93
        StatusWindow, 90
        Staying, 74
        Stopbits, 8
        Subdirectory, 41
        Supply, 111

        Target, 4, 5, 6, 17, 18, 39, 40, 41, 73, 171
        TheNet, 122, 171
        Therein, 98
        Timeout, 8, 85, 113, 116, 144
        Transparent, 19, 32, 52
        Tunes, 121

        Unproto, 69, 71, 100
        Unshift, 17, 105
        Untested, 144
        UPGRADE, 7, 8, 11, 144
        Uplink, 67
        USB, 111

        Verbose, 81, 82
        VFO, 7, 110, 111

        Welcome, 95

        XFLOW, 11, 142
        XMITOK, 10, 75, 97, 107, 144
        Xmodem, 3, 36, 37, 131, 132, 155, 158, 163, 166, 167
        XOFF, 161
        XON, 161

        YAPP, 123, 131
        Ymodem, 3, 36, 37, 132, 155, 156, 158, 163, 166, 167

        Zap, 2, 3,  4, 6, 7, 10, 6, 16, 17, 20, 24, 25, 26, 36,  37,  39, 
                 41, 44, 46, 47, 66, 67, 68, 69, 72, 74, 80, 81, 82,  93, 
                 95, 142
        Zmodem, 9, 10, 6, 54, 55, 126, 127, 132, 133, 136, 143, 155, 156, 
                 157, 158, 159, 161, 163, 165, 166, 167








        LAN-LINK.DOC (c) G3ZCZ 1988 - 1994