PLOTTER/PRINTER INSTALLATION
 & PROBLEM DETERMINATION
 
 A MICRO CADAM* Installation Guide Supplement
 
 
 
 
                                   
                                   
                          April 30, 1993
                                   
                     Copyright (C) 1988 by ALTIUM
                            An IBM Company
                      Charlotte, North Carolina 28257
                                   
                This document shall not be reproduced
                 nor shall the information therein be
                 used by or disclosed to others except
                  as expressly authorized by ALTIUM,
                        An IBM Company.         
                                   
             ALTIUM is a registered trademark of ALTIUM,
                        An IBM Company.     
               MICRO CADAM is a trademark of ALTIUM,
                        An IBM Company.     

 Part I - Installation
 
 SERIAL RS-232-C INTERFACE PLOTTERS
 
 Check Hardware Connections
 
 Cable:  Figures 1 & 2 illustrate the required data cable
 configurations for stand-alone interface between MICRO CADAM
 supported plotters and supported computers.  You should make or
 order a cable specifically for your computer rather than trying to
 set up a communications link using any spare RS-232-C cable that
 you may have.  Because of the many misinterpretations of the
 RS-232-C "standards" in the computer industry, a working cable on
 one system may prove useless on another.
 
 
          (COMPUTER) FEMALE DB-9        (COMPUTER) FEMALE DB-25TO        
 (PLOTTER) MALE DB-25       *           TO(PLOTTER) MALE DB-25
 **
 
          1    -----  4                 1     -----  1  SHIELD         
 2        -----2      2                 ----- 3
          3    -----  3                 3     -----  2
          4    -----  5 & 6             7     -----  7
          5    -----  7                 5, 6, 8       -----             
 20
          6 & 8-----  20
          7    -----  8
 
 
                               Figure 1
  CALCOMP COLORMASTER, HEWLETT PACKARD, HOUSTON INSTRUMENTS, IBM, &
                        NICOLET ZETA PLOTTERS
                                   
 
 
          
          (COMPUTER) FEMALE DB-9        (COMPUTER) FEMALE DB-25          
 TO (PLOTTER) MALE DB-25                TO DB-25  (PLOTTER) MALE
          
          1    -----  8                 Use the straight 25 to 25
 pin cable     2            -----       3     that came with the
 plotter and connect  3                 ----- 2      to the port
 marked TO DTE HOST.  4                 ----- 20                       
          5    -----  7
          6    -----  6
          7    -----  4
                      8                 ----- 5
          9    -----  22
                                   
                               Figure 2
                    CALCOMP 1040GT SERIES PLOTTERS
 
   *HP Cable #24542G for 9-pin serial interface (#24542H for HP 7550A Plotter only)
 
 **HP Cable #13242G for 25-pin serial interface (#17255D for HP 7550A Plotter only)
 
 Identify COM1, COM2 and COM3: To determine serial port addresses,
 connect the cable between the computer and plotter and enter
 dir>com1 at the DOS prompt.  If the cable is connected to the
 serial port addressed as COM1 the system will return the DOS
 prompt.  If the cable is not connected to COM1, the error message
 "Error reading device COM1, abort, retry, ignore?" will result.
 Enter a to let this abort, and then confirm the error by entering
 dir>com2.  Return the DOS prompt.  If operating with an IBM PS/2
 check for COM3 thru COM8, which are also valid serial port
 addresses.
 
 Appearance of a flashing curser (without the DOS prompt),
 indicates an address conflict between serial ports -- consult your
 computer's Serial/Parallel Adapter documentation to change
 addresses.
 
 Check Computer Communications Settings
 
 The config.sys file of the root directory must include the
 appropriate plotter device driver statement.The autoexec.bat file
 (root directory) should include a path to DOS files, a set and a
 mode command statement. These commands tell the system which
 computer I/O port will be used and how the data is to be
 transmitted to the plotter.   Sample file statements:
          
          config.sys
          buffers=20
          files=20
          shell=c:\command.com  /e:384 ip
          device=c:\mcadam\mousesys.sys/g:mouse
          device=c:\mcadam\plothp.sys
          device=c:\mcadam\gsscgi.sys
          break=on
          
          autoexec.bat                                                 
 cls                                                 echo off          
 echo micro cadam autoexec.bat boot file      
          prompt=$p$g                                                  
 device=c:\mcadam\ibmrga12.sys                       
          
 path=c:\;c:\dos;c:\mcadam;c:\mcadam\bin;c:\mcadam\gimsample
          set mcadam=la03e8 /i4/dmouse /c 02f8 /s050   
          echo serial plotter port setup
          set c:\mcadam\plothp.sys=com1
                  * mode com1:96,n,8,1,p
          cd c:\mcadam
          reset
          
 * A common interface mode where:  address=com1;  baud rate=9600;
 parity=no/off;  data bits=8;  stop bit=1; automatic restart for
 buffer refill=p.   Caution: 9600 is the maximum baud rate.   The 
 plothp.sys drivers recognize the DOS statement set
 orientation=portrait as a command to rotate output 90! when plot
 data rotation is defined at 0! in the MICRO CADAM model.  Warning: 
 only 1 printer/plotter device driver may be loaded, and the
 gsscgi.sys device driver statement must be the last device
 statement listed.
 
 
 Check Plotter Settings
 External or internal programmable settings on the plotter tell it
 how to receive data from the computer (i.e., eavesdrop or
 standalone, remote or local, baud rate, odd/even/off parity, data
 bits, stop bits).  Plotter communications settings must be set to
 match the computer (Reference Part II - Plotter Settings).
 
 
 PARALLEL INTERFACE PRINTERS
 
 Check Hardware Connections
 Data transmission to printers is normally done through the
 parallel interface.  Consult your output device manual for set-up
 instructions specific to your environment.
 
 Cable:  Most printers use a standard Centronics parallel interface
 cable.  Connect the female DB-25 connector to the computer's
 parallel port addressed as LPT1 or LPT2 and the other end to the
 proper receiving port on the printer.
 
 Identify LPT1 and LPT2:  Determine which parallel port is being
 addressed by entering dir>lpt1 at the DOS prompt.  If the cable is
 connected to the parallel port addressed as LPT1 the current
 directory will be generated on the printer and the system will
 return the DOS prompt.  If the cable is not connected to the
 parallel port addressed as LPT1, the  error message "Error reading
 device LPT1, abort, retry, ignore?" will result.  Enter a to
 abort.  Confirm the error by entering dir>lpt2.  This should
 return the DOS prompt confirming the parallel port is addressed as
 LPT2.
 
 Check Computer Communications Settings
 The config.sys file of the root directory must include the
 required printer device driver file.  The autoexec.bat file of the
 root directory must include a set command (the mode command is not
 necessary), the instruction that tells the system which computer
 I/O port will be used.  Sample files:
 
          config.sys
          device=c:\mcadam\vdidypgd.sys
          device=c:\mcadam\epson100.sys
          device=c:\mcadam\gsscgi.sys
          break=on
 
          autoexec.bat
          cls
          echo off
          echo micro cadam autoexec.bat boot file
          prompt=$p$g
          path=c:\;c:\dos;c:\mcadam;c:\mcadam/bin;c:\mcadam\gimsampl
          set mcadam=/a03e8/i4dmouse/c02f8/s050
          set c:\mcadam\epson100.sys=lpt1
 
 Check Printer Settings
 Consult the device manufacturer's product support center or
 operators manual for set-up instructions specific to your
 environment.  Reference Part III - Printer Settings.
 
 
 
 
 
 
 Part II - Plotter Settings
 
 MICRO CADAM uses a hardwire or direct  handshake (not XON/XOFF or
 ENK/ACK).  The following plotter settings are recommended when
 plotting in a stand-alone environment.  Consult the device
 manufacturer's product support center or operator manual for
 set-up instructions specific to your environment.
 
 CALCOMP COLORMASTER
 Driver:  CLRMSTR.SYS
 Graphics Mode:  RASTER
 Switch 1:  1=UP (ON), 2=DN (OFF), 3=UP (ON), 4=DN (OFF)
 Switch 2:  1-4 UP (ON)
 
 CALCOMP PLOTMASTER
 Driver:  CLRMSTR.SYS
 Graphics Mode:  RASTER
 Switch 1:  1=UP (ON), 2=DN (OFF), 3=UP (ON), 4=DN (OFF)
 Switch 2:  1-4 UP (ON)
 
 CALCOMP 1023
 Driver:  CCP_PCI.SYS Filesize:  21848
 Softkey Setup
 Setup Submenu:  Host
 Host Submenu  Format:  PCI
               Data:  8 bit
                         1 stop
                         no parity
               Baud:  9600
               Handshake:  DirCntrl
               Sync:  # of Sync/1
                           Sync char - 2
               Chksum:  disabled
               End Msg:  3
 
 CALCOMP 104X GT SERIES (1041GT, 1042GT, 1043GT, & 1044GT*)
 Driver:  CCP_PCI.SYS
 Switch S1:  1=0 (OFF), 2=1 (ON), 3=0 (OFF), 4=1 (ON), 5=0 (OFF),
 6=0 (OFF), 7 & 8 NOT APPLICABLE
 SoftKey Setup Feature 7
 Sub Menu 0: PARITY=0 (none), BITS/CHAR=8
 Sub Menu 1: STOP BITS=1, CLOCK=0 (internal)
 Sub Menu 2: INTERFACE=0 (serial)
 Sub Menu 3: HOST BAUD RATE=9600, MODE=0 (PCI)
 Sub Menu 4: TERM MUTING=NO, CKSUM ENABLE=NO
 Sub Menu 5: ISOCHRONOUS=NO, EOM=03
 Sub Menu 6: DIRECT CONTROL=YES, XON/XOFF=NO
 Sub Menu 7: TERM BAUD RATE=9600, DUPLEX=0 (full)
 Sub Menu 8: SYNC CODES=1, SYNC CODE VALUE=002
 Note:  Specify SET PAPER_SIZE statement as instructed by MICRO
 CADAM Installation Guide

 HEWLETT PACKARD 7440A
 Driver:  PLOTHP.SYS  Filesize:  27228
 Switch:  S2=0, S1=0, A4/US=0 or 1, B4=1, B3=0, B2=1, B1=0
 
 HEWLETT PACKARD 7470A
 Driver:  PLOTHP.SYS
 Switch:  S2=0, S1=0, Y=0, A4/US=0 or 1, B4=1, B3=0, B2=1, B1=0
 
 
 HEWLETT PACKARD 7475A
 Driver:  PLOTHP.SYS
 Switch:  S2=0, S1=0, Y=0, US=1, A4/A3=0 or 1, B4=1, B3=0, B2=1,
 B1=0
 
 HEWLETT PACKARD 7550A                  
 Driver:  PLOTHP.SYS
 SoftKey Setup Features
 Menu 1: Mode = ENHANCED
 Menu 2: Environment = STANDALONE
 Menu 3: Handshake = HARDWIRE
 Menu 4: Connection = DIRECT
 Menu 5: Duplex = FULL
 Menu 6: Connection = DIRECT
 Menu 7: Parity = 8 BITS & OFF
 Menu 8: Baud Rate = 9600
 
 HEWLETT PACKARD 7570A DRAFTPRO
 Driver:  PLOTHP.SYS
 Switch 1:  0=OFF, 1=ON, 2=OFF, 3=ON, 4=OFF, 5=OFF, 6=OFF, 7=ON,
 8=ON, 9=OFF, 10=OFF,                    11=OFF
 
 HEWLETT PACKARD 7580B & 7585B (Cut-sheet)
 Driver:  PLOTHP.SYS
 Interface Mode:  RS-232-C
 Baud Rate:  9600
 Switch 1:  OFF/ODD/DUPLEX-FULL/HARDWIRE/NORMAL
 Switch 2:  EXPAND/NORMAL/STANDALONE/NORMAL/NORMAL
 
 HEWLETT PACKARD 7586B (Cut sheet and roll-feed)*
 Driver:  PLOTHP.SYS
 Interface Mode:  RS-232-C
 Baud Rate:  9600
 Switch 1:  OFF/ODD/DUPLEX-FULL/HARDWIRE/NORMAL
 Switch 2:  NORMAL/EXPAND/NORMAL/STANDALONE/NORMAL/NORMAL
 
 HEWLETT PACKARD 7595A DRAFTMASTER I  (Cut-sheet) &
 HEWLETT PACKARD 7596A DRAFTMASTER II (Cut-sheet and roll-feed) *
 Driver:  PLOTHP.SYS
 from SERIAL SoftKey Setting                     from SERIAL SoftKey
 Setting                   from MAIN SoftKey Setting
 Dataflow: REMOTE & STANDALONE                   Bypass: OFF                
 Rotate: OFF
 Baud: 9600                Monitor: OFF          Invert: OFF
 Parity: 0                 Duplex: FULL          Expand: ON
 Hardwire: ON              Auto-Disc: OFF        Emulate: ON

 HOUSTON INSTRUMENTS DMP-29 & DMP-50 SERIES (51, 51MP, 52, 52MP,
 56, 56A, 56C)
 Driver:  HIDMPL.SYS        Filesize:  10376
 State 2 Mode: Baud Rate=9600, URAT Parity Bit 8=0,
 Handshake=TOGGLE, Pass Through Port Option=TOGGLE
 Note:  Driver is hardcoded to communicate through COM1 only.
 
 HOUSTON INSTRUMENTS DMP-40 SERIES (40, 41, 42) --  UNTESTED BY
 ALTIUM, An IBM Company.
 Driver:  HIDMPL.SYS
 State 2 Mode: Baud Rate=9600, URAT Parity Bit 8=0,
 Handshake=TOGGLE, Pass Through Port Option=TOGGLE
 Note:  Driver hardcoded to COM1 only.
 
 IBM 6180
 Driver:  PLOTHP.SYS
 Switch:  S2=0, S1=0, Y=0, A4/US=0 or 1, B4=1, B3=0, B2=1, B1=0
 
 IBM 6184
 Driver:  PLOTHP.SYS
 Switch 1:  0=OFF, 1=ON, 2=OFF, 3=ON, 4=OFF, 5=OFF, 6=OFF, 7=ON,
 8=ON, 9=OFF, 10=OFF, 11=OFF
 
 IBM 6186-1 COLOR PLOTTER (Cut-sheet) &
 IBM 6186-2 COLOR PLOTTER (Cut-sheet and roll-feed)*
 Driver:  PLOTHP.SYS
 from SERIAL SoftKey Setting                     from SERIAL SoftKey
 Setting                   from MAIN SoftKey Setting
 Dataflow: REMOTE & STANDALONE                   Bypass: OFF                
 Rotate: OFF
 Baud: 9600                Monitor: OFF          Invert: OFF
 Parity: 0                 Duplex: FULL          Expand: ON
 Hardwire: ON              Auto-Disc: OFF        Emulate: ON
 
 IBM 7371
 Driver:  PLOTHP.SYS
 Switch:  S2=0, S1=0, Y=0, A4/US=0 or 1, B4=1, B3=0, B2=1, B1=0
 
 IBM 7372
 Driver:  PLOTHP.SYS
 Switch:  S2=0, S1=0, Y=0, US=1, A4/A3=0 or 1, B4=1, B3=0, B2=1, B1=0
 
 IBM 7374
 Driver:  PLOTHP.SYS
 Interface Mode:  SERIAL
 Baud Rate:  9600
 Switch 1:  OFF/ODD/DUPLEX-HALF/EXPAND/NORMAL    
 
 IBM 7375-1 (Cut-sheet)
 Driver:  PLOTHP.SYS
 Interface Mode:  SERIAL
 Baud Rate:  9600
 Switch 1:  OFF/ODD/DUPLEX-HALF/DIRECT CONNECT/NORMAL                        
 Switch 2:  EXPAND/NORMAL/STANDALONE/NORMAL/NORMAL
 
 IBM 7375-2 (Cut-sheet and roll-feed)*
 Driver:  PLOTHP.SYS
 Interface Mode:  SERIAL
 
 Mode #6 HPGL P67 Option
 Driver:  PLOTHP.SYS
 SW 01:  1=UP, 2=DN, 3=DN, 4=UP, 5=UP, 6=UP, 7=UP, 8=UP
 SW 02:  1=8 UP
 SW 03:  1=UP, 2=UP, 3=UP, 4=UP, 5=UP, 6=UP, 7=UP, 8=UP
 
 * CCP_PCI.SYS and PLOTHP.SYS drivers are capable of multiple-frame
 plot output on roll-feed models.  Enter SET NFRAMES=X (where X is the
 number of 45" frames required) in the DOS environment before the plot
 program is executed.  Default frame is 1.
 
 JDL 850 EWS (with GL-Processor Firmware Rev. 2.0 or later)
 Driver  PLOTHP.SYS
 I/O1:  128K
 FUNC:  PLOT
 I/O2:  9600, PNON, DB8, STP1, DTR, 32K
 PEMU: 758E
 PLOT:  PC10
 
 NICOLET ZETA 824 & 836 with P63 Option
 Mode #6 HPGL/P63 Option
 Driver:  PLOTHP.SYS
 SW 01:  1=UP, 2=DN, 3=DN, 4=UP, 5=UP, 6=UP, 7=UP, 8=UP
 SW 02:  1=UP, 2=DN, 3=UP, 4=UP, 5=UP, 6=UP, 7=UP, 8=DN
 SW 03:  1=UP, 2=DN, 3=DN, 4=UP, 5=UP, 6=DN, 7=DN, 8=DN
 
 WESTERN GRAFTEC MP2300
 Driver:  PLOTHP.SYS
 RS-232-C Switch S2:  1=ON, 2=OFF, 3=ON, 4=ON, 5=OFF, 6=OFF, 7=OFF,
 8=ON, 9=OFF, 10=OFF
 
 Part III - Printer Settings
 
 Consult the device manufacturer's product support center or operator
 manual for set-up instructions specific to your environment.  Note
 that some printers have options that allow emulation of other
 supported devices -- use the device driver required for the printer
 being emulated.  Printers require a standard 25 pin parallel cable
 unless noted.
 
 EPSON 80 SERIES (RX-80, MX-80, FX-80, & FX-85)
 Driver:  EPMX80.SYS
 
 EPSON 100 SERIES (FX-100, RX-100, FX-185)
 Driver:  EPMX100.SYS
 Note:  The EPMX100.SYS driver produces a maximum plotting frame of
 10.25" x 13".
 
 EPSON FX-286 & FX-286E
 EPSON Mode
 Driver:  EPMX100.SYS
 Switch Panel 1:  1=OFF, 2=OFF, 3=OFF, 4=ON, 5=OFF, 6=ON, 7=ON, 8=ON
 Switch Panel 2:  1=ON, 2=OFF, 3=OFF, 4=OFF
 Note:  The EPMX100.SYS driver produces a maximum plotting frame of
 10.25" x 13".
 
 HEWLETT PACKARD THINKJET
 Cable:  Figure 1
 Driver:  THINKJET.SYS                           Filesize:  41000
 Warning: Device currently unsupported - driver too big to load into
 RAM memory!
 
 HEWLETT PACKARD LASERJET SERIES II
 Driver:  LASERJET         Filesize:  49144
 The laserjet.sys recognizes the SET RESOLUTION=XXX command line.  The
 XXX may be either 75, 100, 150, or 300.  These numbers are the
 resolution in dots per inch (dpi).  The higher the number the clearer
 the picture, but the longer the time required to plot.
 
 IBM PROPRINTER 4201 B/W & PROPRINTER XL 4202 B/W
 Driver:  IBMGPR.SYS       Filesize:  24700
 Switch:  1=OFF, 2=OFF, 3=OFF, 4=OFF, 5=OFF, 6=ON (line feed)
 Note:  Driver allows narrow carriage output only!
 
 IBM GRAPHICS PRINTER 5152
 Driver:  IBMGPR.SYS                             
 
 IBM COLOR PRINTER 5182
 Driver:  IBMPRCOL.SYS     Filesize:  39876
 
 JDL 850 EWS
 Driver:  IBMGPR.SYS (IBM mode) or EPMX100.SYS (Epson mode)
 EMUL:  IBM or EPSN
 FUNC:  PR-P (Centronics parallel interface)
 PLOT:  PC10
 
 OKIDATA MICROLINE 84 & 93
 Driver:  OKID84.SYS       Filesize:  25860
 
 OKIDATA MICROLINE 92
 Driver:  OKID92.SYS       Filesize:  23552
 
 PRINTRONIX MVP, P300, & P600
 Driver:  PRNTRX.SYS       Filesize:  26216
 
 STROBE 100, 200, & 260
 Driver:  STROBE.SYS
 
 TOSHIBA P351
 Driver:  TOS1350.SYS      Filesize:  31620
 Note:  The TOS1350.SYS driver produces a maximum plotting frame of
 10.25" x 13".