O1W.DK help file.
  Loading in the file O1W.DK will set up Band-in-a-Box for the Korg O1\W
synthesizer. It will set up :
             1. Drum #'s for Korg 01/W (Patch 9 )
             2. Patch Map (assigned to factory settings of Korg 01/W)
             3. Startup Patches and Channels in Midi window.
  If you have modified the Patches in your O1/W from the factory settings
you may have to modify the Patch Map in BB (from the MIDI pull down menu).

  The only remaining step for you is to setup the Korg O1\W in Multi-Timbral
mode to receive multiple instruments at once. In "Program mode" the O1W
will only play 1 instrument at a time. In Combination mode it will play
up to 8 at once- so you want to be in combination mode and setup a
combination.

 To Setup the O1/W, from the front panel:
  1. Go to Combination Mode "COMBI". Select combo #0 by pressing 00 on the
     # pad.
  2. Then press the EDIT COMBO button to EDIT The Combination
  3. You will then be using the PAGE + and PAGE - keys to PAGE
     through the Combination setting up each of the 8 instruments
     each of the A-H keys represents a different instrument.

     Setup your Combination as follows:

                  A    B     C      D     E      F      G      H
                 Bass Piano Drums Guitar Horns Strings Melody Thru
Page 0 Combination type MULTI
Page 1 Program # B06  B01    A09   B04    B22    B07    B04    B04
Page 2 Channel    2     3    10     7      8      6      4      5
Page 3 Key Window Type ALL= C-1/ G9
Page 4 Output    90    90    90    90     90     90     90     90
Page 5 Transpose  0    0      0     0      0      0      0      0
Page 6 Pan Pot    5:5 is in the middle - can separate as you like
Page 7 Enable Prg All should be Enabled
Page 8 Effect 1= "4:Room" :ON
                  0.7 D022 E76 HD10    L:0 H:0 80:20
       Effect 2 = "19:Chorus 1  ":ON
                  M60 S0.30 D010 TRI   L:0 H:0 86:14

Then Go to PAGE 9 and SAVE the Combination by pressing the 'G' key twice.
IT IS ESSENTIAL THAT YOU SET THE 'GLOBAL CHANNEL' ON THE O1\W TO AN UNUSED
CHANNEL - EG. CHANNEL 1 . DO THIS FROM THE 'GLOBAL' BUTTON THEN KEY #5.
OTHERWISE A PATCH CHANGE SENT ON THE GLOBAL CHANNEL WILL CHANGE THE
COMBINATION FROM THE "BAND-IN-A-BOX COMBO" TO A DIFFERENT COMBO!!!

  Once you have done this , Band-in-a-Box is ready to Play your O1\W
just by you selecting COMBO 0 from the O1\W panel ( as long as you
have loaded in the O1\W.DK file into BB and then saved it as MYSETUP.DK)


YOU WILL NOW BE READY TO GO WITH Band-in-a-Box AND THE O1\W !

                                                 Have Fun!