DISK TECHNICIAN(R)
                          FACTORY TEST FOR SEAGATE(R) DRIVES

                                      USER GUIDE
                                     Version 1.22

                   Disk Technician Factory Test For Seagate Drives
                      is a Disk Technician Corporation product,
                       distributed by Seagate Technology, Inc.




          License Agreement:

          Ownership of the Disk Technician(R) Factory Test For Seagate
          Drives programs remains exclusively with Disk Technician
          Corporation, which provides the Disk Technician Factory Test For
          Seagate Drives programs. License to use these programs is granted
          only to Seagate Technology(R) Inc. authorized OEMs, system
          integrators, distributors and their dealers.

          WARNING! Unauthorized or uninformed use of this product may result
          in irretrievable data loss, or other damage.

          You may use these programs and make copies thereof. All copies
          must be full and complete and must include the copyright notice.
          You may not rent, sell, assign, lend, give, or otherwise transfer
          the Disk Technician Factory Test For Seagate Drives programs to
          any person. Any attempt to transfer the Disk Technician Factory
          Test For Seagate Drives programs or any rights under this License
          is void.

          YOU MAY NOT ALTER, DIVIDE, BREAK, MODIFY, ADAPT, TRANSLATE,
          DECOMPILE, DISASSEMBLE, OR REVERSE ENGINEER THE DISK TECHNICIAN
          FACTORY TEST FOR SEAGATE DRIVES PROGRAMS IN ANY MANNER FOR ANY
          PURPOSE WHATSOEVER. YOU MAY NOT USE THE PROGRAMS OR ANY PORTIONS
          THEREOF IN ANY DERIVATIVE WORKS.

          This License is effective until terminated. You may terminate it
          by destroying the programs and supporting materials together with
          all copies in any form. This License will also terminate if you
          fail to comply with any terms or condition of this License. You
          agree upon such termination to destroy the programs and all
          supporting materials together with all copies.

          This License is governed by the laws of the State of California.

          Disclaimer of Warranty:

          The Disk Technician Factory Test For Seagate Drives programs are
          furnished to you by Disk Technician Corporation. There is no
          warranty provided. If the programs or any materials provided
          therewith are defective in any way, notify Disk Technician
          Corporation immediately. Disk Technician Corporation does not
          warrant that the functions contained in the programs will meet
          your requirements or that the operation of the programs will be
          uninterrupted or error-free. THE PROGRAMS CONTAINED IN THIS
          PACKAGE ARE PROVIDED "AS IS" WITHOUT WARRANTY OF ANY KIND, EITHER
          EXPRESSED OR IMPLIED, INCLUDING, BUT NOT LIMITED TO, THE IMPLIED
          WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A PARTICULAR
          PURPOSE. THE ENTIRE RISK RELATED TO THE QUALITY AND PERFORMANCE OF
          THE PROGRAMS IS ON YOU. IN THE EVENT THERE IS ANY DEFECT, YOU
          ASSUME THE ENTIRE COST OF ALL NECESSARY SERVICING, REPAIR, OR
          CORRECTION.






                                          i




          This agreement constitutes the complete and exclusive statement of
          the terms of the agreement between you and Disk Technician
          Corporation. It supersedes and replaces any previous written or
          oral agreements and communications relating to the software. No
          oral or written information or advice given by Disk Technician
          Corporation, its dealers, distributors, agents or employees will
          create any warranty or in any way increase the scope of the
          warranty provided in this agreement, and you may not rely on any
          such information or advice.

          Patents, Servicemarks, Trademarks, Copyrights:

          U.S. and foreign patent(s) pending.

          Disk Technician(R) is a registered trademark of Disk Technician
          Corporation. Finds And Fixes Hard Disk Problems While You Use Your
          Other Software(SM), and We Make Technology Easy and Affordable(SM)
          are servicemarks of Disk Technician Corporation. Seagate(R),
          Seagate Technology(R), and the Seagate(R) logo are registered
          trademarks of Seagate Technology Incorporated. All other
          trademarks and servicemarks are acknowledged.

          (C)1991-93 DISK TECHNICIAN CORPORATION. All rights reserved.



































                                          ii




          *****************************************************************
                                  Table of Contents:
          *****************************************************************

          Legal...........................................................i

          Introduction....................................................1

          Requirements....................................................2

          Setup...........................................................3

          Operating Instructions..........................................4

          Using The Test Results..........................................6

          Product Support Services........................................6

          Appendix A: Eligible Seagate Drives
                      And Matching Controllers/Adapters...................7

          Appendix B: Installing Jumpers And Terminators.................11

          Appendix C: White Paper On Disk Technician Factory Test
                      For Seagate Drives.................................12

          Appendix D: Disk Technician Gold And The Rest
                      of The Hard Drive Reliability Story................17

          Appendix E: White Paper On Disk Technician Gold................18




























                                         iii

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                   Introduction:
         *****************************************************************

         Disk Technician Factory Test For Seagate Drives puts the power
         of Seagate factory testing in your hands. It requires no special
         hardware and is fast and easy to use. Its two tests assure the
         reliability of Seagate drives for you and your customers:

           * A Quick test rapidly identifies gross failures.

           * Media certification creates a new, updated media defect map
             and recertifies the drive for normal use.

         Disk Technician Gold(R), the retail end-user version, puts the
         power of Seagate factory testing in your customers' hands. It
         makes hard discs continuously self-repairing. It's the first hard
         disc preventive maintenance software that works all of the time
         -- in the background.

         Disk Technician Factory Test For Seagate Drives was developed
         especially for you. That makes you our most highly-valued source
         for how to make it better. We need your suggestions. Please let
         us hear from you.


































                                         1

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                   Requirements:
         *****************************************************************

           * AT-286, -386, or -486 class machine with at least 640K of
             RAM and a 1.2 megabyte 5.25" or 1.44 megabyte 3.5" floppy
             drive.

               NOTE: Some older AT-286 clones do not support AT (IDE)
               drives. If you are using one of these early computers as
               a test system, you may find that you are unable to test
               certain drives unless you update the computer's BIOS.

               Also, make certain that your test system is set-up so
               that, if a diskette is loaded into the floppy drive, it
               will boot from the floppy drive.

           * The recommended controller/adapter for the hard drive to be
             tested. See "Appendix A" for details.

               NOTE: To precisely match Seagate factory testing and
               assure your customers that their hard drives have been
               recertified on that basis, it is best use the recommended
               controller or adapter.

               Disk Technician Factory Test For Seagate Drives may
               operate with controllers and adapters not listed in the
               README.DOC. However, these have not been tested or
               certified with Disk Technician Factory Test For Seagate
               Drives and may give invalid results.

           * A printer.

           * A MS-DOS 5.0 or 6.0 bootable 1.2 megabyte 5.25" or 1.44
             megabyte 3.5" diskette.























                                         2

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                       Setup:
         *****************************************************************

         Copy all files from the Disk Technician Factory Test For Seagate
         Drives distribution diskette to the DOS 5.0 or 6.0 bootable
         diskette.  This will be your work copy.



















































                                         3

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                              Operating Instructions:
         *****************************************************************

         Because Disk Technician Factory Test For Seagate Drives
         automatically configures itself to each Seagate drive, you will
         NOT need to:

           * Change any CMOS settings when setting-up or testing
             different drives.

           * DOS format or FDISK any drive prior to testing.



         WARNING!!! WARNING!!! WARNING!!! WARNING!!! WARNING!!! WARNING!!!
              All data on the drive being tested will be destroyed.
              For nondestructive testing, use Disk Technician Gold.
         WARNING!!! WARNING!!! WARNING!!! WARNING!!! WARNING!!! WARNING!!!



           1.  Make certain that the power is off, then install the
               Seagate hard drive and recommended controller/adapter in
               the test system. See "Appendix A" for details. Please be
               certain that:

                 * You have correctly installed all jumpers and
                   terminators on the drive to be tested. See "Appendix B"
                   for details.

                 * You are using the recommended controller or adapter.
                   See "Appendix A" for details.

                 * For MFM and RLL (ST412-type) drives, confirm that the
                   interleave is set at 1 prior to testing. If it is not,
                   low-level format with an interleave value of 1.

           2.  Be sure the printer is on and connected.

           3.  Turn on the computer and boot from the Disk Technician
               Factory Test For Seagate Drives work copy diskette.

               The opening screen will appear with a flashing message that
               Disk Technician Factory Test For Seagate Drives is
               "Configuring To The Test Drive. Please Wait." When
               configuration is complete, you will see another flashing
               message, "Press any key to continue." Press any key to go
               to the "Tests" menu.

                 NOTE: Disk Technician Factory Test For Seagate Drives may
                 not automatically recognize all drives. In these cases,
                 you will see a list of eligible drives on screen.
                 Highlight the correct drive and then press ENTER to
                 continue.



                                         4

               Disk Technician Factory Test for Seagate Drives Manual


           4.  Press ENTER to start the "Quick test." The "Quick test"
               screen will appear and testing will start.

               Or use the up/down arrow keys to select "Media
               certification." (If you select "Media certification," go to
               step 7 now.)

               The "Quick test" rapidly identifies gross failures,
               including the inability to seek and/or to perform
               read/write operations. The "Quick test" does the following
               operations on the drive:

                 * Seek testing.

                 * Quick read and write testing of the entire drive for
                   soft and hard errors.

           5.  When the test is finished, you will see the "Quick test
               report," with a pass/fail result. Type P for a printed
               report.

                 NOTE: To remove from service all new defect locations
                 detected by Disk Technician Factory Test For Seagate
                 Drives, simply perform a high-level format under
                 the appropriate operating system (DOS, UNIX, etc.).

           6.  Press the Escape key to return to the "Tests" menu. Or
               press F10 to quit.

                 NOTE: If you choose to quit now, skip instructions 7-9
                 and go to the last section, "Using The Test Results. "To
                 test a different drive now, turn off the computer and
                 begin again from step 1, above."

           7.  Use the up/down arrow keys to select "Media certification,"
               then press ENTER to start testing. The "Media
               certification" screen will appear and testing will start.

               Media certification creates a new, updated media defect map
               and recertifies the drive for normal use. It performs the
               following operations on the entire drive:

                 * Seek testing.

                 * Comprehensive read and write testing of the entire
                   drive for soft and hard errors.

                 * Media defect identification.










                                         5

               Disk Technician Factory Test for Seagate Drives Manual


           8.  When the test is finished, you will see the "Media
               certification report," with a pass/fail result. Type P for
               a printed report.

               Save the printed report and return it along with the
               customer's drive.

                 NOTE: To remove from service all new defect locations
                 detected by Disk Technician Factory Test For Seagate
                 Drives, simply perform a high-level format under
                 the appropriate operating system (DOS, UNIX, etc.).

           9.  Press the Escape key to return to the "Tests" menu. Or
               press F10 to quit.

                 NOTE: To test a different drive now, turn off the
                 computer and begin again from step 1, above.

         *****************************************************************
                              Using The Test Results:
         *****************************************************************

           1.  For optimal customer satisfaction: if the test drive passes
               the "Quick test," it is best to perform "Media
               certification" to assure that the drive is recertified for
               normal use.

           2.  Include a copy of the test report with the hard drive when
               you return it to your customer. This will provide assurance
               that the drive has been recertified for normal service by
               Seagate factory testing.

         *****************************************************************
                             Product Support Services:
         *****************************************************************

         For product support and troubleshooting, please call Disk
         Technician Technical Support at 619 272 4000. Technical Support
         is available Monday through Friday, 8 a.m. to 5 p.m., Pacific
         Time.

         Support is also available on the Disk Technician Corporation
         electronic Bulletin Board System (BBS). It can be reached by
         modem 24 hours a day, 7 days a week, at 619 272 9240.

         Disk Technician Factory Test For Seagate Drives is continuously
         updated. New revisions can be obtained from the Seagate
         Technology Bulletin Board System (BBS). Seagate's BBS can be
         reached by modem 24 hours a day, 7 days a week, at 408 438 8771.









                                         6

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                     Appendix A:
             Eligible Seagate Drives And Matching Controllers/Adapters
         *****************************************************************
         Disk Technician Factory Test for Seagate Drives V1.22.

         The following are Seagate drives supported by version 1.22.  Also
         listed are the controllers and adapters we recommend you use.
         Controller and adapter numbers prefaced with ST are products of
         Seagate, those prefaced with TMC are products of Future Domain.

           NOTE: To precisely match Seagate factory testing and assure
           your customers that their hard drives have been recertified on
           that basis, it is best use the recommended controller or
           adapter. Disk Technician Factory Test For Seagate Drives may
           operate with controllers and adapters not listed in the
           README.DOC. However, these have not been tested or certified
           with Disk Technician Factory Test For Seagate Drives and may
           give invalid results.

         =================================================================
         Model Number   Controller/Adapter
         ------------   ------------------
         ST1057A        ST08                
         ST1090A        ST08                
         ST1090N        TMC1670/TMC1680     
         ST1096N        TMC1670/TMC1680     
         ST1100         ST22M               
         ST1102A        ST08                
         ST1106R        ST22R               
         ST1111A        ST08                
         ST1111N        TMC1670/TMC1680     
         ST11200N       TMC1670/TMC1680     
         ST11201N       TMC1670/TMC1680     
         ST1126A        ST08                
         ST1126N        TMC1670/TMC1680     
         ST1133A        ST08                
         ST1133N        TMC1670/TMC1680     
         ST1144A        ST08                
         ST1150R        ST22R               
         ST1156A        ST08                
         ST1156N        TMC1670/TMC1680     
         ST1162A        ST08                
         ST1162N        TMC1670/TMC1680     
         ST11700N       TMC1670/TMC1680     
         ST11701N       TMC1670/TMC1680     
         ST11750N       TMC1670/TMC1680     
         ST11751N       TMC1670/TMC1680     
         ST1186A        ST08                
         ST1186N        TMC1670/TMC1680     
         ST1201A        ST08                
         ST1201N        TMC1670/TMC1680     
         ST1239A        ST08                
         ST1239N        TMC1670/TMC1680     
         ST124          ST22M               
         ST12400N       TMC1670/TMC1680     
         ST12401N       TMC1670/TMC1680     
         ST125          ST22M               
                                         7

               Disk Technician Factory Test for Seagate Drives Manual


         ST12550N       TMC1670/TMC1680     
         ST12551N       TMC1670/TMC1680     
         ST125A         ST08                
         ST125N         ST02/TMC1670/TMC1680
         ST138          ST22M               
         ST138A         ST08                
         ST138N         ST02/TMC1670/TMC1680
         ST138R         ST22R               
         ST1400A        ST08                
         ST1400N        TMC1670/TMC1680     
         ST1401A        ST08                
         ST1401N        TMC1670/TMC1680     
         ST1480A        ST08                
         ST1480N        TMC1670/TMC1680     
         ST1481N        TMC1670/TMC1680     
         ST151          ST22M               
         ST157A         ST08                
         ST157N         TMC1670/TMC1680     
         ST157R         ST22R               
         ST1581N        TMC1670/TMC1680     
         ST177N         ST02/TMC1670/TMC1680
         ST1980N        TMC1670/TMC1680     
         ST2106N        TMC1670/TMC1680     
         ST212          ST22M               
         ST2125N        TMC1670/TMC1680     
         ST213          ST22M               
         ST2209N        TMC1670/TMC1680     
         ST225          ST22M               
         ST225N         ST02/TMC1670/TMC1680
         ST225R         ST22R               
         ST2274A        ST08                
         ST2383A        ST08                
         ST2383N        TMC1670/TMC1680     
         ST238R         ST22R               
         ST2502N        TMC1670/TMC1680     
         ST250R         ST22R               
         ST251          ST22M               
         ST251N         ST02/TMC1670/TMC1680
         ST252          ST22M               
         ST253          ST22M               
         ST274A         ST08                
         ST277N         ST02/TMC1670/TMC1680
         ST277R         ST22R               
         ST278R         ST22R               
         ST279R         ST22R               
         ST280A         ST08                
         ST296N         ST02/TMC1670/TMC1680
         ST3051A        ST08                
         ST3096A        ST08                
         ST31200N       TMC1670/TMC1680     
         ST3120A        ST08                
         ST3123A        ST08                
         ST3144A        ST08                
         ST3145A        ST08                
         ST3243A        ST08                
         ST325A/X       ST08                
         ST325N         TMC1670/TMC1680     
         ST3283A        ST08                
                                         8

               Disk Technician Factory Test for Seagate Drives Manual


         ST3283N        TMC1670/TMC1680     
         ST3290A        ST08                
         ST3385         ST08                
         ST3390A        ST08                
         ST3390N        TMC1670/TMC1680     
         ST3500         ST08                
         ST3500N        TMC1670/TMC1680     
         ST351A/X       ST08                
         ST3550         ST08                
         ST3550N        TMC1670/TMC1680     
         ST3600         ST08                
         ST3600N        TMC1670/TMC1680     
         ST3610N        TMC1670/TMC1680     
         ST3655A        ST08                
         ST3655N        TMC1670/TMC1680     
         ST4026         ST22M               
         ST4038         ST22M               
         ST4038M        ST22M               
         ST4051         ST22M               
         ST4053         ST22M               
         ST406          ST22M               
         ST4085         ST22M               
         ST4086         ST22M               
         ST4096         ST22M               
         ST4097         ST22M               
         ST412          ST22M               
         ST41200        TMC1670/TMC1680     
         ST4135R        ST22R               
         ST4144R        ST22R               
         ST41520N       TMC1670/TMC1680     
         ST41600N       TMC1670/TMC1680     
         ST41601N       TMC1670/TMC1680     
         ST41650N       TMC1670/TMC1680     
         ST41651N       TMC1670/TMC1680     
         ST4182N        TMC1670/TMC1680     
         ST419          ST22M               
         ST42000N       TMC1670/TMC1680     
         ST42100N       TMC1670/TMC1680     
         ST42101N       TMC1670/TMC1680     
         ST42400N       TMC1670/TMC1680     
         ST43400N       TMC1670/TMC1680     
         ST43401N       TMC1670/TMC1680     
         ST43402N       TMC1670/TMC1680     
         ST4350N        TMC1670/TMC1680     
         ST4376N        TMC1670/TMC1680     
         ST4385N        TMC1670/TMC1680     
         ST4702N        TMC1670/TMC1680     
         ST4766N        TMC1670/TMC1680     
         ST4767N        TMC1670/TMC1680     
         ST506          ST22M               
         ST9051A        ST08                
         ST9052A        ST08                
         ST9077A        ST08                
         ST9080A        ST08                
         ST9096A        ST08                
         ST9100AG       ST08                
         ST9144A        ST08                
         ST9145AG       ST08                
                                         9

               Disk Technician Factory Test for Seagate Drives Manual


         ST9235A        ST08                
         ST9235AG       ST08                
         ST9235N        TMC1670/TMC1680     
         ST9295AG       ST08                
         ST9295N        TMC1670/TMC1680     





















































                                         10

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                    Appendix B:
                         Installing Jumpers And Terminators
         *****************************************************************

         Your Disk Technician Factory Test For Seagate Drives work copy
         diskette contains a hypertext file called the "Seagate Technical
         Support Desk Reference." This reference contains jumper and
         terminator settings for Seagate drives, controllers and adapters.
         To use this reference:

           1.  From the system prompt, type the following:

                 SETTINGS and then press ENTER.

           2.  Follow the instructions on your screen.










































                                         11

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                              Appendix C: WHITE PAPER
                  Disk Technician Factory Test For Seagate Drives
               And The Elimination of No Problem Found Drive Returns
         *****************************************************************

         The Problem:

         On average, 35% of all drives returned to Seagate Customer
         Service Repair at Oklahoma City for repair (in or out of
         warranty) have absolutely nothing wrong with them.

         These "No Problem Found" (NPF) drives not only waste both Seagate
         and reseller resources, but they also cause customer
         dissatisfaction and damage to Seagate's valuable reputation for
         product quality.

         Seagate's Objective:

         Seagate's objective was to provide a simple solution to No
         Problem Found drive returns by empowering its resellers with the
         ability to perform on-site drive testing with factory-level
         accuracy. In order to be readily adopted and remain in use, any
         proposed solution would have to:

           * Be fast. Resellers must clearly perceive the potential for
             greater profits as a result of quick drive turnaround and
             immediate customer satisfaction.

           * Be easy to learn and operate. Training time must be minimal.
             Test operators selected by resellers are likely to be non-
             technical.

           * Precisely match Seagate factory hardware test results. Both
             Seagate and the resellers must be assured that results
             obtained from the field NPF solution will  correlate to those
             of Customer Service Repair (CSR).

           * Be affordable. Resellers would be unlikely to participate if
             the solution required an investment in special equipment,
             periodic recalibration or maintenance.

         The Solution:

         Disk Technician Factory Test For Seagate Drives is software that
         eliminates No Problem Found drive returns from Seagate's direct
         accounts (and, eventually, from distributors' dealers). It puts
         the power of Seagate factory testing in the resellers' hands.

         It is purposefully designed as a quick and easy to use Go/No-Go
         tool for non-technical operators. As such, it does not perform
         failure analysis. Instead, Factory Test completely exercises and
         tests the drive's electronics and mechanics, tests the media,
         then produces an authoritative "Pass" or "Fail" report with a
         list of any new grown defect locations detected.



                                         12

               Disk Technician Factory Test for Seagate Drives Manual


         A "Pass" result allows Seagate resellers to immediately return a
         No Problem Found drive to their customer with the assurance that
         it has been recertified by Seagate factory testing for normal use.
         A "Fail" result indicates that the drive can be returned to
         Seagate with certainty that the drive requires further analysis
         and repair.

         Factory Test has been extensively researched and examined by
         Seagate Technology and has been found to be an effective method
         of testing and recertifying Seagate disc drives. It was developed
         in close consultation with Seagate Engineering and is designed to
         factory certify Seagate disc drives and avoid needless returns.
         It is the most effective substitute available for Seagate factory
         testing available.

         Disk Technician Factory Test For Seagate Drives achieves all of
         Seagate's objectives for eliminating NPFs at the reseller site:

           * It is fast.  On average it takes only 2 minutes to test a 40
             megabyte IDE drive, although testing time will vary depending
             on drive specifications and the number of defects found.

           * It is easy to learn and use. Factory Test was designed for
             non-technical operators. It automatically recognizes and
             configures itself to Seagate drives.

           * It has been tested against Seagate factory test hardware on
             a large number of hard disc drives to assure that results
             precisely match.

           * No special equipment is needed.  Any AT-class machine is all
             that is required.

           * It is provided free to Seagate's direct accounts (and,
             eventually, to distributors' dealers).

         Requirements:

           * An AT-286/386/486 machine with at least 640K of RAM and a
             1.2 megabyte 5.25" or 1.44 megabyte 3.5" floppy disc drive.

           * The recommended controller or adapter for the hard drive to
             be tested (these are listed in the README.DOC file on the
             Factory Test distribution diskette).

           * A printer.

           * A DOS 5.0 bootable 1.2 megabyte 5.25" or 1.44 megabyte 3.5"
             diskette.

         Setup:

         All files from the Factory Test distribution diskette are copied
         to the DOS 5.0 bootable diskette. This will become the work copy
         diskette.



                                         13

               Disk Technician Factory Test for Seagate Drives Manual


         Operation:

         Factory Test only recognizes and tests Seagate drives. It
         automatically configures itself to any Seagate drive in the test
         program (these are listed in the README.DOC file on the diskette.
         Additional drives may be added at the determination of Seagate).
         Because of this, there is no need to verify or change any CMOS
         settings, DOS format or FDISK any drive to be tested.
         Additionally, because Factory Test overwrites all data on the
         drive being tested -- including sectors marked bad, it will test
         drives formatted under any operating system (i.e. DOS, UNIX,
         Macintosh, etc.).

         The operator simply installs the Seagate drive to be tested with
         the recommended controller or adapter. (A listing of the correct
         jumper and terminator settings for each drive can be found in the
         Seagate Technical Support Desk Reference file on the work copy
         diskette.)

         After making certain that the printer is connected and on, the
         operator inserts the work copy diskette into the computer's
         floppy drive and turns on the system.

         Important! Factory Test overwrites (destroys) all data on the
         drive being tested. This destructive test method allows drives to
         be tested regardless of the operating system under which they
         were formatted (UNIX, DOS, etc.). It also makes testing time much
         quicker.

         How Factory Test Eliminates NPFs:

         Disk Technician Factory Test For Seagate Drives performs
         comprehensive NPF testing of the entire hard disc drive subsystem
         (including electronics, mechanics and media) in the following
         order:

           1. When Factory Test begins, it tests host-to-drive
              communications. It then issues a drive identification
              command to verify that it is operating on a Seagate drive.

           2. Factory Test next obtains geometry for the specific drive
              from its own internal tables and sets the system parameters
              for the drive to be tested.

         Then the operator selects either the Quick Test (to rapidly
         eliminate gross failures) or Media Certification (to recertify
         the drive for normal service).

           3. Next, Factory Test does random and step seek tests.
              These check the drive electronics as well as the positioning
              mechanics (including motor, stepper and positioning system).

           4. The guaranteed good sector 0/0 is tested multiple times
              with all Seagate test patterns and their inversions.




                                         14

               Disk Technician Factory Test for Seagate Drives Manual


           5. If the Quick Test is selected, the media is tested for
              soft, ECC and hard error locations by reading and writing
              to all sectors with a single Seagate test pattern.

           6. If Media Certification is selected, the media is tested
              for soft, ECC and hard error locations by reading and
              writing to all sectors using all Seagate test patterns and
              their inversions.

           7. In the final stage of both the Quick Test and Media
              Certification, defect locations are globally analyzed by an
              expert system for patterns indicating electronic, mechanical
              and media failures.

         The "Pass/Fail" Report

         Upon completion of testing, a report appears on-screen with a
         "Pass" or "Fail" finding, along with a list of media defect
         locations. This report should be printed so that it can accompany
         the drive.

         The Pass/Fail standard for each Seagate drive has been
         predetermined by specifications set by Seagate Engineering.

         If the drive passes the Quick Test, it is recommended to perform
         Media Certification to assure the customer that the drive is
         recertified for normal use.

         If the drive passes Media Certification, a copy of the test
         report containing the updated list of the new media defect
         locations should be included with the drive when it is returned
         to the customer. This provides assurance that the drive has been
         recertified by Seagate factory testing.

           NOTE: To remove from service all new defect locations
           detected by Disk Technician Factory Test For Seagate
           Drives, simply perform a high-level format under
           the appropriate operating system (DOS, UNIX, etc.).

         If the drive fails either the Quick Test or Media Certification,
         a copy of the test report should be included with the drive when
         it is sent to Seagate for analysis and repair. This will
         significantly reduce both diagnostic and turnaround time.

         Benefits:

           * Disk Technician Factory Test is backed by the Seagate
             name.

           * Seagate resellers now have a resource when "failures"
             occur.

           * Seagate resellers enjoy more profit, less handling, less
             work.

           * No Problem Found drives are eliminated by Seagate resellers.


                                         15

               Disk Technician Factory Test for Seagate Drives Manual



           * Rapid turnaround creates happier, more loyal customers.

           * By eliminating NPFs, Seagate's reputation for product
             quality is enhanced.

         Product Support Services:
         For product support and troubleshooting, please call Disk
         Technician Technical Support at (619) 272 4000. Technical Support
         is available Monday through Friday, 8 a.m. to 5 p.m. Pacific
         Time.

         Support is also available on the Disk Technician Corporation
         Bulletin Board System (BBS). It can be reached by modem 24 hours
         a day, 7 days a week, at (619) 272-9240.

         Additional drives may be included in the Factory Test program at
         the determination of Seagate.








































                                         16

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                                    Appendix D:
                                Disk Technician Gold
                                  And The Rest of
                          The Hard Drive Reliability Story
         *****************************************************************

         Seagate drives are born perfect. Before they arrive at your
         door, each one must pass a rigorous quality control process
         that is the acknowledged world standard. And each drive is
         factory certified for long and reliable service.

         So why do you get returns? Call it physics, or call it the law
         of nature. But, as soon as hard drives begin their long life of
         service, a host of microscopic, natural forces also begin a
         relentless attack on the various parts. These cause "grown
         defects," spots on the media surface that can no longer store
         data reliably, and that "grow" after factory certification. As
         they evolve from subtle, to marginal, to bad, grown defects wreak
         havoc with your customers' data. When that happens, you get a
         return. A preventable return.

         Disk Technician Gold makes your customers' hard drives
         continuously self-repairing. It stops grown defects before they
         get a chance to grow up. Operating as a memory-resident device
         driver, Disk Technician Gold goes to work automatically every
         time the computer is switched on. And it stays on the job
         continuously to prevent the very problems that cause drives to be
         returned to you.

         Disk Technician -- either the Factory Test For Seagate Drives
         or the Gold version -- is the only software that uses the same
         soft error test standards as factory quality control to monitor
         every hard disc access -- only tolerating perfect performance.
         However, since Disk Technician Gold is designed to work on "live"
         drives loaded with data, its testing is nondestructive. And, when
         a problem is detected, Disk Technician Gold not only reports it,
         it fixes it. On-the-fly. In the background.

         So how can you do fast turnarounds on returns -- and make your
         customers happy? Just keep Disk Technician Factory Test For
         Seagate Drives on your test bench. And how can you prevent
         returns in the first place -- and keep your customers happy? Just
         recommend Disk Technician Gold. It's the rest of the hard drive
         reliability story.













                                         17

               Disk Technician Factory Test for Seagate Drives Manual


         *****************************************************************
                  Appendix E: White Paper On Disk Technician Gold:
                        Comprehensive Preventive Maintenance
                     For The Hard Disc Drive and Its Subsystems
         *****************************************************************

         The Problem of No Problem Found Drive Returns:

         Before leaving the factory, each Seagate hard disc drive
         undergoes rigorous quality control and is certified for long and
         reliable service. Yet, once these drives are installed in end
         user computer systems, an array of natural microscopic forces
         begins a relentless, continuous attack on the media, electronics
         and mechanics. While these forces can be effectively managed in a
         laboratory environment through scheduled, proactive diagnostics
         and repair, end users can only react to the catastrophic problems
         that these forces will eventually cause if left unchecked.

         However, problems inherent to the hard disc drive itself are only
         a small part of the picture. Failures in other computer
         components such as the power supply also affect data reliability
         and therefore the end user's perception of hard drive quality.

         End users seeing a DOS error message such as DRIVE NOT READY
         cannot distinguish between a problem caused by worn or dirty
         connectors, intermittent ribbon cables, an intermittent power
         supply -- or within the hard drive itself.

         Still other causes of perceived hard drive reliability problems
         that happen after the drive has left Seagate's reseller channel
         include such things as improper drive installation, incorrect
         CMOS setup, viruses, CHKDSK errors, improper software
         installation, and physical abuse.

         In any case, end users are not concerned with inter-industry
         engineering issues and intra-industry finger pointing. Fairly or
         unfairly, when any problem affects their precious data -- no
         matter what the actual cause may be the finger of blame is
         invariably pointed at Seagate and the hard drive is returned for
         repair or replacement.

         It should come as no surprise then, that on average, 35% of all
         drives returned to Seagate Customer Service Repair in Oklahoma
         City for repair -- in or out of warranty have absolutely nothing
         wrong with them. Or that, depending on the reseller, this figure
         can go as high as 80%. It is easy to deduce that servicing these
         No Problem Found (NPF) drives not only wastes both Seagate and
         reseller resources, but also cause customer dissatisfaction and
         damage to Seagate's valuable reputation for product reliability
         and quality.

         End User Resistance to Hard Drive Preventive Maintenance:

         The benefits of hard drive preventive maintenance are many,
         particularly to business and professional users. Because of the
         value of the data stored on their hard drives, these users
         typically own one or more hard disc utility software packages.

                                         18

               Disk Technician Factory Test for Seagate Drives Manual



         Unfortunately, users rarely remember to run these utilities until
         after a severe problem has occurred, too late for preventive
         measures. Nor are these utilities preventive in the proper sense
         of the word, in that they cannot detect or measure soft errors.
         Further, the sole function these utilities provide is media
         surface scanning, which does not address the many other (and much
         more prevalent) causes of hard drive reliability problems.

         In addition, these utilities took from 1-1/2 to 5-1/2 hours to
         run on a 20 megabyte drive, which discouraged regularly scheduled
         maintenance. However, today's desktop computer is much more
         likely to have a 120 megabyte drive, and many new systems are
         shipped with 200 megabyte or greater drives. The effect of this
         is that critically necessary hard drive maintenance time has now
         eclipsed potential computer production time.

         With the decreasing cost of hardware and increasing
         sophistication of software applications, the PC has assumed many
         corporate mission-critical tasks that were previously in the
         domain of mainframes and minis, including things such as
         accounting, vendor and customer records, engineering and
         manufacturing process control. For business users, however, PC
         hard drive data reliability has remained the single, unresolved
         issue.

         Seagate's Objective:

         While Disk Technician Factory Test provides Seagate's resellers
         with a go/no-go software solution to eliminate NPFs once drives
         have arrived back in the channel (for more information, see the
         Factory Test White Paper), no one would disagree that it would be
         far preferable and mutually profitable to prevent these drives
         from being returned in the first place. Further, suppose a
         comprehensive tool could be developed which could detect and
         eliminate all of the previously mentioned problems affecting data
         reliability? Suppose that it could be installed right in the
         computer operating system, such that hard drive preventive
         maintenance would not require end user involvement? One result
         would surely be that unnecessary drive returns would plummet to
         virtually zero. Everyone -- from end users, to dealers, VARs or
         VMRs, to distributors, to System Integrators, to OEMs, to Seagate
         itself -- would enjoy the benefits of self-repairing hard drives.

         Disk Technician Corporation's Objective:

         Disk Technician Corporation wanted to develop a user-independent
         solution to both inherent and environmentally induced hard drive
         problems, as well as non-hard drive problems that affect data
         reliability and hence are perceived to be hard drive-related. In
         order to be an acceptable end user desktop solution, such a
         product would need to:

           * Detect and eliminate grown defects. Media defects develop
             continuously throughout a hard drives service life. These
             must be eliminated in their soft stage, before they cause
             lost and corrupted data, or precipitate a crash.

                                         19

               Disk Technician Factory Test for Seagate Drives Manual



           * Detect imminent electronic, mechanical and media problems in
             the hard drive. If undetected, these can cause sudden,
             catastrophic failures.

           * Detect non-hard drive computer component problems affecting
             data reliability. These can cause lost and corrupted data as
             well as sudden, catastrophic failure.

           * Detect other non-hard drive issues affecting data reliability
             (including CHKDSK errors, viruses, improper software
             installation, improper drive installation and setup, etc.).

           * Precisely match Seagate factory hardware test results.
             Seagate, resellers and end users must be assured that testing
             results obtained from the end user preventive maintenance
             product correlate to Seagate Customer Service Repair's.

           * Be fast. End users will not adopt a product that ties-up
             their systems for any significant period of time.

           * Be easy to learn and operate. A pragmatic hard drive
             preventive maintenance product must assume that the majority
             of its users will be non-technical and have no desire to
             learn the intricacies of hard drives or complex preventive
             maintenance, repair and recovery procedures.

           * Be affordable. Even "must-have" desktop solutions must be
             inexpensive in order to become widely adopted.

         The Solution? Build Both Prevention and Cure Right Into The
         System:

         Disk Technician Gold is a retail product (suggested list price,
         US$149.95) designed to be installed on end user hard disc drives.
         It works constantly in the background to prevent media errors and
         provide advance warning of electronic and mechanical errors as
         the drive functions. Once Disk Technician Gold is installed, no
         further user interaction is required. It replaces traditional
         hard disc maintenance utilities where the user must remember to
         run the software. Disk Technician Gold begins to work the moment
         the computer is turned on and can actually eliminate the types of
         problems that necessitate disc drive returns. It will help ensure
         that disc drives remain where they belong -- at the customer site.

         Seagate Technology, Inc., has tested and approved Disk Technician
         Gold. In their endorsement, Seagate stated that:

           "Disk Technician Gold sets the standard for hard drive
            preventive maintenance software. Seagate recommends the use of
            Disk Technician Gold to ensure error-free data storage
            throughout the service life of your hard disc drive."

         Disk Technician Gold's key component is a 14K memory-resident
         device driver (not a TSR) that becomes part of the DOS operating
         system and Windows 3.1, continuously and automatically providing:


                                         20

               Disk Technician Factory Test for Seagate Drives Manual



           * Error detection, diagnostics and repair -- on the fly, in the
             background, with no system performance degradation.

           * Crash prevention and hard error data recovery and relocation
             -- on the fly.

           * Advance warning of electronic, mechanical and media failure
             for all hard drive and computer components affecting data
             reliability -- on the fly, in the background.

           * Passive system, disc and data diagnostics.

           * Test results that match those of Seagate factory hardware.

         A separate, pull-down menu program provides interleave testing
         and resetting, nondestructive low-level formatting,
         defragmenting, manual drive testing, reports and interface
         customization. An optionally installed virus prevention
         device driver is also included.

         Software Installation, Configuration and Setup:

         Installation of Disk Technician Gold is both simple and
         straightforward. End users either allow the program to make
         installation decisions, or they make their own step-by-step
         choices. Once files are installed, Disk Technician Gold
         configures itself to the host system by measuring and testing the
         specific hardware and software parameters, including hard disc
         drive geometry. It then performs a system integrity test,
         followed by media certification (see the (see the System
         Integrity Test Hard Disc Media Certification sections in this
         white paper for more information). Once these steps have been
         completed, no further user interaction is required.

         How Real-Time Error Detection Works Without Performance
         Degradation:

         Disk Technician Gold detects errors by testing all hard drive
         accesses while working transparently in the background of other
         programs, without interrupting normal activity, and without
         system performance degradation. In fact, because it handles
         block data transfers more efficiently than DOS, there is a net
         gain of about 1% in average data transfer rate with Disk
         Technician Gold installed. (The rate will be slightly slower on
         very large data transfers; faster on small ones.)

         When a soft error is detected, its location is recorded in the
         databank (a special file created during installation).

         The next time the computer is booted, Disk Technician Gold
         automatically performs a Bootup System Check (which includes a
         series of test routines designed to quickly check the major
         components of the hard drive and its subsystems). The databank is
         scanned for any new error locations recorded since the last
         bootup. Any data in these locations is copied into RAM, then each
         location is tested by writing, then reading back, worst case test
         patterns and their inversions.
                                         21

               Disk Technician Factory Test for Seagate Drives Manual



         Disk Technician Gold is the only software able to measure the
         exact number of attempts the hard drive makes while accessing a
         particular sector. If testing determines that the soft error is
         normal (non-repeating), the data is returned to its original
         location. This is because a non-repeating soft error is a
         harmless, random and normal event.

         However, an abnormal (repeating) soft error is dangerous and may
         continue to recur at the same location unless corrective action
         is taken. It is a strong indicator that the sector is in a
         failure mode (i.e., the soft error rate is likely to escalate
         rapidly to hard, or unreadable, status). If testing determines
         that the number of soft errors is in excess of the threshold for
         reliable data storage set by Seagate engineering, the data is
         relocated to a new, safe location. The unsafe location is then
         blocked from further use by marking it bad in the FAT, all
         automatically without operator intervention.

         After the data is safely rewritten, Disk Technician Gold records
         the location and type of error in the databank, then uses the
         information for two separate purposes:

           1. Intermittent error detection and elimination. Disk
              Technician Gold compares past test results with current
              results to determine if a repeating soft error hit
              (occurrence) is intermittent. This is when an area produced
              a repeating soft error hit in the past, was repaired, and
              has now produced another such hit.

              If Disk Technician Gold's expert system rules that the hit
              is recurring intermittently, any data in the area affected
              is moved to a good area and the unsafe area is marked bad
              in the FAT.

           2. Hardware failure advance warning. The final step in the
              Bootup System Check is an expert system analysis of the
              databank to determine if the error is part of a developing
              pattern indicating imminent hardware failure. The importance
              of this step to data reliability cannot be overemphasized,
              since the majority of perceived hard drive failures are not
              actually caused by the hard drive itself. Patterns
              recognized by the expert system must not only encompass the
              hard disc drives electronics, mechanics and media, the
              controller or adapter -- but also ribbon cables and
              connectors, as well as non-hard drive computer components
              that affect data reliability, such as the power supply.

         Each of the many causes of hardware failure has its own, unique
         signature. For example, as the disc platter spindle bearing
         begins to fail, the platters begin to wobble microscopically. The
         further away from the platter spindle bearing, the greater the
         wobble. This may cause variations in the flying height of the
         read/write heads with respect to the platters. This, in turn,
         results in an intermittent high soft error rate, greatest on the
         outer edges of the discs and gradually decreasing towards the
         spindle.

                                         22

               Disk Technician Factory Test for Seagate Drives Manual


         When such a failure pattern is recognized, Disk Technician Gold
         displays a message directing users to immediately back-up their
         data and consult a hardware service technician.

         However, people responsible for maintaining data integrity and/or
         hard drive systems on multiple computers (MIS management, PC
         managers and coordinators, service maintenance departments, VARs,
         consultants, etc.) were concerned that, despite the seriousness
         of the warning message, it might still be ignored. For these
         people, then, the warning message can be self-modified to direct
         end users to a specific course of action.

         Depending on the type of failure, the user typically receives
         from a few days' to a few weeks' advance warning. As a diagnostic
         aid to service technicians, the users guide contains a list
         ranking the most likely reasons the warning message was
         generated.

         The entire Bootup System Check, including testing and repairs,
         typically takes only a few seconds, and may be bypassed (as a
         convenience for users who must reboot their systems often). Note
         that testing, repair, relocation of data and updating of the File
         Allocation Table (FAT) all occur as part of the bootup process.

         The net result is that all hard drive and associated data
         reliability issues are handled automatically and transparently as
         operating system background tasks.

         Real-Time Recovery From Critical And Hard Errors:

         Most of Disk Technician Gold's real-time error detection and
         preventive maintenance functions are transparent. The single
         exception is when it detects a critical error (defined as one
         that would result in data loss or a drive crash). There are three
         types:

           1. Excessive soft errors. These indicate imminent failure,
              because on the next access attempt the soft error rate may
              have escalated to such a degree that the area may be totally
              unreadable (a hard error). For this same reason, any hard
              disc location exhibiting excessive soft errors during
              Seagate final quality control testing is marked in a "Bad
              Track Report" or "Microdefect Map" for removal from use.

           2. Excessive soft errors and Error Correction Code (ECC) was
              invoked to reconstruct data. (ECC is defined as a
              proprietary series of algorithms, specific to an individual
              controller or hard drive, used to reconstruct data after it
              has exhausted its preset number of attempts to read data
              from a track or sector. This should not be confused with
              on-the-fly ECC.) On the next disc access, the soft error
              rate may have escalated such that ECC may not be able to
              reconstruct the data.
              Note that Disk Technician Gold does not use ECC alone as a
              criterion for determining media reliability. Here are three
              of many reasons:


                                         23

               Disk Technician Factory Test for Seagate Drives Manual


                A. Individual controller and hard drive designs vary
                   widely in the number of retries they will make to get
                   data before invoking ECC. Many older XT-class
                   controllers allow 30 and more retries (soft errors)
                   before invoking ECC, an unacceptably dangerous
                   situation for data.

                B. Conversely, technology now being introduced in small
                   form drives do not allow any retries whatsoever before
                   invoking ECC.

                   Because soft errors are both commonplace and typically
                   non-repeating in the normal PC hard drive environment,
                   ECC-dependent error detection could result in an
                   untimely and unwarranted condemnation of a perfectly
                   good drive.

                C. Until recently, most drives and controllers reported
                   ECC information, which was ignored by DOS, but
                   available to diagnostic software. Today, however, most
                   block transfer drives (IDE and SCSI) and advanced
                   controllers do not return ECC status at all, such that
                   diagnostic software cannot detect any ECC activity
                   whatsoever.

           3. Hard error (the area was completely unreadable). In this
              case, ECC may or may not have been invoked. If it was
              invoked, it failed to reconstruct the data. If not invoked,
              it was because the data involved did not meet ECC criteria
              for potential reconstruction.

         Imagine someone working in an application such as Lotus 1-2-3 or
         WordPerfect. The person has just opened a file that is in the
         process of being read from the hard drive into RAM. Suddenly,
         without warning, DOS generates an error message such as "Sector
         not found," or "Disk error reading FAT," followed by "Abort,
         Retry, Fail?". Until the introduction of Disk Technician Gold,
         the only options at this point were rarely successful, after-the
         -fact recovery and reconstruction attempts.

         However, when Disk Technician Gold encounters a critical error,
         it immediately begins a series of emergency actions:

           1. It recovers the data from the affected area, using a
              combination of seek-profiling, ECC and other proprietary
              techniques.

           2. The recovered data is recorded in the databank, along with
              the error location.

           3. Disk Technician Gold sounds an audio warning signal and
              displays an on-screen message to alert users that a critical
              error has been encountered. The message prompts users to
              save their work, exit the program they are using, and reboot
              their systems:



                                         24

               Disk Technician Factory Test for Seagate Drives Manual


              Users working in some graphic environments are alerted to
              critical errors by the audio signal only. A special decal
              (called the Audio CueCard) that is usually affixed to the
              keyboard or monitor frame, is included to provide the same
              step-by-step instructions displayed on-screen:

         4. When the system is rebooted, Disk Technician Gold tests the
            area, repairs it if possible, or, if the area is unrepairable,
            relocates the data to a new, safe location and blocks the
            unsafe location from further use.

         Once the problem has been resolved, Disk Technician Gold updates
         the databank and FAT, and returns to the system prompt. The user
         may then safely resume working in the interrupted program.

         Real-Time Virus Prevention:

         Disk Technician Gold includes an optionally installed, 7K memory-
         resident Virus Detector to help protect systems and data. Like
         the Error Detector, the Virus Detector is a device driver that
         loads into RAM during bootup and works transparently in the
         background of other programs.

         The Virus Detector helps to protect hard drives against the most
         common form of viral infection, where viruses attach themselves
         to other files and begin mutating and reproducing.

         Disk Technician Gold acts to stop viruses before they can attach
         themselves to critical files by continuously monitoring write
         activity to registered file types. Whenever an attempt is made to
         write one of these files, Disk Technician Gold sounds an audio
         warning signal and displays an on-screen message.

         Of course, not all write attempts to protected files indicate the
         presence of a virus. However, Disk Technician Gold does make
         users aware of suspicious write attempts and provides the option
         to abort them.

         Menu-Driven Tests:

         A key benefit of Disk Technician Gold is that, once installed, no
         user interaction is needed to maintain the hard drive system in
         factory-perfect condition. However, should users wish to perform
         comprehensive drive tests, Disk Technician Gold includes several
         on a separate, pull-down menu program:

         System Integrity Test. This battery of tests is similar to, but
         more comprehensive than, the Bootup System Test. Tests include:

           * A self-examination of Disk Technician Gold for evidence of
             virus contamination, and for the integrity of the critical
             databank file.

           * Checking the hard drives seek mechanisms for gross failure.
           * Confirming the ability of DOS to create, open, write, read,
             close and delete a file on the drive being tested.


                                         25

               Disk Technician Factory Test for Seagate Drives Manual


           * Verifying the integrity of the boot record, directory, and
             FATs.

           * DOS CHKDSK-type routines to identify lost clusters,
             crosslinked chains, allocation errors, and subdirectory
             errors.

         Like the Bootup System Test, the System Integrity Test also tests
         and repairs, detects intermittent errors, and checks for signs of
         hardware failure. The System Integrity Test normally takes about
         one minute for most drives, depending on the size and speed of
         the drive, the computer, and the nature and number of problems
         found.

         Hard Disc Media Certification. This is Disk Technician Gold's
         most comprehensive test. Media Certification thoroughly tests
         every area on the hard drive for soft, ECC and hard errors. It
         either repairs those areas that produced errors; or, if an area
         is unrepairable, it relocates any data in the area to a new, safe
         location and marks the area bad in the FAT.

         In addition to test and repair, Media Certification initializes
         (or updates) the databank, recreates an updated media defect map,
         and recertifies the drive for reliable data storage and normal
         use.

         Media Certification typically takes from 20 seconds to five
         minutes per megabyte, depending upon the speed of the computer
         and hard drive. An interrupt/resume feature allows users to leave
         the operation and return to other applications. Then, when they
         return to Media Certification, they will be asked if they wish to
         resume from where they stopped.

         Interleave Test/Low-Level Format. Interleaving matches the way
         data is arranged on hard disc recording tracks to the speed at
         which the controller can read the data sequentially. Disk
         Technician Gold tests various interleave settings, then
         determines and displays the optimal setting for maximum data
         throughput speed. Users may then perform a nondestructive low-
         level format and reset the interleave to the determined setting,
         or choose their own.

         For drives that allow low-level formatting and resetting of the
         interleave, choosing the correct interleave can make a
         significant difference in data access time. Drives that do not
         allow low-level formatting and resetting of the interleave are
         quickly identified as ineligible by Disk Technician Gold
         (typically those using the SCSI interface, IDE drives, drives
         using translating controllers, and even some MFM/RLL drives).

         However, low-level formatting and resetting of the interleave on
         "ineligible" drives are unnecessary, since these procedures only
         need to be performed once in the lifetime of a drive and have
         already been done by Seagate.

         An Important Improvement In Failsafe Architecture:


                                         26

               Disk Technician Factory Test for Seagate Drives Manual


         Some of the operations performed by Disk Technician Gold require
         relocating data, and at certain times the data being relocated
         only exists electronically in RAM. Should a power failure occur
         at precisely this moment, some data could be lost. (It should be
         noted that, since data relocation occurs rapidly, there is little
         risk of losing data during Disk Technician Gold operations as a
         result of power failure.)

         However, for battery-powered computer users, or those who require
         the ultimate assurance against data loss, Disk Technician Gold
         provides an optional safe mode (also called failsafe
         architecture) for media certification, testing and resetting
         interleave, nondestructive low-level formatting, and
         defragmenting.

         The safe mode guards against data loss by requiring that a copy
         of data undergoing relocation remains recorded on the hard drive
         at all times, either in its original location or in a special
         duplicate location. By eliminating instances when data exists
         solely in RAM, the possibility of data loss due to power problems
         is eliminated.

         Disk Technician Gold's failsafe architecture offers a significant
         improvement over previous methods. The problem was one of limited
         effectiveness: data was protected only in the event that power
         failed while the data file itself was being accessed. However, if
         the FAT or a directory was being accessed when power failed, all
         data on the affected drive could be lost. With Disk Technician
         Gold, failsafe architecture works even if the FATs and directory
         are being updated at the time of power failure.

         Additional Features:

         Media Defect Report. This report looks much like the Defect Map
         affixed to ST506/412 drives, although it is more detailed because
         of the additional types of errors detected by Disk Technician
         Gold's expert system and continuous testing.

         The Media Defect Report shows the location and number of bad
         sectors on the drive, as well as the reason why they have been
         marked out. (A bad sector is defined as one that cannot store
         data reliably, as determined by Seagate engineering standards.
         Such sectors are blocked from use by marking them bad in the
         FAT.)

         Monitored/Soft Error Report. This report shows the sectors on the
         hard drive that produced a repeating soft error hit during
         testing, but were successfully repaired. These sectors are
         monitored during subsequent tests in order to determine whether
         the hits were random or are part of a repeating error pattern
         indicating an intermittent error or impending hardware failure.

         If subsequent testing determines the sector to be unreliable, it
         will automatically be blocked from use by marking it bad in the
         FAT. Then, test information for this sector will be deleted from
         the "Monitored/Soft Error Report" and added to the "Media Defect
         Report."

                                         27

               Disk Technician Factory Test for Seagate Drives Manual


         Command Line Operation. Those responsible for maintaining
         multiple systems may wish to set-up a user-transparent hard drive
         optimization program. The option of command line operations
         provides the ability to bypass menus, set-up time-specific, self-
         executing batch files, etc.

         Additionally, users who normally leave their systems on
         continuously can setup a command line to run Disk Technician
         Gold's Bootup System Check occasionally, in order to test and
         repair error locations detected by the device driver program.
         Still other users may prefer to schedule automatic drive
         defragmenting by setting-up a self-executing batch file.

         System Requirements:

         * IBM PC, XT, AT, -286, -386, -486, PS/1, PS/2 or 100 percent
           compatible with 640K of memory.

         * About 14K of RAM for the Error Detector device driver (high
           memory loadable).

         * MS-DOS 3.1 - 6.0; DR DOS 3.41, 5.0 and 6.0.

         * Compatible with Windows 3.1. However, Windows is not a
           requirement.

         * Hard disc drive.

         Hard Drive Specifications:

         * Interfaces and Drives:  IDE, SCSI-1, SCSI-2, Fast SCSI-2, ESDI,
           ST506/412.

         * Controllers and Encoding Schemes:  MFM, RLL, ARLL, ERLL,
           translating, ZBR (Zone Bit Recording).

         * Partitions:  Supports any size DOS partition.

         Optional Requirements:

         * 7K of RAM for the Virus Prevention device driver (high memory
           loadable).

         * A Microsoft mouse or 100 percent compatible.














                                         28

               Disk Technician Factory Test for Seagate Drives Manual


         Other:

         * Works with most on-the-fly data compression software, including
           DoubleSpace, Stacker, SuperStor, SuperStor Pro.

         * Works with QEMM 386, 386 MAX and most other third-party memory
           managers.
         * Works with both hardware and software caching.

         * Works with programs that keep a duplicate version of the FAT in
           RAM (such as the DOS program FASTOPEN) or on the hard drive.

         * Not copy protected.

         * Free, unlimited technical support by telephone, fax and BBS.

         Conclusion:

         Disk Technician Gold software ensures PC hard disc drive data
         reliability by providing continuous, real-time background
         diagnostics, repair and recovery -- coupled with advance warning
         of imminent failure for hard drive electronics, mechanics and
         media, as well as other hard drive-related computer components
         that affect data. Once installed, Disk Technician Gold becomes
         part of the DOS operating system and requires no further user
         involvement.

         Disk Technician Gold is manufactured by Disk Technician
         Corporation, of San Diego, California. It is sold worldwide
         through its authorized distributors and is available at dealers
         everywhere. Development of Disk Technician technology has been
         continuous since 1980, paralleling the introduction of personal
         computer hard drives. The first commercial version was shipped in
         March, 1987. Since that time, newer versions have kept pace with
         advancements in hard drive, controller, operating system and CPU
         development, culminating with Disk Technician Gold, which
         prevents data loss by making hard drives continuously self
         -repairing.

         In 1992, Seagate Technology Inc. determined that test results
         from Disk Technician software precisely matched those of its
         factory test hardware, and began distributing the Seagate version
         of Disk Technician to its distributors for field testing and
         recertification of its drives. For more information, call Steve
         Luster at Disk Technician Corporation, (619) 274-5000.


         Disk Technician Corporation
         1940 Garnet Avenue
         San Diego, California 92109 USA
         Corporate Telephone 619 274 5000
         Technical Support 619 272 4000



                                      -END-


                                         29