CONVERGE - A CRT Testing Program


          DESCRIPTION:

            CONVERGE is a highly shareware program which is a useful
          evaluation tool for testing VGA (and higher) resolution monitors.
          CONVERGE will show such anomalies as geometric distortion,
          pincushion, misconvergence, and color smearing. Such testing is
          extremely valuable in evaluating monitor performance (you will be
          amazed at how many high-priced high-rez monitors are mis-
          converged!) when purchasing, or to spot potential trouble in an
          existing monitor.

          DISCUSSION:

            Color CRT monitors use 3 separate colors (red, blue and green)
          to optically generate the various shades of the color spectrum on
          the monitor face. Proper operation requires that each of the
          electron guns inside the picture tube be precisely aligned to
          it's assigned color phosphor dots on the picture tube face. (If
          you look at your monitor face with a magnifying glass, you can
          actually see the 3 colors of phosphor dots.) If any of these guns
          are mis-aligned, the resulting display can exhibit blurred color,
          bad color, or a distorted image.

            Besides mis-convergence (the color alignment mentioned above),
          monitors are often plagued with raster (scanning) distortion. To
          paint the image on the picture tube, the beams from the 3
          electron guns are swept across the face of the picture tube in a
          particular pattern. The pattern is an extremely fast left-to-
          right sweep that is repeated in a downwards fashion. Older CGA
          monitors used a very slow sweep rate, and as a result, tended to
          flicker. New high-resolution monitors operate at a much faster
          rate, so the eye does not perceive any noticeable flicker from
          the screen.

            If the circuitry inside the monitor is operating improperly, or
          if the circuitry is of a cheap design, then certain raster
          distortion effects become apparent when using the convergence
          grid.

            PINCUSHION DISTORTION is a 'bending' of the left and right
          edges of the picture on the screen:


                     _______________________
                     \                     /
                      \                   /
                      |                  |
                      |                  |
                     /                    \
                    /______________________\




                                                                     Page 1





                          CONVERGE - A CRT Testing Program



          This type of distortion is caused by a mis-adjustment in the
          horizontal (left-right) deflection circuitry. You can test for
          this type of distortion by selecting the convergence grid and
          holding a ruler or other straight-edged object up to the monitor
          screen. By examining the white vertical bars at both the left and
          right edges of the screen, any pincushion distortion should be
          clearly seen. Some monitors such as the NEC 3F,4F,5F and 6F
          series have an adjustment control to correct this.

          KEYSTONE DISTORTION is a trapezoidal shaped pattern. Typically it
          appears as an image which is wider at the top of the screen, then
          tends to become narrower at the bottom:

                    ______________________
                    |                    |
                    |                    |
                     |                  |
                     |                  |
                      |                |
                      |________________|

          This type of distortion is invariably caused by an inadequate or
          malfunctioning power supply in the monitor. Occasionally a weak
          flyback transformer will create this symptom as well. The
          convergence grid pattern again may be used, only in this case the
          top and bottom white lines are measured for length. If there is a
          noticeable difference (approximately 1/8" for a 14" monitor),
          there is something wrong with the monitor or it's design.

          GEOMETRIC DISTORTION refers to a non-symmetrical scanning
          pattern. Usually this is evidenced by a distorted corner,
          typically in the upper right corner of the screen:

                   ________________________
                   |                      /
                   |                     /
                   |                    |
                   |                    |
                   |                    |
                   |____________________|

          Geometric distortion comes from an improperly corrected picture
          tube. During manufacture, small magnets are placed in certain
          locations on the rear portion of the picture tube. Most monitor
          manufacturers do a pretty good job of alignment, but occasionally
          one slips through. This is particularly true of the Taiwanese
          monitors. Again, the convergence grid may be employed to check
          for this, as the outer white rectangle should have 90 degree
          square corners. Occasionally some types of monitors will exhibit
          a 'blooming' effect, most notably in the center of the screen.
          This appears as a bulging outwards of the grid squares, much like
          that of a balloon surface that is expanding.




                                                                     Page 2





                          CONVERGE - A CRT Testing Program



          COLOR ALIGNMENT (CONVERGENCE) is crucial for a clear, sharp
          image, particularly at high resolutions. As mentioned earlier in
          this discussion, the three electron guns (red, blue and green)
          must align with their respective phosphor dots to produce a
          proper image. If this alignment is off, the edges of any graphic
          elements will tend to have fuzzy edges, or a slight color shadow.
          This is where the convergence grid really shines. The vertical
          lines are yellow in color, which requires exact alignment of the
          red and green guns. The horizontal lines are magenta, which
          requires exact alignment of the red and blue guns. Finally, the
          outer rectangle is white, which requires the exact alignment of
          all three guns.

            Any color mis-convergence will show up as a separation of
          color, or the appearance of color shadowing. For example, if the
          red and blue guns are off, the horizontal magenta line will tend
          to be blue on one side, and red on the other. Occasionally
          geometric scan distortion will appear, causing the line to be
          perfect at one end, and separate at the other. The author recalls
          one instance where a monitor was so bad that the magenta line
          actually turned into separate blue and red lines! A similar
          situation occurs with the vertical yellow lines, only this time
          the colors will be red and green.

            Lastly, the overall color balance of the monitor may be
          observed with each of the 3 color flood screens. Look for any
          blotchy areas or shadows. Blotches are usually caused by a defect
          in the phosphor coating. Shadowy patches are usually a result of
          improper demagnetization of the shadow mask, and can usually be
          cleared up with a thorough degaussing. (Turn the monitor on and
          off several times, waiting about 2 to three minutes per cycle.)
          The white screen shows the overall color balance and 'color
          temperature' of the phosphors. Some monitors tend to have a
          'warm' white, leaning a bit towards the red, while others tend to
          appear greenish, similar to florescent lamps. This is more of a
          personal preference.

            For those people who are trained in electronic repair of
          televisions and monitors, this program is also a handy tool to
          use when fixing monitors. WARNING! - If you are NOT TRAINED to
          perform these types of repairs, DO NOT disassemble or take your
          monitor apart! If your monitor is exhibiting any of the symptoms
          mentioned, please take your monitor to a repair facility! Lethal
          electrical current is present inside the monitor, which can cause
          serious injury or death!

          PROGRAM OPERATION:

            The program initially tests to see if a VGA-compatible graphics
          adapter is present. If so, then the program will display the
          convergence grid. By pressing the space bar, the program will
          cycle through each screen indefinitely. To exit the program,




                                                                     Page 3





                          CONVERGE - A CRT Testing Program


          press the ESC key. NOTE: the space bar has no effect if a
          particular screen is specified in the command line.

          PROGRAM PARAMETERS:

            Sytax: CONVERGE [/c] [/b] [/g] [/r] [/w] [?]

                ? - Echos a brief help text on the screen. No action is
                    taken.

               /c - Displays the convergence grid. Each square is exactly
                    on a 1:1 pixel aspect ratio. (Each side is exactly the
                    same number of pixels in length.)

               /b - Displays the blue flood screen.

               /g - Displays the green flood screen.

               /r - Displays the red flood screen.

               /w - Displays the white flood screen.

          SHAREWARE CONCEPT:

            Shareware is a non-conventional approach to software
          distribution. Unlike regular commercial programs, shareware
          allows a 'try-before-you-buy' approach. In most cases, the
          programs are just as bit as good (if not better in some
          instances!) as the programs you buy at a computer store.

            Shareware ISN'T freeware! In most cases, the software author is
          a professional who makes at least part of his or her living on
          the registration of the software program. Typically the user is
          enticed into registration by added features, free updates, etc.

            Shareware depends upon the user to make it work. It's up to
          you!

          Registration:

            This program is 'donate-ware', which is similar in concept to
          shareware. The author makes no claims as being a professional
          software engineer, rather, the author is a disabled hardware
          engineer who enjoys tinkering with programs, and making the
          hardware work better.

            If you find that this program is useful, and saves you some
          time and headaches, the author would appreciate a $5.00 (US)
          suggested donation. This amount would include a 'registered' copy
          of the program (without the shareware notice), and the eternal
          thanks from the author. Considering that the cost of monitors,
          this program may make the difference between a wise purchase and
          a costly mistake. With that in mind, 5 bucks is a very small
          investment! Of course, any amount is appreciated. Oh, please



                                                                     Page 4





                          CONVERGE - A CRT Testing Program


          specify whether you want a 360K, 5-1/4" or 720K, 3-1/2" floppy
          when you register.

          .....and the address is:

                     Brent Turner
                     P.O. Box 3612
                     Fullerton, CA, 92634-3612

            NOTE: Foreign (non-US) users please include a few extra bucks
          for the postage! Thanks.

          THE LEGAL STUFF:

            This software is distributed on an as-is basis. The author has
          made reasonable attempts to ascertain it's performance, but
          cannot guarantee that it will work in every instance. The author
          is not responsible for any damages, or loss of data resulting
          from the use of this program.

            The shareware version of this program may be freely distributed
          as long as all files are included in the package. The registered
          version may not be copied or duplicated.

            Shareware vendors may distribute this program as long as the
          cost per disk does not exceed $5.00. This program may be included
          (bundled) with other programs of like nature, so long as the
          above cost-per-disk stipulation is met.

            The original source code is not available.



























                                                                     Page 5